## Slide 1: MeRHIC Design
V.Ptitsyn
on behalf of MeRHIC Design team:
M. Bai, J. Beebe-Wang, I. Ben-Zvi, M. Blaskiewicz, A. Burrill, R. Calaga, X. Chang, A. Fedotov, H. Hahn, Y. Hao, L. Hammons, D. Kayran, V. N. Litvinenko, G. Mahler, B. Parker, E. Pozdeyev, T. Roser, A. Pendzick, S. Plate, T. Rao, S. Tepikian, D. Trbojevic, E.Tsentalovich, N. Tsoupas, J. Tuozzolo, G. Wang

## Slide 2: Talk Outline
MeRHIC layout and general description
Design beam parameters and luminosity
Design components:
  Electron linac
  Recirculation passes
  Interaction region
  Injector
Summary

## Slide 3
STAR
PHENIX
e-
p
4 GeV
electrons
80-250 GeV
protons
100 GeV/u
Au ions
RHIC and MeRHIC
  MeRHIC – Medium energy eRHIC .
  First stage of the electron-ion collider at BNL.
  Electron acceleration is based on energy-recovery linacs.
  Electrons collide with protons and ions from RHIC Blue ring. Only minimal modifications of existing RHIC rings at IR region.
  Polarized electron and proton beams. Longitudinal polarization orientation at the collision point for both beams.
  Parallel operation with the p-p (or ion-ion) collisions at PHENIX and STAR detectors.
Up to 63 GeV center mass energy

## Slide 4
MeRHIC at IR2 region
(April 09)
Linac 1
Linac 2
Main ERLs; 36 cavities x 18 Mev/cav = 0.65 GeV per linac
0.75, 2.05, 3.35 GeV
0.1, 1.4, 2.7 GeV
Pre-accelerator 90 MeV ERL
Electron gun
0.1 GeV
Beam dump
2nd harmonic
cavities
Fundamental cavity on 4 Gev pass
IR2 region features: - asymmetric detector hall (appropriate for asymmetric detector for e-p collisions) - long wide (7.3m) tunnel on one side from the IR (enough space to place energy recovery linac(s))
Main components:
100 MeV injector on the basis of polarized electron gun (50 mA) and pre-accelerator ERL. -Two main ERLs (one of them in the RHIC tunnel) with maximum 0.65 GeV energy gain per linac. -Recirculation passes: warm magnets, acceptable synchrotron radiation power.
4 GeV
e-
p

## Slide 5: Proton and ion beam for MeRHIC
Goal: modifications for proton (ion) beam have to be minimal
IR design: use of existing triplets and D0 magnets, removal of IR2 DX magnets, addition of warm dipole magnets.
Addition of two spin rotators in Blue ring.
Required proton beam parameters are either already achieved or planned to be achieved in 2-3 years for RHIC operation.
MeRHIC will take advantages of planned improvements in RHIC (for RHIC operation): 56 MHz SRF, stochastic cooling (for ions) …

## Slide 6: MeRHIC parameters for e-p collisions
 | Baseline design (no cooling) |  | Pre-cooled at the injection energy |  | With high energy cooling (CEC) | 
 | p | e | p | e | p | e
Energy, GeV | 250 | 4 | 250 | 4 | 250 | 4
Bunch repetition time, ns | 105 | 105 | 105 | 105 | 105 | 105
Bunch intensity, 1011 | 2.0 | 0.31 | 2.0 | 0.31 | 2.0 | 0.31
Bunch charge, nC | 32 | 5 | 32 | 5 | 32 | 5
Normalized emittance, 1e-6 m, 95% for p / rms for e | 15 | 73 | 6 | 29 | 1.5 | 7.3
rms emittance, nm | 9.4 | 9.4 | 3.8 | 3.8 | 0.94 | 0.94
beta*, cm | 50 | 50 | 50 | 50 | 50 | 50
rms bunch length, cm | 20 | 0.2 | 20 | 0.2 | 5/20 | 0.2
beam-beam for p /disruption for e | 1.5e-3 | 3.1 | 3.8e-3 | 7.7 | 0.015 | 7.7/30
Peak Luminosity, 1e32, cm-2s-1 | 0.93 |  | 2.3 |  | 9.3 | 

## Slide 7: MeRHIC Linac Design
703.75 MHz
1.6 m long
Drift
1.5 m long
100 MeV
100 MeV
4 GeV
65m total linac length
All cold: no warm-to-cold transition
E.Pozdeyev
Based on BNL SRF cavity with fully suppressed HOMs
Critical for high current multi-pass ERL
Modular structure
I. Ben-Zvi
Current breakdown of the linac
N cavities = 6 (per module)
N modules per linac = 6
N linacs = 2
L module = 9.6m
L period = 10.6 m
Ef = 18.0 MeV/m
dE/ds = 10.2 MeV/m

## Slide 8
Recirculation pass lattice
Achromatic and isochronous arc design
Flexible Momentum Compaction Lattice-> adjustable M56 parameter
Large dipole filling factor (64%) -> reduced synchrotron radiation (< 2kW/m)
Initial dipole and quadrupole magnet design has been developed
Vertical arrangement
of recirculation passes
D. Trbojevic, N. Tsoupas
27.8m

## Slide 9: IR Design Features
Provides the integration of detector dipole magnets into the beam separation scheme
Provides the ability to vary the proton beam energy from 80 to 250 GeV at constant electron beam energy.
Provides effective SR protection:
soft bend (~0.05T) is used for final bending of electron beam
Focusing elements are located far from the IP (first electron quad at 11m)
© J.Bebee-Wang
p, Au
e
Solenoid, 4 T
1T,3m
dipole
1T,3m
dipole
40 m
Soft
dipole
Soft
dipole

## Slide 10
Injector and Pre-accelerator Design
Gatling Gun (Ek=200keV)
10 MeV Injector
90 MeV Linac
1.4, 2.7, 4 GeV
11 m
11 m
10 MeV x 50 mA
0.5 MW Beam Dump
from MeRHIC
arcs
to MeRHIC vertical combiner
10 MeV Booster Linac
30 m
Injector Parameters:
Polarized Gun (200kV)
Cathode GaAs,
Laser 780nm
Emax= 10 MeV
Iavr =50 mA,
Q per bunch =5nC
Design realizes bunch compression and spin direction control
Pre-accelerator linac:
Standard MeRHIC linac cryomodule (~10m) with 5x703 MHz 5-cell cavities and one 3rd harmonic 2.11 GHz inside.
Two transition sections (0.5 m each) attached from both ends
Energy gain 90 MeV
Output beam parameters :
E=100 MeV
Iavr=50 mA
Ipeak=500 A
Reprate = 9.8 MHz
Emittance =70 mm-mrad
Bunch length = 2-3 mm
dE/E = 1E-3
X. Chang and D. Kayran

## Slide 11
Summary: MeRHIC Design Status
The lattices of all machine components (injector, recirculation passes, linac, interaction region, mergers/splitters) have been developed. (D. Trbojevic’s and D.Kayran’s talks)
The interaction region with the detector fully integrated into the accelerator environment has been designed. (J. Beebe-Wang’s talk)
The most important beam dynamics effects, defining achievable beam parameters, machine luminosity and polarization have been studied. (M.Blaskiewicz’s, M.Bai’s amd Y.Hao’s talks)
No show-stoppers had been found.
Design development of high current polarized electron gun is underway. (X.Chang’s talk)
Conceptual designs of superconducting linac and its cryomodule have been done.
(I. Ben-Zvi’s talk)
Engineering realization of various design aspects and accelerator system (magnets, vacuum, civil construction …) has been considered. (J. Tuozzolo’s talk)
Detailed cost estimate of MeRHIC has been completed, including all machine systems, civil construction and utilities. In early October 2009, an Internal BNL Committee reviewed the MeRHIC cost estimate. The cost came to ~$350mln (without the detector).