## Slide 1: EIC simulation under PHENIX Geant4 framework
Jin Huang
(BNL)

## Slide 2: Overview

## Slide 3: Overview
PHENIX software framework (Fun4All)
  Compact C++/STL framework, driving the analysis cycles
  Same framework to handle simulation and real data analysis
  Allow save/readback data object at any given breakpoint of analysis flow through formatted ROOT TTree files (DST)
  Software packages and expertise available in PHENIX internal repository
PHENIX Geant4 framework was systematically introduced around 2010 to drive Geant4 under PHENIX software framework
  PHENIX upgrade project has been heavily using this framework (sPHENIX proposal, “ePHENIX” concept and fsPHENIX concept)
  Large scale simulation production >6TB data for sPHENIX DOE scientific review alone
Beyond PHENIX
  Decision to relocate the framework and Geant4 part to GitHub for wider access/collaboration
  Continue evolving the framework
  Merge features from EICROOT or GEMC? Suggestions? Comments?

## Slide 4: Three major detector proposal/concept currently developed under PHENIX Geant4
sPHENIX proposal submitted to DOE
An EIC detector concept on top of sPHENIX
forward sPHENIX to bridge these two concepts

## Slide 5: The sPHENIX detector
sPHENIX: major upgrade to the PHENIX experiment aim for data @ 2020
Physics Goals: detailed study QGP using jets and heavy quarks at RHIC energy region
Baseline consists of new large acceptance EMCal+HCal built around recently acquired BaBar magnet. Additional tracking also planned
Successful DOE scientific review last month
A good foundation for future detector upgrades
Baseline detectors for sPHENIX
sPHENIX MIE, http://www.phenix.bnl.gov/plans.html

## Slide 6: An EIC detector concept
RICH
GEM
Station4
EMCal
HCal
GEM
Station2
R (cm)
HCal
p/A
EMCal
GEMs
EMCal & Preshower
TPC
DIRC
η=+1
η= 4
-1.2
GEM
Station3
GEMs
Station1
η=-1
e-
Aerogel
z (cm)
ZDC
z≈12 m
Outgoing
hadron
beam
Roman Pots
z≫10 m
R (cm)
z ≤ 4.5m
BBC
ePHENIX Δg projection
-1<η<+1 (barrel) : sPHENIX + Compact-TPC + DIRC
-4<η<-1 (e-going) : Crystal calorimeter + GEM trackers
+1<η<+4 (h-going) :
  1<η<4 : GEM tracker + Gas RICH
  1<η<2 : Aerogel RICH
  1<η<5 : EM Calorimeter + Hadron Calorimeter
Along outgoing hadron beam: ZDC and roman pots
Cost: sPHENIX MIE + 75M$ (including overhead + contingency)
arXiv:1402.1209

## Slide 7: Implementation in sPHENIX Geant4 An event display for SIDIS @ x≈5×10-3 and Q2=10 (GeV/c)2 Integrated in PHENIX software framework Material and field map implemented in details
p, 250 GeV/c
e-, 10 GeV/c
DIS e-
IP
TPC
GEMs
EMCal
Gas RICH
Aerogel
DIRC
Babar coil
EM Calo.
Hadron Calo.
EM Calo.
Hadron Calo.
BBC
Detailed layer structure implemented according to HBD NIM

## Slide 8: Or you can turn on/move a subset of detector on the macro level
IP
p/A
e-
e-going GEMs
-4.0<η<-1
TPC
-1<η<+1
h-going GEMs
1<η<2
TPC
GEMs
eGEM
RICH
gas RICH
1<η<4
Fringe field
1.5 T main field
Fringe field
Geant4 model of detectors inside field region
Tracking
Hadron PID
η
p/A
e-
DIRC
-1<η<+1
Aerogel RICH
1<η<2

## Slide 9: Physics before the EIC era:
p↑
p/A
IP
GEMs
Hadron Calo.
The ePHENIX forward detector can be constructed earlier → a unique forward program with RHIC’s pp/pA collision
White paper submitted to BNL in Apr 2014
Single jet in GEANT4
pT = 4.1 GeV/c, eta = 3
ePHENIX GEM + H-Cal
→ Forward jet with charge sign tagging
→ Unlock secrets of large AN in hadron collisions
+ reuse current silicon tracker & Muon ID detector
→ polarized Drell-Yan with muons
→ Critical test of TMD framework
+ central detector (sPHENIX)
→ Forward-central correlations
→ Study cold nuclear matter in pA

## Slide 10: More features

## Slide 11: Structure of PHENIX analysis framework (Fun4All)
Formatted ROOT file (DST)
Raw Data (PRDF)
G4/G3 Simulation
Input Managers
Output Managers
Fun4AllServer
Analysis
Module 1
Formatted ROOT file (DST)
Raw Data (PRDF)
Simulated Raw Data
Histogram Manager
Root File of histograms
From Dr. Chris Pinkenburg (BNL)
Analysis
Module N
…..
ROOT Command line
Output/Readback at any stage

## Slide 12: Implementation of Geant4
PHENIX framework link and use Geant4 like many other external packages (e.g. DB, fast jet, etc.)
Detector configurable from ROOT macros
Detector choose how to import data from Geant4 to data nodes (integrated G4Steps out-of-box)
Easy configure for different input formats, Geant4 physics list, etc.
Run Geant4 event display and control through ROOT command lines. A GUI will be nice
Analysis modules n
Digitalization
Detector Module 1
Geometry +Materials
Event generator
Pythia/HEPMC/…
Data nodes
Geant4 Tracking
Initial particles
PHENIX Analysis Framework
w/ interface to configuration macro in ROOT
Geant4 libs
Detector Module n
Outputs
...
Analysis modules 1
...
Real data

## Slide 13: SPACAL simulation
SPACAL implemented in sPHENIX simulation framework, in reference to Alexander Kiselev’s work in EICROOT for EIC RD1 and BeAST simulation
Covered full azimuthal and |η|<1.1 in s/ePHENIX
Large scale (TBs) simulation run with full Geant model of 20M fibers
10GeV, e+
2 cm
Side view
Energy resolution by Z. Liang
Elec. E ΔE/E
1 GeV 16%
4 GeV 8%
10 GeV 6%
s/ePHENIX implementation of SPACAL
Fibers :
diameter of 0.5mm
Spacing of 1mm
Hermetic and projective design in progress
R = 95cm
1-D projective SPACAL towers

## Slide 14: ePHENIX Gas RICH
R (cm)
Z (cm)
RICH Mirror
RICH Gas
Volume (CF4)
η=1
η=2
η=3
η=4
Entrance
Window
Focal plane
HBD detector
spherical
mirror
center
IP
High momentum hadron ID require gas Cherenkov
  CF4 gas used, similar to LHCb RICH
Beautiful optics using spherical mirrors
Photon detection using CsI−coated GEM in hadron blind mode
Magnetic field line most along track within the RICH volume → minor ring smearing due to track bending
Active R&D: recent beam test by the stony brook group
Beam test data
StonyBrook group
Purity
PID purity at η=4 (most challenging region w/ δp)
Courtesy: Stonybook group
Fermilab T-1037 data
Ring size (A.U.)

## Slide 15: Some RICH event display Courtesy: Nils Feege <nils.feege@stonybrook.edu>
photon tracking in full event
RICH Ring @ focal plane

## Slide 16: Final words
PHENIX analysis framework adopted Geant4 simulation around ~2010
All detector/analysis configuration are scriptable (through ROOT interface)
Three full detector proposal/concepts developed, large scale multi-TB simulation run
Framework is evolving, looking forward to adopting new features, new ideas and welcoming new users
Looking forward to a forum for discussing simulation issues in EIC community

## Slide 17: Backup

## Slide 18: Summary
Plan: PHENIX → sPHENIX → ePHENIX
ePHENIX : a comprehensive detector concept for 10x250 GeV EIC
h-going arm of ePHENIX perfect for forward pp/pA measurement (fsPHENIX), if constructed earlier
  Talk: CG.00003 Cesar da Silva
Active study on going : detector R&D, full simulation
Read more: https://www.phenix.bnl.gov/plans.html
Tracking
Hadron PID
EM and hadron calorimeter
η

## Slide 19: TPC resolution: Caveat - Magnetic Field Effect and Correction
Ideally, magnetic field along z axis for TPCs. BX/Y terms → corrections
Field map can reach quoted uniformity for Babar (±3% for central tracking volume) by some tuning on the yoke
But is it good enough for TPC? – Further optimization needed
  Assumption in LOI: we can deal with it in the end
→ Field correction ~ few mm in Rφ

## Slide 21: Implementing most complex geometry in current PHENIX G4 simulation
RICH Gas Container
TPC
TPC
TPC
RICH Windows
spherical mirror
Eight azimuthal sector
TPC
RICH Windows
spherical mirror
Six azimuthal sector
Full HBD w/ readout
RICH Windows
spherical mirror