## Slide 1: Future p-A: RHIC machine perspective Wolfram Fischer
15 April 2013
Jet Quenching RBRC Workshop, BNL
Notes: 14:30, 30 min

## Slide 2
2 superconducting 3.8 km rings
2 large experiments
100 GeV/nucleon ions up to U
255 GeV polarized protons
Performance defined by
1. Luminosity L
2. Proton polarization P
3. Versatility (species, E)
Relativistic Heavy Ion Collider 1 of 2 ion colliders (other is LHC), only polarized p-p collider

## Slide 3: Content
What do we have for p+Au collisions?
What do we still need for p+Au collisions?
Luminosity projection

## Slide 4: Delivered Integrated Luminosity and Polarization
Nucleon-pair luminosity: luminosity calculated with nucleons of nuclei treated independently; allows comparison of luminosities of different species; appropriate quantity for comparison runs.
Heavy ion runs
Polarized proton runs
Integrated luminosity L [pb-1]
Integrated nucleon-pair luminosity LNN [pb-1]
--- RHIC-II performance is here ---

## Slide 5: RHIC luminosity and polarization goals
parameter |  | unit | achieved |  | goals |  |  | 
Au-Au operation |  |  | 2011 |  | ≥ 2014 3D stochastic cooling + 56 MHz SRF |  |  | 
energy | GeV/nucleon |  | 100 |  | 100 |  |  | 
no colliding bunches | … |  | 111 |  | 111 |  |  | 
bunch intensity | 109 |  | 1.3 |  | 1.3 |  |  | 
avg. luminosity | 1026 cm-2s-1 |  | 30 |  | 40 |  |  | 
p-p operation |  |  | 2012 |  | ≥ 2013 source |  | ≥ 2014 source + e-lenses | 
energy | GeV |  | 100 | 255 | 100 | 250 | 100 | 250
no colliding bunches | … |  | – 107 – |  | – 107 – |  | – 107 – | 
bunch intensity | 1011 |  | 1.6 | 1.7 | 1.6 | 2.0 | 1.8 | 2.5
avg. luminosity | 1030 cm-2s-1 |  | 33 | 105 | 30 | 150 | 60 | 300
avg. polarization* | % |  | 59 | 52 | – 60 – |  | – 65 – | 
*Intensity and time-averaged polarization as measured by the H-jet. Luminosity-averaged polarizations, relevant in single-spin colliding beam experiments, are higher. For example, for intensity-averaged P = 48% and Rx = Ry = 0.2 (250 GeV, 2011), the luminosity-averaged polarization is P = 52%.

## Slide 6: Asymmetric ion species under consideration in RHIC (to date)
proton-gold (p-Au)
not yet done, part of the design
requires moving IR6 and IR8 DX magnets horizontally by ~1 cm
deuteron-gold (d-Au)
operated in 2003 and 2008
copper-gold (Cu-Au)
operated in 2012
Polarized proton-polarized 3He (ph-3Heh)
likely request when 3Heh is available
RBRC Workshop on 3Heh at BNL, 28-30 September 2011

## Slide 7: What do we have for p+Au collisions?
RHIC was designed for p+Au collisions
  Independent rings except DX magnets
  DX magnets movable (~1 shift)
With stochastic cooling initial Au beam size is at its maximum
  Allows for DX move in IR6 and IR8 only (~1 shift)
Solutions for lattice, injection and acceleration
  Lattice takes advantage of stochastic cooling
Machine with fast setup (beam-based feedbacks)
Experience with asymmetric collisions (d+Au, Cu+Au)
Proton beam with Nb = 2x1011, P = 55% with upgrades (OPPIS): Nb = 3x1011, P = 65%
Au beam with Nb = 1.3x109
with upgrades (EBIS/Booster/AGS/RHIC): 2.0x109 (emittance?)

## Slide 8: RHIC Design Manual
Run-11: Lavg = 30×1026cm-2s-1
Run-12: Lavg = 10.5×1031cm-2s-1 (with Pavg = 53%)

## Slide 9: RHIC Design Manual (July 1998)
IR design with beam splitting DX dipoles first
DX dipole
D0,Q1—Q3
DX dipoles
Lmag = 3.7 m, Bmax = 4.3 T
large aperture (18 cm coil ID)
only magnets that need training (~5 for IR6/8 only)
Notes: MAKE REAL CALCULATION FOR DX MOVE

## Slide 10: Now have full 3D stochastic cooling for heavy ions
M. Brennan, M. Blaskiewicz, F. Severino, PRL 100 174803 (2008); PRSTAB, PAC, EPAC
longitudinal kicker (closed)
horizontal kicker (open)
horizontal and vertical pickups
longitudinal pickup
5-9 GHz, cooling times ~1 h
vertical kicker (closed)
Notes: Frequency range: 5-8 GHz transverse, 6-9 GHz longitudinal

## Slide 11: Stochastic cooling in U—U operation

## Slide 12: Cu-Au store – new mode in 2012
10%/h
transverse emittances
luminosities
beam loss rates
25 mm.mrad
120x1026cm-2s-1
Cu and Au have different - intrabeam scattering growth rates (~Z4Nb/A2) rIBS,Au ≈ 2x rIBS,Cu
- cooling rates (~1/Nb) rSC,Au ≈ 3x rSC,Cu
Stores start with large e after undergoing instability at transition
Possible with stochastic cooling
Increase bunch intensity until loss at transition
Notes: Fillno 16991 06/15/12, last night

## Slide 13: p+Au easier with stochastic cooling
only need to accommodate initial Au emittances
sufficient to move IR6 and IR8 DX magnets
S. Tepikian, D. Trbojevic, C-A/AP/447 (Jan. 2012)
colliding IR move DX by 1cm

## Slide 14: p+Au easier with stochastic cooling
non-colliding IR
no DX move
S. Tepikian, D. Trbojevic, C-A/AP/447 (Jan. 2012)

## Slide 15: Beam control improvement – feedbacks on ramp
Blue orbits
xmean
ymean
xrms
yrms
M. Minty, A. Marusic et al.
Qx
Qy
Qy = 2/3
DQy = 0.006
x,yrms ≈ 20 mm ≈ 3% of rms size
Orbit feedback on every ramp allows for
Smaller yrms (smaller imperfection resonance strength)
Ramp reproducibility (have 24 h orbit variation)
Tune/coupling feedback on every ramp allows for
Acceleration near Qy = 2/3 (better P transmission compared to higher tune)
0.7
0.66
-0.2
0.3
Orbit [mm]
Tune
Notes: Fillno 15443, one of best stores

## Slide 16: Time-in-store as fraction of calendar time
Run-12 with low failure rates in all systems
Highest time-in-store ratios to date even with increased APEX time during 255 GeV protons, and few weeks per species
Have higher failure rates in Run-13 so far
85%
60%

## Slide 17: What do we still need for p+Au?
Demonstrate DX move by 1 cm
  Can be done at end of Run-13
  Move for p beam in Yellow, Au beam in Blue (different from d-Au)
If p beam in Blue is needed (and Au beam in Yellow)
  Modify vacuum pump stands in IR6 and IR8
  Modify shielding IR6 and IR8
Operate with new injection and acceleration scheme
  Inject and accelerate Au to intermediate level above transition Then inject p and accelerate both beams
Ensure that luminosity can be measured
Study DX aperture and possible experimental background

## Slide 18: Moving IR6 and IR8 DX magnets by 1cm
Bellows allow for 1 cm movement
Installed shielding creates tight spaces but acceptable “6:00 the bellows and ion pump stand were swapped to make space for the shielding, … cannot be moved because of the ion pump stand” (M. Mapes)
Easier to have p in Yellow, Au in Blue (different from d-Au!)
=> Clear preference for Au beam in Yellow ring.
(Workshop on Physics of p+A Collisioins in RHIC, 7-9 Jan 2013)
Can be done in ~ 1 shifts (i.e. during a run) when properly prepared in previous shut-down

## Slide 19: p+Au injection and acceleration
time
Lorentz factor g
107.4
25.4
10.5
injection Au
injection p
store Au (close to gtr)
acceleration Au (cross transition)
acceleration p, Au
collision p+Au
Note: now tolerate ion beam instabilities at transition to obtain higher intensity (can be cooled down again), not possible with p+Au since have smaller aperture available
maintains same frev for both beams

## Slide 20: ZDC Lumi Monitor Acceptance (M. Bai)
The 3.58 mrad common angle through IP for head-on collisions can blind the ZDC detector right behind DX magnet
ZDC
ZDC
Au
p
Au
p
neutron
neutron
DX
DX

## Slide 21: ZDC Lumi Monitor Acceptance (M. Bai)
Layout between DX and D0
D0 magnet
DX magnet
neutron
ZDC
Move ZDC downstream?

## Slide 22: ZDC Lumi Monitor Acceptance (M. Bai)
If not enough room to move ZDC downstream, need to find a way to reposition ZDC
  move not only DX magnet but also the beam pipe between DX and D0
  Difficult but could be explored

## Slide 23
DX aperture measurement with beam, Y. Luo, A. Marusic, S. Tepikian
04/10/13

## Slide 24
DX aperture measurement with beam, Y. Luo, A. Marusic, S. Tepikian
04/10/13
Analysis pending.

## Slide 25: Asymmetric collisions (p+Au)
p+Au energies: 100.8 GeV p on 100.0 GeV/nucleon Au (gp = gAu = 107.4)
For energy scan need to match Lorentz factor g of both beams
LNN/week, min/max pb-1 15 37

## Slide 26: Summary
p+Au is possible max energy 100 GeV/nucleon for both beams
Stochastic cooling for ion beams helps: DX move only in IR6 & IR8, no Au beam growth
DX move in ~1 shifts possible upgrade for pp2pp in IR6 requires change of DX bellows will reduce flexibility, cannot move DX magnets during run
New injection/acceleration scheme store Au beam above transition for ~15 min
Luminosity estimate based on p beam available (anticipated), and Au beam available (anticipated)
  LNN = 15 pb/week min (now) LNN = 37 pb/week max (few years)