## Slide 1: SpinQuest Layout + LongQuest Upgrade
Z=24m
Ion Absorber
Blocks
Effective Thickness:
5.1m
(200”)
Space for detectors
8.7m
5.5m
EMCal
PHENIX EMCal:
2m(H) x 4m(W)
~1m thick;
Long-lived A’
decay:
A’ -> e+ + e-
A’ decay fiducial volume:
Z = 33 ~ 37m
To measure di-electrons
(or di-photons)
w/ EMCal + pre-Shower Det.
f.v.
Z=33-37m

## Slide 2: Put A PHENIX EMCal Detector in the Back Room
beam
EMCal Detector
Trig-2
Trig-1
1cm Pb
EMCal:
- E > 1 GeV
- dE/E = 11%/sqrt(E)
Long-lived decay:
A’ -> e+ + e-
Z = 33 ~37m
Trigger & PreShower detectors
Provide hit position information (x,y,z), dx=dy ~1cm
Physics + Detector Simulation
Needed for acceptance study

## Slide 3: Details of PHENIX EMCal (we will get 2 sectors)
2m
4m
Shashlik-type Pb scintilator
1 tower is 5.52*5.52*33 cm3
4 towers make a module
Total # of readout channels if
gang 4-”PMTs”:
36 x 3 x 6 = 648 (2592)
6x6 modules make a super module
3x6 supermodules make a sector
1 sector covers 2x4 m2, weights about 22t(std)

## Slide 4
Battleship Steel
beam
4 EMCal modules;
16 SiPM channels
Trig-2
Trig-1
1 cm Pb: (e/photon shower
detection/tracking)
EMCal: dE
LongQuest
218” (554 cm)
41”
(104 cm)
20”
Gap
118”
(300 cm)
64” (163 cm)
41” (104 cm)
51”
25 meter down stream from the target
Depleted Uranium, 16 plates
Last Station-4 PropTube MuID
Hole
22”
12”
12”
Supporting Frames Available for new detectors
Overhead Loading Dock
Crane Access
75”
60”
EMCal + Pre-Shower Detectors
Space available in the back room
DarkQuest Biweekly
Optimal design pending
Details of the Back Room for LongQuest

## Slide 5: LongQuest
beam
ST4-MuID
Last detector
E1039
ST4-MuID
Last detector
E1039
Room for additional
detectors

## Slide 6: A Telescope with EMCal Modules:3/5/2020
Goals – to trigger and measure the energy of
High energy electrons:
  - (Trig-1 & large dE)
High energy photons:
-(NOT Trig-1) & Trig-2 & large dE
trigger/or hit rates
Energy spectra
2 x 11 cm
2 x 11 cm
2x2 SiPM
2x2 SiPM
2x2 SiPM
readout
2x2 SiPM
4 x 4 = 16 SiPM readout channels
beam
4 EMCal modules;
16 SiPM channels
Trig-2
Trig-1
1cm Pb
EMCal: dE
Tower Size:
5.5 x 5.5 cm^2
(one channel)

## Slide 7: EMCal Shower Energy and Spatial Resolutions
11cm
- One EMCal Module = 4 Readout Towers
Electron position resolution: dX=dY ~1cm possible
with pre-shower detector (scintillator bars)
STAR Fermilab Test Beam Result with SiPM Readout (2019)