## Slide 1: EMCal Upgrade at SeaQuest 06/15/2018 Ming Liu, Paul Reimer, Kun Liu

## Slide 2: SeaQuest at the Intensity Frontier at Fermilab
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
High intensity proton beam: “beam dump mode” @SeaQuest/E1067
35,000 fb-1 (in a 2-year parasitic run, 1.4x1018 POT @5% beam)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
B-factory@KEK: 50K fb-1 (~2023)
- Beam dump mode: p+Fe collisions! Target ~ 10%λI
- Parasitic run with other fixed target experiments, E906/E1039
LDRD/ER: 2016-2018
Trigger upgrade, parasitic runs

## Slide 3: Dark photon trigger detectors completed at LANL, 4/2017
Trigger detector installed
and
took data in 2017!

## Slide 4: Displaced Dark Photon Trigger Detectors Work Well!
<eff> ~>95%
Physics analysis in progress

## Slide 5: EMCal Upgrade Proposal

## Slide 6: Dark Photon/Higgs Search at Beam Dump Experiments @Fermilab
- WIMP search – mass > 10GeV,
- Needs low mass coverage, mass < 10GeV
E1067/SeaQuest search for low mass dark particles:
- mass =1 MeV – 10GeV

## Slide 7: CIPANP18 – Update on Physics
17 MeV dark photon candidate
NA64, arXiv:1803.07748
Gori et al, arXiv:1804.00661
17MeV
A possible way to access larger
coupling, by using shorter “FMag”,
drill a longer hole inside the FMAG –
background could increase

## Slide 8
17MeV
17MeV

## Slide 9: Details of PHENIX EMCal
2m
4m
Shashlik-type Pb scintilator
1 tower is 5.52*5.52*33 cm3
4 towers make a module
Total # of readout channels if
Gang 4-”PMTa” with one SIPM:
One sector = 36 x 3 x 6 = 648 (2592)
6*6 modules make a super module
3*6 supermodules make a sector
1 sector is about 2*4 m2, weights about 22t(std)
Weight = (5.5x5.5x33)x11g/cm^3x4(per module)x36(per super-module)x18(per sector)
= 28,500 kg/sector, if 100% Pb; reality < 20,000kg.

## Slide 10: Physics goals and recent work
LOI of dark matter search in dimuon channel was presented to PAC in June 2015. Obtained very positive feedbacks.
A phase-II of EMCal and possibly HCal was also mentioned. PAC suggested we submit the new proposal based on the results obtained from this first phase
The detector proposed in the first phase was successfully installed and accumulated one week worth of data before E906 shuts down
We will continue to take the dimuon data parasitically with E1039

## Slide 11: Ongoing and potential collaboration/support
Ongoing support from LANL LDRD: $300k for FY-18
Submitted joint proposal with KEK/RIKEN/TokyoTech: $270k for FY-18 if supported
Collaboration with PHENIX/sPHENIX EMCal group and STAR forward upgrade groups on detector support

## Slide 12: Proposed work and timeline
Ultimate goal:
Have the full detector ready for installation before the end of this calendar year
Install the detector either during the accelerator maintenance downtime, or the summer shutdown in 2019
Take data with E1039 for at least one year
Immediate goal:
Ship the detector to Fermilab either in July or some later time
Find some onsite space (D0 assembly hall?) with crane support and basic utilities for the EMCal test work
EMCal installation: much depending on the E1039 installation and operation schedule

## Slide 13: Future: Seek new HEP Support: $350K/year
LDRD/ER: 2016-2018
  Established physics case
  Upgraded DAQ bandwidth
    10+ x
  Built, commissioned dark photon trigger in 2017
    Parasitic data w/E906
  Add EMcal for di-electron
    New low mass region: 1 – 200 MeV
  Physics analysis
Parasitic run w/ E1039
  2019-2021
HEP support needed: 2019-2022
  0.5 Staff
  1 PD
  $350K/year, for 4 years
Support data taking w/ E1039
  Dark photon trigger & EMCal operation, calibration and maintenance
    2018-2020
  Data analysis and publication
    2019-2021
Physics beyond 2020+
  Expand the physics with a dedicated dark matter search program at Fermilab
    5% beam time -> 20+% at SeaQuest
  Upgrade tracking around dump
  Optimize the spectrometers

## Slide 14: E-1067 Future Upgrade: Phase-II 2020 ~ 2025+
Add tracking detectors close to “target” to improve mass resolution
Add EMCal, PID
e+/-, h+/- , π+/-
EMCal