## Slide 1: Direct Search for Dark Photons at Fermilab
Ming Liu (PI), Zhongbo Kang(co-PI, T-2), Kun Liu (co-PI), Hubert van Hecke, Sanghoon Lim, Pat McGaughey, Richard Van de Walter, Vincenzo Cirigliano(T-2)

## Slide 2: Today’s Presentations
Overview and Plan – Ming Liu (P-25, PI)
Theoretical progress – Zhongbo Kang(T-2, co-PI)
Experimental highlights – Kun Liu (P-25, co-PI)

## Slide 3: People Involved
Experimental efforts
  Ming Liu, Kun Liu(PD, Staff), Pat McGaughey, Hubert van Hecke, Sanghoon Lim(PD), Richard Van de Water, Grass Wang(PD)
Theoretical effort
  Zhongbo Kang
  Vincenzo Cirigliano
External collaborators
  Fermilab/SeaQuest, BNL/sPHENIX
  SLAC/N. Toro, P. Schuster
  Caltech/Y. Zhang
  Univ. Cincinnati/S. Gori

## Slide 4: The Physics

## Slide 5: Dark Matter?
F. Zwicky, ApJ 86 (1937) 217, V. Rubin et al, ApJ 238 (1980) 471
Galaxies’ rotation curve
Gravitational lensing (Hubble 2007)
Planck: 2013
Benson’s talk @CIPANP 2015
Notes: It is widely accepted today that visible matter only account for 5% of matter and energy, with 25% dark matter .. With many compelling experimental obseravtions , how ever the nature of dark matter and dark energy remtain as the biggest scientific challenges for hunam being … sa they only interactio with SM particels very weakly .. Only shown in gravitaiton sectors ..

## Slide 6
Dark matter self-interaction:
Bullet cluster
Coincidence of dark matter and stars: sigma/m < 1 cm2/g

## Slide 7: Why Dark Sectors?
WIMP being excluded?
Recent anomalies observed by satellite and terrestrial experiments suggest a new “dark sector”
  “Portals” to the SM
    “vector portal”: dark photon
    “scalar portal”: dark Higgs
    “neutrino portal” and more …
“Sub-GeV” low mass weakly-interacting dark particles become very interesting!
Mass: O(MeV ~ GeV)
High-intensity colliders (B-factories) and fixed target experiments (Fermilab, JLab, LHC etc.) offer an ideal environment to probe these new ideas.
Notes: What are the DM? WIMP is considered one of the primary candidates of DM …

## Slide 8: Portals to a Dark Sectors?
SM symmetries limit the allowed couplings
  scalar, vector, tensor interactions etc.
SM
g, W±,Z0,γ, H
Dark Sector
particles &
interactions
E-1067/SeaQuest: Dark photon (vector) and Dark Higgs (scalar) Portals

## Slide 9: Intensity Frontier at Fermilab: 120 GeV Beam
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
World’s highest intensity high energy proton beam:
“beam dump mode” @E-1067
50,000 fb-1 (in 1 year of parasitic run)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
B-factory@KEK: 50,000 fb-1 (~2023)
- Capture most beam in beam dump mode: p+Fe collisions!
- Parasitic run mode possible with other experiments, E906/E1039

## Slide 10: Dark Photons and Dark Higgs Productions in p+Fe Collisions at Fermilab
Photon portal: “vector”
Higgs portal: “scalar”
θ = μ v/mh2
Fermilab(in preparation)
SHiP/CERN(in preparation)
J-Lab12(on-going)
KEK B-factory(on-going)
and more …
Fermilab (in preparation)
SHiP/CERN (in preparation)

## Slide 11: Our Approach and Expected Signals
Dark photon/Higgs trigger upgrade
Unique signals
  Displaced dimuon decay vertex for long-lived particles
  Invariant mass peak in dimuon mass spectrum
Beam time
  Run parasitically with E906/E1039 (2017-2019)
  Possible dedicated runs later with upgraded (e+/-, h+/-)
Z (meter)
-- 2.5%
-- 6.0%
Dimuon mass resolution

## Slide 12: Integrated theory efforts
Signal: detailed calculation for dark photon cross section
To provide expected dimuon signal from dark photon decay as function of decay length L and model parameters (ε, mA’), theory team will
  Compute Dark photon production cross section at both LO and NLO
  Derive the branching ratio of dark photon to dimuon
  Theory team: expertise in perturbative QCD and effective field theory for resummation
Background: detailed calculation for Drell-Yan cross section
Main background is DY dimon production: reliable computation of the cross section is essential to calculate our experimental sensitivity to (ε, mA’), and understand implication of dark photon search
  We have a NLO DY code that works well in the required energy range
  Calculations will be performed in the necessary energy and kinematic regions
Dimuon signal
Drell-Yan background

## Slide 13: LDRD Tasks & Schedules
Today

## Slide 14: Proposed LDRD Budget

## Slide 15: Progress in FY16
Theoretical work
MC simulations and detector optimization
Trigger detector R&D
Trigger detector readout R&D
Trigger detector mechanical support

## Slide 16: Theoretical Progress
Dark photon production at LO

## Slide 17: Progress in Theory and Simulations
Active theoretical collaboration
    LANL (Kang, Vitev, Cirigliano, Gupta, Graesser et al)
    SLAC (Toro, Schuster, Gori et al)
    Caltech(Zhang, An et al)
    SBU (Zhong, Essig)
  cross check dark photon and dark Higgs signals
    Long-lived decays
    Bump search from “prompt” productions
    SM backgrounds
Physics and detector simulations
  New root-based event GEANT4 package (Kun, DavidK)
  New trigger optimization (LANL, U. Michigan)
  Study the impacts of parasitic runs with E906/E1039
    Detector and trigger optimization
    Improve polarized dimuon/DY signals
    Improve reference single muon spin asymmetry signals from target/dump

## Slide 18: A New High-Granularity Displayed Dimuon Vertex Trigger
Y-Plane (non-bending) Trigger:
A quadrant panel: 80cm x 80cm (100cmx100cm @ST-2)
  ST1: 1cm x 1cm x 80 cm scintillating strips, SiPM readout
  ST2: 2cm x 2 cm x 100 cm strips
- Straight line projection, σZ ~30cm
Displaced z-vertex, mostly low mass < 3GeV
St1
St2
Coincident Z-vtx
window matched@L2
Dimuon Z-vertex (cm)
Z
High rejection power, low rate, << 1 kHz(current E906 DAQ limit)
X
Y
ST1
ST2
Y-channels per quadrant:
1x V1495
80(St1) + 50(St2) + 8x2 (St4-Y1,2) = 146
96+64 = 160 inputs possible
  (2NIM=RFCLK+ComSTOP)
Z1=9m
Z1=12m

## Slide 19: Trigger Detector Optimization Single Muon Z-Vertex Resolutions
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Sigma_Z ~ 30cm
Current
E906
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Forward: 2cm
Backward: 2cm
E906

## Slide 20: E906 Run 2 Data: Dimuon Invariant Mass and Reconstructed Z-Vertex
E906 Trigger and event selection optimized
for high-mass dimuons, mass > 2.5GeV ;
Low-mass dimuons are rejected by trigger.
Dimuon event z-vtx distributions
after target/dump separation;
No events observed beyond Z-vtx > 2m
J/Psi
Psi’
Drell-Yan
Rndm

## Slide 21: Displaced Dark Photon Trigger Logics
Q1 (LVL1)
Q2 (LVL1)
Q3 (LVL1)
Q4 (LVL1)
LVL2
(vtxZ matching)
4 x 16-bit from 4 V1495 boards
(2 x 32LVDS cables)
Q1: 80(ST1’) + 50 (ST2’) + 2x8(ST4-Y1/2) = 146, FANOUT ST4 Hodo (or EMCal Cluster)
DAQ/Data stream
TS
(12 inputs total)
(1-free bit available)
DP Trigger
1-bit
DAQ Trigger
LVDS cable 2x16ch bundle available
V1495

## Slide 22: Low Mass Prompt Dimuon Trigger Rate Study
Current E906 setup
Proposed 2-layer trigger upgrade (10x improvement)
Additional Y-trigger after ST-3 absorber, and also using existing E906 X-Plane trigger
(additional ~2x improvement)
Current E906 DAQ 1kHz, can be improved to ~10+kHz with small cost
20+kHz possible for next run (reprograming trigger firmware etc.), details in Kun’s highlight presentation
Parasitic mode: use up to ~10% DAQ bandwidth
Expected (Prompt) Low mass dimuon trigger performance

## Slide 23: Trigger Detector R&D

## Slide 24: Plastic Scintillator dE/dx and Particle Identification
Using polystyrene as example (same as FNAL scintillator factory)
Muon dE/dx = 2.41 MeV/cm @ 4 GeV, and 2.69 MeV/cm @ 20 GeV
  11.5% difference
For 4 GeV Kaon vs 20 GeV muon it’s an even bigger difference, 26.5%

## Slide 25: Minimal Thickness for Light Yields
For thickness = 1.0cm, P > 5GeV
  dE/dx = 2.5MeV/cm
  Light yield = 2.5MeV / 100eV ~ 25K photons
  SiPM Eff = 20%
  Scintillating strip light collection Eff = 5%
  Total “light yield” = 25K x 20% x 5% = 250 >>1
Required light output
  Photon detecting eff > 99%

## Slide 26: Trigger Scintillator Options
High quality scintillator bars
  1x1x50cm
  sPHENIX EMCal SiPM readout
  Expensive, ~$100/ch.
Fermilab extruded scintillators + WLSF
  1x1cm
  2x2cm
  SiPM readout
  Low cost, ~$10/ch

## Slide 27: Trigger Detector R&D (I)
Scintillator directly coupled to SiPMs
  In collaboration with sPHENIX group at BNL

## Slide 28: Trigger Detector Prototype R&D (II)
- Fermilab extruded scintillators + WLSF
SiPM readout
Excellent S/B!
Default option now!
2 x 2 x 50 cm + 1mmD WLSF
+ SiPM readout

## Slide 29: Trigger Lab – M30

## Slide 30: Scintillator Trigger Efficiency Study

## Slide 32: Trigger Efficiency

## Slide 33: Sanghoon Working in Lab C114

## Slide 34: Lab C114

## Slide 35: DAQ and Trigger Upgrade R&D Tasks
Improve the DAQ bandwidth
  Xinkun, Kun, Grass, Dave C. et al
Trigger upgrade
  Build scintillator based displaced dimuon trigger detectors
    Mechanical assembly and support structure
    Readout integration
  Develop trigger firmware for displaced vertex
    V1495
  Can use more help
A Standalone DAQ – a sandbox
  DAQ improvement
  Trigger algorithm development (Byron Roe, Daniel Morton, Kun et al)
  Trigger firmware and DAQ integration (LANL)
  Can use more help

## Slide 36: A Standalone DAQ for Trigger Development
PC/Linux: Jlab CODA, Ethernet Readout
CPU MVME5500: old VxWork (Jlab)
“TS” SIS3200
TDC-II
V1495 pulse generator
V1495 L1 Trigger “development brd”
Windows PC: Altara FPGA programing
-CNTRL
-SIS3200, as TS
-TDC-II (x)
-TDC-II (x)
-V1495, trigger inputs
at least 4
-V1495 as trigger
pattern emulator

## Slide 37: DAQ and Trigger Teststand

## Slide 38: Mechanical Frame

## Slide 39: Production WLSF in the Lab

## Slide 40: Stuff in My Office

## Slide 41: Summary: Hardware in Hands
WLSF: Y-11 (200)
  1 mm D, 1,000m
  1.5 mm D, 1,000m
Extruded scintillators
  Produced at Fermilab
SiPMs
  3x3mm, 600
  S13360-3050CS
  Gain ~ 1.7 x 10^6
Mechanical support
  80-20 Al frames
  Assembly
  Safety review
VMEs
  1 VME crate + Linux CPU
  1 Linux computer
New V1495 boards
  4 V1495
  12 daughter cards
  Splitting Y-cables (12x2)
E906 spares
  V1495, 4(LVL-0)+2
  Daughter cards, #?
preAMPs+LVDS
  Fermilab ones
  sPHENIX
TDCs
  Taiwan group
Scintillator trigger
Readout & DAQ integration

## Slide 42: SiPM Readout with Fermilab preamps

## Slide 43: Scope Picture

## Slide 44: SiPM I-V

## Slide 45: SiPM Irradiation Study

## Slide 46: Fermilab Extruded Scintillators

## Slide 47: V1495 Trigger Logic Unit R&D

## Slide 48: Dark Photon Detection in Dimuon Decay Channel
Drell-Yan like
p0, h, … decay
Bremsstrahlung
p
p
l+
l-
(DM)
(DM)
MiniBooNE
Beam-dump

## Slide 49: Dark Photon Decay Modes
“Minimal” Decay:
Dark photon is the lightest in the dark sector;
  SM final state particles only
Long proper decay length: L0 ~ O(1m)
“General” Decay:
Decay into other dark particles,
dominant channel if allowed
  Dark -> Dark
  Dark -> SM particles
(GeV)
D. Curtin, et al, arXiv: 1312.4992
Electron ID
required!

## Slide 50: Preliminary Results: Dark Photon Sensitivity (parasitic run w/ E906/1039)
Signals considered:
Drell-Yan like
Eta decays
Bremsstralung
Covers a wide range of unexplored parameter phase space
Displaced dimuons
- Minimal SM background
Prompt dimuons
- Excellent coverage over BELLE-II
projection
- Possible dedicated runs later to fully
restore mass < 3GeV (Phase-II)
Phase-II with upgrades
Access below 200MeV with di-electrons
( add EMCal)
Work in progress!

## Slide 51: Dark Higgs
Phase-I:
High-mass: μ+μ- and hadrons
Advantage of using hadron beams
with muon probes over electrons
Phase-II:
Low-mass: e+e-, <200MeV possible
High-mass: hadrons, (5x)
Y. Zhang et al, arXiv:1502.06983
arXiv:1312.4992
θ = μ v/mh2
e+e-
μ+μ-
Electron ID
upgrade!

## Slide 52: Projected Dark Higgs Sensitivity POT:1.4x1018 (Phase-I)
Dimuons with downstream displaced decay vertices
Limited sensitivity to “prompt” large mixing case due to small cross-section
Dark Higgs or dark photons?
  Dimuon kinematic and angular distributions
Phase-II
  Dedicated high luminosity runs optimized for low mass acceptance, mass<3GeV
Y. Zhang (2015)
5x
25x
1x

## Slide 53: LDRD Tasks & Schedules
Today

## Slide 54: Plan for FY17-FY18 and Beyond
DAQ upgrade
Trigger detector integration
Data taking
Install PHENIX EM Calorimeters at SeaQuest/E-1067
  Electron and charged pion identification
  Cover low mass below dimuons

## Slide 55
F Mag
K Mag
St-1 trigger plane, 160 x 160 cm
Made of 1cm x 1cm x 160cm
scintillators
St-2 trigger plane, 200 cm x 200 cm
Made of 2cm x 2cm x 200cm
scintillators

## Slide 56: Displaced Dark Photon Trigger Integration
Q1 (LVL1)
Q2 (LVL1)
Q3 (LVL1)
Q4 (LVL1)
LVL2
(vtxZ matching)
4 x 16-bit from 4 V1495 boards
(2 x 32LVDS cables)
Q1: 80(ST1’) + 50 (ST2’) + 2x8(ST4-Y1/2) = 146, FANOUT ST4 Hodo (or EMCal Cluster)
DAQ/Data stream
TS
(12 inputs total)
(1-free bit available)
DP Trigger
1-bit
DAQ Trigger
LVDS cable 2x16ch bundle available
V1495

## Slide 57: DAQ Upgrade
Current E906 mode
  Log event on every trigger
  Store each event on disk at each trigger
New DAQ mode
  Store event on buffer during the spill ~4 Sec
  Send data to disk when no beam, ~56 Sec
  Low dead time
  High bandwidth

## Slide 58: E-1067 Future Upgrade: Phase-II 2020 ~ 2025+
Add tracking detectors close to “target” to improve mass resolution
Add EMCal, PID
e+/-, h+/- , π+/-

## Slide 59: Two Possible Configurations and Their Impacts
Two configurations:
Option I: use EMCal to
replace the absorber
Option II: insert EMCal between H3 and absorber (will need to slightly adjust station-3 position)
Potential impacts on our primary physics goal:
Muon identification power
Acceptance? (MC shows no impact)
Occupancy in station-4 and thus our raw trigger rate
Data volume and DAQ deadtime?
Test MC samples (for each scenario):
500k single 𝛑/μ/e tracks with 5 GeV < P < 115 GeV
1M high mass (M > 4 GeV) target DY pairs
2E10 inclusive pp collisions (see, MC simulation talk by David K.)

## Slide 60: EMCal from PHENIX/RHIC
2 EMCal sectors are available from PHENIX experiment at RHIC, ~end of 2016
  One sector:
    2m x 4m, 18 (3x6)super modules
    Super module = 36 modules; Module = 4 towers
    36 x 4 x 18 = 2592 channels
    Could gang 2x2 (or 3x3) into one ADC/TDC readout
- dE/E = 8.1%/sqrt(E) + 2.1%
- dT < 200 ps
- Excellent e/pi separation

## Slide 61: Phase-II: Displaced Low Mass Dark Photons with EMCal upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, PHENIX/RHIC etc.
DAQ upgrade
  100+ kHz
Timeline of dedicated runs
  2020+
Detector configuration
  Access low mass region with optimized Fmag settting
Projection: POT 1.4 x 1018

## Slide 62: FY16: Scientific Impacts to the Community
SLAC Dark Sectors Workshop: 4/28-30, 2016
Community Report arXiv:1608.08632
1st exposure of Fermilab dark photon/Higgs
program to the community (Kun, Ming)
BNL Dark Interactions Workshop: 10/4-7, 2016
Our Fermilab dark photon/Higgs program
got highlighted at opening plenary talk (Toro)
- Two invited talks on Fermilab (Arun, Ming)

## Slide 63: FY16 Summary
Met all FY16 milestones
Recognized by the community as an important experiment
In good progress to meet FY-17 goals
  Experimental
  Theoretical

## Slide 64: Impacts on the 2014 US P-5 Report
E1067/SeaQuest: Great Discovery Opportunities at the Fermilab Intensity Frontier!
Notes: P5 reprot highted the 5 sciecne driver …
We respond to the call of P5 report and identified a new opportunity to explore key physics at Femirlab intensity frontier

## Slide 65: Summary and Outlook
Phase-I
  Great discovery potential!
  Add a new displayed vertex trigger
  Early parasitic data taking 2017-2019+
    A short dedicated run up to ~1 month if needed
  POT 1.4 x1018
Phase-II
  Possible detector upgrade later, add electrons and hadrons
  A new dedicated dark matter program at Intensity Frontier!
Dark Higgs
search
2015
2016
2017
2018
2019
2020+
Preparation Phase-I (parasitic runs)
Phase-II

## Slide 66: Backup

## Slide 67
LOI submitted to Fermilab PAC May 20, 2015
A joint experimental and theoretical collaboration
(most E906/E1039 + new members, ~60)
---------------------------------------
Phase-I: (parasitic runs)
Addition of a new displaced dimuon trigger to tag long-lived downstream decayed dark photons (dark Higgs).
Parasitic data taking with E1039 in 2017-2019;
  A short dedicated run (up to ~1 month) if needed.
POT 1.44x1018
Phase-II: (upgrade)
Dedicated runs later with EMCal/HCal upgrades, e+/- and h+/- capabilities.
Cover the full parameter phase space allowed by beam energy and luminosity
POT: >> 1.4x1018
Phase-II request will be presented to PAC at a later time.
Notes: Responding to P5 reprot, we submitted LOI last month .. And the membership is growing …

## Slide 68
A heart-full endorsement
from Fermilab Director and PAC
July 15, 2015!
New experiment! E-1067
LANL LDRD support:
- FY16-17-18
- $1M to implement
the trigger/DAQ upgrade and theory development
Goals:
Trigger installed, 2017
Physics run, 2017-18
Preliminary results 2018!

## Slide 69: Outline
ER Goals
  Discovery Physics
  People involved
    Also train postdocs and students
Highlights of First Year Accomplishment
  Trigger detector R&D
    Scintillator study
    WLSF readout study
    SiPM radiation test at LANACE and Fermilab
    Extruded scintillator with WLSF efficiency study
    Mechanical supporting frame R&D
    SiPM readout
    Selected techonolgy for the trigger
  DAQ R&D
    A new readout scheme, ~x20 gain in bandwidth
    Modification of Firmware
    Proof og principle done
  Full trigger and physics MC simulations
    New DarkPhoton simulation package developed
    Trigger acceptance study done
    Detector config optimiazation done
  Trigger detector production
    Extruded scintillators from Fermilab
    All SiPM purchased I nhand
    80-20 Al frames purchased in hand
  Dark photon physics simulations and sensitivity study
    Preliminary study done
    Work in progress paper
  Theoretical calculations of Dark Photon and Dark Higgs production at Fermilab
    SLAC + U cincinati theory groups
    Caltech theory group
Impact:
  Dark sector physics community report paper writing and more
    SLAC workshop
    BNL workshop
    Being recognized by the community for its importance
Future Plan – FY17
  SiPM readout R&D
    sPHENIX Hcal system, under evaluation
    Fermilab SiPM preamp + LANL digital boards, under evaluation
    Cost reduction to fit LDRD budget
  E1067 system integration
    DAQ upgrade compled by 2016
    Trigger installation commisioning early 2017 (new TDC needed)
  E1067 data taking
    Commisioning and data taking
    1/2017 – Summer 2017
    Data monitoring and Calibration
  Theoretical progress
    Dark photon
    Dark Higgs
    Background DY study
    Sensitivity study
  Publish papers
    Dark photon production at LO and NLO
    An invited mini review paper
Future Plan - FY18
  Physics data analysis using FY-17 data
  Final theoretical calcualtioons
    Full differential calcualtions of signal and background
    Full simulation pcckage to study sensitivity
  Publish preliminary results
  Continue taking high stat data with E1039 (Pol DY)
  Develop a new major/long term dedicated dark photon and dark Higgs search program at Fermilab High Intensity Frontier
  Seek additional support from HEP/NP?
    Under discussion with Rajan Guta
    FWP to HEP?
  New proposal to upgrade the detector
    Much wider search phase space with di-electronics
    Resue PHENIX EMCal for
    Seek LANL Early Career Fund
    At the end next E906 run (7/2017), install new EMCal
  Plan-B if no pol DY (backup slides)
    Ask additional years for beam time with dedicated dark phonton search , with upgraded DAQ and Trigger
    New proposal to Ferilab PAC or Dir

## Slide 70
From the CMB to the late universe: Energy budget over cosmic time
WMAP web site

## Slide 71: SLAC Dark Sectors Workshop April 28 – 30, 2016

## Slide 72: Reviewers
Mark Makela (LANL) and Gordan Krnjaic (FNAL) have tentatively agreed to be experimental and theory reviewers for this LDRD.