## Slide 1: FY17 Highlights of Dark Photon Search at Fermilab
Ming Liu, P-25
Dark Photon/Higgs Search @Fermilab LDRD/ER Team

## Slide 2: SeaQuest at the Intensity Frontier at Fermilab
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
High intensity proton beam: “beam dump mode” @SeaQuest/E1067
35K fb-1 (in a 2-year parasitic run, 1.4x1018 POT @5% beam)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
B-factory@KEK: 50K fb-1 (~2023)
- Beam dump mode: p+Fe collisions! Target ~ 10%λI
- Parasitic run mode possible with other experiments, E906/E1039
SeaQuest

## Slide 3: Goals and Scope of the Project (from Proposal)

## Slide 4: People Involved
Experimental efforts (P-25)
  Ming Liu, Kun Liu(PD, Staff), Sho Uemura (PD, 11/2016-), Grass Wang(PD, 7-9/2016), Pat McGaughey, Hubert van Hecke, Andi Klein, Cesar da Silva, Matt Durham, Sanghoon Lim(PD), Shaun Newman(P-21, Mechanical Engineer), Xinkun Chu (Student, graduated 5/2017), Xuan Li (PD), Marie Boer (PD), Dave Kleinjan, Alex Wickes, Jeff Bacon, Richard Van de Water
Theoretical effort (T-2)
  Zhongbo Kang
  Vincenzo Cirigliano
External collaborators
  Fermilab/SeaQuest
  BNL/sPHENIX
  SLAC/N. Toro, P. Schuster
  Caltech/Y. Zhang
  Univ. Cincinnati/S. Gori
  And growing …
All 8 final trigger detector modules were constructed at LANL and shipped to Fermilab 4/2017

## Slide 5: A New High-Granularity Displayed Dimuon Vertex Trigger
Y-Plane (non-bending) Trigger:
A quadrant panel: 80cm x 80cm (100cmx100cm @ST-2)
  ST1: 1cm x 1cm x 80 cm scintillating strips, SiPM readout
  ST2: 2cm x 2 cm x 100 cm strips
- Straight line projection, σZ ~30cm
Displaced z-vertex, mostly low mass < 3GeV
St1
St2
Coincident Z-vtx
window matched@L2
Dimuon Z-vertex (cm)
Z
High rejection power, low rate, < 1 kHz(current E906 DAQ limit)
X
Y
ST1
ST2
Z1=9m
Z1=12m

## Slide 6: Achievements in the 1st Year (FY16)
Completed trigger detector R&D and technology down selection
  Extruded scintillators, produced at Fermilab
  WLSF, procured from Kuraray, Japan
  SiPM readout in strong magnetic field, procured from Hamamatsu, Japan
Completed preliminary design of the mechanical frame
  80/20 AL frame selected
  Assembled 4 out of 8 80/20 box-frames at LANL
Redesigned DAQ readout with a new architecture
  Take advantage of the beam spill structure: 4sec/60sec
  Preliminary new DAQ firmware developed and tested
Designed new trigger logic circuit and electronics
  CAEN V1495 logic boards for LVL-1
Developed a new GEANT simulation package
  Preliminary physics study
New DAQ R&D
TB @LANL

## Slide 7: Major Tasks and Accomplishments in FY17
Successfully commissioned the new DAQ and integrated the dark-photon trigger system
  DAQ bandwidth improved by ~10
  A new displaced dimuon trigger electronics & firmeware
Designed and built full trigger detectors at LANL
  Extruded scintillators + WLSF + SiPMs
  80-20 Al box frames + global supporting structures
  Station-1:
    4 quadrants, 80x80cm^2 each, 320 channels
  Station-2:
    4 quadrants, 100 x 100 cm^2 each, 200 channels
  Optical calibration system
  LV/HV power distribution and control boards
Installed and commissioned trigger detectors
  Timing resolution: < 1.5 nS (collision rate ~ 19nS)
  Track hit eff. > 96% (from cosmic)
Took data parasitically with E906
  E1039 delayed ~1.5y, scheduled to start in 2018
  E906 data taking extended by 1 year, ended 7/2017
Complete DAQ Upgrade
Complete trigger detector construction
Trigger detector installation and commissioning
Take data with E1039(E906)
Goals
Accomplishments

## Slide 8: Very Successful Team Work!

## Slide 9: Completed modules, 8 of them in total!
Station-1: 80 x 80 cm2, 80 channels
Station-2: 100 x 100 cm2, 50 channels

## Slide 10: Optical Calibration, LV/HV Power Distribution and Controls Systems
Designed, built and
tested at LANL
3 x 8 optical outputs

## Slide 11: Trigger, DAQ R&D and Cosmic Test @LANL
TDC_1
TDC_2
Trigger & DAQ hardware and firmware designed and tested at LANL, in collaboration with Fermilab Engineers
Readout from a full module for cosmic test
  Full SiPM readout
  V1495 trigger logic + TDC read out
  E906 upgraded DAQ and firmware
- Timing resolution, better than 1.5nS (19nS RF)
- Detector eff > 96%

## Slide 12: All 8 Trigger Detectors Designed and Built at LANL, Truck loaded to Fermilab
Eight trigger detector modules
Electronics and Power supplies

## Slide 13: Trigger Detector Systems Installed and Commissioned @FNAL
LVL-1 + LVL-2
Trigger &
Calibration
Systems
Station-2 Trigger Plane

## Slide 14: Publications and Presentations
Papers:
  Dark Sector Community Report, 2016, arXiv:1608.08632
  US DOE Cosmic Vision Whitepaper, 2017, arXiv:1707.04591
  An invited review paper on SeaQues/E1067, Mod. Phys. Lett. A, 2017, Vol. 32, Issue 10
  A phenomenology paper in preparation
Presentations:
  BNL Dark Sector Physics Workshop, 10/2016
  DOE Cosmic Frontier Workshop, 3/2017
  Fermilab PAC discussion, 7/2017
  APS/DNP, 10/2017
  HPS Mini-Symposium, 10/2017, SLAC
  Light Dark World International Forum 2017, 10/2017, Pittsburgh
Being recognized in the community as an important new player:
Our Fermilab dark photon/Higgs program highlighted at opening plenary talk, BNL Dark Interactions
Invited talk at HPS mini-Symposium 2017
Invited plenary talk at Light Dark World 2017
BNL Dark Interactions 2016
Light Dark World 2017

## Slide 15: Impacts of this LDRD
Produced two ECR Proposals
  A new LHCb forward tracking upgrade based on the detector technology developed here (funded, LANL/ECR FY17-19)
  A new search for dark matter in di-electron channel (a new proposal, FY18-20)
Provided important hardware trainings for postdocs and young staff
  After many years of mostly on data analyses and simulations
Possible new HEP program of high P-5 impact
Visibility of LANL to outside world in Science and Technology R&D

## Slide 16: Experimental Challenges: Plan vs Reality
Much larger detector R&D project: DAQ, readout & control
SeaQuest schedule changes since proposal:
E1039 installation delayed by ~1.5 year
E906 continued data taking till ~7/2017
  No dedicated installation time, 2-month delay
E906 Operation
E1039 installation & operation
LDRD trigger construction, installation,
commissioning & data taking, analysis
Commissioning done in 2 weeks
LDRD data taking
& analysis
Reality:

## Slide 17: Plan for FY18
More data taking with E1039 in 2018
Data analysis and preliminary publication
  Alignment and calibration
  Tracking
Possible EMCal upgrade? New proposals?

## Slide 18: New Ideas Developed: Displaced Low Mass Dark Photons with EMCal upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, PHENIX/RHIC etc.
Timeline of dedicated runs
  2020+
Detector configuration
  Access low mass region with optimized Fmag settting
Projection: POT 1.4 x 1018

## Slide 19: Summary and Outlook
Completed Trigger and DAQ Upgrade
Took data with E906 in FY17
Take more data with E1039 in FY18
Complete data analysis and publication
Phase-I
  Great discovery potential!
  A new vertex trigger & DAQ++
  Early parasitic data taking 2017-2020+
  POT 1.4 x1018 or more
Phase-II
  Possible detector upgrade later, add electron and hadron capability
  A new dedicated dark matter program at Intensity Frontier!
Dark Higgs
search
2015
2016
2017
2018
2019
2020+
Preparation Phase-I (parasitic runs)
Phase-II

## Slide 20: backup

## Slide 21: outline
  Overview of the scope of LDRD
  Achiements in FY16 ()
  Major achievements in FY17
    DAQ upgrade
    Trigger detector construction, installation and commissioning
    Data taking
    Publications, invited talks, reviews etc – being recognized by the HEP community
    New ideas developed for the future long-term program
  Challenges faced in detector R&D, installation and commisionging
    Uncertainties in E906 operation schedule and E1039 startup
    Cost & schedule of detector/DAQ upgrade, much larger than original plan
    Change of E906 operation schedule impacted detector upgrade, installation and commissioning
  Plan for FY18 and beyond
    Run17 data analysis, preliminary search results
    Produce realistic projections based on Year 17 run, for future parasitic runs w/ E1039, and
    More data taking with E1039 in FY18:
      May 2018 – July 2018, followed by analysis
      10/2018 – 10/2020 long run
  Impacts on other programs
    TWO ECRs developed, based on the detector technology and science developed in this ER, Kun-EMCal, Cesar - LHCb
    new idea for future program – ECR for EMcal upgrade, develop a long term Dark Photon/Higgs program at Fermilab after E1039, 2020+
    LHCb adopted this technology for the forward tracker upgrade
  Highlight the scope of the project
  Challenges
    Technical challenges in hardware and software R&D
    Experimental schedule uncertainty

## Slide 22: Developing a long term program at Fermilab
New ideas
  Low mass region with di-electroncs
  QCD-like Dark Sector physics
  EMCal upgrade (recycled from PHENIX)
Dedicated accelerator based beam-dump dark sector physics program
  Dark photon
  Dark Higgs
  Dark “QCD” mesons
  Complete major program by 2025, when SHiP@CERN is on line

## Slide 23: Trigger detectors completed at LANL and shipped to Fermilab 4/2017

## Slide 24
Dark Photon/ER
FY16 Goals
Ming’s whiteboard

## Slide 28
A target Drell-Yan event
A beam-dump dark photon event --- parasitic run possible!
E906/E1039
E1067

## Slide 29: LDRD/ER leveraged on others’ contributions
Stimulated great interest from others
Leveraged expertise from external collaborators
  Fermilab preamp
  Theoretical study
    A new NSF fund, Prof. S. Gori
  New experimental collaborators
    Russian collaborators, two new institutions
    HEP groups: Univ. Kentakey,

## Slide 30: Phase-I Expectation: Dark Photons (parasitic run w/ E906/1039)
Signals considered:
Drell-Yan like
Eta decays
Bremsstralung
Covers a wide range of unexplored parameter phase space
Displaced dimuons
- Minimal SM background
Prompt dimuons
- Good coverage
- Possible dedicated runs later to fully
restore mass < 3GeV (Phase-II)
Phase-II with upgrades
Access below 200MeV with di-electrons
( add EMCal)
Work in progress!

## Slide 31: Projected Dark Higgs Sensitivity POT:1.4x1018 (Phase-I)
Dimuons with downstream displaced decay vertices
Limited sensitivity to “prompt” large mixing case due to small cross-section
Dark Higgs or dark photons?
  Dimuon kinematic and angular distributions
Phase-II
  Dedicated high luminosity runs optimized for low mass acceptance, mass<3GeV
Y. Zhang (2015)
POT:4x1020

## Slide 32: E-1067 Future Upgrade: Phase-II 2020 ~ 2025+
Add tracking detectors close to “target” to improve mass resolution
Add EMCal, PID
e+/-, h+/- , π+/-
EMCal

## Slide 33: A Great Opportunity Dark Photons and Dark Higgs Search at SeaQuest
Photon portal: “vector”
Higgs portal: “scalar”
θ = μ v/mh2

## Slide 34: Dark Photon Detection in Dilepton Channel
Drell-Yan like
p0, h, … decay
Bremsstrahlung
p
p
l+
l-
(DM)
(DM)
MiniBooNE
Beam-dump
~ Fixed target w/
electron beams

## Slide 35: Dark Higgs
Phase-I:
High-mass: μ+μ- and hadrons
Advantage of using hadron beams
with muon probes over electrons
Phase-II:
Low-mass: e+e-, <200MeV possible
High-mass: hadrons, (5x)
Y. Zhang et al, arXiv:1502.06983
arXiv:1312.4992
θ = μ v/mh2
e+e-
μ+μ-
Electron ID
upgrade!

## Slide 36: EMCal from PHENIX/RHIC
2 EMCal sectors are available from PHENIX experiment at RHIC, ~end of 2016
  One sector:
    2m x 4m, 18 (3x6)super modules
    Super module = 36 modules; Module = 4 towers
    36 x 4 x 18 = 2592 channels
    Could gang 2x2 (or 3x3) into one ADC/TDC readout
- dE/E = 8.1%/sqrt(E) + 2.1%
- dT < 200 ps
- Excellent e/pi separation

## Slide 37: FY17: Scientific Impact to the Community, Invited talks and Publications …
BNL Dark Interactions: 10/4-7, 2016
Our Fermilab dark photon/Higgs program
highlighted at opening plenary talk
- Two talks, by Arun, Ming
DOE HEP Cosmic Visions: New Ideas for Dark Matter, 3/2017
Showcased Fermilab dark photon/Higgs program
Contributed to Community Whitepaper