## Slide 1: Status of Dark Photon/Higgs Search Upgrade
Kun Liu and Ming Liu
Los Alamos
With Grass, Dave C., Xinkun et. al.

## Slide 2: Outline
Physics of dark sectors
  Mass: MeV ~ GeV
Detector upgrade
  Displaced dimuon trigger
  DAQ improvement
New opportunity
  EMCal from PHENIX, available this fall
  electron/hadron ID @SeaQuest!
Possible schedules and tasks
  E906 extended ~summer 2017
  DAQ, Trigger work summer shutdown
  PHENIX EMcal installation

## Slide 3: Dark Matter?
F. Zwicky, ApJ 86 (1937) 217, V. Rubin et al, ApJ 238 (1980) 471
Galaxies’ rotation curve
Gravitational lensing (Hubble 2007)
Planck: 2013
Benson’s talk @CIPANP 2015
Notes: It is widely accepted today that visible matter only account for 5% of matter and energy, with 25% dark matter .. With many compelling experimental obseravtions , how ever the nature of dark matter and dark energy remtain as the biggest scientific challenges for hunam being … sa they only interactio with SM particels very weakly .. Only shown in gravitaiton sectors ..

## Slide 4: No Luck so far in Direct Search for WIMP
WIMP being excluded?
Recent anomalies observed by satellite and terrestrial experiments have motivated dark matter models introducing a new “dark sector”
There are “portals” between the dark sector and the SM.
  “vector portal”: dark photon
  “scalar portal”: dark Higgs
  …
“Sub-GeV” low mass weakly-interacting dark particles become very interesting!
Mass: O(MeV ~ GeV)
In particular, high-intensity colliders (B-factories) and fixed target experiments (Fermilab, JLab, LHC etc.) offer an ideal environment to probe these new ideas.
- Imaginable space for these experiments is rapidly disappearing
- the “natural” theory space is also disappearing.
- I like to think that Dark Matter is on solid ground, maybe not!!!
Montgomery’s talk at CIPANP2015
“a vision of nuclear and particle physics”
Notes: What are the DM? WIMP is considered one of the primary candidates of DM …

## Slide 5: Portals to a Dark Sectors?
SM symmetries limit the allowed couplings
  scalar, vector, tensor interactions etc.
SM
g, W±,Z0,γ, H
Dark Sector
particles &
interactions
E-1067/SeaQuest: Dark photon (vector) and Dark Higgs (scalar) Portals

## Slide 6: Dark Photons and Dark Higgs Productions in p+Fe Collisions at Fermilab
Photon portal: “vector”
Higgs portal: “scalar”
θ = μ v/mh2

## Slide 7
LOI submitted to Fermilab PAC on May 20, 2015
A joint experimental and theoretical collaboration
(most E906/E1039 + new members, ~60)
---------------------------------------
Phase-I: (parasitic runs)
Addition of a new displaced dimuon trigger to tag long-lived downstream decayed dark photons (dark Higgs).
Parasitic data taking with E1039 in 2017-2019;
  A short dedicated run (up to ~1 month) if needed.
POT 1.44x1018
Phase-II: (upgrade)
Dedicated runs later with EMCal/HCal upgrades, e+/- and h+/- capabilities.
Cover the full parameter phase space allowed by beam energy and luminosity
POT: >> 1.4x1018
Phase-II request will be presented to PAC at a later time.
Notes: Responding to P5 reprot, we submitted LOI last month .. And the membership is growing …

## Slide 8
A heart-full endorsement
from Fermilab Director and PAC
July 15, 2015!
New experiment! E-1067
LANL LDRD support:
- FY16-17-18
- $1M to implement
the trigger upgrade and theory development
Goals:
Trigger installed, 2017
Physics run, 2017-18
Preliminary results 2018!

## Slide 9: Dark Photon Detection in Dimuon Decay Channel
Drell-Yan like
p0, h, … decay
Bremsstrahlung
p
p
l+
l-
(DM)
(DM)
MiniBooNE
Beam-dump
Also see: S. Gori, S. Gardner and K Liu’s talks

## Slide 10: Dark Photon Decay Modes
“Minimal” Decay:
Dark photon is the lightest in the dark sector;
  SM final state particles only
Long proper decay length: L0 ~ O(1m)
“General” Decay:
Decay into other dark particles,
dominant channel if allowed
  Dark -> Dark
  Dark -> SM particles
(GeV)
D. Curtin, et al, arXiv: 1312.4992
Electron ID
required!

## Slide 11: Expectations from GUT
After EWSB, there is a coupling ε between the dark photon and the photon (also the Z, less important at low energies).
Theoretical prejudice for a mass scale
mA’ ~ √ε mEW ~ (MeV – GeV)
e.g. Arkani-Hamed & Weiner;
Cheung, Ruderman, Wang, Yavin;
Morrissey, Poland, Zurek;
Essig, Schuster, Toro;

## Slide 12: Dark Photon Current and Future Limits
Several new results in recent years
and more to come
Muon (g-2) region disfavored
- for A’ directly decay into SM;
- but allowed with some “invisible modes”
New experimental proposals
Fermilab E-1067 beam dump,
SHiP at CERN

## Slide 13: Detector Upgrades and Expected Signals
Dark photon trigger upgrade
  Add a fine-granularity scintillating strip based trigger/tracking to tag dimuons from the same decay Z-vertex
  A new trigger for events with displaced down-stream dimuons
Unique signals
  Displaced dimuon decay vertex for long-lived particles
  Invariant mass peak in dimuon mass spectrum
  Mostly from beam dump (target ~10% λI.)
Beam time
  Run parasitically with E906/E1039 (2017-2019)
  Possible dedicated runs later with upgraded (e+/-, h+/-)
Z (meter)
-- 2.5%
-- 6.0%
Dimuon mass resolution

## Slide 14: A New High-Granularity Displayed Dimuon Vertex Trigger
Y-Plane (non-bending) Trigger:
A quadrant panel: 80cm x 72cm (100cmx72cm @ST-2)
  ST1: 1cm x 1cm x 80 cm scintillating strips, SiPM readout
  ST2: 2cm x 2 cm x 100 cm strips
- Straight line projection, 30cm Z-vertex resolution
Displaced z-vertex, mostly low mass < 3GeV
St1
St2
Coincident Z-vtx
window matched@L2
Dimuon Z-vertex (cm)
Z
High rejection power, very low rate, << 1 kHz(current E906 DAQ limit)
X
Y
ST1
ST2
Y-channels per quadrant:
1x V1495
72(St1) + 72(St2) + 8x2 (St4-Y1,2) = 116
96+64 = 160 inputs possible
  (2NIM=RFCLK+ComSTOP)
72x4x2 =576 SiPMs needed (600)
Z1=9m
Z1=12m

## Slide 15: Single Muon Z-Vertex Resolutions
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Current
E906
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Forward: 2cm
Backward: 2cm
E906

## Slide 16: Displaced Dark Photon Trigger
Q1 (LVL1)
Q2 (LVL1)
Q3 (LVL1)
Q4 (LVL1)
LVL2
(vtxZ matching)
4 x 16-bit from 4 V1495 boards
(2 x 32LVDS cables)
Q1: 72(ST1’) + 72 (ST2’) + 2x8(ST4-Y1/2) = 160, FANOUT ST4 Hodo (or EMCal Cluster)
DAQ/Data stream
TS
(12 inputs total)
(1-free bit available)
DP Trigger
1-bit
DAQ Trigger
LVDS cable 2x16ch bundle available
V1495

## Slide 17: Low Mass Prompt Dimuon Trigger Rate Study
Current E906 setup
Proposed 2-layer trigger upgrade (10x improvement)
Additional Y-trigger after ST-3 absorber, and also using existing E906 X-Plane trigger
(additional ~2x improvement)
Current E906 DAQ 1kHz, can be improved to ~10kHz with small cost
100+kHz possible in the future (reprograming trigger firmware etc.)
Parasitic mode: use up to ~10% DAQ bandwidth
Expected (Prompt) Low mass dimuon trigger performance

## Slide 18: Trigger Scintillator Options
High quality scintillator bars
  1x1x50cm
  sPHENIX EMCal SiPM readout
  Expensive, ~$100/ch.
Fermilab extruded scintillators + WLSF
  1x1cm
  2x2cm
  SiPM readout
  Low cost, ~$10/ch

## Slide 19: Trigger Prototype R&D (I)
- 10mm x 10mm x 500 mm
- Scintillators + SiPM readout
- Cosmic rays
- Fast <~ 10nS rising time

## Slide 20: Trigger Prototype R&D (II)
- Fermilab extruded scintillators + WLSF
SiPM readout
Excellent S/B!
Default option now!
2 x 2 x 50 cm + 1mmD WLSF
+ SiPM readout

## Slide 21: DAQ and Trigger Upgrade R&D Tasks
Improve the DAQ bandwidth
  Xinkun, Kun, Grass, Dave C. et al
Trigger upgrade
  Build scintillator based displaced dimuon trigger detectors
    Mechanical assembly and support structure
    Readout integration
  Develop trigger firmware for displaced vertex
    V1495
  Can use more help
A Standalone DAQ – a sandbox
  DAQ improvement
  Trigger algorithm development (Byron Roe, Daniel Morton, Kun et al)
  Trigger firmware and DAQ integration (?, LANL?)
  Can use more help

## Slide 22: A Standalone DAQ for Trigger Development
PC/Linux: Jlab CODA, Ethernet Readout
CPU MVME5500: old VxWork (Jlab)
“TS” SIS3200
TDC-II
V1495 pulse generator
V1495 L1 Trigger “development brd”
Windows PC: Altara FPGA programing
-CNTRL
-SIS3200, as TS
-TDC-II (x)
-TDC-II (x)
-V1495, trigger inputs
at least 4
-V1495 as trigger
pattern emulator

## Slide 23: Hardware in hand/Ordered
WLSF: Y-11 (200)
  1 mm D, 1,000m
  1.5 mm D, 1,000m
Extruded scintillators
  Quote, in progress
SiPMs
  3x3mm, 600 ordered
  S13360-3050CS
  Gain ~ 1.7 x 10^6
Mechanical support
  80-20 Al frames
  Safety review
VMEs
  1 VME crate + Linux CPU
  1 Linux computer
New V1495 boards
  2 V1495
  6 daughter cards
  Splitting Y-cables (12)
E906 spares
  V1495, 4(LVL-0)+2
  Daughter cards, #?
preAMPs+LVDS
  Fermilab ones
  sPHENIX
Scintillator trigger
Readout & DAQ integration

## Slide 24: Progress in Theory and Simulations
Active theoretical collaboration
    LANL (Kang, Vitev, Cirigliano, Gupta, Graesser et al)
    SLAC (Toro, Schuster, Gori et al)
    Caltech(Zhang, An et al)
    SBU (Zhong, Essig)
  cross check dark photon and dark Higgs signals
    Long-lived decays
    Bump search from “prompt” productions
    SM backgrounds
Physics and detector simulations
  New root-based event GEANT4 package (Kun, DavidK)
  New trigger optimization (LANL, U. Michigan)
  Study the impacts of parasitic runs with E906/E1039
    Detector and trigger optimization
    Improve polarized dimuon/DY signals
    Improve reference single muon spin asymmetry signals from target/dump

## Slide 25: Search Mode (1): Long-lived Dark Photons
Reconstructed dimuons with downstream Z-vertex:
3m < Z-vertex < 6m
Very low trigger rate, << 1kHz
Almost SM background free
Dimuon mass peak
- 5x1012 ppp ( current E906)
200 days
1.4 x 1018 POT (recorded)
4 events contours (2-sigma)
2-sigma (95%) exclusion plots
Excellent coverage of uncharted region!

## Slide 26: Search Mode (2): “Prompt” Dark Photons vs Drell-Yan Z-vertx < 3m
Expected Drell-Yan like signal and backgrounds:
Drell-Yan Background
Dark photon
signal
Excluded phi
resonance region
Work in progress …,
Understaning BG ...

## Slide 27: Summary: Dark Photon Sensitivity (parasitic run w/ E906/1039)
Signals considered:
Drell-Yan like
Eta decays
Bremsstralung
Covers a wide range of unexplored parameter phase space
Displaced dimuons
- Minimal SM background
Prompt dimuons
- Excellent coverage over BELLE-II
projection
- Possible dedicated runs later to fully
restore mass < 3GeV (Phase-II)
Phase-II with upgrades
Access below 200MeV with di-electrons
( add EMCal)
Work in progress!

## Slide 28: Dark Higgs Search at E-1067
Phase-I:
High-mass: μ+μ- and hadrons
Advantage of using hadron beams
with muon probes over electrons
Phase-II:
Low-mass: e+e-, <200MeV possible
High-mass: hadrons, (5x)
Y. Zhang et al, arXiv:1502.06983
arXiv:1312.4992
θ = μ v/mh2
e+e-
μ+μ-
Electron ID
upgrade!

## Slide 29: E-1067 Dark Higgs Sensitivity POT:1.4x1018 (Phase-I)
Dimuons with downstream displaced decay vertices
Limited sensitivity to “prompt” large mixing case due to small cross-section
Dark Higgs or dark photons?
  Dimuon kinematic and angular distributions
Phase-II
  Dedicated high luminosity runs optimized for low mass acceptance, mass<3GeV
Y. Zhang (2015)
5x
25x
1x

## Slide 30: Future E1067/SeaQuest Upgrade
Fine-pitched vertex trigger
Efficiently trigger on the dilepton pairs generated from downstream while suppressing the background rate
Significantly enlarge the fiducial region from ~2m to ~6m
Supported by LANL LDRD
EMCal/HCal
Add e+/- and 𝜋+/- capabilities to SeaQuest spectrometer
Extend the physics reach to A’ from 𝜋0 decay, dark 𝝆, and hadronic decay mode for heavier A’
Re-commission the existing detectors (EMCal from PHENIX being considered)
Modest upgrades with significantly increased physics reach.
Data taking expected to start in summer 2017!

## Slide 31: Phase-II: Displaced Dark Photons with future detector “EMCal/HCal” upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, PHENIX/RHIC etc.
DAQ upgrade
  100+ kHz
Timeline of dedicated runs
  2020+
Detector configuration
  Access low mass region with optimized Fmag settting
Projection: POT 1.4 x 1018

## Slide 32: EMCal from PHENIX/RHIC: this Year!
2 EMCal sectors are available from PHENIX experiment at RHIC, ~Sept/Oct 2016
  A sector:
    2m x 4m, 18 (3x6)super modules
    Super module = 36 modules
    Module = 4 towers
    36 x 4 x 18 = 2592 channels
    Could gang 2x2 (or 3x3) into one ADC/TDC readout
dE/E = 8.1%/sqrt(E) + 2.1%
dT < 200 ps

## Slide 33
- We can ship two PHENIX EMCal
detectors to Fermilab this summer;
cost: $5~10K
- Install them at SeaQuest, later?

## Slide 34: Two Possible Configurations and Their Impacts
Two configurations:
Option I: use EMCal to
replace the absorber
Option II: insert EMCal between H3 and absorber (will need to slightly adjust station-3 position)
Potential impacts on our primary physics goal:
Muon identification power
Acceptance? (MC shows no impact)
Occupancy in station-4 and thus our raw trigger rate
Data volume and DAQ deadtime?
Test MC samples (for each scenario):
500k single 𝛑/μ/e tracks with 5 GeV < P < 115 GeV
1M high mass (M > 4 GeV) target DY pairs
2E10 inclusive pp collisions (see, MC simulation talk by David K.)

## Slide 35: μ/𝛑 separation: case 1 vs. case 2 vs. original
Orignal
Case 1
Case 2
μ survival chance
𝛑 survival chance
For μ survival chance (or μ-ID efficiency), all 3 cases are very close to 100%
For 𝛑 survival change (or 𝛑 contamination):
  original design is around 0.5%
  case 1 is around 10%
  case 2 is around 0.1%
μ identification favors case 2

## Slide 36: Station-4 occupancy: case 1 vs. case 2 vs. original
Avg. H4T occupancy per MATRIX1 event
Avg. RawMATRIX1 per spill
Run 12525
Run 12525
Case 1
Case 1
Original
Original
Case 2
Case 2
In terms of both raw trigger rate and station-4 occupancy, case 2 works much better than case 1
By adding EMCal between station-3 and absorber (case 2), we could also slightly improve w.r.t our current design
Station-4 occupancy and raw trigger rate favors case 2

## Slide 37: Extra DAQ requirements: case 1/2 vs. original
If fully instrumented, 2 sectors of EMCal add 5184 channels to our DAQ:
5184/64 = 81 new TDCs
81/7 = 12 new VME crates (includes 12 new ROCs and trigger interface cards)
data volume per event will be increased by ~5% (based on simulation)
If 4 towers are ganged together, total number of channels reduced by a factor of 4:
1296/64 = 21 new TDCs
21/7 = 3 new VME crates (includes 3 new ROCs and trigger interface cards)
data volume per event will be increased by ~3%
Adding EMCal requires significant amount of extra electronics; but adds very little deadtime, this is good!

## Slide 38: Summary: EMCal Upgrade
2 sectors (4×4 m2 coverage) PHENIX EMCal will be available after this summer almost for free (not including shipping and instrumentation)
With EMCal installed, we will be able to access:
  dark photon from 𝛑0 decay
  dark 𝝆 decays to 𝛑𝛑
  enhanced dark higgs sensitivity
Two different scenarios of including EMCal have been studied via MC, and it poses little impact to our primary physics goal
Potential bonus of better background rejection on trigger level (studies underway).

## Slide 39: Schedules of SeaQuest Experiments
E-906 complete data taking in summer 2017
  Summer shutdown 8/1-11/6, 2016
E-1067 Timeline – Dark photon/Higgs Search!
  Phase-I (Parasitic run) with E906/E1039: 2017-2019
  (Phase-II: detector upgrades and dedicated runs)
E-1039 will replace current E906 targets with a polarized NH3 target.
  No change to E906 spectrometer setup
  New target located about 3.5m upstream of the beam-dump, ~6% λI.
  Target/trigger installation: 2016 - 2017
  Data taking: 2017 – 2019
E-1027 polarized Main Injector (future)
Dark photon(Higgs)
Search: 2017-2019
parasitic run, E906/E1039
E-1039 starts
E906 started
E-1067
A lot of upgrade tasks can be
achieved this summer before next run!
DAQ upgrade
Trigger upgrade
(EMCal)

## Slide 40: backup

## Slide 41: 2014 US P-5 Report
Great Opportunities at the Fermilab Intensity Frontier!!!
Notes: P5 reprot highted the 5 sciecne driver …
We respond to the call of P5 report and identified a new opportunity to explore key physics at Femirlab intensity frontier

## Slide 42
What is Dark Matter?
Dark sector
WIMP
Extra dimension
Sterile neutrino
Axion & ALPs
Superheavy
DM
…
Dark Matter
Recent results from the LHC and direct detection experiments “challenge” the traditional WIMP paradigm and motivate the exploration of new ideas.

## Slide 43: Intensity Frontier at Fermilab: 120 GeV Beam
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
World’s highest intensity high energy proton beam:
“beam dump mode” @E-1067
35,000 fb-1 NN (in 2 years of parasitic runs)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
B-factory@KEK: 50,000 fb-1 (~2023)
- Capture most beam in beam dump mode: p+Fe collisions!
- Parasitic run mode possible with other experiments, E906/E1039

## Slide 44: A New High-Granularity Displayed Dimuon Vertex Trigger
Y-Plane Trigger:
A quadrant panel: 50cm x 50cm, 1cm thick
  1cm x 1cm x 50 cm scintillating strips, SiPM readout
- Straight line projection, 30cm Z-vertex resolution
- Displaced z-vertex, mostly low mass < 3GeV
Coincident with St-4 Hodos(muons), or EMCal(e+/-)
Y-channels per quadrant:
1x V1495
50(St1) + 50(St2) + 8x2 (St4-Y1,2) = 116
96+64 = 160 inputs possible
  72+72+16 = 160 (possible)
  (2NIM=RFCLK+ComSTOP )
Bigger one?!, 72 channel per Q/station
  576 SiPMs needed (600)
St1
St2
Coincident Z-vtx
window matched@L2
Dimuon Z-vertex (cm)
Z
High rejection power, very low rate, << 1 kHz(E906 DAQ limit)
X
Y

## Slide 46: V1495 Board 2 Altara FPGA Chips: Cyclone-V
Trigger lookup table

## Slide 47: E-1067 Future Upgrade: Phase-II 2020 ~ 2025+ ?
Add tracking close to “target” to improve mass resolution
Add EMCal + Hcal, PID?
e+/-, h+/- , π+/-

## Slide 48: Phase-II: Access Low Mass Region with e+e- with future detector upgrades
p
p
l+
l-
S. Gardner, R. Holt et al

## Slide 49: Phase-II: Full Coverage with future detector “EMCal/HCal” upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, RHIC/JLab etc.
DAQ upgrade
  100 kHz
Timeline of dedicated runs
  2019+
Detector configuration
  Access low mass region with optimized Fmag settting
Projection: POT 1.4 x 1018

## Slide 50: Phase-II: Probe Non Abelian Dark Sector with future detector “HCal” upgrades
non-Abelian dark sector process
S. Gardner and R. Holt
[Note: Batell, Pospelov, and Ritz, PRD 80 (2009) 095024 for a review re fixed target expts.]
Here we consider a non-Abelian (gluon) portal
[Baumgart et al., JHEP 0904, 014 (2009); Gardner and He, PRD 87 (2013) 116012]
The “shining through walls” design – unique to Seaquest – makes this possible ,
to yield, e.g., via a “minimal” decay….

## Slide 51: E-1067: A New Program to Probe Dark Sector in Beam Dump Mode
E906/E1039: Targets ~10% λI

## Slide 52: Summary and Outlook
Phase-I
  Great discovery potential!
  Add a new displayed vertex trigger
  Early parasitic data taking 2017-2019+
    A short dedicated run up to ~1 month if needed
  POT 1.4 x1018
Phase-II
  Possible detector upgrade later, add electrons and hadrons
  A new dedicated dark matter program at Intensity Frontier!
Dark Higgs
search
2015
2016
2017
2018
2019
2020+
Preparation Phase-I (parasitic runs)
Phase-II

## Slide 53: Vector Portal and Dark Photon A simplest model of dark sector
An extra U(1)X, kinetic mixing
Not suppressed by mass scale
Holdom
Galison, Manohar
SU(3)C x SU(2)L x U(1)Y x U(1)X

## Slide 54: Expectations from GUT
After EWSB, there is a coupling ε between the dark photon and the photon (also the Z, less important at low energies).
Theoretical prejudice for a mass scale
mA’ ~ √ε mEW ~ (MeV – GeV)
e.g. Arkani-Hamed & Weiner;
Cheung, Ruderman, Wang, Yavin;
Morrissey, Poland, Zurek;
Essig, Schuster, Toro;

## Slide 55: Current Limits on Dark Photon Search
BaBar (2014)
Slide credit: Bertrand Echenard

## Slide 56: Current E906 Trigger & DAQ System
……
Comm.
Stop/Trigger
L2-Trigger
V1495 (1)
Trigger Supervisor
Threshold Discriminator
TDC (xx)
L1-Trigger
V1495 (4)
(96)
DAQ
Hits/
Start
L0 Trigger: not “actively” used
- 4 V1495 boards available
L1 Trigger: in operation
- 4 V1495 boards
(2) for Y-plane, not used
(2) for X-Plane, in use
- 700nS latency
L2 Trigger: pass through
1 V1495
Could do simple look-up
TS: Trigger Supervisor
VME/CPU
Ethernet
Pulse Gen.
V1495 @TB
L2: limited I/O
1(O), 5(I), 32x
only 2 (I) used
Hodos

## Slide 57: PHENIX EMCal
Key specs:
Tower size: 5.525 × 5.535 cm2
Number of towers per sector: 72 × 36
Active sampling cells: 66
  Scintillator: Polystyrene, 0.4 cm
  Absorber: Pb, 0.15 cm
Active depth: 37.5 cm
Radiation Length: 18
Nuclear Int. Length: 0.85
Energy resolution
𝛑/e separation
2 sectors available in this summer!