## Slide 1: Direct Search for Dark Photons and Dark Higgs in Beam-dump Mode at E-1067/SeaQuest at Fermilab
Ming X. Liu
Los Alamos National Laboratory

## Slide 2: Intensity Frontier at Fermilab: 120 GeV Beam
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
World’s highest intensity high energy proton beam:
“beam dump mode” @E-1067
50,000 fb-1 (in 1 year of parasitic run)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
B-factory@KEK: 50,000 fb-1 (~2023)
- Capture most beam in beam dump mode: p+Fe collisions!
- Parasitic run mode possible with other experiments, E906/E1039

## Slide 3
LOI submitted to Fermilab PAC May 20, 2015
A joint experimental and theoretical collaboration
(most E906/E1039 + new members, ~60)
---------------------------------------
Phase-I: (parasitic runs)
Addition of a new displaced dimuon trigger to tag long-lived downstream decayed dark photons (dark Higgs).
Parasitic data taking with E1039 in 2017-2019;
  A short dedicated run (up to ~1 month) if needed.
POT 1.44x1018
Phase-II: (upgrade)
Dedicated runs later with EMCal/HCal upgrades, e+/- and h+/- capabilities.
Cover the full parameter phase space allowed by beam energy and luminosity
POT: >> 1.4x1018
Phase-II request will be presented to PAC at a later time.
Notes: Responding to P5 reprot, we submitted LOI last month .. And the membership is growing …

## Slide 4
A heart-full endorsement
from Fermilab Director and PAC
July 15, 2015!
New experiment! E-1067
LANL LDRD support:
- FY16-17-18
- $1M to implement
the trigger/DAQ upgrade and theory development
Goals:
Trigger installed, 2017
Physics run, 2017-18
Preliminary results 2018!

## Slide 5: Outline
Physics of dark sectors
  Mass: MeV ~ GeV
Detector upgrade
  Displaced dimuon trigger
  DAQ improvement
New opportunity
  EMCal from PHENIX, available this fall
  Electron/hadron ID
Schedules

## Slide 6: Dark Photons and Dark Higgs Productions in p+Fe/BeamDump at Fermilab
Photon portal: “vector”
Higgs portal: “scalar”
θ = μ v/mh2

## Slide 7: Dark Photon Detection in Dilepton Decay Channel
Drell-Yan like
p0, h, … decay
Bremsstrahlung
p
p
l+
l-
(DM)
(DM)
MiniBooNE
Beam-dump
~ Fixed target w/
electron beams

## Slide 8: Detector Upgrades and Expected Signals
Dark photon trigger upgrade
  Add a fine-granularity scintillating strip based trigger/tracking to tag dimuons from the same decay Z-vertex
  A new trigger for events with displaced down-stream dimuons
Unique signals
  Displaced dimuon decay vertex for long-lived particles
  Invariant mass peak in dimuon mass spectrum
  Mostly from beam dump (target ~10% λI.)
Beam time
  Run parasitically with E906/E1039 (2017-2019)
  Possible dedicated runs later with upgrade (e+/-, h+/-)
Z (meter)
-- 2.5%
-- 6.0%
Dimuon mass resolution

## Slide 9: A New High-Granularity Displayed Dimuon Vertex Trigger
Y-Plane (non-bending) Trigger:
A quadrant panel: 80cm x 80cm (100cmx100cm @ST-2)
  ST1: 1cm x 1cm x 80 cm scintillating strips, SiPM readout
  ST2: 2cm x 2 cm x 100 cm strips
- Straight line projection, σZ ~30cm
Displaced z-vertex, mostly low mass < 3GeV
St1
St2
Coincident Z-vtx
window matched@L2
Dimuon Z-vertex (cm)
Z
High rejection power, low rate, << 1 kHz(current E906 DAQ limit)
X
Y
ST1
ST2
Y-channels per quadrant:
1x V1495
80(St1) + 50(St2) + 8x2 (St4-Y1,2) = 146
96+64 = 160 inputs possible
  (2NIM=RFCLK+ComSTOP)
Z1=9m
Z1=12m

## Slide 10: Trigger Detector Optimization Single Muon Z-Vertex Resolutions
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Sigma_Z ~ 30cm
Current
E906
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Forward: 2cm
Backward: 2cm
E906

## Slide 11: Low Mass Prompt Dimuon Trigger Rate Study
Current E906 setup
Proposed 2-layer trigger upgrade (10x improvement)
Additional Y-trigger after ST-3 absorber, and also using existing E906 X-Plane trigger
(additional ~2x improvement)
Current E906 DAQ 1kHz, can be improved to ~10+kHz with small cost
20+kHz possible for next run (reprograming trigger firmware etc.)
Parasitic mode: use up to ~10% DAQ bandwidth
Expected (Prompt) Low mass dimuon trigger performance

## Slide 12: Trigger/DAQ Upgrade
In good progress, to be installed by 2016
- Extruded scintillators + WLSF
SiPM readout, frames
Improve DAQ rate, x20+ expected

## Slide 13: Search Mode (1): Long-lived Dark Photons
Reconstructed dimuons with downstream Z-vertex:
3m < Z-vertex < 6m
Very low trigger rate, << 1kHz
Almost SM background free
Dimuon mass peak
- 5x1012 ppp ( current E906)
200 days
1.4 x 1018 POT (recorded)
4 events contours (2-sigma)
2-sigma (95%) exclusion plots
Excellent coverage of uncharted region!

## Slide 14: Search Mode (2): “Prompt” Dark Photons vs Drell-Yan Bump hunt at Z-vertx < 3m
Expected Drell-Yan like signal and backgrounds:
Drell-Yan Background
Dark photon
signal
Excluded phi
resonance region
Work in progress:
- optimization …,
- understand BG ...

## Slide 15: Phase-I Expectation: Dark Photons (parasitic run w/ E906/1039)
Signals considered:
Drell-Yan like
Eta decays
Bremsstralung
Covers a wide range of unexplored parameter phase space
Displaced dimuons
- Minimal SM background
Prompt dimuons
- Excellent coverage over BELLE-II
projection
- Possible dedicated runs later to fully
restore mass < 3GeV (Phase-II)
Phase-II with upgrades
Access below 200MeV with di-electrons
( add EMCal)
Work in progress!

## Slide 16: Dark Higgs
Phase-I:
High-mass: μ+μ- and hadrons
Advantage of using hadron beams
with muon probes over electrons
Phase-II:
Low-mass: e+e-, <200MeV possible
High-mass: hadrons, (5x)
Y. Zhang et al, arXiv:1502.06983
arXiv:1312.4992
θ = μ v/mh2
e+e-
μ+μ-
Electron ID
upgrade!

## Slide 17: Projected Dark Higgs Sensitivity POT:1.4x1018 (Phase-I)
Dimuons with downstream displaced decay vertices
Limited sensitivity to “prompt” large mixing case due to small cross-section
Dark Higgs or dark photons?
  Dimuon kinematic and angular distributions
Phase-II
  Dedicated high luminosity runs optimized for low mass acceptance, mass<3GeV
Y. Zhang (2015)
5x
25x
1x

## Slide 18: E-1067 Future Upgrade: Phase-II 2020 ~ 2025+
Add tracking detectors close to “target” to improve mass resolution
Add EMCal, PID
e+/-, h+/- , π+/-

## Slide 19: EMCal from PHENIX/RHIC
2 EMCal sectors are available from PHENIX experiment at RHIC, ~end of 2016
  One sector:
    2m x 4m, 18 (3x6)super modules
    Super module = 36 modules; Module = 4 towers
    36 x 4 x 18 = 2592 channels
    Could gang 2x2 (or 3x3) into one ADC/TDC readout
- dE/E = 8.1%/sqrt(E) + 2.1%
- dT < 200 ps
- Excellent e/pi separation

## Slide 20: Phase-II: Displaced Low Mass Dark Photons with EMCal upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, PHENIX/RHIC etc.
DAQ upgrade
  100+ kHz
Timeline of dedicated runs
  2020+
Detector configuration
  Access low mass region with optimized Fmag settting
Projection: POT 1.4 x 1018

## Slide 21: Summary and Outlook
Phase-I
  Great discovery potential!
  A new vertex trigger & DAQ++
  Early parasitic data taking 2017-2019+
  POT 1.4 x1018 or more
Phase-II
  Possible detector upgrade later, add electron and hadron capability
  A new dedicated dark matter program at Intensity Frontier!
Dark Higgs
search
2015
2016
2017
2018
2019
2020+
Preparation Phase-I (parasitic runs)
Phase-II

## Slide 23: EMCal Upgrade: More Opportunities
2 sectors (4×4 m2 coverage) PHENIX EMCal will be available after this summer almost for free (not including shipping and instrumentation)
With EMCal installed, we will be able to access:
  dark photon from 𝛑0 decay
  dark 𝝆 decays to 𝛑𝛑
  enhanced dark higgs sensitivity
Two different scenarios of including EMCal have been studied via MC, and it poses little impact to our primary physics goal
Potential bonus of better background rejection on trigger level (studies underway).

## Slide 24: Comparison with SHiP Proposal
120 GeV@FNAL: 2017 -2019
1.4x1018 POT or more, future dedicated runs
400 GeV@SPS: 2025 -2030
4x1020 POT

## Slide 25: Dark Photon Decay Modes
“Minimal” Decay:
Dark photon is the lightest in the dark sector;
  SM final state particles only
Proper decay length: L0 ~ O(1m)
“General” Decay:
Decay into other dark particles,
dominant channel if allowed
  Dark -> Dark
  Dark -> SM particles
(GeV)
D. Curtin, et al, arXiv: 1312.4992
Electron ID
required!

## Slide 26: Two Possible Configurations and Their Impacts
Two configurations:
Option I: use EMCal to
replace the absorber
Option II: insert EMCal between H3 and absorber (will need to slightly adjust station-3 position)
Potential impacts on our primary physics goal:
Muon identification power
Acceptance? (MC shows no impact)
Occupancy in station-4 and thus our raw trigger rate
Data volume and DAQ deadtime?
Test MC samples (for each scenario):
500k single 𝛑/μ/e tracks with 5 GeV < P < 115 GeV
1M high mass (M > 4 GeV) target DY pairs
2E10 inclusive pp collisions (see, MC simulation talk by David K.)

## Slide 27: μ/𝛑 separation: case 1 vs. case 2 vs. original
Orignal
Case 1
Case 2
μ survival chance
𝛑 survival chance
For μ survival chance (or μ-ID efficiency), all 3 cases are very close to 100%
For 𝛑 survival change (or 𝛑 contamination):
  original design is around 0.5%
  case 1 is around 10%
  case 2 is around 0.1%
μ identification favors case 2

## Slide 28: Displaced Dark Photon Trigger
Q1 (LVL1)
Q2 (LVL1)
Q3 (LVL1)
Q4 (LVL1)
LVL2
(vtxZ matching)
4 x 16-bit from 4 V1495 boards
(2 x 32LVDS cables)
Q1: 80(ST1’) + 50 (ST2’) + 2x8(ST4-Y1/2) = 146, FANOUT ST4 Hodo (or EMCal Cluster)
DAQ/Data stream
TS
(12 inputs total)
(1-free bit available)
DP Trigger
1-bit
DAQ Trigger
LVDS cable 2x16ch bundle available
V1495