## Slide 1: Intelligent Experiments Through Real-Time AI - Fast Data Processing and Autonomous Detector Control for sPHENIX and Future EIC Detectors
Ming Liu
Los Alamos National Laboratory
for the Fast-ML Team
DOE Fast-ML Presentations
November 30, 2022

## Slide 2: Today’s Presentations
Overview, 10’
  - Ming Liu (LANL)
Physics simulation and AI-ML algorithms, 10’
  - Dantong Yu (NJIT)/Cameron Dean(MIT)/Zhaozhong Shi(LANL) /Tingting Xuan(SBU/NJIT)/Hang Qi(MIT)/Hao-Ren Jeng(MIT)/Beilei Jiang(NTU)
HLS4ML and firmware implementation, 5’
  - Micol Rigatti (FNAL)/Nhan Tran(FNAL)/Phil Harris(MIT)
Demonstrator implementation, 5’
  - Jakub Kvapil (LANL)/Yasser Corrales(MIT)/Noah Wuerfel(LANL)/Jo Schambach(ORNL)/Kai Chen(CCNU)/Lang Lei(CCNU)/Beilei Jiang(NTU)

## Slide 3: Today’s Presentations
Overview, 10’
  - Ming Liu (LANL)
Physics simulation and AI-ML algorithms, 10’
  - Dantong Yu (NJIT)/Cameron Dean(MIT)/Zhaozhong Shi(LANL) /Tingting Xuan(SBU/NJIT)/Hang Qi(MIT)/Hao-Ren Jeng(MIT)/Beilei Jiang(NTU)
HLS4ML and firmware implementation, 5’
  - Micol Rigatti (FNAL)/Nhan Tran(FNAL)/Phil Harris(MIT)
Demonstrator implementation, 5’
  - Jakub Kvapil (LANL)/Yasser Corrales(MIT)/Noah Wuerfel(LANL)/Jo Schambach(ORNL)/Kai Chen(CCNU)/Lang Lei(CCNU)/Beilei Jiang(NTU)

## Slide 4: Overview
- Ming Liu

## Slide 5: Project Goals and Deliverables
Task 2
Task 4
Task 1
Task 3
Selective streaming real-time AI and autonomous detector control:
Deliver a demonstrator for p+p and p+Au running for sPHENIX -> generalizable for applications in experiments at the EIC
4 interconnected key tasks:
Constraints:
MVTX data rate = 300 kHz
INTT data rate = 9.4 MHz
Trigger latency = 10μs

## Slide 6: Leaderships and Technical Roles
New teams joined later in early 2022:
Dr. Jo Schambach, ORNL, PHENIX/EIC readout integration, sPHENIX MVTX and EIC/ePIC readout lead
Dr. Kai Chen, CCNU, FELIX-AI-Trigger hardware integration, FELIX developer at BNL for ATLAS, also sPHENIX
Prof. Song Fu, NTU, data acceleration

## Slide 7: Technical Approaches and Highlights - I
sPHENIX MVTX and INTT
full simulations of p+p collision
Jakub
Convert simulated hits to sPHENIX real data like bit-stream to feed FPGA/AI

## Slide 8: Technical Approaches and Highlights - II
Dantong

## Slide 9: Technical Approaches and Highlights - III
Primary focus:
achieving low latency, real-time processing of data, and deployment of algorithms with high efficiency
FELIX 711@FNAL
Micol/Phil

## Slide 10: sPHENIX Readout and AI-ML HF Trigger Integration
DCM-2 receives data from digitizer, zero-suppresses and packages
SEB collects data from a DCM group (~20)
EBDC Event Buffer and Data Compressor (~40)
Buffer Box data interim storage before sending to the computing center (6)
On Detector
Rack Room
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To
HPSS
(Computing Center)
100+ Gigabit
Crossbar
Switch
INTT
Streaming Readout (SRO) + AI/ML
TPC
MVTX
EMCal
iHCal
oHCal

## Slide 11: From sPHENIX to ePIC: Streaming + AI/ML DAQ
DCM
DCM
DCM
FEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Network
Switch
Buffer Box
EBDC
DAM
DCM
DCM
DCM
FEB
Online
Data Filter
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
DCM
DCM
DCM
FEB
EBDC
DAM
RDO
Online
Data Filter
Online
Data Filter
Monitoring
Timing System
Detector Control
To permanent storage and nearline processing
O(10 Tbps)
O(0.5 Tbps)
O(0.1 Tbps)
FEB = Front End Electronics Board
RDO = Front End Aggregation & E/O I/F
DAM = Data Aggregation Module
EBDC = Event Buffer / Data Compressor
O(2 Pbps)
(sPHENIX)
ePIC detector
SRO + AI/ML
from Jo’s talk at ePIC collab. mtg

## Slide 12: Summary and Outlook
Carried out full sPHENIX physics and detector simulations of heavy quark and QCD backgrounds
Developed preliminary AI-algorithms for sPHENIX HF triggers
Completed MVTX SRO
INTT SRO demonstrated
Implemented a toy AI-algorithm in HLS4ML in FELIX
Work in progress to implement full sPHENIX trigger in a simplified hardware
On track to complete a demonstrator in 2023
Future plan/proposal:
Extend project by 2 years, 2024 ~ 2025
Implement the demonstrator for sPHENIX p+p run in 2024
Develop ePIC TDR of SRO with AI/ML for EIC CD2(2024) and CD3(2025) based on our work
Note: completed; in progress

## Slide 13: Physics simulation and AI-ML algorithms
- Dantong Yu

## Slide 14: AI Trigger Pipeline
Fetch events from event buffer to Processing
Data Pre-processing Clustering
Tracking + Outlier hits Removal
Triggering
Triggers on TPC

## Slide 15: Simulations
Most simulations have focused on sPHENIX
  ePIC detector simulations for EIC are under rapid changes
We simulated 2 different physics events (all 200 GeV pp collisions)
  Minimum bias with all heavy flavor decays rejected for background
  D0→K- π+ in minimum bias for signal
Simulations have been improved throughout the year
  Added full service material for MVTX
  Added realistic hit duplication in MVTX from pixel pulse length
Dataset
  8 million Events - 50% signal/noise.
  8 million Events - 0.1% signal/noise.

## Slide 16: Algorithm Flow
Strategy is to construct a large scale AI algorithm with all elements of trigger
  Algorithm is factorizable into core physics components
  Emulates the normal reconstruction workflow
  Use of core components allows for intermediate physics validation
Silicon
Pixel
Hits
Graph Track reconstruction
Labelled
Track
Hits
Displaced
Vertex Reconstruction
Track Momentum Regression
Trigger Decision
(D/B Indentification)
Reconstructed
Track Momenta
Displaced Vertices
Graph NN
AI Algorithm Block
AI Algorithm Block
AI Algorithm Block
Bipartite

## Slide 17: Tracking as Graph Neural Networks
Graph neural networks are a popular way of posing tracking problems in physics
  Sparse hits in space do not fit traditional ML architectures
  Growing sub-field of geometric deep learning
Data is structured as a graph of connected hits
  Connect plausibly related hits using geometric constraints and learn best associations and parameters of connected hits (tracks)
See also:
https://exatrkx.github.io/

## Slide 18: Three Types of Potential Interactions in Model Event Decay
Local track-to-track interactions, such as determining whether two tracks share the same origin vertex.
Track-to-global interactions, such as determining the collision vertex of the event and potential secondary vertices of decaying.
Global-to-track interactions, such as comparing each track's origin with the collision vertex of the event.
Pair-wise Relations (Set/Graph/Attention)
Graph Aggregation
(Bipartite Graph aggregation)
- vertexing
Graph Distribution and Bypassing (Bipartite Graph)
- parent/daughter
Notes: This slide illustrates the main problem, it might be good to move this early
Adding high level explanation of the challenge “Find the secondary Vertex”
Vertex Parents

## Slide 19: Bipartite Graph Networks with Set Transformer (BGN-ST) Model Architectures
Set Encoder with Bipartite Aggregator (SEBA) Blocks
Notes: difficult to understand them .. backup slide?
Put This slide in backup, its a detail of next slide

## Slide 20: Experiments: Physics Driven BGN-ST
1% signal/background ratio |  |  | 0.1% signal/background ratio |  | 
Background Rejection | Efficiency | Purity | Background Rejection | Efficiency | Purity
90% | 72.5% | 7.25% | 90% | 78% | 0.78%
95% | 48.9% | 9.78% | 95% | 50% | 1.0%
99% | 15.0% | 15.0% | 99% | 17% | 1.7%
99.33% | 10.5% | 15.74% | 99.33% | 11.0% | 1.65%
Notes: Can you quote the signal efficiency for a background efficiency of 1% ( a rejection of 99%)
We compare our model with the ParticleNet(PN)+SAGPool method proposed in \cite{zhu2021new}. We also use Set Transformer and GarNet as our baselines because they are also well-suited to the problem of classifying a set of tracks. Table 2 compares the performance between BGN-ST and the baseline models. From Table 2, we observe that BGN-ST outperforms all other methods by a significant margin. It usually takes no more than one day to train the Set Transformer, GarNet and BGN-ST on a single GPU card. The baseline PN+SAGPool has more parameters than ours. It takes two to three days to train the baseline model PN+SAGPool.

## Slide 21: Status and Outlook
Demonstrated BGN-ST outperforms selected state-of-the-art methods [1,2]
  Improves the task accuracy and AUC score by about 15%
  Architecture benefits from pairwise interactions between tracks and allows a two-way scattering and gathering for effective information exchange and adaptive graph pooling
  Adopts the physics-aware concept and introduces explicit physics properties such as transverse momentum
Next step: From optimal performance of state-of-the-art methods, develop firmware implementations
  Understand what is feasible and condense the model into latency and resource constraints
[1] Xuan, Y. Zhu, G. Borca-Tasciuc, M. X. Liu, Y. Sun, C. Dean, Y. C. Morales, Z. Shi, D. Yu, End-To-End Pipeline for Trigger Detection on Hit and Track Graphs in, Accepted by Thirty-Fifth Conference on Innovative Applications of Artificial Intelligence, IAAI.
[2] Xuan, G. Borca-Tasciuc, Y. Zhu, Y. Sun, C. Dean, Z. Shi, D. Yu, Trigger Detection for the sPHENIX Experiment via Bipartite Graph Networks with Set Transformer in European Conference on Machine Learning and Principles and Practice of Knowledge Discovery in Databases (ECML-PKDD 22).

## Slide 22: hls4ml translation and firmware implementation
- Micol Rigatti and Phil Harris

## Slide 23: Hardware and Firmware Implementations
Selective data streaming in sPHENIX will use the FELIX board. FELIX is a 16-lane Gen-3 PCIe card with 48 transmitters and receiver optical links. The on-board FPGA is a Kintex Ultrascale XCKU115FLVF1924-2E
The FELIX Firmware implements the interface for the PCIe, the interface for the transmitters and receiver optical links, the routing of data, and the clock and resets logic.

## Slide 24: Hardware Configuration
A second FELIX is connected to the first FELIX through the optical transceivers, as a dedicated FPGA hardware for smart control and real-time decision-making for TPC readout in the selective data streaming architecture.
The AI Engine will search for displaced tracks to identify tracks from heavy quark decays that are pointing away from the nominal beam center. Such a signal will initiate the readout of the TCP detector.
The firmware of the AI Engine will implement the Neural Network deployed using hls4ml, the PCIe interface, and the optical link interface.

## Slide 25: Schedule – completed
1
The Fermilab test stand has been set up: the FELIX board BNL711 is set up in a Host Computer.
2
On the Host Computer, the FELIX driver and the software application is been installed.
3
The data movement between the BNL711 and the Host Computer is been tested. The data are emulated inside the BNL711.
4
The hsl4ml workflow is been tested with the Kintex Ultrascale XCKU115 as a target generating the IP of a simple NN
5
The IP of the simple NN is in the integration phase with the Wupper module (PCIe engine)
XILINX PCIe End Point
Interrupt controller
DMA read
DMA control
DMA write
Wupper PCIe engine
Wupper core DMA engine
PCIe Gen3 x8
Simple NN IP
Data emulator

## Slide 26: Schedule – next steps and challenges
Test the functionality of the NN and the data routing mechanism
Fit the NN in the FELIX Firmware complying with timing constraints.
The workflow of hls4ml generates an IP considering available the resources of the target FPGA. We need to route the NN considering the already routed FELIX Firmware.
NEXT STEP: the analysis of the FELIX Firmware in terms of resources to drive the hls4ml implementation of the NN
NEXT STEP: the integration of the IP of the simple NN is in with the Wupper module (PCIe engine)
APPLICATION
OPERATING SYSTEM
FELIX HW & FW (BNL711)
FELIX DRIVER
The FELIX card is a data router. It needs an application to be instructed on the data movement.
The application relies on an OS and a driver interfacing the FELIX card.
Inserting the NN in the FELIX Firmware will change how the driver interfaces with the card
The testing part right now relies on the interplay of Hardware, Firmware, and Software
Interfacing the board to test the NN is the other real challenge
Meeting the timing in this condition is the real challenge
1
2
3
4

## Slide 27: GNN Implementation in hls4ml
Simplified Graph-based encoding to hls4ml-style interface
https://arxiv.org/pdf/2112.02048.pdf
First version of hls4ml-based Graph encoder available
Critical optimization needed in construction of Graph-based mapping

## Slide 28: GNN Planned Upgrade in hls4ml
Active work is underway to improve the GNN implementation
Base implementation has been updated twice in 2022
A third update will start in mid December, focusing on 3 examples
  Example 1: Tri-muon reconstruction with the LHC (muon endcaps)
  Example 2: Heavy flavor tracking at sPHENIX
  Example 3: Silicon strip tracking at LHC
Current Graph encoder to be optimized (adjacency matrix computation)
  Aiming to centrally rework this with core hls4ml developers
  Will be a central project across several domains
@200 MHz, 1590 Cycles → 7.5μs
Notes: Add text

## Slide 29: Demonstrator Implementation
- Jakub Kvapil

## Slide 30: Demonstrator Development @ LANL, ORNL and CCNU
Why a demonstrator?
A lot of sPHENIX technologies under rapid development at the time of proposal
sPHENIX DAQ will be ready in early 2023
  Parallelize development in early stage to be ready for final deployment
More FELIX boards available later
  The AI core logic will be implemented on VC709 which is the FELIX protoboard (share similar resources and is supported)
LANL Setup

## Slide 31: Demonstrator Implementation
sPHENIX raw data
Simulation
KC705
(MVTX)
KC705
(INTT)
AI FPGA
VC709
GPU/CPU processing
Fast HF
trigger output
Beam vertex(x,y) alignment,
calibration etc.
e-Link/PCIe
g-Link
DONE
DONE
Work in Progress
Work in Progress
Both KC705 and VC709 will be replaced by FLX712 at deployment stage

## Slide 32: sPHENIX RAW Data Simulation
In order to test the full loop feedback AI system detector hits must be known.
Code developed to transform MC JSON hit patterns into MVTX and INTT raw data streams
LANL

## Slide 33: KC705 Raw Data Transmission
Simulated data must be streamed to the AI VC709/FLX712 FPGA
KC705 is used to read the MC data via PCI XDMA and transmit them using g-Links
One link for MVTX and one for INTT
63:32
31:0
Package ID
Head
One packet
64 bit
payload 1
payload 2
63:48
0x0000
47:32
0x0000
31:16
0x0000
15:0
0x0000
63:48
0x0001
47:32
0x0001
31:16
0x0001
15:0
0x0001
payload 3
63:48
n
47:32
n
31:16
n
15:0
n
63:48
0xFFFF
47:32
0xFFFF
31:16
0xFFFF
15:0
0xFFFF
payload n+2
payload 2^16+1
…
…
PCIe Width: 64bit
CCNU

## Slide 34: FLX712 Raw MVTX Data Transmission to AI-FPGA
ORNL
FELIX input: up to 24 GBT links at 3.2 Gbps payload rate
MUX Logic: multiple GBT packets into raw data packets with header
GTH output: ~8 GTH wizard data streams (8b10b encoded) at up to 14 Gbps
KCU105 simulates the AI/FPGA board that receives the GBT data and contains the AI engine
Implemented GTH wizard example design to measure bit errors and verify received data

## Slide 35: Timeline and Outlook
2021
2022
2023
2024
2030+
Project funded by DOE FOA
  Dec. 2021 (Lab)
  Jan. 2022 (Univ.)
MVTX & INTT SRO
Fast tracking & trigger algorithms in place
Initial FPGA bitstream
GPU feedback machine R&D
Refine interface between system and detectors
Improve algorithms with latest data stream
Pre-commissioning
Deploy device at sPHENIX
pp/pA run
EIC preliminary TDR (CD2)
Final design for EIC TDR (CD3)
Take advantage of new technology if required
Deploy device at EIC
Future plan
Great progress, on track to succeed in 2023

## Slide 36: Backup slides

## Slide 37
MVTX
INTT: Two Silicon Strip Barrels
TPC
iHCAL
EMCAL
Event Timing: Reject out of time MVTX hits with INTT

## Slide 38: Feed MVTX/INTT MC Hits to AI Engine
KCU105
(MVTX)
KCU105
(INTT)
VC 709 (FPGA/AI)
g-Links
MVTX/INTT events matching
(50 beam crossings )
MVTX/INTT Evts
Hits + VTX(x,y, Z)
HF Trigger
NN Algorithm
AVG Beam
VTX(x,y)
Raw MVTX and INTT data packets:
~20 pp collisions (MB events) @4MHz pp
- 1 MVTX packet @5uS strobe:
50 INTT packets (RF)
Glinks: 1 MVTX and 50 INTT data packets (~5us worth of data)
Step-1
Step-2
Step-3

## Slide 39: sPHENIX and EIC Schedules
sPHENIX Run Plan: 2023-2025
pp and pAu run in 2024
EIC Project Plan (as of 11/05/2022)
ePIC TDR for CD2/CD3A, 2024
Final design/construction, 2025

## Slide 40: EIC: ePIC DAM Candidates: ATLAS “FELIX”
Current ATLAS Phase 1/ sPHENIX FELIX BNL-712v2
FELIX FLX-181 Prototype (BNL)
Current Design of FELIX FLX-182
(Hao Xu, BNL, DAQ WG meeting 7/2021)
Assembled 24ch FLX-181 with 25 Gbps FireFly FMC+

## Slide 41: FELIX Status