## Slide 1: sPHENIX MVTX Upgrade
Ming Liu
Los Alamos National Lab
for the sPHENIX Collaboration

## Slide 2: Outline
Science
MVTX upgrade
Physics prospects

## Slide 3: sPHENIX – the Next Generation HI Experiment @RHIC
To study the inner workings of QGP with,
  Jets
  Upsilons
  Heavy flavors

## Slide 4: Heavy Quarks - Unique Probe of QGP
Study mass dependence
  Jet quenching
  Flow – interaction with medium
Access QGP properties
MeV
1
10
102
103
104
mu md
LQCD
TQGP
mc
mb
Tc
ms

## Slide 5: Charm RAA
RAA (D-meson) ~ RAA (h) at high pT ~> 4 GeV/c
significant suppression of charmed hadron RAA in central A+A collisions
strong charm-medium interactions
mass effect expected important at low pT, dead-cone effects etc.

## Slide 6: Charm V2
v2 of D0 follows the same trend as light hadrons
Charm quarks flow the same as light quarks
Strong coupling to medium at low pT?

## Slide 7: Beauty?
RAA (B->e) > RAA (D->e, h) @low pT
B+ & b-jet ~ light hadrons & charm @high pT
STAR, QM17
Highly desired:
precision measurements of
B @low pT ~< 50GeV

## Slide 8: MVTX:MAPS-based Vertex Detector
A separate upgrade project for the baseline sPHENIX: Jet + B-tagging
Parallel Activities
MAPS-based Vertex Detector (MVTX)
Intermediate Silicon Strip Tracker (INTT)
Baseline
Upgrades

## Slide 9: MVTX Proposal
ALICE ITS Upgrade:
Inner Barrel Tracker
sPHENIX Inner Tracking
Adapt ITS/IB
- Min. Risks
- Max. Phys.
Major challenges:
- Readout
- Mechanics
R = 23/32/39 mm
Z = 271 mm

## Slide 10: ALPIDE Timing & Trigger
Well fit sPHENIX/RHIC environment, 10MHz Clock (LHC 40MHz)
DV=Q/C
v
t
PIX_IN
tr> 100 μs
tf~= 10 ns
OUT_D
STROBE
~5-6 ms
~5-6 μs
v
t
OUT_A
threshold
sPHENIX trigger latency: ~4 μs

## Slide 11: sPHENIX vs ALICE Specifications
 | ALICE (Run3) | sPHENIX
Pb+Pb / Au+Au | 100 kHz (50kHz) | 200 kHz
p+p | 400 kHz (200kHz) | 13 MHz
Trigger | 50 kHz | 15 kHz
Event size, dN/dη: sPHENIX = 1/3 ALICE (pp), 1/5 ALICE(AA)
sPHENIX
ALICE

## Slide 12: RHIC Multi-Year Plan: sPHENIX 2022-2026+
Precision 2nd vertexing for B-tagging:
  Tracking resolution better than 50um @pT=1GeV
  High multiplicity HI collisions
  Low multiplicity but high rate p+p collisions
  High efficiency and high purity
B hadrons/pT<15GeV: O(1M)
b-jets/pT>15GeV: O(100K)
Evolving

## Slide 13: MVTX Proposal Status
Pre-proposal submitted to DOE, 2/2017
  Follow-up discussions with DOE and BNL managers
Update proposal to DOE, early 2018
  Expanded science + Cost & Schedule
  Assumed funding starts ~FY19
A growing collaboration
  15+ institutions from US and abroad
Early R&D by LANL internal fund
  FY17-19, $5M
  Readout and mechanical design

## Slide 14: MVTX Readout and Control R&D at LANL
Power Board
Filtering
Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5~10 m
GBT Optical Links
9-sensor Stave
sPHENIX GL-1 & GTM
DCS
CAN bus
Power supplies
Power
Trigger & Clock
LANL, UT-Austin, LBNL, BNL, ALICE/ITS …
Established the readout chain test: ALPIDE + KC705(RU) + FELIX + RCDAQ/sPHENIX
RUv.10 arrived last week, 10/21/2017
ALPIDE and Power Unit being tested
ALPIDE

## Slide 15: R&D at LANL
Power unit test
ALPIDE/Stave evaluation test bench

## Slide 16: Simulation for b-jet and B-meson
Design to Simulation
sPHENIX Geant4 display of pT=30 GeV/c B+-hadron
MVTX and INTT _
_ MVTX Ladders modeled in details
MVTX sensors

## Slide 17: Physics Channels: Open Charm and Beauty
Hadron | Abundance | ct (mm)
D0 | 61% | 123
D+ | 24% | 312
Ds | 8% | 150
Lc | 6% | 60
B+ | 40% | 491
B0 | 40% | 455
Bs | 10% | 453
Lb | 10% | 435
b-tagged jet and cor.
60%
0.5%
pT<15 GeV
pT>15 GeV
Exploring and more

## Slide 18: Tracking Performance with Full GEANT
MVTX geometry modeled and digitized according to ALICE ITS/IB
Cluster resolution: ~5 µm
DCA2D , DCAz<30 µm down to 1 GeV/c
DCA_rf
DCA_z
Fake hit fraction

## Slide 19: B-jet tagging
Multi-tracks w/ large DCA
2nd vertex mass reco’s
CMS work-point, Phys. Rev. Lett. 113, 132301 (2014)

## Slide 20: B-hadron Tagging
Impact parameter (DCA) method to tag non-prompt D0 from B-meson decays
Inclusive and exclusive channels possible

## Slide 21: Projected RAA
Open questions: energy loss and medium properties

## Slide 22: Project Elliptical Flow v2
Open questions: quasi-particle and medium interactions

## Slide 23: Summary: Exciting Science
sPHENIX is the next flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets
  Upsilons
  B-jets and B hadrons
MVTX will complete QGP heavy flavor physics
  Unambiguous determination of key parameters of QGP properties and interactions
  Precision study of the “inner workings of QGP”(LRP15)
Complement & extend current and future RHIC and LHC QGP programs
sPHENIX Three Physics Pillars
Jets
Upsilons
B
D

## Slide 24
4th sPHENIX Collaboration Meeting at BNL, June 2017

## Slide 25: Summary and Outlook
sPHENIX collaboration fully engaged toward physics in early 2020s with the baseline detectors
MVTX upgrade will bring in the 3rd science pillar – open heavy flavor physics and more
Strong support from the community, LANL LDRD etc.
Great opportunity to advance our understanding of the inner workings of QGP
2017
2018
2019
2020
2021
2022
2023+
sPHENIX:
CD-1
MVTX:
Construction
1st beam
Installation
Full
proposal
Installation
Day-1 physics

## Slide 26: MVTX Funding & Schedule
Tied to sPHENIX and ALICE schedule
  Stave production
  Readout electronics
  Minimize technical risk and R&D cost
Cost based on ALICE/ITS and similar recent STAR & PHENIX upgrade projects
  STAR HFT
  PHENIX FVTX

## Slide 27: Schedule
sPHENIX ready for installation: 4/2021
sPHENIX installed and ready for commission 7/2022
sPHENIX commission complete 9/2022
First beam 1/2023
sPHENIX CD-4 1/2024
Install INTT 4/22/2022
MVTX ready for installation: ~1/2022 (or with INTT, ~4/2022)
MVTX installed and ready for commission 7/2022
MVTX ready for beam: 1/2023

## Slide 28: Monolithic-Active-Pixel-Sensors (MAPS) The next Generation State of the Art Pixel Tracker
Advantages of ALICE MAPS/ALPIDE:
  Very fine pitch (28x28 μm)
  High efficiency (>99%) and low noise (<10-6)
  Fast readout, ~5 μS
  Ultra-thin/low mass, 50μm (~0.3% X0)
  On-pixel digitization, low power dissipation
An ideal detector for QGP b-jet physics!
50 μm
28 μm
ALPIDE design
FPC
9 Chips
Cooling plate
A 9-chip MAPS stave, 1.5 x 27cm2

## Slide 29: Scope of the MVTX Project
MAPS Staves & Electronics
  MAPS staves “MoU” to build 68 ITS inner Barrel Staves
    No modification
  Readout Electronics R&D
    Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Modify/reprogram RU & FELIX for sPHENIX
    R&D by LANL LDRD
  Production:
    Extend ALICE/ITS MAPS stave production
      WBS 1.5.3.1, LANL
      sPHENIX personnel help at CERN
    Reproduce additional ALICE/RU & ATLAS/FELIX
      WBS 1.5.2.1, UT-Austin
      WBS 1.5.2.2 , LANL
    Final assembly and test in US
      WBS 1.5.3, LBNL
  Ancillary systems, “adopt” ALICE system
    Power distribution, cables, crates, racks etc.,
      WBS 1.5.2.3, LBNL
    Slow control, safety and monitoring
Mechanics & Cooling
  Some changes to ALICE/ITS inner tracker mechanical structures, WBS 1.5.3
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration, WBS 1.5.4
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Carbon frames etc., LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Minor modification to fit sPHENIX
    Smaller heat load than ALICE ITS
  Metrology and Survey

## Slide 30: Detector Assembly
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Assembly of layers and carbon fiber structure into half-detector
Stave testing at each step
Metrology survey

## Slide 31: Sheet 3, showing extended inner tracker with current outer composite shell

## Slide 32: Sheet 1, section view of sPHENIX inner detector assembly (inside the superconducting solenoid magnet), the ALICE service barrel has been modified – shortened, see later sheets for detail

## Slide 33: sPHERNIX cross-section view, including envelope for services; TPC and INTT, the following 2 slides detail views -
TPC services (one end)
INTT services, (one –end)