## Slide 1: MVTX/INTT R&D
Ming Liu
Los Alamos
Many inputs from Walt, Alex, Sho, Hubert,
Cesar, Xuan, Dan, Rachid, Itaru and the MVTX group

## Slide 2: MVTX/INTT Integration Review: around the week of June 25
w/ ~50cm FPC power extension
  @LANL, voltage drop, noise pickup
  MVTX conical structure modification, reduced radius
w/ 10cm extension FPC – Plan A
  INTT layout, “cables” and supporting structures
  Final extension bus ~1.2m, INTT, summer 18
  MVTX conical structure modification
  10cm HS signal simulation now ..
  Early R&D possible? right now, ~Sept 2018 @CERN
  Mechanical mockup: MVTX+INTT + .. , @BNL, LANL
w/o FPC extension – Plan B
  Revisit INTT layout, cables and supporting structures
  Final 1.2m bus, summer 18
  MVTX conical structure modification
INTT/MVTX simulations
  New INTT postdoc, INTT optimization, including supporting structure
Resources
  MIT engineers Jim/Jason ?
  Walt, Dan, Mike L, Hubert, Chris …, new $$ from non-MIE BNL project? New engineers?

## Slide 3: MVTX Flexible Printed Circuit (FPC) Extend MVTX Service Cables? Maximum +10cm for HS signal, TBD through R&D
506.2 mm
16 mm
41.9 mm
16.15 mm
Extend FPC/signal path by ~10cm
Power connection
Signal connection
Extend by ~10cm
signal
Power cable
Extension ~50cm
Also Impacting
SamTec
Cable length:
5~7m

## Slide 4
ALICE ITS/IB HIC: Signal, AVDD and DVDD

## Slide 5
ALICE ITS/IB HIC: Signal, AVDD and DVDD

## Slide 6: FPC R&D @CERN and LANL
High-speed signal, 1.2Gbps
Analogy and Digital Power
Extension
Try to extend high-speed portion of FPC by 10cm @CERN, ~September 18
2) Try to extend AV and DV by ~50cm at LANL, ~summer 18

## Slide 7
Caps, resistors, connectors, etc
ITS/IB FPC, 50cm long;
CERN can make FPC up to 60cm long, but needs to be confirmed

## Slide 8: Requires New Design

## Slide 9: End View of ALICE Patch Panel

## Slide 10: Near Term Action Items: after Day-1 discussion
FPC simulation, with 10cm extension on signal
  May – June,18
Mechanical design of conical sector for:
  Default 50cm FPC
  Extended 60cm FPC
  With extended ~50cm PWR extension
  Build 3-D print mockup, with INTT configuration
Produce ~50cm PWR extension to study voltage drop and also possible noise pickup

## Slide 11: Full MVTX+INTT system test beam at Fermilab in ~Feb 2019
MVTX will carry out full system beam test with final staves, in ~Feb 2019.
INTT will carry our full system (Sensors+HDI + ~1m-long Extension-Bus + ROC) in ~Feb 2019
A full mockup of MVTX + INTT system could be tested at Fermilab Test Beam facility

## Slide 12: Cost reduction and in-kind contributions
Carbon structures
  In-kind, CYSS & End-Wheels
  Alternative fabrication sites:
    France – ALICE cost ?
    Italy – ALICE cost?
    Korea – also quote for end-wheels, and make ”real mockup”?
    China ? – possibility of CYSS etc.
Integration and interface structures
  BNL sPHENIX/MIE provide the interface?
  RIKEN contribution?
Stave and RU testing at CERN?
  In-kind, students/postdocs at LHC

## Slide 13: Forward MAPS detector for sPHENIX/EIC
Develop a forward 3~4 planes MAPS detectors for both EIC and f/sPHENIX forward tracking
  2 x 6staves/plane + 2 x 2 RUs for readout
  MFT-like disk array inside the INTT supporting tube
MAPS-disks

## Slide 15: Day-1 discussion

## Slide 16: MVTX Detectors
Mechanical system integration
Electrical system integration

## Slide 17: To Do List – Mechanical Integration
FPC extension
  Signal path, +10cm
  Power extension, ~50cm
SamTec cable length vs signal quality
  5~7m
  RU location, MVTX electrical system integration
Carbon structure and connector design
  FPC HS signal connectors
  FPC power extension connectors
  MVT Service barrel and mechanical system integration
  Installation procedure

## Slide 18: INTT-MVTX Conflict
INTT 4-layers
Extend cables to move the conical structure further out in z-direction
FPC data cable is the HDI and can’t be easily extended, CERN will produce a prototype FPC (add ~10cm) for testing, ~Sept. 2018
Make long power extension, ~50cm,
Reduce angle of cone to free up space for INTT services (how much is needed?)
Redesign patch panel/cable connection shape and location

## Slide 19: MVTX Mockup & FPC Extension R&D
Extend FPC/data
cable by ~10cm?, R&D
PWR extension
L=15cm
Extended power cables AVDD/DVDD:
L = ~50cm, and possibly with 2~3 different lengths, like 30cm and 40cm
Separate PWR and signal connections at different Z-locations.

## Slide 20: SamTec Cable and FPC Extension R&D

## Slide 21: MVTX and INTT Integration
It is clear from this detail view the conical region of the MVTX detector barrel with the INTT that the MVTX will need to translate in Z…, but there is a limitation;
Optimize INTT design to fit within the limitation

## Slide 22: INTT Readouts from both North and South
h=0
h=1
105 cm
35cm
Bus Extender
The bus extender needs to run to ROC boards (reuse FVTX ROC) outside TPC.
Minimum length is 105cm – ladder length + distance to ROC board.
ROC
Boards
Bus Extender
ROC
Boards
Identical to FVTX Big Wheel
ROC boards mount off inner EMCAL

## Slide 23: INTT supported off Inner HCal from Dan Cacace/BNL
Very hard/Impossible for MVTX to have such a long extension

## Slide 24: Mechanical Integration - Model of MVTX with INTT inside TPC with the addition of two concentric composite cylinders; - INTT would like to use the outer shell of the MVTX as the inner shell of the INTT half detectors as a part of their cooling gas containment volume.
Location in Z where the inner-hcal ends (see control drawing) Z=2175.0 mm
Location of conflat flange on beam-pipe
- MVTX Electronics Racks;
- PS racks

## Slide 25
DETECTOR SECTION
SERVICES, SUPPORT SECTION
ALICE HALF-BARREL ASSY
Service Barrel: Design and Fabrication, modify ALICE design
MVTX will have a similar but much smaller service barrel
Need:
Support structure and
installation procedure

## Slide 26: To Do List – Readout and Controls
Update firmware, sync with latest ALICE firmware
  Scrubbing etc.
  Burn-in test, stability
Detector Control System (DCS) integration
  Power distribution and monitoring
  LV, “HV” and temperature
Sensor operation optimization
  Scan parameters for optimal operation
  Laser test bench setup at LANL
Multi-stave readout
  Up to 3 staves per RU
  Default: 1 stave per RU

## Slide 27: MVTX Electronics, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 28: Sensor and Electronics R&D @LANL
ALPIDE evaluation and optimization
  MOSAIC + Single Chip/Stave
  Cosmic and source
  Laser system
Power unit tested
  PU + MOSAIC
  PU + RU
Full readout chain demonstrated
  ALPIDE + RUv1.0 + FELIX v1.5 + RCDAQ
  Full stave + RUv1.x + FELIX v2.0 + RCDAQ
Mechanical system integration
  Conceptual design developed
  MVTX+INTT integration
  FPX & SamTec cables
  RU location etc
Collimator
Sr90 source
MVTX
ALPIDE chip
Scintillator

## Slide 29: Parallel Effort at UT-Austin – Shared R&D

## Slide 30: Summary: Major Remaining R&D
Mechanical/Electrical integration with INTT+TPC
  Carbon structure design
  FPC extension
  Support structure and installation procedure
Full electrical system control
  Power
  Safety and interlock
  Online monitoring & controls
Integrate readout system firmware/software with slow controls
  Multi-stave readout with single RU
Detector & Physics simulations

## Slide 31: backups

## Slide 32: More slides

## Slide 33: sPHENIX CAD model sectioned - view showing overall scale of sPHENIX detector; including all three tracking elements; MVTX, INTT and TPC
3,285.235 mm
NOTE; MVTX service cone and supports are not shown, MVTX offset in Z by 18cm
INTT
TPC

## Slide 34: BNL control envelope drawing - needs update for TPC, INTT, MVTX, MB Z location of the inner Hcal is at 2175,0mm
Z=2175mm

## Slide 35
Aluminum Flex
Copper Flex
Bidge Flex

## Slide 36
Aluminum Flex
Copper Flex

## Slide 37: INTT-MVTX Space Conflict
INTT 4-layers
Currently a clear conflict between the INTT and MVTX
  INTT only includes ladder, no connectors, cooling barbs, etc
R&D items:
Extend cables to move the conical structure further out in z-direction;
Design/optimize INTT layers to fit current MVTX geometry;
  FPC data cable can’t be easily extended (max additional ~10cm, machine limit)
  Reduce angle of cone – redesign C-structures and connectors
|η|<0.95
|η|<1.09
|η|<1.28
|η|<1.12
INTT Acceptance
@ |z|=10

## Slide 38: INTT + TPC

## Slide 39: Cross-section view from CAD model of MVTX, INTT, TPC, beam-pipe, plus two composite conical shells: MVTX radius are increased by 1.5mm to have a minimum 2mm gap between beam pipe and then inner MVTX structures

## Slide 40: Gap between conical shell (CYSS) of MVTX and inner layer of INTT is 11.58 mm
Dist= R61.58 – R50
= 11.58mm

## Slide 41: 56.0 mm gap between INTT and inner radius of TPC
Gap= R200-R143.5
= 56mm

## Slide 42: Offset from OD of beampipe and innermost component of the MVTX
New gap 2.025 mm

## Slide 43: Offset needed to install split MVTX into run location around beampipe, passing over 2.75 in conflat flange
37.6mm