## Slide 1: MVTX Status and Plan
Ming Liu
For the MVTX Detector Group
06/06/2018
sPHENIX Collaboration Meeting

## Slide 2: Outline
Project Status
MVTX full proposal
R&D Highlights
Plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 3: Toward Realizing MVTX …

## Slide 4: A Short Summary …
From Dave & Gunther talk
Feb. 2018
sPHENIX workshop in China, 4/2018
Korean consortium under discussion, led by Prof. Y. Kown
Extensive discussion of integration @MIT
MVTX+INTT+TPC…
https://indico.bnl.gov/event/4380/

## Slide 5: MVTX Status: Where do we stand?
BNL (w/ DOE) is actively exploring ways to secure funding for MVTX
  sPHENIX MIE at CD-2 (when baseline defined)
  Or a parallel project
BNL/MIT facilitating advanced funding for stave and RU production beginning Oct. 2018
  MVTX/INTT subsystem integration mini-review planned for 7/19/2018
  Procurement readiness review in September 2018

## Slide 6: MVTX Full Proposal

## Slide 7: MVTX: Monolithic-Active-Pixel-Sensor-based VerTeX Detector
sPHENIX Inner Tracking
“Adopt” ALICE/ITS
Mini. risk,
Max. physics
sPHENIX @RHIC
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
MVTX could also be a day-1 EIC detector

## Slide 8: MVTX Enables the 3rd Science Pillar
Jets
Upsilons
Open Heavy Flavor
Bottom quarks are heavy (4.2 GeV)
Produced in initial collision, probe QGP evolution
Well controlled in pQCD
Provide access to fundamental transport properties
Jin/Xin’s talk

## Slide 9: B-Hadron & b-Jet Tagging
Physics Reminder
Detected using the long lifetime of bottom quark hadrons:
  Displaced tracks
  Large 2nd vertex invariant mass
Need high precision tracking and vertex determination – MVTX!
Need excellent jet detection capabilities – sPHENIX!
Jin/Xin’s talks

## Slide 10: MVTX Physics Highlights
Heavy quarks – unique probe of QGP w/ new scales, mc, mb
  Study mass dependence
    Jet quenching & energy loss
    Flow – interaction with medium
  Access QGP properties
    Temperature, density, coupling, transport coefficients, viscosity etc.
MeV
1
10
102
103
104
mu md
LQCD
TQGP
mc
mb
Tc
ms
“B meson and b-jet modification”
“B meson and b-jet flow”
Jin/Xin’s talk

## Slide 11: R&D Progress and Highlights

## Slide 12: MVTX Electronics, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 13: MVTX Full Readout Chain Demonstrated
Readout Unit configures Stave using USB interface
FELIX distributes clock to Readout Unit
Readout Unit distributes clock to the Stave
Stave is triggered, sends data at 1.2Gb/s
Configured GBT link to recover clock from FELIX
Readout Unit receives the data and sends the data to FELIX over fiber using GBT link
FELIX packs data, stores it on disk using RCDAQ - the sPHENIX data format and software
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave

## Slide 14: MVTX Test Beam at Fermilab 02/20-03/10, 2018
Goals:
  Test full readout chain
  Evaluate ALPIDE sensor performance
Experimental setup
  A 4-sensor telescope
  Full readout chain: MAPS+RU+FELIX+RCDAQ
Parasitic with INTT run
Very productive & collaborative
120 GeV
proton
4-sensor
Telescope

## Slide 15: Fermilab Test Beam Results (I)
4-hit track
Cluster size: 2.1 ~ 2.4
Mostly single tracks
4-sensor telescope
# of tracks per triggered event
Cluster size
120 GeV proton beam

## Slide 16: Fermilab Test Beam Results (II)
Hit Efficiency > 99.5%
Pixel size (~28um)
Hit Spatial Resolution: < 5 um

## Slide 17: MVTX Detector Integration
Electrical system
  Readout, power, controls
Mechanical system
  Support and cooling
Office of System Integration
MVTX:
3 layers
48 staves
Mickey/Walt’s talks

## Slide 18: Toward INTT-MVTX Conflict Resolution
INTT 4-layers
MVTX: Extend cables to move the conical structure further out in z-direction
FPC data cable is the HDI and can’t be easily extended
Make longer power extension ~50cm (current: 15cm)
Reduce angle of cone to free up space for INTT services
Redesign patch panel/cable connection shape and location
INTT: optimize detector layout and support for integration
Walt/Mickey’s talks

## Slide 19: MVTX Mockup & FPC Extension R&D
PWR extension
L=15cm
Extended power cables AVDD/DVDD:
L = ~50cm, and possibly with 2~3 different lengths, like 30cm and 40cm
Separate PWR and signal connections at different Z-locations.
Extend power cables to ~ 50cm

## Slide 20: Plan for next 6+ months
Detector simulation for integration: INTT + MVTX + TPC … urgent!
  TPC-INTT-MVTX tracking optimization for integration
  Physics performance study, 3 or 4-layer INTT etc.
Mini-review, July 19
  MVTX/INTT subsystem integration
  Technical readiness of stave and RU for production
Production readiness review in September
  Stave and RU production at CERN beginning 10/2018
  Advanced funding, BNL/MIT
  MVTX + INTT + rest sPHENIX integration
Near term R&D
  MVTX carbon structure and integration
    End wheels
    Service barrel
  Electrical system integration
    Readout
    Slow control & power
  MVTX+INTT joint test beam at Fermilab, ~Feb/Mar 2019
Budget profile & schedule smoothing
  RHIC operation budget and cash flow
  MVTX production schedule
  Prepare for CD-2 MIE integration

## Slide 21: Summary
MVTX full proposal completed
  Expanded science
  sPHENIX baseline (CD-2)
  New collaborators, on physics/software and hardware
Cost and schedule being updated
  Major item cost and production plan
  Funding profile smoothing
  Advanced funding for staves and RU production at CERN
Excellent progress in R&D
  Full readout and controls proof-of-principle demonstrated
  Conceptual integrated mechanical system design developed
MVTX+INTT+TPC integration in progress
  Electrical and mechanical system
  sPHENIX wide coordination through Office of System Integration
To be ready for sPHENIX Day-1 Physics in 2023
  sPHENIX and later EIC possibility
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 22: Backup slides

## Slide 23: Monolithic-Active-Pixel-Sensors (MAPS) ALPIDE: The next Generation State of the Art Pixel Sensor
Advantages of ALICE MAPS(ALPIDE):
  Very fine pitch (27x29 μm)
  High efficiency (>99%) and low noise (<10-6)
  Excellent time resolution, ~5 μs
  Ultra-thin/low mass, 50μm (~0.3% X0)
  On-pixel digitization, low power dissipation
An ideal detector for sPHENIX and EIC physics!
50 μm
28 μm
ALPIDE design
FPC
9 Chips
Cooling plate
A 9-chip MAPS stave, 9 x (1.5 x 3 cm2)

## Slide 24: sPHENIX Tracking System
TPC
INTT
MVTX
Excellent Tracking system:
  TPC: Time Projection Chamber
  INTT: Intermediate Silicon Strip Tracker
  MVTX
TPC:
R = 20-80cm
INTT:
R =6,8,10,12cm
MVTX:
R=2.3, 3.2, 3.9cm
2m

## Slide 25: Fermilab Test Beam Summary
Successfully operated the full readout chain
  RU Configured and readout 4 ALPIDEs
  FELIX successfully integrated into RCDAQ
Sensor Performance
  Cluster Size
  Threshold parameters
  trigger delay
High multiplicity events
  ALPIDE occupancy runs with 10cm lead bricks
Online Monitoring
  Hit distribution, relative alignment
Analysis confirmed telescope performance
  Hit resolution < 5 um

## Slide 26: Fermilab Beam Test Block Diagram
CLK recovered from
FELIX through GBT link;
Trigger from FELIX
4-ALPIDE Telescope
4 5m SamTec Cables, 1.2Gbps

## Slide 27: 4 Sensor Telescope at Fermilab
KC705
External Trigger
4-ALPIDE Telescope;
5m long SamTec cables
RU
Si Time Kit
External Clock

## Slide 28: R&D Gameplan
ALPIDE Characterization
ALPIDE Triggered & Continuous Modes
Remote Readout Unit programming (over fiber)
Readout Unit Radiation Upset (Scrubbing) Firmware
FELIX programming (over PCIe).
RCDAQ (sPHENIX DAQ) finalization
Flex Cable Extension
System Optimization & Documentation

## Slide 29
A Test Bench at LANL
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5 m
Optical Links
9 Sensor Stave
RCDAQ
One HIC and 5+ individual ALPIDE chips.
MOSAIC miniDAQ
Power Board

## Slide 30: Trigger Latency and Signal Shaping Time Study
Lower the OUT_D threshold (IDB) increases the trigger duration time, but also increases the cluster size which might include more background hits.
In the continuous readout mode, “trigger/strobe” can start as early as ~1uS
Default set
Lower Threshold
(Lower the IDB)
sPHENIX
trigger
Nice work done by Xuan, Sho and Alex + others

## Slide 31: MVTX Flexible Printed Circuit (FPC) Extend MVTX Service Cables? Maximum ~60cm for HS signal, TBD through R&D
506.2 mm
16 mm
41.9 mm
16.15 mm
The 9 silicon chips are read out in parallel: each chip sends its data stream to the end of Stave by a dedicated differential pair, 100 mm wide. Two additional differential pairs distribute the clock and configuration signals.
CHIP 1
CHIP 9
……
CHIP 2
Extend FPC/signal path by ~10cm – challenging!

## Slide 32: SamTec Cable and FPC Extension R&D

## Slide 33: To Do List
FPC extension
  Power extension, ~50cm
SamTec cable length vs signal quality
  5~7m
  RU location, MVTX electrical system integration
Carbon structure and connector design
  FPC HS signal connectors
  FPC power extension connectors
  MVT Service barrel and mechanical system integration
  Installation procedure

## Slide 34: MVTX Carbon Structures
IB CYSS
Layer 0
Layer 1
Layer 2
Detector carbon frames:
CYlindrical Support
Structure (CYSS)
- End Wheels
Carbon structures need modifications w.r.t. ALICE for installation in sPHENIX

## Slide 35: MVTX Mechanical Conceptual Design
View of MVTX half detector assembly with extended central barrel
IB CYSS
Layer 0
Layer 1
Layer 2
27cm
MVTX Staves
Stave layout
Beam view
Needed extension for sPHENIX INTT integration, ~6cm possible

## Slide 36: INTT Support Structure from Dan Cacace, 4/27/2018