## Slide 1: MVTX Overview
Ming Liu
Pre-QM sPHENIX Collaboration Meeting
November 1-2, 2019
Fudan Univ., China
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 2: MVTX Detector
Service cone: signal, power, cooling
and mechanical support
MVTX
parameters
End-Wheel
Extended power FPC
CYSS: Cylindrical Shell Structure
3-layer sensor barrel
- 48 staves, 27.1cm long
- 432 chips

## Slide 3: Scope of the MVTX Project - WBS3.2
MVTX sensor & Electronics
  Detector assembly & integration: $4.8M
    QA & assembly
      RU boards @UT-A
      Half detectors @LBNL
      FELIX boards @LANL/BNL, 6+spares(2)
    Ancillary systems - “adopt” ALICE ITS system
      Power, slow control & monitoring etc.
  Readout integration
    Frontend: ALICE/ITS RU
    Backend: ATLAS FELIX
Mechanical system
  Modify ALICE/ITS detector support structures
    End Wheels
    Cylindrical structure shells
    Service half barrels
  Mechanical system integration,
    Design & simulations, MIT/LANL
    Composite structure production, LBNL and other possible commercial vendors
    Non-composite structure, MIT
    Installation tooling etc., LANL/MIT/LBNL/BNL
  Adopt ALICE cooling plant design
    Modified to fit sPHENIX, MIT/BNL
  Production @CERN: $1.4M, a separate BNL R&D project
    - 84 ALICE/ITS-IB (modified) staves from CERN
      In production, complete by 2020
      acceptance test @LBNL, 48+spares(2-inner layers+)
    - 60 ALICE/ITS-RU from CERN
      All produced, acceptance test @UT-Austin, 48+spares(12)
To be updated with review

## Slide 4: Project Status Update: 11/01/2019
Confirmed long SamTec readout cables recently – last key integration R&D hardware
  11.4m long cables, > 10m desired length
MVTX mechanical design: excellent progress
  Obtained quotes from outside companies based on preliminary designs for CYSS and End-Wheels
  MVTX/sPHENIX integration/insertion workfest , 11/14 @BNL, MVTX/INTT/TPC…
Early R&D fund released
  MVTX mechanical engineering design, MIT/LANL
  Preparation for Stave and RU acceptance test, LBNL, UT-Austin
July 2019 MVTX Cost & Schedule Review Response submitted
  WBS, PMP, Risk Registry, P6 updated
  Updated PMP and review response submitted to DOE
  We are ready for full production
Plan to start the MVTX production activities as soon as funds available
  Preparation for Stave and RU acceptance test & QA in US, LBNL and UT-A
  Carbon structure prototype production, site selection etc
Stave and RU production
  Stave production in progress at CERN
  60 MVTX RUs delivered to CERN
  Power mezzanine and transition boards produced at UT-A

## Slide 5: Funding Profile (FY19+20, 21,22)
sPHENIX MVTX Budget Profile |  |  |  | 
 | FY20 | FY21 | FY22 | Total
3.02.01 Management | $233,668 | $209,596 | $101,338 | $544,602
3.02.02 Electronics | $569,582 |  |  | $569,582
3.02.03 Mechanics and Assembly | $1,370,727 | $307,183 | $113,468 | $1,791,378
3.02.04 Integration and Infrastructure | $368,185 | $399,262 | $15,491 | $782,938
Performance Measure Baseline | $2,542,162 | $916,041 | $230,297 | $3,688,500
Contingency | $762,649 | $274,812 | $69,089 | $1,106,550
Total Project Cost | $3,304,811 | $1,190,853 | $299,386 | $4,795,050
From July MVTX Review:
MVTX funding profile: FY20 -22
Can we move some FY20 ($3.3M) activities to FY21 ($1.2M),
with minimal impact to the project?

## Slide 6: Schedules – Smooth Funding Profile?
Candidates for possible delays, from FY20 to FY21:
Carbon Structure production
PU and CAEN PS
Cooling system
Delay stave test and detector assembly work at LBNL
Recent new quotes for carbon structures: CYSS & EndWheels
Possible cost saving through commercial companies
Carbon structure full production possible in FY20, w/ big saving
Fully aligned with sPHENIX via external milestones
Possible Plan-B for FY20?

## Slide 7: MVTX Readout, Power and Controls Hardware Tested
Power Board
Flex PCB Filtering Capacitors
Samtec Twinax “FireFly”, ~10m
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
CAEN Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX/DAM
one pixel
ALPIDE pixel:
Shaping
Digitization
Zero-suppression
3x buffer
ATLAS Front-End Link eXchange (FELIX):
sPHENIX Data Aggregation Module(DAM)
Slow control
Mike’s talk

## Slide 8: MVTX Global Mechanical System Integration
L = 350.0 cm
MVTX system preliminary design, with two parts:
  Part-1: from MVTX to PP-1b, all power PCB, 40cm
  Part-2: length TBD later, from PP-1b to PP-2
TPC
TPC
R= 209.6cm
INTT
MVTX
PP-1a:
short signal cables
PP-2:
Signal and power cables
PP-1b:
power cables
Service Barrel

## Slide 9: MVTX – Half Detector

## Slide 10: MVTX detector in sPHENIX
TPC volume, length 216 cm
INTT detector, 2 layers
MVTX detector with service cylinder
Support brackets for TPC and INTT

## Slide 11: ITS/IB Commissioning @CERN, 9/2019
ITS/IB : top half barrel
ITS/IB : bottom half barrel
9/2019@CERN

## Slide 12
ITS/IB RU and PU, w cables

## Slide 13
PU & CAEN PS

## Slide 14: Preliminary Mechanical Design Completed
Active discussions on mechanical design and fabrications
  MIT, LANL, LBNL
One-day MVTX/sPHENIX insertion mock up workshop
11/14/2019 @BNL, Russ, Camelia et al
MVTX, INTT, TPC …

## Slide 15: MVTX Insertion – Mockup in WBS2.x

## Slide 16: 2019 Fermilab Test Beam Highligts

## Slide 17: 2019 MVTX Test Setup
From view
Stave housing (four staves)
beam
Stave housing sits on a motion table which can be moved in (x, y) plane perpendicular to the nominal beam direction. It can also be rotated (+40, -40) degrees (see photo on right). Operation was done at counting house.

## Slide 18: Very Successful Test Beam @Fermilab 5/20-25, 6/17-22, 2019
4 staves
2 RUv1.1
1 PU
1 FELIX Server + RCDAQ
sPHENIX GTM
11.4m Custom SamTec Cable
Negative pressured cooling for staves
120GeV p-beam
10kHz (30kHz)
Beam intensity:
30k ~ 120k ppp
RU-2: 1 stave
RU-1: 3 staves
FELIX
GTM
SamTec: 11.4m
(2.6m+8.8m)
5m SamTec
Data & Control
Beam Trigger
4-stave telescope
Timing & Trigger
RCDAQ
Online Monitoring
- 1 fully functioning
9-chip stave;
- 3 staves with a few
broken sensors
A full system with final sensor/readout* hardware:
Multi-Stave + Multi-RU -> FELIX readout demonstrated
sPHENIX GTM integrated
Long readout SamTec cable certified
Cooling system demonstrated
* RUv1.1 identical to the final RUv2 electrically

## Slide 19: Online Analysis: Detector Misalignment & Hit Spatial Resolution
Typically staves offset by,
Horizontally: 20 x 30um = 600 um
Vertically: 5 x 30 um = 150 um
Hit spatial resolution:
peak_sigma_core = 0.55 (pixel size ) =15 um
Chip spatial resolution = 15/sqrt(2) = 11 um
Ref plane
Delta_X/Y

## Slide 20: ALPIDE Sensor Operation Optimization
“ALICE Default Settings”
- “Pile up” integration time ~ 5uS
“Stretched Settings” for sPHENIX trigger study
- Pile up integration time ~ 8uS
64 cells x 106nS = 6.8uS
sPHENIX Trigger Latency ~ 4.7uS
sPHENIX Trigger Latency ~ 6.8uS

## Slide 21: Offline Analysis
From Yasser

## Slide 22
Beam angle: 0
(eta ~0)
Beam angle: 40
(eta ~1)
MVTX 4-Stave Telescope
Offline analysis in progress: all TB data in RCF
https://wiki.bnl.gov/sPHENIX/index.php/MAPS-based_Vertex_Detector_(MVTX)

## Slide 23: Offline Analysis: Cluster size vs Angle
@ 0-degree
Cluster Size ~ 2.4
@ 40-deg
Cluster Size ~ 3.0
To calibrate MC simulations and tracking
Stave geometry, alignment
Clustering

## Slide 24: Confirmed New MVTX Long SamTec Readout Cables 8.8m + 2.6m = 11.4m (10m desired for sPHENIX; ALICE 8m cables)

## Slide 25
Jo is testing the sPHENIX readout cables
Nice job!

## Slide 26: 11.4m SamTec Readout Cable Test @CERN
Double looped readout cables:
  Effective length = 2 x 11.4 m = 22.8m
  Data rate: 1.2Gbps
  One overnight run, ~10hrs
  Error rate < 1.4 x10-14
Production cable: 11m (>10m)

## Slide 27: Carbon Structure Production
Visited WorkShape 9/19/2019
  Walt and Ming, Simon
WorkShape well prepared
  Updated the design files
MIT design work good progress, well ahead of time
  Early Carbon structure review for pre-production, Nov/Dec 2019?
Other companies, CA..
  Received quotes for CYSS, End-Wheels
LBNL in progress

## Slide 28: sPHENIX Stave Production Started!
sPHENIX Production started in 9/2019
  Bi-weekly meeting on Thursday 5PM/CERN (9AM/LANL)
~10 staves/month
  Limited by Wire bonding , 2~3 staves/week
Production period: ~10 months
  Complete by the end of 2020
First stave production tick-off meeting 10/14
Show Antonello’s slides
- “The FPC production is well advanced, we have already the first batch of 24 pieces available.”
- ~200 golden chips available
- “The orders for the power extension cables and for the transport plates have been sent out.“
Discussed the work-package for the wire bonding last Friday 9/20/2019, 2~3 staves/week or ~10/month,

## Slide 29: Final RU Board Tested at UT-A in October
60 sPHENIX RUs produced at CERN
10 RUs produced for LANL R&D
Visited UT-A, 10/14-18, 2019
Jo was available for the full week
Alex T. joined for one day to discuss readout firmware/software plan
10 RUs from LANL tested, all good!
  One bad transceiver, 1 out of 30, <~ 5%
Develop a plan for testing 60 sPHENIX RUs
Gerd, Yasser, Alex

## Slide 30: R&D at LANL
Full ITS/IB QA testbench in operation
Python GUI developed for telescope readout and control operation
CAEN PS being tested

## Slide 31: Summary: Near Term TO-DO List
Carbon structure cost estimate
  LBNL CF update
  Follow up with US vendors for quotes
  Select vendor(s) for pre-productoin
Continue mechanical system design
  CYSS, EW, SB
  Global insertion system design and full mockup
A full “8-stave + 8-RU + 1-FELIX + 1-PU + 1 GTM” chain test
  10 RU available
  1 PU arrived at LANL from LBNL
  8-stave/HICs telescope frame being designed
  RU & FELIX Firmware update in progress
  Slow control software & GUI
  A possible test beam run later this year
RU acceptance QA at UTA
  Initial test in October, 10RUs
Prepare for stave acceptance QA at LBNL
FELIX production and test
  Jointly with sPHENIX TPC, at BNL? Or LANL?
2019 test beam data analysis
sPHENIX Stave production at CERN
We will follow up the progress closely, production, Test & QA
- bi-weekly meetings with CERN
ITS system surface commissioning at CERN
Now --- May 2020
A good opportunity to learn about the
system operation and controls;
Working on a coordinated effort within MVTX/sPHENIX,
Signup page,
https://docs.google.com/spreadsheets/d/1YBAyouW8geJHUPpzRyLlzN4ePW4YzI8glI5xI66N3ww/edit#gid=0

## Slide 32: Summary
Completed essential R&D for readout integration
  Full 9-chip stave readout per RU
  Multi-RU readout per FELIX
  Long readout cables
  sPHENIX GTM
Completed preliminary mechanical design
Improve MC detector response, clustering – in progress
  Calibration data with incident angles, 0, 10,20,30,40,45
Stave and RU production at CERN - in good progress
July MVTX review response submitted to DOE
We are ready for the full production and the physics!

## Slide 34: sPHENIX Timeline

## Slide 35: Very Productive Visit to CERN
Walt Sondheim & Ming Liu
09/16-20, 2019
  sPHENIX 84 Staves production
  sPHENIX 60 RUs test plan
  sPHENIX SamTec cable test
  Carbon structure facility visit
  ITS Commissioning activities

## Slide 36: MVTX Readout and Power Cable Route
sPHENIX MVTX: 7.9+m
  Cable-A: 1.4 m
  Cable-B: 6.5+ m
  Power cable:4.7+ m
Desired ~10m
PWR
RU
PU
Cable-A: 2.65m
ALICE ITS/IB final readout cables: ~8m
Cable-B: 5.3m
BNL has approved “non-halogen free” cables for sPHENIX

## Slide 37: MVTX Project Status & Plan 09/27/2019
MVTX Review response – received feedback on Thursday
  On-going discussions with sPHENIX project office, some edits and revision of PMP doc
  Produce a formal review response report, to ALD and BNL Project Office
  Smooth funding profile for FY20, plan-B
Full mechanical insertion mockup, MVTX/INTT/TPC
  cost & schedule in WBS2.x
Plan to start the MVTX production activities as soon as funds available
  Preparation for Stave and RU acceptance test & QA in US, LBNL and UT-A
  Carbon structure prototype production, site selection etc
Updates from recent CERN Visit, 9/16-20, 2019

## Slide 38
Data run-log in sPHENIX Wiki,
Nice work by Xiaochun et al. @GSU
Jin’s test beam analysis framework
Offline analysis in progress

## Slide 39: MVTX Goals – the 2nd TB, 6/17-22, 2019
Test and confirm optimal MVTX operation parameters for sPHENIX
  Threshold scan, analogy shaping time etc.
  Study chip hit efficiency vs trigger(strobe) latency
    dT = 1 ~ 10 uS
    Impact on occupancy & pileup
Parameters predetermined from laser scan at LANL, in good progress
    Single chip readout with MOSAIC with pulsed laser (~MIP)
    Threshold and noise
    Analogy shaping time
    Strobe delay and length

## Slide 40: Study MAPS Performance with Pulsed Laser @LANL
Inject “MIP” signal, focused laser beam
  850 nm laser, 4ns wide pulse, ~1 MIP
  50kHz trigger
  Find optimal MAPS operating parameters
Pixel hits
Laser system
MOSAIC Testbench

## Slide 41: Laser Scan Data – Pixel Hit Efficiency vs Trigger Delay
One of “Stretched Settings” for sPHENIX trigger
MAX: 64 cells x 106nS = 6.8uS
~ 4.7 us
sPHENIX Trigger
Pixel (Row-Col)
~ 4.7 us
sPHENIX Trigger latency
Pixel (Row-Col)

## Slide 42: MVTX experts help ALICE/ITS – to help us!
Dave’s talk
from Monday
ITS surface commissioning now:
~ May 2020
Great opportunity to learn about ITS/MVTX detectors
Training on technical details
Developing tools
Build up operation experience

## Slide 43: MVTX Schedules and Milestones (3/2019) concerns & challenges
CY-2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
End Wheels
CYSS
Half barrel #1
Half barrel #2
Half barrels
arrive @BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrels
@sPHENIX IR
Ready for beam;
sPHENIX day-1 run
FELIX
production
Barrel Assembly & Testing @LBNL
sPHENIX: CD1/3a PD2/3
MVTX
1st collisions
Installation
Global integration
/interface design
design & procure
interface to
sPHENIX rails
Design & procure
sPHENIX rails
Funding delays –
Stave production delayed at CERN
- Impact on following test & assembly
- preparation work @LBNL, UT-A
Lack of R&D $ for mech. desgin work
- MIT, LBNL, LANL
- “advanced cash” running out MIT, LANL
Running low in schedule contingency …

## Slide 44
Report from April BNL PD2/3 Reviews: Silicon Detectors - MVTX, INTT

## Slide 45
MVTX Risks - all in P6 now
WBS, PMP documents updated
Schedule & Labor profile updated in P6
(Glenn, Irina )
Need project fund NOW to meet the goals!

## Slide 47: ITS Surface Commissioning
A lot of activities
Also require a lot of shifts, and EXPERTS!
Current status:
  Turn on layers, stave-be-stave, checking V,I,T
  Safety interlock important

## Slide 49: R&D Highlights
Very successful TB at Fermilab, 5/13-25, 2019
  Confirmed the long 11.4m SamTec readout cable
  Confirmed the full stave readout
  Confirmed multi-RU readout per FELIX
  Confirmed sPHENIX GTM with FELIX
A 2nd TB, study optimal MAPS operation points
  Parasitic with INTT+TPC, 6/17-21
Preliminary mechanical design developed
  To prototype CYSS and Layer-2 End-Wheel this summer
  France, Italy, CERN, contacted and under discussion
Improve MC detector response, clustering – in progress
  Took calibration data with incident angles, 0, 10,20,30,40,45
TB later at LBNL/LANL – in preparation
  Scan stave material budget with 50MeV p-beam
  8-stave + 8-RU +1-PU + 1-FELIX + 1-GTM + RCDAQ, the full complete readout chain
    Hardware will be available soon

## Slide 50: Monolithic Active Pixel Sensors (MAPS) The Next-Generation, State-of-the-Art Pixel Tracker
Advantages of ALICE PIxel DEtector (ALPIDE) sensor:
Very fine pitch (27μm x 29μm), for superb spatial resolution
High efficiency (>99%) and low noise (<10-6), for excellent tracking
Time resolution, as low as ~5 μs, for less pileup
Ultra-thin/low mass, 50μm (~0.3% X0), for less multiple scatterings
0.5M channels with on-pixel digitization, for zero-suppression and fast readout
Low power dissipation, 40mW/cm2, for minimal service materials
An ideal detector for QGP physics!
50 μm
~28 μm
ALPIDE design
Flexible Printed Circuit(FPC)
9 Chips
Cold plate
A 9-chip MAPS stave, 1.5cm x 27cm
ALPIDE sensor:
1.5cm x 3.0cm, 0.5M pixels

## Slide 51: MVTX Full Readout Chain Demonstrated (3/2018)
4-hit track
4-MAPS telescope
120 GeV proton
beam
Tracking spatial resolution
achieved: <5 um
4-MAPS
telescope
Fermilab Test Beam: Feb-Mar, 2018

## Slide 52
MVTX
MVTX Test Beam, May 2019

## Slide 53: Run Types – Details being documented in MVTX wiki
Horizontal stave scans (many good runs)
Vertical stave scans
Angular stave scans and tilted runs
Electron beam at 5 GeV (one long run)
Extruded aluminum & Lead-block runs
Run1040
Run0877
Run0978
From Xiaochun

## Slide 54
120GeV p-beam
4-stave Telescope
Negative Pressure Cooling System
2 RUs,
PU,
PS
Motion Table
(X,Y,Phi)

## Slide 55: First Collision Signals
sPHENIX GTM

## Slide 56: Staves, RUs, PU etc.
2 RUs
PU

## Slide 57
Telescope
RUs & PU
Cooling System;
negative pressure
@-30%ATMP (-5PSI)
120GeV p-beam
Telescope
120GeV p-beam

## Slide 58
When MAPS parameters off the optimal point, less hits collected

## Slide 59
No hits seen when MAPS parameters far-off the optimal point

## Slide 60: Installation

## Slide 61: The Team @Fermilab
Matt, Hubert, Cameron, Gerd, Zongze,
Xuan, Xiaochun, photo by Ming
Sho, AlexT
Not shown: Sanghoon, Yasser, Martin, Walt,
Abel. Chris …
Data taking shift in the evenings: 7PM – 7AM
Beam: every other Monday –Friday 8:00AM – 8AM

## Slide 62: 3-D event Display: p+Pb collision
Stave-1
Stave-2
Stave-3
Stave-4
Cameron

## Slide 63: Offline Analysis: Cluster size vs Angle Run 877, angle – 30 dgr
Cluster Size = 2.7

## Slide 64: Offline Analysis: Cluster size vs Angle Run , angle = 40
Cluster Size ~ 3.0
More work follows by Yasser, Sanghoon et al
Everyone is welcome to join the effort!
Stave geometry
Stave alignment
Clustering
Tracking
Update MVTX MC response in GEANT