## Slide 1: MVTX Goals – the 2nd TB, 6/17-22, 2019
Test and confirm optimal MVTX operation parameters for sPHENIX
  Threshold scan, analogy shaping time etc
  Study chip hit efficiency vs trigger(strobe) latency
    dT = 1 ~ 10 uS
  Parameters predetermined from laser scan at LANL, in good progress
    Single chip readout with MOSAIC with pulsed laser (~MIP)
    Threshold and noise
    Analogy shaping time
    Strobe delay and length
Schedule & activities:
  Installation done, ORC reviewed 6/10
  Data taking, 6/19-22
  Decommissioning & send back to LANL, 6/22 (Sat)

## Slide 2: ALPIDE Sensor Study
“Default Settings”
“Stretched Settings” for sPHENIX trigger
MAX: 64 cells x 106nS = 6.8uS
More detailed study during the 2nd TB next week: 6/19-22, 2019
- Many MAPS parameters to tune
~ 4.7 us
sPHENIX Trigger

## Slide 3: Study MAPS Performance with Pulsed Laser @LANL
Inject “MIP” signal
  850 nm laser, 4ns wide pulse, ~1 MIP
  50kHz trigger
  Find optimal MAPS operating parameters
Pixel hits
Laser system
MOSAIC Testbench

## Slide 4: Laser Scan Data – Pixel Hit Efficiency vs Trigger Delay
One of “Stretched Settings” for sPHENIX trigger
MAX: 64 cells x 106nS = 6.8uS
~ 4.7 us
sPHENIX Trigger
Pixel (Row-Col)
~ 4.7 us
sPHENIX Trigger
Pixel (Row-Col)

## Slide 5: MVTX Telescope 2nd Test Beam Run @Fermilab 6/19-21, 2019
MVTX telescope
installed
INTT
TPC

## Slide 6: System Setup
4 staves
2 RUv1.1
1 PU
1 FELIX Server + RCDAQ
sPHENIX GTM
11.4m Custom SamTec Cable
Negative pressured cooling
120GeV p-beam
10kHz (30kHz)
Beam intensity:
30k ~ 120k ppp
RU-2: 1 stave
RU-1: 3 staves
FELIX
GTM
SamTec: 11.4m
(2.6m+8.8m)
5m SamTec
Data & Control
Beam Trigger
4-stave telescope
Timing & Trigger
RCDAQ
Online Monitoring
- 1 fully functioning
9-chip stave;
- 3 staves with a few
broken sensors
Multi-Stave + Multi-RU -> FELIX readout demonstrated
sPHENIX GTM integrated
Long readout SamTec cable certified
Cooling system demonstrated

## Slide 9: To Do’s
Ship them back to LANL, and also to Alex T.
Offline analysis
  Alignment
  Efficiency, resolution
  Calibrate laser data