## Slide 1: MVTX Commissioning Document Collections … BNLBox: https://bnlbox.sdcc.bnl.gov/index.php/f/16904602
ITS’ surface commissioning
  Full system
    Readout
    DSC
    Cooling
    Safety interlock
  Online monitoring
  Endurance test
Half-detector test @LBNL, in late 2021
  Single stave QA
Full system test @BNL, in early 2022

## Slide 2: MVTX Half-Detector Test @LBNL
Test staves at each assembly step on the assembly jig, with MOSAIC setup
  Noise/occupancy
  Threshold
  Dead pixels …
Also after each layer assembled
  Repeat tests from #1, MOSAIC
After the half-detector assembled
  Final connectors & cables installed
  Need the full readout for testing?
  MOSAIC requires a special data cable/connector @PP3 (Plan-A)
    Multi-MOSAIC setups, 4?
    Test again @BNL later also
Test setup at LBNL:
MOSAIC system
  Individual Stave QA
  Good for step #1,2, and #3 with a special data cable
Small scale MVTX readout (plan-B)
  FELIX + RU + PU
  use the final readout cables
  Possible multiple stave readout
  QA software and online monitoring
    Zhaozhong? Working on ITS QA,
    Mario?
@PP3: power and signal connectors
Plan-B for half-detector QA:
Connectors @PP3 are easy to manage for the final readout setup
Challenge is the “available time” to setup full readout chain @LBNL
  FELIX, RU, PU, Server
  Software development could be most time consuming
- Test each stave on the assembly jig w/ MOSAIC

## Slide 3: ALICE ITS Surface Commissioning Experience - detector control and status monitor
WinCC – required

## Slide 4: ITS Surface Commissioning: Checked all chips - hit occupancy, errors
WinCC – NOT required

## Slide 5: ITS Surface Commissioning: All Chips - threshold, dead pixels
WinCC – NOT required

## Slide 6: MVTX QA and Online Software
Can we reuse/adapt ITS2 software?
  Detector control (Win-CC required)
  Detector monitoring (No Ein-CC)
WinCC required for online control, page 3
  But not for page 4,5 monitoring outputs
Things special for sPHENIX
  New data format in progress
  FLX fdaq could be used for initial work
  sPHENIX decoder