## Slide 1: Configuration, Calibration and Monitoring
ITS Upgrade – Readout Electronics Review
CERN, 29 January 2019
Gianluca Aglieri Rinella, Magnus Mager, Markus Keil

## Slide 2
OUTLINE
  Configuration
  Calibration

## Slide 3
OUTLINE
  Configuration
  Calibration

## Slide 4
Configuration Tasks
At start of Run:
(Chip power-on procedure: Switching clock off, power on, clock on) -> not each run
Configure RUs
Synchronise all RUs and pixel chips
Write (and dump) all chip registers
Mask pixels / columns
Set / correct PB voltages
During Run:
Periodic refresh of mask
Masking of new noisy pixels / double columns
Reaction to interrupts / change in chip conditions
Automatic recovery of ill-behaving chips?
Reaction on power cycles

## Slide 5
Configuration example 1: Initial configuration of ALPIDE chips
Estimate of the number of interactions needed for the initial configuration of the ALPIDE chips at the start of the run. The initial configuration of the ALPIDE chips can be subdivided into three types of configuration commands: register write commands that can be sent to all ALPIDE chips (BROADCAST), register write commands that have to be sent individually to the chips because of different settings (SINGLE CAST) and the (individual) downloading of the noisy pixel mask

## Slide 6
Configuration – Number of Interactions
Writing of configuration registers (Detailed table in the backup):
  18 registers in broadcast -> 72 CTRL interface write operations / OL stave
  42 single cast commands / chip -> 1960 – 8232 CTRL interface write ops / OL stave (range: writing all/no double column disable)
Masking of pixels
  2 * N(pixels to be masked) CTRL interface write operations e.g. 10 pixels per chip -> 3920 write operations / OL stave
Reading back of configuration registers:
  Reading back all (written) config registers: 11760 CTRL interface read operations / OL stave (NB: no broadcast read)
Treatment of readback values:
  In case of mismatch: warning / write again
  For counter-type registers: store value

## Slide 7
Configuration example 2: Mask refresh
The mask refresh is an example of a configuration procedure during the run. The mask refresh is necessary to correct SEU-induced changes in the pixel masking. These changes happen in both directions (masking and unmasking), but due to sample size the more important effect is the masking of working pixels.

## Slide 8
Configuration – Mask Refreshing
Refreshing of the mask to counter SEUs during data taking.
Assumption: all noisy (masked) pixels in different rows (worst case)
Clear the masks in all rows w/o masked pixels (to unmask pixels masked by SEU)
  35 CTRL interface write operations per chip
Rewrite masks in rows with masked pixels
  8 CTRL interface write operations per noisy pixel
  Two different options:
  Option 1: Complete reconfiguration of mask: (35 + 8* Nnoisy) CTRL interface write operations per chip*
  Option 2: Unmasking only pixels in rows without noisy pixels: 35 write operations per chip** NB: In this option, falsely masked pixels in rows with real noisy pixels stay masked.
*): 41 + 14*Nnoisy for chip 7 **): 41 for chip 7

## Slide 9
Configuration – General Considerations
Fred: local or central (how many processes?)
Configuration database:
  Format to be defined
  Translation from database information to command sequences: where?
  Local copy of database information for connected staves?
In case of on-the-fly masking: (how) is this logged in a conditions DB?

## Slide 10
OUTLINE
  Configuration
  Calibration

## Slide 11
Calibration Tasks
Calibration Tasks:
Calibration of voltage drops / correct set voltage
Threshold Tuning
Threshold Scan
Digital Scan
Black / White events
FIFO scan
Noise occupancy (out of run and possibly during run)
DAC scan (not regularly, but needs to be available)
As baseline, all scans to be run during MD. Frequency to be adjusted according to results, e.g. threshold tuning in interfill? Constant noise occupancy measurement, also during run?

## Slide 12
Readout / DCS architecture
Simplified view of the readout and DCS architecture
Try to understand where/ how the calibration fits in
RU
CRU
readout
ALF
Event Building
FRED
QC
WinCC/ECS

## Slide 13
Threshold Scan
Current Procedure:
Main loop:
nChips configuration commands (set charge)
50 Pulse commands (Triggers generated on-chip)
Readout
Full scan:
5M configuration commands / stave
1.28M triggers (pulse) at max. 2.5 kHz
Total raw data volume O(100 GB / stave), typically 300 – 400 GB
Number of configuration commands can be reduced by using broadcast commands 5M -> 100k
x 50 charge steps
x 512 rows

## Slide 14
Threshold Scan
Basic scan sequence
The main scan sequence can be parametrized as follows
This corresponds to the full scan of an entire row
With appropriate parameter settings the sequence can be used for threshold scan, threshold tuning and digital scan
Note that the trigger is generated internally by the chips, only a PULSE op code is sent
The data returning from the sequence needs to be subdivided into 50 (stop_dac – start_dac) packets, each corresponding to <npulse> consecutive PULSE commands
for value = start_dac to stop_dac:
WRITE_BC(dac_address, value)
for i = 0 to npulse:
SEND_OPCODE(PULSE)
WAIT(n_wait_cycles)

## Slide 15
Calibration Tasks
Standard Calibration Scans:
Write chip registers
Send software triggers / opcode (PULSE)
Read data
Evaluate in QC
Requirements:
Ability to generate software triggers with fixed frequency and in fixed sequence with configuration commands
Events need to be correlated with register writing -> 0 data loss / flow control
RU
CRU
readout
ALF
Event Building
FRED
QC
WinCC/ECS

## Slide 16
Calibration Procedure
Minimal Calibration Procedure (Outside data taking / machine development?):
e.g. Threshold scan: 512 x 50 Config commands, 512 x 2500 Triggers / Pulse commands
With broadcast: ~ 100k Config commands / OL Stave
~ 5M Pulse commands (Counting each control interface separately)
Scan | Rows | Config cmds / row | Triggers / row | Output | Comment
VCASN Tuning | 4 | 50 | 50 x 50 | -> Config DB | 
ITHR Tuning | 4 | 50 | 50 x 50 | -> Config DB | 
Threshold Scan | 512 | 50 | 50 x 50 | -> “Calibration DB” | 
Noise Occupancy | N/A | N/A | N/A | -> Config DB | Determination of noisy pixels to be masked
Noise Occupancy | N/A | N/A | N/A | -> ”Calibration DB” | Measurement of noise occ after masking

## Slide 17
Calibration Procedure
Additional calibration scans:
Scan | Rows | Config cmds / row | Triggers / row | Output | Comment
Digital Scan | 512 | 0 | 50 |  | 
Black / White Frames | N/A | N/A | 50 |  | 
FIFO scan | N/A | N/A | N/A |  | 
DAC scan | N/A | N/A | N/A |  | 

## Slide 18
Calibration Tasks
Calibration Scans 2:
Write chip (RU, power board) registers
Read chip (RU, power board) registers
Evaluate in QC?
Requirements:
Need to define path for evaluation
RU
CRU
readout
ALF
Event Building
FRED
QC
WinCC/ECS
?

## Slide 19
Calibration – General Considerations
Most calibration scans consist of both configuration commands and data taking
  Need for high level commands that execute scan routines
  Analysis in QC framework (e.g. data returned from threshold scans)
  Possible procedure: Issue command to scan 1 row -> Read events -> Pass to QC for analysis
  Needs flow control (can not lose events)
  But: Not all calibration tasks return event data, but can also return register readings, voltage measurements etc. (FIFO scan, DAC scan …)
Output (result) data:
  Calibration -> Configuration: part of the calibration results need to go to the configuration database (threshold settings, noisy pixels)
  Calibration -> Offline: status of the detector (thresholds, dead regions...) is needed for offline. Save each calibration with period of validity. Calibration database?
  Does readout need to know about masked pixels, chips?

## Slide 20
Backup

## Slide 21
OUTLINE
  Configuration
  Calibration
  Monitoring

## Slide 22
Monitoring Tasks
ALPIDE:
ADCs (Temperatures, Voltages)
Status counters
Debug chain?
Readout Units:
Counters
Summary status
Temperatures, Currents, Voltages
Power boards:
Status
Voltages, Currents, Temperatures

## Slide 23
Monitoring – General Considerations
To be defined / checked: latency, rate, real-time reaction?
Monitoring needs to generate interrupts (change in conditions during running)
  SEL / Module power off
  Chip conditions change (some information will also come from QC)
For reaction on module off: need RU module that links PB channels

## Slide 24
Threshold Scan
Basic scan sequence
The main scan sequence can be parametrized as follows
This corresponds to the full scan of an entire row
With appropriate parameter settings the sequence can be used for threshold scan, threshold tuning and digital scan
This could be run from inside the readout unit, but it can also be simply understood as a high-level command that causes the coherent execution of config and pulse commands
Note that the trigger is generated internally by the chips, only a PULSE op code is sent
The data returning from the sequence needs to be subdivided into 50 packets, each corresponding to <npulse> consecutive PULSE commands
for value = start_dac to stop_dac:
WRITE_BC(dac_address, value)
for i = 0 to npulse:
SEND_OPCODE(PULSE)
WAIT(n_wait_cycles)

## Slide 25
Threshold Scan
Full scan would look like this:
for value = start_dac to stop_dac:
WRITE_BC(dac_address, value)
for i = 0 to npulse:
SEND_OPCODE(PULSE)
WAIT(n_wait_cycles)
Configuration: Select Row
Start Configuration

## Slide 26
Threshold Scan
Data flow in the threshold scan; data types and volume for one single row
*: to be done after completion of all rows
Raw Data from Stave
Event Decoding
Histogramming
Fitting
Averaging*
2500 * 196 chip events
Should be treated as 50 packets, each corresponding to 50 consecutive PULSE commands
~1 GB of raw data
~500M pixel hits
To be divided into 50 packets, analogously to raw data
200k 50-bin histograms (8-bit per bin sufficient)
Entries correspond to counts per pixel per trigger packet (0-50)
Error function fit to histograms yields 3 floats per pixel (thresh, noise, c2)
-> 3 x 200k floats
(For speed: differentiate histo and use avg, rms)
4 floats per chip (threshold, noise, both with RMS)
To be stored in DB
+ number (lists?) of dead pixels

## Slide 27
Threshold Scan
Timing Considerations:
HIC Local Bus:
1 event corresponds to 1024 x 7 hits per local bus: 1024 x 7 hits = 14336 Byte (no clustering, neglecting headers) -> 28672 clock cycles (80 MHz) = 358 ms
-> Maximum sustained trigger rate ~2.5 kHz -> 1 s per row (2500 triggers) + time needed for configuration changes
HS Data lines:
Data transfer on local bus corresponds to 320 Mbps; 400 Mbps on the HS data lines with 8b10b encoding correspond to 320Mbps without -> the HS data lines have same bandwidth as local bus
-> Time for triggering and readout ~ 10 minutes (8.5 min + overhead for config changes)

## Slide 28
Threshold Scan
Timing Considerations:
Event size / Flow control
1 event corresponds to 1024 x 196 hits per OL stave: 200k hits = 400 kByte (no clustering, neglecting headers)
Can the readout chain handle events of this size?
For calibration no event should be dropped
  Do we need a handshake for this?
  Can this be ensured via the trigger rate?

## Slide 29
ALPIDE Control Registers
Address | Register | Broadcast | Single cast | Monitor
0x0000 | Command Register | - | - | 
0x0001 | Mode Control Register | ✓ |  | 
0x0002 | Region Disable 0-15 |  | ✓ | 
0x0003 | Region Disable 16-31 |  | ✓ | 
0x0004 | FROMU Configuration Register 1 | ✓ | ? (MEB Masking?) | 
0x0005 | FROMU Configuration Register 2 | ✓ | - | 
0x0006 | FROMU Configuration Register 3 | ✓ (calib only) | - | 
0x0007 | FROMU Pulsing Register 1 | ✓(calib only) | - | 
0x0008 | FROMU Pulsing Register 2 | ✓(calib only) | - | 
0x0009 | FROMU Status Register 1 | - | - | ✓
0x000A | FROMU Status Register 2 | - | - | ✓
0x000B | FROMU Status Register 3 | - | - | ✓
0x000C | FROMU Status Register 4 | - | - | ✓
0x000D | FROMU Status Register 5 | - | - | ✓

## Slide 30
ALPIDE Control Registers
Address | Register | Broadcast | Single cast | Monitor
0x000E | DCLK / MCLK DAC Settings | ? | ✓ | 
0x000F | CMU Buffer DAC Settings | ? | ✓ | 
0x0010 | CMU / DMU Config Register | ? | ✓ | 
0x0011 | CMU / DMU Status Register | - | - | ✓
0x0012 | DMU Data FIFO [15:0] | - | - | 
0x0013 | DMU Data FIFO [23:16] | - | - | 
0x0014 | DTU Config Register | ? (x2) | ✓ (x2) | 
0x0015 | DTU DAC Register | ? | ✓ | 
0x0016 | DTU PLL Lock Register 1 | - | - | ✓
0x0017 | DTU PLL Lock Register 2 | ✓ | - | 
0x0018 | DTU Test Register 1 | - | - | 
0x0019 | DTU Test Register 2 | - | - | 
0x001A | DTU Test Register 3 | - | - | 
0x001B | BUSY min width | ✓ | - | 

## Slide 31
ALPIDE Control Registers
Address | Register | Broadcast | Single cast | Monitor
0x0300 – 0xFB00 | Double Column Disable Register | - | ✓ (x 32) | 
0x0340 – 0xFB40 | Region Status Register | - | - | ✓ (x 32)
0x0600 | Monitor and Override Register | ✓ | - | 
0x0601 | VRESETP | - | - | 
0x0602 | VRESETD | ✓ | - | 
0x0603 | VCASP | ✓ | - | 
0x0604 | VCASN | - | ✓ | 
0x0605 | VPULSEH | ✓ |  | 
0x0606 | VPULSEL | ✓ | - | 
0x0607 | VCASN2 | ✓ | - | 
0x0608 | VCLIP | ✓ | - | 
0x0609 | VTEMP | - | - | 
0x060A | IAUX2 | - | - | 
0x060B | IRESET | ✓ | - | 

## Slide 32
ALPIDE Control Registers
Address | Register | Broadcast | Single cast | Monitor
0x060C | IDB | ✓ |  | 
0X060D | IBIAS | ✓ |  | 
0x060E | ITHR |  | ✓ | 
0x060F | Buffer Bypass Register | ✓ | - | 
0x0610 | ADC Control Register | ✓ | - | 
0x0611 | ADC DAC Input Value | ✓ | - | 
0x0612 | ADC Calibration Value Register | - | - | ✓
0x0613 – 0x0627 | ADC Value Registers | - | - | ✓
0x0700 | SEU Error Counter | - | - | ✓
0x0701 | Test Control Register | - | - | 
0x0702 – 0x0707 | Debug Streams | - | - | (✓)

## Slide 33
Mask Refreshing
Clear masks in rows w/o noisy pixels
Write pixel config reg (clear data, select mask) - 1 write operation
Select all columns - 1 write operation
Select all rows w/o noisy pixels - 32 write operations
Clear all selected bits - 1 write operation
Reconfigure rows with masked pixels (assume each pixel in different row): loop over rows and
Set col bit of noisy pixels - 1 write operation
Write pixel config reg (set data, select mask) - 1 write operation
Set row select bit - 1 write operation
Clear row select bit - 1 write operation
Toggle data to select complementary columns - 1 write operation
Clear data bit - 1 write operation
Set row select bit - 1 write operation
Clear all selected bits - 1 write operation
Repeat for each row with noisy pixels