## Slide 2
SY4527
Eur 5900
Basic 600W model
A2518
Eur 2050
8V/10A 8-ch individual floating
A1676A
Eur 1470
Branch controller
Up to 6 crates
EASY3000
Eur 2850
Crate for hostile area
A3009B
Eur 7750
8V/9A/45W 12-ch floating
3.3V output
that powers 1.8V digital and analog rails
A3486
Eur 13000
220/400Vac->48Vdc
2ch/2kW / 1ch/4kW

## Slide 3
IB staves: 48 staves
Need 24 power boards & 48 readout units
  1 power board (2 units) powers 2 IB staves.
  1 readout unit read 1 IB stave
  48 channels from CAEN that provides 3.3V for power boards
  (How much for readout boards?)
  19” wide X 7U VME crate has 21 slots.
    4 slots per 2-staves (2-slot for power boards, 2-slot for 2 readout units).
    1 crate for 10 staves.
    5 crates needed.
3.3V channels
  1.5A per CAEN 3.3V channel into power boards.
  48 channels total.
-5V channel:
  1 channel per crate (5 crates total).
  1A per channel spec.