## Slide 1: System scrubbing & re-programming
Johan Alme
johan.alme@uib.no
ITS RU Production Readyness Review 13. April 2018

## Slide 2: FPGA Programming Overview
Standard operation (with beam while running)
  Microsemi ProAsic3
    Flash-based -> always programmed
  Xilinx Kintex Ultrascale
    Programmed at power-on or via command to PA3
    Programmed from Flash memory
Remote updating (without beam)
  Flash memory – Xilinx image
    SEUs in flash memory  Updates during technical stops
    Update via downlinks
    Update through I2C
  Proasic3
    Only needed for feature/bug fix updates
    Updated via JTAG
I2C
FLASH PROM
FLASH FPGA PROASIC3
REGULATORS
CLOCK
SUPPLY SENSE TEMP SENSE
JTAG
POWER MEZZANINE
TRANSITION BOARD
SCA
GBTx0
GBTx1
GBTx2
VTRX
VTTX
VTRX
LTU/ CTP
CRU / O2 FLP
POWER UNIT
POWER UNIT
DETECTOR SENSORS
SRAM FPGA XILINX ULTRASCALE
USB3
FX3
I2C

## Slide 3: Scrubbing
Scrubbing is an error correction technique that uses a background task to periodically inspect/correct errors in a data memory.
  Data memory = Config mem of Xilinx Ultrascale
  Errors caused by single event upsets
Relevant scrubbing techniques for the RU:
  Xilinx Soft Error Mitigation Core (sem IP) 1
    Supported by Xilinx
    Detection and correction
    Fast
    Black box design
    Sem IP core only partially mitigated
    Scan starts from zero upon an upset
  External Scrubbing network
    Proven solution (ALICE TPC RCU1) 2
    Full control of design
    No support by Xilinx
    Substantially slower than sem IP
    Mitigation of Flash and aux FPGA is needed
Aux FPGA
1 https://www.xilinx.com/support/documentation/ip_documentation/sem_ultra/v3_1/pg187-ultrascale-sem.pdf
2 https://cds.cern.ch/record/1141616, chapter 4

## Slide 4: RU Aux FPGA Versions
Summer 2017: First test version
  Includes working UART, flash and selectmap interface w/wishbone bus structure
  All other interfaces can be electrically verified
Oct 2017 – Feb. 2018: Irradiation test versions
  CHARM test:
    Only init programming supported
    I2C interface not ready
  Prague tests (December/January):
    I2C interface ready
  Oxford test (March):
    Scrubbing and CRC check included
    File upload to flash via Xilinx
June 2018: Final firmware, 1st version - Improved version of Oxford test firmware
  Slimmer wishbone bus
  Faster I2C access, faster scrubbing/init programming
  ECC encoded flash content + ECC decoding
  TMR of components involved in Xilinx programming

## Slide 5: June 2018 version of RU Aux FPGA Firmware
Wishbone bus:
  7b address/8b data
  Better fit with I2C protocol – improves speed for reading/writing
Asynchronous Reset
  Better fit for FPGA technology
Buffer memory replaced by FIFOs
  Enables pipelining
  Small FIFOs for file uploading/selectmap readback
  2 x 128 Bytes ping-pong memory for flash reading incl. ECC check
  Improves speed of programming/scrubbing
Local TMR1 on components involved in programming actions
UART possibly removed due to resource limitations
  By use of generic in code
Improvements:
1 https://ntrs.nasa.gov/archive/nasa/casi.ntrs.nasa.gov/20170004736.pdf, slide 54

## Slide 6: Logical structure of Samsung Flash
Figure shows logical structure of Flash
Upon configuration/scrubbing the parameters page is read first
  This gives location of file and filesize in flash
  The init config file / scrubbing file can be located anywhere in the flash
General robustness measures:
  Recognizable bytes added to know the parameter page is programmed
    i.e. AA995566 first
  Add ECC encoding of parameters page
  Make a double/triple copy of the parameter page on different blocks
  Use the 128 bytes of extra space per page for ECC code – calculate ECC on the fly when reading the page1
    All pages comes with a spare section
  Add double copy of all content2
1 TN-29-08: Hamming Codes for NAND Flash Memory Devices (Micron)
TN-29-63: Error Correction Code (ECC) in SLC NAND Introduction
2 This will be implemented dependent on FPGA resources and cross section estimates on logic in PA3

## Slide 7: Flash Read Controller
Flash has 128 Bytes ECC encoded packets
  Aux FPGA buffers 128 bytes of data
  calculates ECC + syndrome  corrects single bit errors in the memory
  ECC corrected buffer is read by config controller while flash interface fills second buffer
Single bit errors are corrected and reported  Non-critical error
Double bit errors are reported and operation is halted  critical error
  If double copy is implemented on Flash, the module must also include logic for the switch-over to the second copy.
  Critical error only if there is a double bit error in the same 128 B packet in both copies of the bitstream.

## Slide 8: Key figures
Feature | Beamtest version | Final version (40 MHz system clock)
Programming file1 uploading via UART | ~8 mins | ~8 mins (if supported)
Programming file1 uploading via I2C (using CRU) | ~60 mins | ~16 mins
Programming file1 uploading via Xilinx FIFO (using CRU) | ~30 sec | ~30 sec
FLASH: 4K page read time | ~525 us | ~325 us
Initial Programming of Xilinx from Flash | ~5 sec | ~3 sec ~1.7 sec2
Blind Scrubbing of Xilinx from Flash | ~3.8 sec | ~2.4 sec ~1.3 sec2
I2C Single Register Read | ~183 us | ~39 us
I2C Single Register Write | ~133 us | ~39 us
Resource utilization | 7268/13824 COREs3 8/24 RAMs | 4400/13824 COREs4 9/24 RAMs
1 Original Xilinx bitfile 24MB
2 Estimate with 80 MHz sys clock – not realistic with current device & TMR included
3 Only I2C master includes TMR
4 Only I2C master includes TMR – ECC decode/correction not included
 TMR on all modules should be possible (but challenging) with current device

## Slide 9: Conclusion
The Aux FPGA design has been proven to work within the specs of the experiment.
The Aus FPGA design behaves reliable in beam1
Ongoing work is to:
  Improve radiation tolerance
  Improve efficiency of design
Potential future functionality:
  Frame by frame readback and verification
    With the current architecture this is easy to implement
    Dependent on the resources on the PA3
TODO: Software package
  Software is needed to generate files for the flash contents and for uploading the files.
  Flash contents – ECC encoded:
    Parameter pages
    Initial configuration files
    Scrubbing files
  Scrubbing files can only be generated by reading back the allready programmed device  can be done by JCM tool1.
  Adapt JCM SW using RU instead of dedicated HW
    Desirable for generating scrubbing files
1 For Oxford beamtest results: https://indico.cern.ch/event/698929/contributions/2928323/attachments/1625746/2588858/oxford_beamtest.pdf
2 JTAG configuration manager: http://ieeexplore.ieee.org/document/7577336/

## Slide 10: BACKUP SLIDES

## Slide 11: Code & Documentation
Code: https://gitlab.cern.ch/alice-its-wp10-firmware/RUv1_auxFPGA
Documentation: https://twiki.cern.ch/twiki/bin/view/ALICE/AuxFPGA

## Slide 12: Oxford version of RU aux FPGA Firmware
Internal clock: 40 MHz
Reset: External power on reset chip guarantees known power up state
  Same POR chip as for TPC RCU2
  Reset is also available as command via I2C.
  Synchronous reset
Wishbone interface ensures that all operations are remotely accessible
  Read/write selectMap
  Read/write flash
  status information

## Slide 13: Mass Production Testplan (simplified)
I2C interface:
Execute read ID from selectMAP
Execute read ID from Flash
Set pattern on SCA GPIOs to verify connectivity
Set/Read other IOs via Wishbone bus to verify connectivity
UART/I2C interface:
Read out spare section of first page in each block in flash
  VERY IMPORTANT! This will provide information on Valid Blocks on Flash!
Upload config file to Flash. Read back and verify.
  Use Fast interface via Xilinx (XUC programmed with JTAG)
Configure Xilinx from Flash. Verify.
Scrub Xilinx from Flash. Verify.
Erase Flash. Verify.

## Slide 14: Flash Memory SEU cross section
From the Prague irradiation campaign, the SEU cross section in the Flash Memory is estimated1 to:
  (0  1) 10-16 cm2/bit
  (1  0) 10-21 cm2/bit
A typical scrubbing file has a 1:20 ratio of Ones vs Zeros
A typical programming file has a 1:50 ratio (given no default values written to BRAM)
Three measures for correcting of errors in the programming file stored in flash memory will be implemented in the PA3 firmware (next slide).
1 Study done by Matteo Lupi (matteo.lupi@cern.ch)

## Slide 15: Probability of fatal error in Flash
Combined cross-section:
  CS1:20 = 4.76E-18 cm2/bit
Probability of double bitflip in a random ECC block:
  P(random) ≈ (CS1:20*ECC_size)2 *ECC_blocks = 6.3E-22
Probability of double bitflip in a specific ECC block:
  P(specific) ≈ P(random)/ECC_blocks = 2.5E-29
Combined Probability, same ECC block hit in both flash chips:
  P(random ∩ specific) = P(random) * P(specific) = 1.6E-50
 1E-40 double bitflips in same ECC block in both flash chips during 10h spill for all boards
Important numbers:
ECC block size: 1048 bits
# ECC blocks on Flash: 2.52E+07
Est. flux Run 3: 1 kHz/cm2
Est. fluence 10h spill: 3.6E+07 cm-2
Cross-section (10): 1.0E-21 cm2/bit
Cross-section (01): 1.0E-16 cm2/bit
Ratio 1:0 scrub-file: 1:20

## Slide 16: Flash cell robustness measures for the bitstream
Three measures are implemented or planned:
  Storing the programming file inverted
    Utilizing the 1:20 ratio of 1s vs 0s
  Adding Hamming encoding of the bitstream
    128 bytes ECC encoded blocks
    Single error correction, double error detection
  Store two copies of all the files in the Flash1
    The Flash itself has two identical memories in the package
    Content can be mirrored without any penalty regarding file uploading
This gives:
  P(fatal error) == P(double bitflip in the same ECC encoded block in both copies of the file)
    Fatal error = init config/scrubbing not operative
    Cross Section fatal error = 1.6e-50
1 This will be implemented dependent on FPGA resources and cross section estimates on logic in PA3

## Slide 17: Project work flow
All source and documentation files is checked into wp10-GIT
  WP10 GIT structure guideline is followed
Project is fully script based. Microsemi toolchain needed to compile/synthesise/P&R
BITVIS UVVM1 simulation environment is used for verification.
  All modules will have individual testbenches
1 http://www.bitvis.no

## Slide 18: Configuration/reconfiguration
All modules are controlled by an adressable bus interface.
selectMAP and Flash interface are command based
  This means that the interfaces ONLY does protocol implementation  easy to adapt design for future changes.
  Note: Both selectMAP and Flash supports streaming on reading/writing
Note: The address structure are not finished
Operational modes define the ongoing configuration tasks
  The configuration controller then takes control over the flash interface and the selectmap interface.
  Accessing these modules from the bus will then only give you status – and a possibility to abort the ongoing operation.
  Other modules are still accessible
Selectmap commands:
  Read (8 bit)
  Write (8 bit)
  Init
  Startup
  Abort
Flash commands:
  Read (8 bit)
  Write (8 bit)
  Erase all
  Block Erase
Operational modes:
  Initial configuration
  Scrubbing from flash
  (Frame readback and reconfig)

## Slide 19: Selectmap communication
The command based interface enables debugging by using simple scripts over UART (or I2C)
  Example: read STAT register 
  The only difference from the TPC RCU Xilinx Virtex2pro is the inclusion of the bus width (8bit = 0xBB THEN 0x11).
Commands to do initial configuration:
  INIT
  WRITE x numOfBytes
  STARTUP
For scrubbing:
  WRITE x numOfBytes
  STARTUP
https://www.xilinx.com/support/documentation/user_guides/ug570-ultrascale-configuration.pdf
Assumes all other info is stored on flash/remotely