## Slide 1: Firmware Overview
J. Schambach

## Slide 2: Readout Unit Connectivity

## Slide 3: Readout Unit Firmware Purpose
Power Unit (PU)
Data @ 3.2 Gb/s
Trigger
GBTx
GBTx
GBTx
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
SRAM
FPGA
FLASH
FPGA
Programmable Logic
FLASH
Memory
SCA
Optical transceiver
VTRx
Optical transceiver
VTRx
Optical transceiver
VTTx
Data @ 3.2 Gb/s
Data @ 3.2 Gb/s
Control
FLASH
Memory
Readout Unit
Clock (40MHz)
Control (80 Mb/s)
Data: 9 x 960 Mb/s
or 16/28 x 320 Mb/s
Main Tasks of the Readout Unit:
Receive triggers (heartbeat & physics) from CTP & decode
Receive “control” information from CRU
Deliver triggers to stave sensors
Control, configure and monitor stave sensors
Receive data from stave; decode & compress
Deliver monitoring information to CRU (forwarded to DCS)
Deliver CRU framed data packets to CRU
Determine and handle busy information
Monitor and control Power Board
Handle radiation upsets in programmable logic (& sensors)
GBT Links
Copper Links
From/To ITS
From/To CRU
Power Board

## Slide 4: Flash FPGA

## Slide 5: Flash FPGA: Configuration and Scrubbing
Details in
“System scrubbing & re-programming” talk

## Slide 6: ProAsic3 Firmware
Components w/ TMR

## Slide 7: SRAM FPGA

## Slide 8: Readout Firmware Overview

## Slide 9: Firmware modules - Status
Control Interface (Wishbone bus)
  Implemented and tested (lab, test beams)
  Sending and receiving control words over USB and GBT
Power Board Interface
  Implemented and tested for all 4 I2C busses
  Controls sensor power, read status, currents, and voltages
Alpide Control
  Implemented and tested for all 5 FireFly connectors
  Handles configuration and triggers to sensors
Data Readout and Packaging
  2 Flavors: Inner Barrel (MGT transceivers), Outer Barrel (GPIO fabric logic)
  Implemented and tested for MGT (lab, test beams)
  Outer Barrel path under development (only receiving logic different)
  Receives data from sensors, deserialization, idle removal
  Add CRU protocol and Trigger info
  Send data packets over GBT
  Some features still missing (OB sensor data packaging, sparsification)
GBTx Communication
  Implemented and tested (lab, test beams)
  Use only single GBT link for now for trigger, control, and data
  Full access to Wishbone via CRU protocol
Trigger Handler
  Proof of principle implemented and tested
  Needs additional work (pipelining, additional triggers, …)
Radiation Monitor
  Implemented and tested
  SEU observation
System Monitor
  Implemented and tested
  Read voltages, temperatures
USB interface to wishbone
  Implemented and tested
  Used for tabletop tests, lab setups
FIFO interface to PA3
  Implemented and tested
  Used for fast firmware update of flash
  Can be used from GBT (via CRU control protocol)
Datapath Monitor
  Implemented to monitor protocol, gbtx
Error/Busy Handling
  Still missing

## Slide 10: Radiation Protection: Triple Modular Redundancy
TMR completed
To be TMR’ed
No TMR planned
TMR Status

## Slide 11: Alpide Data Path Details

## Slide 12: Data Flow

## Slide 13: Inner Barrel Data Format
Legend:
C<n>W<m>: Cable <n>, Word <m>
Cx_Id: FIFO identifier (1-9, 5bit)
SOP: CRU Start-of-Packet
EOP: CRU End-of-Packet
BC: Bunch Crossing ID (12bit)
Data out of the Alpide Readout firmware module in the inner barrel mode arrives with a rate of 8 bits every 120MHz clock period. Nine 8-bit data words from one cable are combined with an ID for the FIFO they originate from into an 80 bit GBT word as shown here. A round-robin MUX collects data from each of the nine cables. Finally, the data is framed with the appropriate CRU protocol words, and trigger and status information is added to complete a CRU data packet.
Header

## Slide 14: Outer Barrel Data Format
Legend:
C<n>W<m>: Cable <n>, Word <m>
Cx_Id: FIFO identifier (1-28, 5bit)
SOP: CRU Start-of-Packet
EOP: CRU End-of-Packet
BC: Bunch Crossing ID (12bit)
For the outer barrel mode, the same principle on the previous slide applies, but with modified rates and number of fragments combined into a GBT word.
Header

## Slide 15: Continuous Readout
HB = Heart Beat Trigger
HBF = Heart Beat Frame
Strobe<x> = Trigger strobe to sensor with trigger time = BC+Orbit at time<x>
BCID<x> = BC ID (part of SDH) (with BC+Orbit) at time<x> after HB
Data = Sensor Pixel addresses
SOP = “Start Of Packet” (CRU protocol)
EOP = “End Of Packet” (CRU protocol)
“Continuous” readout in ITS is accomplished by using “long” (10’s of µ-seconds) strobe lengths (firmware triggered) with short (10’s of nano-seconds) inter-strobe periods to initiate readout. ITS RU firmware therefore divides a “Heartbeat Frame” into several “Strobe” frames with fixed strobe lengths, synchronized to the received heartbeat triggers.
Heart Beat Triggers come every 89.4 µs, so trigger strobes (“frames”) in this example would be approximately 89.4 / 4 = 22.3 µs long and each Heart Beat Frame (HBF) would thus contain 4 packets from the RU. This parameter is programmable and could be adjusted, e.g. to 89.4/8 to have 8 “sub-frames” in each HBF
Data will appear from the sensor some tens of ns after the end of the strobe signal, and some 40MHz clock cycles later on the GBT links. Data contained in each packet corresponds to all physical signals (“events”) between times tx and tx+1. The packets might also contain the busy status for individual sensors of an RU, which could then be used to determine the need for throttling at the CTP.
Although data packets are shown here contiguous, it is possible that “DATA” GBT words are interspersed with “IDLE” or “SWT” (for DCS data) during data transmission to the CRU. Since there is the possibility of SEUs in the RUs’ FPGAs, there will be a “timeout provision” in the CRU protocol to determine if a packet is corrupted/incomplete/missing.

## Slide 16: CRU Data
FID
3
Time
RU 1
RU 2
RU 8
…
…
8 Readout Units
(up to 3 fibers each)
FID
0
FID
1
FID
2
FID
3
FID
0
FID
0
FID
1
FID
2
FID
0
FID
0
FID
1
FID
2
FID
0
HB1
HB2
FID
3
Need to be combined into 1 Heart Beat Frame (HBF) in FLP
DMA to FLP memory

## Slide 17: Data Hierarchy
Cable 1
Cable 9
RU
…
Cable 1
Cable 16
RU
…
Cable 1
Cable 28
RU
…
RU
....
CRU/FLP
CRU/FLP
.......
EPN
......
....
IB
MB
OB
9
16
28
8
....
8
192
24 (12 FLP?)
8

## Slide 18: Data Format: GBT to CRU to FLP
GBT RDH
CRU memory
FLP memory
79…………………….……………….……….…………0
127……………………………………………………………………...…63………..……………………………………………………………...…0
0x00
0x04
0x08
0x0C
0x10

## Slide 19: Utilization Report
Site Type | Used | Available | Util %
CLB | 6038 | 41460 | 14.56
CLBL | 3062 |  | 
CLBM | 2976 |  | 
LUT as Logic | 23100 | 331680 | 6.96
using O5 output only | 466 |  | 
using O6 output only | 19961 |  | 
using O5 and O6 | 2673 |  | 
LUT as Memory | 0 | 146880 | 0.00
LUT Flip Flop Pairs | 6970 | 331680 | 2.10
fully used LUT-FF pairs | 855 |  | 
LUT-FF pairs with one unused LUT output | 5736 |  | 
LUT-FF pairs with one unissued Flip Flop | 5160 |  | 
Unique Control Sets | 931 |  | 
CLB Registers | 26374 | 663360 | 3.98
CARRY8 | 757 | 41460 | 1.83
F7 Muxes | 702 | 165840 | 0.42
F8 Muxes | 287 | 82920 | 0.35
F9 Muxes | 0 | 41460 | 0.00
Site Type | Used | Available | Util %
Block RAM Tile | 146 | 1080 | 13.52
RAM36/FIFO | 134 | 1080 | 12.41
RAMB36E2 only | 134 |  | 
RAM18 | 24 | 2160 | 1.11
RAMB18E2 only | 24 |  | 
CLB Logic
BLOCKRAM

## Slide 20: Control Interfaces

## Slide 21: Detector Control System (DCS) Paths
CANBUS
FLASH PROM
FLASH FPGA PROASIC3
SUPPLY SENSE TEMP SENSE
SCA
GBTx0
GBTx1
GBTx2
VTRX
VTTX
VTRX
LTU/ CTP
CRU / O2 FLP
POWER UNIT
POWER UNIT
DETECTOR SENSORS
SRAM FPGA XILINX ULTRASCALE
USB3
FX3
I2C
I2C
I2C
I2C
Readout Unit
DCTRL

## Slide 22: Control Interface
Wishbone Bus
Wishbone Master
Wishbone Slave 1
Wishbone Slave 2
Wishbone Slave n
Control
Interface
FPGA
.
.
16 bit Data
15 bit Address
1 bit R/W
32 bit
FiFo
FiFo
32 bit
Optional
Wishbone Bus Structure

## Slide 23: Controls Protocol
Based originally on 32bit USB words sent over FX3
DCS -> FPGA
  Write Request:
  Read Request:
FPGA -> DCS
  Write Response:
    None (no acknowledgement, but errors are kept in a wishbone slave register – associated with the wishbone master - for possible later interrogation)
  Read Response:
  Errors are kept in a wishbone slave register – associated with the wishbone master - for possible later interrogation
W/R=1 | Module Addr[6:0] | Reg Addr[7:0] | Data[15:0]
W/R=0 | Module Addr[6:0] | Reg Addr[7:0] | Don’t Care[15:0]
Error | Module Addr[6:0] | Reg Addr[7:0] | Data Response[15:0]
31 24 16 0
31 24 16 0
31 24 16 0

## Slide 24: GBT Controls Transactions
GBT – SWT: Single Word Transaction
No problem on downstream path:
Only kind of communication
Upstream path: SWT interspersed between data packets
SWT
0
Transaction Parameters
79
0
75
DV

## Slide 25: GBT Control Protocol
Use CRU protocol “Single Word Transactions” (SWT) as a means for both downlink and uplink of control information
Every USB transaction described in previous slides maps exactly to one SWT GBT word
For radiation testing purposes, we implemented SWT words containing duplicated USB packets
Downstream and Upstream GBT words have the same format:
  Downstream GBT words contain request packets to the wishbone bus
  Upstream GBT words contain response packets from the wishbone bus
A Python module for interacting with the CRU “SWT handler” using the above protocol was developed based on the O2 Python module “libReadoutCard”
The User Interface of this “SWT” module are the following functions:
  clrFifos(): Clear the SWT FIFOs in the firmware
  write(mod, addr, data): Write “data” to module “mod” at register address “addr”
  read(mod, addr): Read register “addr” in module “mod”
0 | SWT (0x3) | Don’t Care (12b) | Duplicated USB Word (32 bit) | USB Control Word (32 bit)
DV 76 64 32 0
80 bit GBT word + Data Valid (DV)

## Slide 26: CANbus Controls Transactions
ID[10] | ID[9] | ID[8] | ID[7] | ID[6] | ID[5] | ID[4] | ID[3] | ID[2] | ID[1] | ID[0]
N[6] | N[5] | N[4] | N[3] | N[2] | N[1] | N[0] | C[3] | C[2] | C[1] | C[0]
MsgID[10:4] = N[6:0] = NodeID
MsgID[3:0] = C[3:0] = Command
Emulate a “network topology”: Divide 11-bit CAN ID field into a “Node ID” and a “Command” field:
Allows for up to 128 nodes per CAN network
CANbus Opencores controller for raw packets
High-Level-Protocol on top of controller to define a node based communication interface and to define simple READ and WRITE transactions & responses with appropriate payload
Interface to wishbone bus same as GBT:
  Input & Output FIFOs
  Wishbone Master for transactions on bus
WB slave interface in controller to configure protocol parameters like baud-rate and filters
Electrical pass-through

## Slide 27: CANbus Test Setup
Anagate “CAN Quattro” CAN controller
Opencores “Project CAN” protocol controller
Wishbone interface to PA3 firmware for configuration
Configured for 1Mbps baud rate
“CAN Monitor” from Anagate to generate and receive standard and extended ID CAN packets with up to 8 bytes payload

## Slide 28: Alpide Control Implementation
Firmware Logic
Physical Implementation

## Slide 29: Power Board – Interface to Readout Unit
Two 8-channel Power Units are combined into one board stack called a “Power Board”.
Each Power Unit provides power for up to 8 modules (16 per Power Board)
In layers 5 & 6 each Power Board provides power for one full stave (one power unit per half-stave)
In all other layers, each Power Unit provides power for one stave, so there are 2 staves per Power Board
Each Power Unit is interfaced to a Readout Unit via 2 (differential) I2C buses, with multiple devices per bus
Each Power Board consisting of 2 Power Units therefore has a total of four I2C buses
In layers 5 & 6, each Power Board interfaces to one Readout Unit (a total of four I2C buses per Readout Unit)
In all other layers, each Power Unit interfaces to one Readout Unit (a total of two I2C buses per Readout Unit)
Control via two I2C wishbone slaves (one per Power Unit) allows setting and monitoring voltages, currents, temperature thresholds and power status
Middle Layer Configuration
Outer Layer Configuration

## Slide 30: Power Board – Readout Unit Pairing
Outer Layers
Middle Layers
Inner Layers
I2C
I2C
I2C
I2C
I2C
I2C
I2C
I2C
I2C
I2C
I2C
I2C

## Slide 31: Trigger Interface – Optical Splitting
Low radiation area
Mini-frame
ITS
Passive optical splitting 1:16 (1:32 also possible)
16×
12×
Sensor
Readout Unit
Up to 28×
Each optical line is split into 16/32 lines by a passive optical splitter, which can withstand the foreseen TID level (10 kRad) and does not suffer from SEU.
As each LTU has 12 optical drivers, a 1:16 splitting ratio (at least) will be ok
optical
optical
copper
The CTP directly drives a set of Local Trigger Units (LTUs), each responsible for delivering the trigger to a specific detector.
ITS will have its own LTU
ITS LTU will drive 12 (or 6) Single Mode, 1030nm SFP+ Modules.

## Slide 32: Optical Fiber Power Loss Tests
Splitter | Power loss Ideal splitter [dB]1 | Power loss Measured [dB] | Margin [dB]2
1:2 splitter | 3 | 3.686 | 16.689
1:4 splitter | 6 | 6.838 | 13.539
1:8 splitter | 9 | 10.535 | 9.841
1:16 splitter | 12 | 14.333 | 6.044
1:32 splitter | 15 | 16.359 | 4.983
As a general rule, the link loss margin should be greater than approximately 3 dB to allow for link degradation over time3.
The dynamic range for the chosen Transmitter & Receiver is about 20 dB
  The LTU has been verified to support the powerful Avago AFCT-57D3ANMZ transmitter.
The power tests shows that all topologies have a margin > 3 dB
  This is in line with the specifications given by the manufacturer of the splitter
1 The numbers for ideal power loss is taken from
http://www.thefoa.org/tech/ref/testing/test/couplers.html
2 Margin is given based on:
- the Avago AFCT-57D3ANMZ transmitter (optical power output +5 dBm)
- the VTRx sensitivity (-15.376 dBm)
3 Fiber optics association: http://www.thefoa.org/tech/lossbudg.htm

## Slide 33: Data Streaming

## Slide 34: Schematic Setup for Data Streaming Tests
Kintex
Ultrascale
DC/DCs
GBTx
SCA
PA3
Flash
PROM
Inner Barrel Module
Power
Board
CRU
Remote Control
Power Supply
PC
ADC
GPIO or I2C
Select
Map
I2C
9 DATA
DCTRL
DCLK
10
10
GBT
RUv1
Power
Power
UART/USB-2
Power
CLK

## Slide 35: Data Streaming Test Setup
FLP
Altera Arria-X DevKit
RUv1
Power Board Prototype
“CRU” Emulator
Inner Barrel Module
CRU

## Slide 36: CRU Interface Tests
Three different Interfaces from CRU to Readout Unit tested: SCA, SWT, Data
SCA interface provided by both C++ and Python library via register write/read.
Tested with Python interface library to read voltages, currents and temperatures from RU SCA
SWT interface provided by both C++ and Python library via registers that access SWT FIFOs in CRU firmware
Tested with Python interface library to read and write registers from various wishbone slaves
Data Path Configuration interface via C++ library to interface with configuration registers
Setup Data Streaming into one of 3 modes:
  Packet Mode
  Raw Link streaming (continuous mode)
  Packet Emulator (for testing)
Trigger Interface Path with configurable source:
  CTP Emulator (firmware from CTP group)
  TTC PON (from LTU)
Data output via DMA over PCIe to memory of FLP in 8kByte packets
Option to record memory pages to a disk file for later analysis

## Slide 37: CRU simplified logical data flow
Trigger Emulation inside CRU Firmware

## Slide 38: Data Arrival in CRU - Continuous and Triggered
Continuous Readout
Triggered Readout

## Slide 39: CRU: “Readout Card” (ROC) Interface library

## Slide 40: ITS Readout – Data Rate Specifications
ALICE baseline requirements:
50 kHz Pb-Pb
200 kHz p-p
ITS design specification:
100 kHz Pb-Pb
400 kHz p-p

## Slide 41: Data rate – PbPb @ 100kHz per Readout Unit

## Slide 42: ROC bench tool performance
FLP 2 CRUs 4 PCIe endpoints
Total throughput

## Slide 43: Backup Slides - Firmware

## Slide 44: Firmware Development Environment
E-group: All communication between firmware developers is organized through membership in a CERN e-group (alice-its-wp10-firmware@cern.ch). The e-group is also used for access control to the version control system (gitlab) and the issue tracking system (JIRA)
Online Documentation: Documentation of hardware, Firmware, and software is posted at the WP10 Twiki page in the “ALICE Web” Twiki: https://twiki.cern.ch/twiki/bin/view/ALICE/ITS-WP10
Hardware Programming languages: We decided to allow 3 different firmware languages: VHDL, Verilog and System Verilog. Currently, the prototype development is on the Xilinx 7-series, and the Vivado toolset supports all 3 languages.
Tool Sets: The current design of the Readout Unit (RU) foresees the main programmable logic to be a Xilinx SRAM based Kintex UltraScale(+). Prototyping was started with a Xilinx Kintex-7. These devices are supported by the Xilinx Vivado Toolset. We are currently using Vivado version 2017.4. The RU design also includes a flash-based device to support scrubbing. This device is foreseen to be the ProAsic-3 from Microsemi which is supported by the Microsemi Libero SoC Design Suite. To develop detector specific logic on the CRU requires the use of the Altera Quartus toolset. We are considering evaluating this toolset in the future. For FX3 (USB) firmware design, we are using the Cypress EZ-USB Suite & GPIF-II Designer.
Simulations: Currently two toolsets are used for firmware test benches: Mentor Modelsim and Cadence Incisive (NCSim). The Cadence tools is only used by CERN collaborators at the moment.
Coding Style: For firmware coding in VHDL, a coding style document was developed: https://twiki.cern.ch/twiki/bin/view/ALICE/FwDevFlowMethods
Scripting: Most firmware toolsets support scripting in Tcl. Tcl is the scripting languate integrated in the Vivado tool environment. The firmware projects developed in WP10 are required to include a Tcl script to create the project and compile it to ensure common project configuration amongst developers. An optional “Makefile” can be used to call targeted Tcl scripts for various tasks (project creation, compilation, simulation, etc…)

## Slide 45: Software
Hardware Platform: The main supported platform is currently a PC running the CERN CentOS 7 (CC7) operating system with Vivado 2016.4 and Modelsim SE 10.4a installed. Similar features can be achieved by using the Windows mingw platform with the Msys shell, but full compatibility with the Linux development is not guarantied by WP10
Software Environment: To ensure compatibility for software co-development it is recommended to install the Linux Developer Toolset in CC7 (https://linux.web.cern.ch/linux/devtoolset/), which provides more up-to-date compilers and libraries. Python is used for scripting to interact with the WP10 prototype hardware (currently via USB). We use the Continuum Analytics Anaconda platform (Python 3.6 version) to provide the python tools (https://www.continuum.io/anaconda-overview). This platform is also available for Windows.
Version Control: CERN gitlab is used for version control of the firmware and software development within WP10. The gitlab group for WP10 is located at: https://gitlab.cern.ch/alice-its-wp10-firmware/. Membership in this gitlab group is via the e-group. Various projects are hosted in this gitlab group, the main prototype development is currently in the project “itswp10”.
Issue Tracking: CERN JIRA is used for issue tracking. The WP10 issues are tracked underneath the ALICE project JIRA at: https://alice.its.cern.ch/jira/projects/IT.
File exchange: Files that are too big or not version controlled are exchanged via a shared CERNbox. Currently, this is by invitation only, since the CERNbox account used is a private account.

## Slide 46: Backup Slides – Control Interfaces

## Slide 47: Opencores CAN Protocol Controller
https://opencores.org/project,can
Written in Verilog
Supports basic CAN and extended CAN
  11-bit ID and 29-bit ID
  ID mask and filtering
Up to 1Mbps operation
Transmit/receive/error interrupts
Wishbone interface (8-bit address and data)
Register map compatible with Philips SJA1000 CAN Controller IC
  https://www.nxp.com/docs/en/data-sheet/SJA1000.pdf
Size: 12k gates (930 flip-flops)

## Slide 48: CANbus protocol proposal
ID[10] | ID[9] | ID[8] | ID[7] | ID[6] | ID[5] | ID[4] | ID[3] | ID[2] | ID[1] | ID[0]
N[6] | N[5] | N[4] | N[3] | N[2] | N[1] | N[0] | C[3] | C[2] | C[1] | C[0]
MsgID[10:4] = N[6:0] = NodeID
MsgID[3:0] = C[3:0] = Command
Command Code | Meaning
1 | DATA
2 | “WRITE” command
3 | Write Response (optional)
4 | “READ” command
5 | Read Response
7 | ”STATUS” or “ALERT”
Emulate a “network topology”: Divide 11 bit CAN ID field into a “Node ID” and a “Command” field:
Write (2) | Write Command
Bytes 0 - 1: | “Address” of this “WRITE”.
Bytes 2 – 3: | “Data”
Write Response (3) | Length = 3
Bytes 0-1: | “Address” (copied from the received message).
Byte 2: | Status resulting from this write or sub-command. A value=0 indicates successful completion. Non-zero values indicate (various) errors (to be determined)
Write Request:
Write Response:
Read (4) | Length= 2
Bytes 0-1: | “Address” of this “READ”.
Read Request:
Read Response (5) | Length 2 to 4 bytes
Byte 0-1: | “Address” of this “READ” (copied from the received message).
Bytes 2-3: | 2 additional bytes representing data value resulting from “reading” the requested address. Lack of these bytes (i.e. a short message) indicates an invalid read address/request.
Read Response:
Command Codes
Allows for up to 128 nodes per CAN network

## Slide 49: OpenCores CAN Protocol Controller Simulations
Tested using a simple Bitvis UVVM style testbench
Two instances of the CAN controller connected
Two separate WB interfaces to write to each controller
40 MHz clock

## Slide 50: OpenCores CAN Protocol Controller Simulations
Bit Timing Register (BTR0) configured for 4x baud clock prescale
tSEG1 set to 7 baud clocks, tSEG2 set to 3 baud clocks, in BTR1
tSYNCSEG is always 1 baud clock
Gives us a bit rate of 40 MHz / (4 * (1+7+3)) = 1Mbps

## Slide 51: OpenCores CAN Protocol Controller Simulations
Simulation waveforms, showing initial WB transactions on both controllers, CAN transmission, and CAN IRQ lines going low after message

## Slide 52: OpenCores CAN Protocol Controller Simulations
sample_point marks the point where bits on rx_i are being sampled
The simulated bit period is 1 us, as it was configured for
The sampling point is located at 7/10ths of a microsecond into each bit, corresponding to what tSEG1 and tSEG2 were configured for

## Slide 53: OpenCores CAN Protocol Controller Simulations
Testbench log
# UVVM: ID_LOG_HDR 4940.0 ns TB seq. Start a transaction from CAN0 to CAN1
# UVVM: -------------------------------------------------------------------------------------------------------------------------------------------------------------------------
# UVVM: ID_BFM 5115.0 ns TB seq. wb_write(A:x"0A", x"BB") completed. Set TXID1 to xBB
# UVVM: ID_BFM 5465.0 ns TB seq. wb_write(A:x"0B", x"08") completed. Set TXID2 to x08, 8 bytes data
# UVVM: ID_BFM 5815.0 ns TB seq. wb_write(A:x"0C", x"11") completed. Set data1 to x11
# UVVM: ID_BFM 6165.0 ns TB seq. wb_write(A:x"0D", x"22") completed. Set data2 to x22
# UVVM: ID_BFM 6515.0 ns TB seq. wb_write(A:x"0E", x"33") completed. Set data3 to x33
# UVVM: ID_BFM 6865.0 ns TB seq. wb_write(A:x"0F", x"44") completed. Set data4 to x44
# UVVM: ID_BFM 7215.0 ns TB seq. wb_write(A:x"10", x"55") completed. Set data5 to x55
# UVVM: ID_BFM 7565.0 ns TB seq. wb_write(A:x"11", x"66") completed. Set data6 to x66
# UVVM: ID_BFM 7915.0 ns TB seq. wb_write(A:x"12", x"77") completed. Set data7 to x77
# UVVM: ID_BFM 8265.0 ns TB seq. wb_write(A:x"13", x"88") completed. Set data8 to x88
# UVVM: ID_BFM 8615.0 ns TB seq. wb_write(A:x"01", x"01") completed. Request transmission on CAN0
# UVVM:
# UVVM:
# UVVM: ID_LOG_HDR 8615.0 ns TB seq. Wait for CAN1 to receive message
# UVVM: -------------------------------------------------------------------------------------------------------------------------------------------------------------------------
# UVVM:
# UVVM:
# UVVM: ID_LOG_HDR 125613.5 ns TB seq. Got interrupt from CAN1.
# UVVM: -------------------------------------------------------------------------------------------------------------------------------------------------------------------------
# UVVM: ID_BFM 125790.0 ns TB seq. wb_check(A:x"00", x"XX")=> OK, received data = x"3E". Check that CAN0 transmit interrupt was set
# UVVM: ID_BFM 126140.0 ns TB seq. wb_check(A:x"02", x"XX")=> OK, received data = x"2C". Check that CAN0 transmit complete status bit is set
# UVVM: ID_BFM 126315.0 ns TB seq. wb_check(A:x"00", x"XX")=> OK, received data = x"3E". Check that CAN1 receive interrupt was set
# UVVM:
# UVVM:
# UVVM: ID_LOG_HDR 127315.0 ns TB seq. Verify message received by CAN1
# UVVM: -------------------------------------------------------------------------------------------------------------------------------------------------------------------------
# UVVM: ID_BFM 127490.0 ns TB seq. wb_check(A:x"14", x"BB")=> OK, received data = x"BB". Verify received RXID1
# UVVM: ID_BFM 127840.0 ns TB seq. wb_check(A:x"15", x"08")=> OK, received data = x"8". Verify received RXID2, 8 bytes data
# UVVM: ID_BFM 128190.0 ns TB seq. wb_check(A:x"16", x"11")=> OK, received data = x"11". Verify received data byte 1
# UVVM: ID_BFM 128540.0 ns TB seq. wb_check(A:x"17", x"22")=> OK, received data = x"22". Verify received data byte 2
# UVVM: ID_BFM 128890.0 ns TB seq. wb_check(A:x"18", x"33")=> OK, received data = x"33". Verify received data byte 3
# UVVM: ID_BFM 129240.0 ns TB seq. wb_check(A:x"19", x"44")=> OK, received data = x"44". Verify received data byte 4
# UVVM: ID_BFM 129590.0 ns TB seq. wb_check(A:x"1A", x"55")=> OK, received data = x"55". Verify received data byte 5
# UVVM: ID_BFM 129940.0 ns TB seq. wb_check(A:x"1B", x"66")=> OK, received data = x"66". Verify received data byte 6
# UVVM: ID_BFM 130290.0 ns TB seq. wb_check(A:x"1C", x"77")=> OK, received data = x"77". Verify received data byte 7
# UVVM: ID_BFM 130640.0 ns TB seq. wb_check(A:x"1D", x"88")=> OK, received data = x"88". Verify received data byte 8
Set up TX buffer on CAN0 with message for CAN1 (ID 0xBB)
Wait for CAN1 to receive message
Verify message contents

## Slide 54: CAN bus testing on RUv1
AnaGate CAN Monitor program
Readout Unit PA3 GUI software (RX buffer registers)
Readout Unit PA3 GUI software (TX buffer registers)
AnaGate CAN adapter used for testing (same as DCS group is using).
Successfully sent/received CAN messages to/from CAN controller in PA3

## Slide 55: Trigger Interface – Splitter Loopback Test
Loopback test including:
  Actual SFP transmitter & receiver
  1:32 splitter
  Result: 24 hrs w/o errors1
1 Test conducted by Jo Schambach

## Slide 56: Backup Slides – Data Streaming

## Slide 57: PCIe40_v1

## Slide 58: CRU v2: PCIe40_v2 from LHCb

## Slide 59: Data rate – PbPb @ 50kHz per Readout Unit