## Slide 1
LVDS
MGT
SRAM
FPGA
10 x 320 Mbps Dout
10 x 320 Mbps Din
GBTx0
SCA e-link
GBT-SCA
GBTx1
GBTx2
10 x 320 Mbps Din
10x320 Mbps Dout
10 x 320 Mbps Din
2xclkdes (40, 160MHz)
VTRx1
Clkdes (40Mhz)
VTTx
VTRx2sm
I2C
4.8 Gbps
4.8 Gbps
4.8 Gbps
4.8 Gbps
4.8 Gbps
HR
Bank
HR
Bank
HR
Bank
I2C
I2C
I2C
I2C
Cypress FX3-USB3
32bit Data
PCLK-100MHz
13bit Ctrl
I2C EEPROM
UART
Flash FPGA
Flash
PROM
12 DIO
Power Unit
Xtal 160MHz
JTAG
Trigger
CRU
CRU
Temperature (RTD)
SCA ADC
RUv1 Block Diagram
2 I2C for monitoring/Control
Trigger
Busy out
8 bit SELECT MAP
28 Data (1.2Gbps)
5 DCLK (MLVDS)
LVDS
5 DCTRL (MLVDS)
28 Data (400/600M)
I2C
2 UsrClk
CANbus
8 MLVDS
LVDS
Transition Board
FireFly
UsrClk
fanout
MGT RefClk
switch
JTAG
Headers
40 MHz
160 MHz
Last Update: 1-Dec-2017
Power Unit
8 MLVDS
En
power
3,3V 2,5V 1,8V
1,5V 1,2V 1V
12V
Monitor voltage/current
FireFly
FireFly
FireFly
FireFly
2 MGT RefClk
Jitter
cleaner
Busy in
MGT
4 AUX IO
5 DIO
5 DIO
2xclkdes (40, 160MHz)
2 Clkdes
2 Clkdes
1 Clkdes
Xtal 160MHz
I2C
I2C
I2C

## Slide 2
A
B
C
D
E
ITS IL
ITS ML/OL
MFT ID
MFT OD
Would require specific “low level” firmware for the MFT
MFT connections:
For the two smallest disks, MFT needs to read sensors at 1.2 Gb/s, at most there are 11 ALPIDEs connected to a single RU, split into 3 ladders, therefore 3 clk/ctrl/data cable assemblies are required.
On the larger disks, switching to 600 Mb/s readout is possible. There are at most 21 ALPIDE connected to a single RU split into 5 ladders, so 5 clk/ctrl/data cable assemblies are required.
1.2 Gb/s
400 or 600 Mb/s
Unconnected
used
unused
Connector

## Slide 3
Possible SRAM FPGA choices:
UltraScale & UltraScale+ pin-to-pin compatible devices in A1156 package (35 × 35 mm2).
Only need to check maximum voltage range for some HR banks between US/US+.
We will likely need 250 (ITS) + 100 (MFT) FPGAs (including spares).
Current

## Slide 4: General Specifications 1
High Speed I/Os
400/600 Mbps readout of sensors via LVDS has not yet been tested. Matthias has created the firmware necessary to test it, but actual hardware test has not yet been done.
Need to check the compatibility for SLVS and MLVS in the various banks and number of inputs needed with these voltages
Need to check the number of links for both ITS and MFT
GBT
GBTx 1 and 3 get their clocks from downlink (CRU & CTP respectively). GBTx 2 gets is clock from GBTx 1 via clkdes line
Bring 3 clkdes into SRAM FPGA: 160MHz, 40 MHz (Serdes clock), 320MHz (?, elink speed)
JTAG is provided via SCA to both SRAM and Flash FPGA in JTAG chain with jumpers to isolate each part. Add local headers for both SRAM and Flash FPGA
Flash FPGA can communicate with CRU via I2C
Busy
Busy in and out channels via MGT need to be provided to investigate busy handling schemes

## Slide 5: General Specifications 2
Radiation Hardness
Choice of Flash FPGA still open. ProAsic3 is preferred choice, but it is rumored it has reprogrammability issues similar to IGLOO2.
Flash FPGA uses SelectMap interface to program SRAM FPGA at power-up. It also uses SelectMap interface for scrubbing. For both purposes, the images are stored in the FlashProm attached to the Flash FPGA (different images?).
Two I2C buses through the GBT-SCA are used for control and monitoring communication with the CRU
During shutdowns when GBT isn’t available, a CANbus interface is used for control & monitoring of PowerUnit. CANbus lines can also be forwarded (via Firmware) from FlashFPGA to SRAM-FPGA to run CANbus core there instead.
SRAM-FPGA is responsible for interaction with PU (control, monitoring, latchup-response). Needs to communicate PU status (including latchup) to FlashFPGA for monitoring via GBT (or CANbus)
For reprogramming the FlashPROM a special firmware could be loaded to SRAM-FPGA to provide data path from GBT through communication bus to FlashFPGA (and in turn to PROM).
Mechanics
Single-sided component mounting

## Slide 6: SRAM FPGA IO resources needed
For each GBT
DP 10 at 320 Mb/s e-links (160 MHz).
DP 1 at 160 MHz clock e-link.
DP 1 at 40 MHz clock e-link.
DP 12 IO pairs for each GBTx.
In total (5 GBT links through 3 GBTx chip), data communication only.
DP 60 toward the GBTx.
Flash FPGA connection
SE 32 select MAP.
SE 32 data/control.
SE 64 total.
FX3 chipset
SE 1 UART.
SE 1 Clock.
SE 14 bit control.
SE 32 Bit data.
SE 48 total.
Power Unit
SE 2 × 3 line (HS I2C ) for (2 power unit).
SE 2 × 16 line (8 analog + 8 digital LU/SEU monitor).