## Slide 1: RUv1 Overview
RUv1 pre-production board
Architecture & details RUv1
RUv1 PCB stackup
RUv1.0 & RUv1.1 differences
Marcel Rossewij

## Slide 2: RUv1 production history
6U VME size
8* RUv1.0 boards produced
  2 * August 2017
  6 * September 2017
13* RUv1.1 boards
  6 * November 2017
  7 * March 2018
Transition Board
Power Mezz
GBT
Fibers
GBTx
PA3
Ultra Scale
USB
To
Power
Board
Power
To
Sensors

## Slide 3: Block schematic

## Slide 4: Trigger

## Slide 5: Data-path
IB: 9 * 1.2 Gbps
MB/OB: 16/28 * 400 Mbps

## Slide 6: Power boards control

## Slide 7: Slow Control
Measurement of
7 * Regulator Voltage
7 * Regulator current
2 * RTD

## Slide 8: PA3 configuration (JTAG)

## Slide 9: US-Flash memory initialization
2 paths forseen:
SCA->I2C
US

## Slide 10: Flash GBTx

## Slide 11: Configure GBTx

## Slide 12: BUSY

## Slide 13: Table Top USB operation

## Slide 14: RUv1 PCB technology
10 layer
  4 signal layers
  4 GND layers
  2 PWR (35μ)layers
Reverse/core-build stackup
Halogenfree material: Panasonic (R1566)
No blind/burries via’s. Only through hole
  OL pad 450μ
  IL pad 500μ
Finish ENIG
# | Name |  |  |  | Diff. pairs | 
 |  |  | width | clearance | width | spacing
1 | Top signal | 18 (35) | 110 | 110 | 110 | 150
 | Core | 150 |  |  |  | 
2 | GND plane | 18 | 150 | 100 |  | 
 | Prepreg | 200 |  |  |  | 
3 | Signal | 18 | 100 | 100 | 100 | 120
 | Core | 200 |  |  |  | 
4 | GND plane | 18 | 150 | 100 |  | 
 | Prepreg | 100 |  |  |  | 
5 | Power plane | 35 | 150 | 100 |  | 
 | Core | 100 |  |  |  | 
6 | power plane | 35 | 150 | 100 |  | 
 | Prepreg | 100 |  |  |  | 
7 | GND plane | 18 | 150 | 100 |  | 
 | Core | 200 |  |  |  | 
8 | Signal | 18 | 100 | 100 | 100 | 120
 | Prepreg | 200 |  |  |  | 
9 | GND plane | 18 | 150 | 100 |  | 
 | Core | 150 |  |  |  | 
10 | Bottom sig. | 18 (35) | 110 | 110 | 110 | 150

## Slide 15: Main changes/fixes RUv1.0 => RUv1.1
Issue | Comment |  |  |  | Status RUv1.1
Current sense offset | Change amplifier (AD626 => AD8418) |  |  |  | Fixed
Re-group e-link clk | Use other GBTx clock-out signal |  |  |  | Done
Match CDCLK to DOUT | GBTx DOUT mismatch 22mm/150ps |  |  |  | Fixed
Mirror GBTxI2C conn. | Fixed Mirror error |  |  |  | Fixed
U28 pin 5-6 swapped | For INIT LED (only informative with scrubbing ) |  |  |  | Fixed
Case C497/680u | 1201 => 7343 |  |  |  | Fixed
Flash mem lines absent | RUv1.0 CE2 & R/B2 wired to header J14 pin 17&19 |  |  |  | Fixed
FAN connector J23 pinout |  | 1 | 2 | 3 | RUv1.1 FAN connector Reversed
 | RUv0 | - | 5V | GND | 
 | RUv1.0 | 12V | 5V | GND | 
 | FAN | GND | 5V/12V | Tacho out | 

## Slide 16: Minor changes/fixes RUv1.0 => RUv1.1
Issue | Comment | Status RUv1.1
Use higher headers | Change component | Fixed
Input voltage to SCA | Route | Done
CAN/JTAG connector | Distance too small => Move J8 & J7 1mm up | Done
Mis-allignment Transitionboard mountingholes | Marcel: 0,3mm (measered + datasheet) Piero: 0,3mm Jo: 0,56 mm (measured on RU in workshop) | Moved 0,4mm to edge
PA3 reset on clkbuf | Yes | Done
FAN-clip Clearance | Move capacitors C169 | Done
U37 MLVDS DE error | Malfunction Power Unit 2 Interface on J1 | Fixed