## Slide 1: RUv1 characterization
Marcel Rossewij
Overview & results all test activities
Jitter introduced by scrubbing
Power supply (LMZ31710 DCDC regulator)
  Currents during Power-on and after configuration
  Magnetic field tests
Spare slides
  DC-Accuracy and voltage drop
  Noise (time & frequency domain)
Sense Amplifier offset error
Clock generation/cleaner/distribution performance

## Slide 2: RUv1 tested functionalities (1)
RU power section
  7 DCDC regulators (accuracy, noise, ripple, Inrush, sequencing)
  ISENSE offset problem solved by replacing amp AD626=>AD8418
Communication with sensors/Alpide using transition board & firefly
  CLOCK, CONRTOL, DATA @ 1.2Gbps and 400 Mbps
Communication via 4.8 Gbps GBT links (GBTx/1/2, VTRx/VTTx)
  Acces & program GBTx using Cern USBI2C dongle (connector bug)
Communication with the SCA-chip
  monitor voltage/current, temperature, VTRx optical power
  I2C, JTAG, GPIO interface
Clock distriburtion: jitter/levels on crystal oscillators, jitter cleaner and clock buffer
USB3 (using FX3 chip) communication & boot from I2C PROM
JTAG chain (primary US & PA3 program, secondary FX3 & GBTX/1/2)
Program Xilinx US with PA3 via select map interface

## Slide 3: RUv1 tested functionalities (2)
Communication with the PU using front pannel I2C
FLASH PROM (access, read-ID, read & write)
CAN transceiver

## Slide 4: RUv1 testes functionalities detailed (1)
Green=Successfully tested, Yellow= not tested, low prio, Grey=Still to be tested
 |  |  | Assigned to | Status | Priority
Polyswitch fuse | F1…F3 | Check hold/trip limits |  |  | Low
Polarity protection | D3 | Check operation |  |  | Low
DC-DC Regulator Input: 5V or 12V | U10…U16 | Functional/Operation | MR | Done | High
 |  | Accuracy | MR | Done | High
 |  | Noise/ripple (RMS) | MR | Done | Medium
 |  | Noise (frequency) | MR | Done | Medium
 |  | Line/load regulation |  |  | Medium
 |  | Efficiency |  |  | Medium
 |  | Switching frequency | MR | Done | Medium
 |  | Current/Temp protection |  |  | Low
 |  | Startup-Sequencing (PWRGD/Inhibit) |  |  | High
GBTx/SCA Reset | S5 | Reset by PWRGD 1V5 |  |  | High
Current sense circuit | U20…U26 | Functional/Operation | MR | Done | High
 |  | Gain & Accuracy | MR | Done | Medium
 |  | Offset | MR | Done | High => change Amp
 |  | Noise |  |  | Low
 |  | Bandwidth |  |  | Low
 |  | CMRR (frequency) |  |  | Low
Inductor/plane Voltage drop | L15…18 L34…39 | Check within FPGA spec |  |  | High
LVDS 1:8 buffer | U17 | Functional/Operation | MR | Done | High
 |  | Output levels |  |  | Medium
 |  | Bandwidth |  |  | Low

## Slide 5: RUv1 testes functionalities detailed (2)
 |  |  | Assigned to | Status | Priority
Jitter cleaner Power 3,3 or 2,5V PLL bandwidth | U18 | Functional/Operation (gets locked) | MR |  | High
 |  | Bypass-mode | MR |  | Medium
 |  | Output levels | MR |  | Medium
 |  | Jitter Attenuation (ps)/Loop bandwidth | MR |  | Medium
 |  | Phase noise plot |  |  | Low
XTAL | X1, X2 | Functional/Operation | MR | Done | High
 |  | Accuracy | MR |  | High
 |  | Enable | MR |  | Medium
 |  | Phase noise |  |  | Low
BUSY/AUX connector | J7 | Functional/Operation (Loopback) |  |  | High
 |  | Vary levels & data rates (e.g. BUSY) |  |  | High
 |  | Check attenuation (frequency) |  |  | Low
Alpide Interface | J2 | Check ITS connectivity |  |  | High
 |  | Check attenuation (frequency) |  |  | Low
 |  | Check data-rates/BER |  |  | Medium
 |  | MGT levels, emphasis & equalization |  |  | Medium
 |  | GPIO levels, emphasis & equalization |  |  | Medium
 |  | Fit FireFly holder |  |  | NA
US reset switch | S6 | Reset Xilinx US FPGA | MR | Done | Medium

## Slide 6
Xilinx US FPGA | J10 | Functional operation (JTAG config) | MR | Done | High
 |  | Access select map register | At | Done | High
 |  | Configure FPGA via select map | Bergen |  | High
 |  | Scrubbing | Bergen |  | High
 |  | MGT (L&R) refclk (clkdes or local) | MR/Jo | Only local | High
 |  | fabric clk (clkdes or local) switch | Jo | Only local | High
 |  | SCA GPIO interface |  |  | High
 |  | GBTx I2C master interface | Jo | Done | High
 |  | SCA I2C slave interface |  |  | Low
 |  | SCA SPI slave interface |  |  | Low
 |  | PA3 SE interface functional |  |  | High
 |  | PA3 SE interface rates |  |  | High
 |  | PA3 diff interface functional |  |  | High
 |  | PA3 diff interface rates |  |  | High
 |  | Place Fan, enough clearance? Works? |  |  | High => move C169
SMA clk out | J21/J22 | Functional operation | MR | Done | Medium
Alpide DCLK/CTRL | U32, U33 | Functional operation | ML | Done all5 | High
 |  | Jitter effects due to triplicated output |  |  | Low
I2C Power board | U34,U35 | Functional operation | Jo | Done | High
 |  | CM/speed/level Margins MLVDS |  |  | Low, 1 kbit 1 meter
J1 Power board | U36,U37 | Functional operation |  |  | Low
FX3 reset | S7 | FX3 reset | MR | Done | Medium
FX3 | U5 | FX3 data interface functional | ML | Done | High
 |  | FX3 data interface endurance/BER |  |  | Medium
 |  | FX3 UART interface |  |  | High
 |  | FX3 I2C PROM boot | MR | Done | High
FX3 control switch | S9 | Boot mode | MR | Done | High

## Slide 7
PA3 | U31 | Functional operation (JTAG config) | MR | Done | Priority
 |  | fabric clk (clkdes or local) | At | Only local | Low
 |  | SCA GPIO interface |  |  | High
 |  | SCA I2C slave interface |  |  | Medium
 |  | Jitter cleaner/buffer control | At/MR |  | Medium
 |  | PA3 resistor reset | Bergen | Fails | Medium =>failed
PA3 reset | U38 | PA3 reset circuit | Bergen | Done | High (fail with high dose)
Flash PROM | U30 | Access Flash Prom ID | At | Done | High
 |  | Perform write/read BER tests | At/JDS |  | High
CAN transceiver | U29 | Functional/Operation |  |  | High
 |  | Loopback-mode |  |  | Low
GBTx | U2 | I2C configuration (US/dongle) | Jo/MR/ML | Done | High
 |  | Data transmission | Jo/MR/ML | Done | High
 |  | Endurance/BER test |  |  | High (5 minutes)
 |  | GBTx Clkdes7 to GBTx1 refclk in | MR | Partly | High
VTRx1 | J3 | Functional operation (transmission) | Jo/MR/ML | Done | High
 |  | LD power via I2C (EC channel) |  |  | Low
 |  | RSSI1 (Photo power to SCA-ADC) |  |  | Low
GBTx/1/2 | U3/4 | I2C configuration (US/dongle) | Jo/MR/ML | Done | High
 |  | Data transmission | Jo/MR/ML | Partly | High
 |  | Endurance/BER test |  |  | High
VTTx | J4 | Functional operation (transmit) | Jo/MR/ML | Partly | High
 |  | LD power via I2C (SCA/US) |  |  | Low
VTRx2 | J5 | Functional operation (receive) | Jo/MR/ML | Partly | High
 |  | RSSI2 (Photo power to SCA-ADC) |  |  | Low
JTAG |  | Chain with US and/or PA3 | MR | Done | High
 |  | Include FX3 and GBTx/1/2 | MR |  | High

## Slide 8: RUv1 testes functionalities detailed (5)
 |  |  |  |  | High
Header | J12 | Check GBTx fusing. Are needed: R277/R278 to disconnect SCA? R279, R282 & R285 fusepower R280, R283 & R286 prog. pulse |  | Remove R277/R278 Mirror header | High Header mirrored Fusing GBTx0 only
SCA | U1 | Access SCA via GBTx | Jo | ? | High
 |  | Analog (DCDC-V&I, RSSI, PT1000) |  |  | High
 |  | GPIO (PA3/US and US config signals) |  |  | High
 |  | I2C | Bergen |  | High
 |  | SPI | Jo |  | Low
 |  | SCA JTAG |  |  | High
JTAG |  | Chain with US and/or PA3 | MR | Done | High
 |  | Include FX3 and GBTx/1/2 | MR |  | High
PA3-Pinheader | J14 | Functional operation from PA3 | MR | Done | High
US-Pinheader | J13 | Functional operation from US | MR | Done | High
LEDs | J10 | Functional operation from US/PA3 | MR/At | Done | High
Switch/push button | S0…3,S8 | Functional operation to US/PA3 | MR/At | Done | High

## Slide 9: Power-on sequence

## Slide 11: DCDC converter magnetic fied test
LMZ31710 tested under different magnetic field strenght, orientation and load conditions. Main conclusions:
LMZ31710 fully operational with B up to 0,5T at 0°and 90°
Efficiency slightly (4%) reduces with increase in B (even less with B at 90°)
Efficiency at higher switching frequencies less affected by presence of B
Ripple increases with B field (less with B at 90°)
No hysteresis effect: after applying 0,5T, efficiency comes back to start value

## Slide 12: Jitter introduced by scrubbing
RUv1 showed increased jitter on its MMCM/PLL outputs when scrubbing is active. (giving DCLK jitter resulting in errors in the Alpide=>RU HSDATA communication)
Tests show same behaviour with Xilinx development boards having an ultrascale device (the jitter increase was not present with the kintex7 devices )
Next sheet shows an increase of the period to period jitter when scrubbing is active. The Jitter increase is non-gaussian (as RMS is hardly affected, mainly the pk-pk jitter).
Subsequent sheet shows that the deviant periods come every 3,25 sec for 0,75 sec
Jitter Issue mitigated by avoiding use of MMCM/PLL for generation of DCLK (fallback solution: employ PA3 PLL)
Board | Device | Jitter (idle) | Jitter (scrubbing)
RUv1 | US | 300 | 900
RUv0 | Kintex7 | 312 | 392
KCU040 | US | 168 | 1120
KCU105 | US | 150 | 850

## Slide 13: Scrubbing-Jitter Issues measured
RMS jitter (14 ps) hardly affected
Peak to peak jitter 100ps => 400ps (less than other)
Period deviations occurs once every few k-waveforms
Scrub | Tavg | Tmin | Tmax | Tp-p | σ | #cnt
OFF | 24,95 | 24,892 | 25,004 | 112ps | 13,6 | 300k
ON |  | 24,773 | 25,160 | 387ps | 13,7 | 

## Slide 14
Managed to trigger on deviant periods
In continuous blind scrubbing mode:
Trigger counters indicated scrubcycle every 60/16=3,75 sec
Deviant period triggers occur every 0,75 sec of the 3,75 sec

## Slide 15
RUv1 characterization
Utrecht University: Marcel Rossewij, Jody Wisman
NIKHEF: Jan-David Schipper, Paul Kuijer

## Slide 16: Measurement results
Power supply (LMZ31710 DCDC regulator)
  DC-Accuracy and voltage drop
  Noise (time & frequency domain)
  Currents during Power-on and after configuration
Sense Amplifier offset error
Clock generation/cleaner/distribution performance

## Slide 18: Power up configuration
0,5

## Slide 19: Voltage variation among different RUv1
Measurement device: Keithley 2100
The averaged measured voltages differ up to 6 ‰ from expected
All voltages well in MIN/MAX limits. 1V2 closest (10mV) to limits
(The VMGT/1V2/VAUX MIN values are corrected for the voltage drop)
rail | Xilinx US |  |  | DCDC set |  | RUv1_0 SN: |  |  |  |  |  | AVG | STD | AVG-Vo | ‰ | max | max-MAX | min | min-MIN | max-min
 | MIN | typ | MAX | Rset | Vo | 3 | 4 | 5 | 6 | 7 | 8 | 3-8 | mV | mV |  | 3-8 | mV | 3-8 | mV | mV
VINT | 0,922 | 0,95 | 0,979 | 2400 | 0,958 | 0,961 | 0,963 | 0,963 | 0,965 | 0,961 | 0,961 | 0,962 | 1,6 | 4,8 | 5 | 0,965 | 14 | 0,961 | 39 | 4
VMGT | 0,98 | 1 | 1,03 | 2100 | 1,009 | 1,013 | 1,015 | 1,013 | 1,015 | 1,013 | 1,014 | 1,014 | 1,0 | 5,3 | 5 | 1,015 | 15 | 1,013 | 33 | 2
1V2 | 1,18 | 1,2 | 1,23 | 1400 | 1,213 | 1,217 | 1,218 | 1,218 | 1,219 | 1,22 | 1,213 | 1,218 | 2,4 | 4,6 | 4 | 1,22 | 10 | 1,213 | 33 | 7
1V8 | 1,752 | 1,8 | 1,854 | 715 | 1,800 | 1,81 | 1,81 | 1,81 | 1,806 | 1,811 | 1,814 | 1,810 | 2,6 | 10,2 | 6 | 1,814 | 40 | 1,806 | 54 | 8
3V3 | 3,2 | 3,3 | 3,4 | 316 | 3,315 | 3,335 | 3,336 | 3,325 | 3,318 | 3,328 | 3,324 | 3,328 | 6,9 | 12,5 | 4 | 3,336 | 64 | 3,318 | 118 | 18
2V5 | 2,375 | 2,5 | 2,625 | 453 | 2,494 | 2,497 | 2,503 | 2,51 | 2,504 | 2,505 | 2,5 | 2,503 | 4,4 | 9,1 | 4 | 2,51 | 115 | 2,497 | 122 | 13
1V5 | 1,35 | 1,5 | 1,65 | 931 | 1,522 | 1,528 | 1,528 | 1,527 | 1,527 | 1,529 | 1,525 | 1,527 | 1,4 | 5,7 | 4 | 1,529 | 121 | 1,525 | 175 | 4

## Slide 20: Hyperlynx DC drop analysis VMGT

## Slide 21: RUv1_0 (SN3) Voltage (drop over L) measurements
VMGT/1V2/VAUX: Measured LDROP (firmware active) up to 12/9/6 mV
Hyperlynx analysis give: LDROP 16/15/12 mV (more MGTs active)
 | min | typ | max | Rset | Vo | location |  | US empty | diff (mV) | Measured (mv) |  | US loaded | diff (mV) | Measured (mV) | diff Loading
VINT | 0,922 | 0,95 | 0,979 | 2400 | 0,958 | Y10 |  | 0,95985 |  |  |  | 0,95893 |  |  | -0,9
VMGT | 0,97 | 1 | 1,03 | 2100 | 1,009 | Y11 |  | 1,01211 |  |  |  | 1,011 |  |  | -1,1
MGTAVCCL | 0,97 | 1 | 1,03 |  |  | L15 | 1,01162 | 1,01125 | -0,4 | 0,6 | 1,00997 | 1,00953 | -0,4 | 0,26 | -1,7
MGTAVCCR | 0,97 | 1 | 1,03 |  |  | L37 | 1,01137 | 1,01089 | -0,5 | 0,6 | 1,00438 | 0,99948 | -4,9 | 4,7 | -11,4
 | 0,97 | 1 | 1,03 |  |  | L34 | 1,01143 | 1,01089 | -0,5 | 0,4 | 1,00437 | 0,99925 | -5,1 | 4,9 | -11,6
1V2 | 1,17 | 1,2 | 1,23 | 1400 | 1,213 | Y12 |  | 1,2151 |  |  |  | 1,2138 |  |  | -1,3
MGTAVTTL | 1,17 | 1,2 | 1,23 |  |  | L16 | 1,2151 | 1,215 | -0,1 | 0,2 | 1,2133 | 1,2132 | -0,1 | 0,1 | -1,8
MGTAVTTR | 1,17 | 1,2 | 1,23 |  |  | L38 | 1,215 | 1,215 | 0,0 | 0,16 | 1,2092 | 1,2061 | -3,1 | 2,9 | -8,9
 | 1,17 | 1,2 | 1,23 |  |  | L36 | 1,215 | 1,215 | 0,0 | 0,15 | 1,209 | 1,206 | -3,0 | 2,9 | -9,0
1V5 | 1,35 | 1,5 | 1,65 | 931 | 1,522 | Y16 |  | 1,5258 |  |  |  | 1,5256 |  |  | -0,2
1V8 | 1,746 | 1,8 | 1,854 | 715 | 1,800 | Y13 |  | 1,8071 |  |  |  | 1,8061 |  |  | -1,0
VCCAUX | 1,746 | 1,8 | 1,854 |  |  | L18 | 1,805 | 1,802 | -3,0 | 3 | 1,8009 | 1,7964 | -4,5 | 4,7 | -5,6
MGTAUXL | 1,75 | 1,8 | 1,85 |  |  | L35 | 1,806 | 1,806 | 0,0 | 0,1 | 1,8025 | 1,8025 | 0,0 | 0,15 | -3,5
MGTAUXR | 1,75 | 1,8 | 1,85 |  |  | L17 | 1,8053 | 1,8053 | 0,0 | 0,13 | 1,8014 | 1,8014 | 0,0 | 0,2 | -3,9
2V5 | 2,375 | 2,5 | 2,625 | 453 | 2,494 | Y15 |  | 2,4929 |  |  |  | 2,4926 |  |  | -0,3
3V3 |  | 3,3 |  | 316 | 3,315 | Y14 |  | 3,3319 |  |  |  | 3,3312 |  |  | -0,7

## Slide 22: DCDC converter output noise measurements
RU_DCDC
US configured
Diff amp.
Lecroy
DA1855A
100MHz
Vout (J1x)
GND (Jx)
Scope
Keysight
DSO-x 3014
High-res
Spectrum analyser
R&S FSL06
x corresponds to DCDC regulator 0...6

## Slide 23: Scope measurement 2V5
Vavg=2,4467V, AC_RMS=1,63mV, fRIPPLE=724kHz

## Slide 24: Spectrum analyser measurement 2V5 (fFUNDAMENTEL=293 kHz)

## Slide 25: Scope measurement 1V8
AC_RMS=1,05mV, fRIPPLE=450kHz

## Slide 26: Spectrum analyser measurement 1V8 (fDOMINANT=470 KhZ)

## Slide 27: Power Rail noise Measurement summary
X | Rail | Scope VAVG | Scope AC-RMS | Scope pk-pk | Scope fRIPPLE (kHz) | SA-freq Dominant (kHz) | SA-dBm Dominant | US requirement
0 | VCCINT | 0,948 | 0,97 | 7,7 | 245 | 246 | -58 | 
1 | VMGT | 1,00 | 1,19 | 9,5 | 245 | 246 | -58 | <10mVpp
2 | 1V2 | 1,199 | 1,07 | 8,6 | 290 | 292 | -63 | <10mVpp
6 | 1V5 | 1,51 | 1,34 | 12,5 | 245 | 246 290 | -60 -57 | 
3 | 1V8 | 1,78 | 1,05 | 8,9 | 450 | 470 | -64 | <10mVpp
5 | 2V5 | 2,46 | 1,63 | 11,5 | 790 | 470 723 | -46 -60 | 
4 | 3V3 | 3,29 | 0,84 | 7,5 | 290 | 292 | -71 | 
Actual noise/ripple likely lower due to probe pick-up
Noise below (<10mV) the US requirements

## Slide 28: Scope measurement MGT_AVCC_R
Vavg=0,98V, AC_RMS=0,71mV, fRIPPLE=249 kHz

## Slide 29: Spectrum analyser measurement MGT_AVCC_R (f=245kHz, 99 kHz)

## Slide 30: Scope measurement VMGT_AUX_R
AC_RMS=1,4mV, fRIPPLE=33kHz

## Slide 31: Spectrum analyser measurement VMGT_AUX_R

## Slide 32: Noise on US sensitive rail. Measurement summary
Rail | Scope VAVG | Scope AC-RMS | Scope pk-pk | Scope fRIPPLE (kHz) | SA-freq Dominant (kHz) | SA-dBm Dominant
MGTAVCC_L | 1,00 | 0,69 | 5,8 | X | 99 | -68
MGTAVCC_R | 0,98 | 0,71 | 5,6 | 248 | 99 245 | -68 -68
MGTAVTT_L | 1,18 | 0,67 | 5,34 | X | 99 | -68
MGTAVTT_R | 1,18 | 0,73 | 5,7 | X | 99 | -68
MGTVCCAUX_L | 1,76 | 1,4 | 8 | 33 | 33 | -66
MGTVCCAUX_R | 1,76 | 1,4 | 8 | 33 | 33 | -67
Actual noise/ripple likely lower due to probe pick-up
UG576 table 5-9: noise <10mVpp
All noise/ripple within limits

## Slide 33: Power-on sequence

## Slide 38: Voltages & currents after Xilinx US configuration: Vin and VINT

## Slide 39: Zoomed: IINT_step=0,65A in 100us, Spike VINT=20mV

## Slide 40: 2V5 & VMGT: IMGT_step=613mA in 100us, Spike VINT=30mV

## Slide 41: 1V2 & 1V8

## Slide 42: 1V5 & 3V3

## Slide 43: Summary Xilinx US power on
US | Empty mA | Loaded mA | Estimated Max | I step mA | V spike mV
VINT | 1000 | 1650 | 4200 | 650 | 20
VMGT | 381 | 994 | 2300 | 613 | 30
1V2 | 380 | 800 | 2600 | 420 | 20
1V5 | 2210 | 2210 | 3400 | 0 | 0
1V8 | 471 | 978 | 1600 | 507 | 20
2V5 | 910 | 910 | 900 | 0 | 0
3V3 | 379 | 532 | 500 | 153 | 15
Vspike increase with Istep
Vspike in acceptable range
Actual currents much lower than Estimated max crrents

## Slide 44: Replacement current sense amplifier due to offest error
Next sheet shows an analysis of the input offset of the AD626 current sense amplifier used with RUv1_0. Due to the single supply operation, the offset is relative large resulting is errors up to 50%.
Subsequent sheets gives an overview of the radiation tested alternatives. It was decided to move to the partly pin-compatible AD8418.

## Slide 46: Current sense amplifier offset
Measurements (and datasheet) indicate AD626 current sense amplifier has input offset of +2,4mV when operated in single supply mode.
Datasheets: Input offset increases 10 times in single supply mode
Therefore AD626 indicate too high currents (yielding in ƞDCDC=101%)
Actual/proper currents indicates ƞDCDC=81%
Typical sense resistors drop = 5...10mV =>Structural error up to 50%
What accuracy is required? => Gianluca: 5% is desired: Solutions:
Correction in calculation
Increase Sense resistor => power increase (100mW)
Change Amplifier.
 | V | I (AD626) | P=V*I(AD626) | Vsense | Rsense | I | P | Vsense | Voffset
Vin with 12V FAN | 12 | 1,21 | 14,52 | mV | mΩ | A | W | mv | mV
Vin without FAN | 12 | 1,07 | 12,84 | keithly |  |  |  | AD626 | AD626
VINT | 0,958 | 1,85 | 1,77 | 7,1 | 5 | 1,42 | 1,36 | 9,25 | 2,15
VMGT | 1,01 | 1,015 | 1,03 | 7,65 | 10 | 0,77 | 0,77 | 10,15 | 2,50
1V2 | 1,21 | 0,81 | 0,98 | 5,48 | 10 | 0,55 | 0,66 | 8,10 | 2,62
1V5 | 1,52 | 2,12 | 3,22 | 8,22 | 5 | 1,64 | 2,50 | 10,60 | 2,38
1V8 | 1,806 | 1,06 | 1,91 | 8,3 | 10 | 0,83 | 1,50 | 10,60 | 2,30
2V5 | 2,49 | 0,913 | 2,27 | 15,9 | 20 | 0,80 | 1,98 | 18,26 | 2,36
3V3 | 3,33 | 0,539 | 1,79 | 24,5 | 50 | 0,49 | 1,63 | 26,95 | 2,45
Total DCDC |  |  | 12,98 |  |  |  | 10,41 |  | 2,39
ƞ |  |  | 1,01 |  |  |  | 0,81 |  | 0,14

## Slide 47: Current sense amplifier alternatives
TID tested current sense amplifiers:
MAX4199 => Too little gain
INAxxxx => cannot operate on 3,3V
So only MAX4372 & AD8418 remain as alternative for AD626AR
AD8418 nearly pincompatible allowing replacement without change PCB
Power collumn involves all 7 sense amps. including dissipation in sense resistors
Test with AD8418 on 1V2 rail (Rsense=5mΩ) :
Vsense=5,5mV,
VO_AD8418=0,1085V =>error=0,5%
 | Vsupply | Iquies. (μA) |  | CM | Gain | Voff (mV) |  |  | Vo_min | Drive | Package |  | TID | Power | Error | 
 |  | typ | Max |  |  | Typ | Max | Trange |  |  |  |  | krad | mW | 25°C | -40...85
MAX4372 | 2,7...28 | 30 | 60 | 0..28V | 20,50, 100 | 300 | ±800 | ±1100 | 0,065 | 1,5Ω | Sot23 | Tullio | 30 | 180 | 1,5% | 5%
MAX4199 | 2,7...7,5 | 42 |  | 0..VCC-1,1 | 10 | ±15 | ±400 | ±600 | 0,1 | 5kΩ | SO8 | Leo | 30 |  |  | 
AD8418 | 2,7...5 | 1300 @3V3 | 2600 | -2..+70V | 20 | ±200 |  | ±400 | 0,015 | 2Ω | SOIC MSOP |  |  | 411 213 | 0,5% 1% | 0,9% 2%
AD626AR | 2,4...10 | 230 | 290 | -2.. 6*(V-1) | 10..100 | 1900 | 2500 | 2900 | 0,030 |  | SOIC |  |  | 120 | 17% | 26%
INA146 | 4,5...36 | 570 | 700 | ..40V |  | 3000 | 10000 |  |  |  |  | RadWg | >24 |  |  | 
INA111 | ±6.. ±18 |  |  |  |  |  |  |  |  |  |  |  | >40 |  |  | 
INA141 | ±2,25.. 18 |  |  |  |  |  |  |  |  |  |  |  | <13 |  |  | 
INA2128 | ±2,25.. 18 |  |  |  |  |  |  |  |  |  |  |  | <2,5 |  |  | 

## Slide 48: Clock generation/cleaner/distribition measurements
Frequency (160.316 MHz) and phase noise of the IQD IQXO-661 oscillator (218 fs) and CDCLVD1212 clock buffer (183 fs) are well within spec.
Also the SI5316 jitter cleaner shows the expected behaviour depending and on its loopback filter settings.

## Slide 49: X1 & X2: 2,5V LVDS crystal clock oscillator
IQD IQXO-661 LFSPXO076300Bulk
Specified freqency: 160,31588 MHz ±50ppm
160.307.864… 160.323.896
Measured frequency: =>Ok (within spec)
X2: FAN off: 160,31526 MHz (R&S PNA, -3,9 ppm)
X1: FAN off: 160,31530 MHz (R&S PNA, -3,6 ppm)
X1: FAN off: 160,31570 MHz (Fluke PM6669, -1,1 ppm)
X1: Fan on: 160,31610 MHz (Fluke PM6669 +1,4ppm)
X1: Fan on: 160,316111 MHz (R&S FSL06, +1,4ppm)
Output voltage: 247mV min, 330mV typ, 454mV max
Measured (TDS6604 & P7360) X1: 350 mV => OK
Measured (TDS6604 & P7360) X2: 410 mV => OK
Specified phase jitter (12kHz to 20 MHz): 1 ps rms max
Measured phase jitter (12kHz to 20 MHz): 0,218 ps => OK

## Slide 50: X2 crystal clock oscillator phase noise analyser output

## Slide 51: U17: CDCLVD1212 2,5V LVDS 2:12 buffer
Output voltage: 250mV min, 450mV max
Measured (TDS6604 & P7380) J19/J20: 330 mV => OK
Specified additional phase jitter (10kHz to 20 MHz) for 100MHz clock: 171 fs rms nominal
Measured Buffer + X1: 284,7 fs
Additional phase jitter = √(284,72-2182)=183 fs
(close to nominal value, slightly above possibly due to 2,5V PS rail ripply/noise.)

## Slide 52: X1 + CDCLVD1212 phase noise analyser output

## Slide 53: Spectrum analyser measurement 2V5 rail (fDOMINANT=293kHz & 724kHz)

## Slide 54: U17: SI5316 jitter cleaner output levels
SFOUT[1:0] | Specified | Min | Typ | Max | Measured
HM | LVDS | 500 | 700 | 900 | 644
ML | Low swing LVDS | 350 | 425 | 500 | 425
HL | CML | 350 | 425 | 500 | 425
MH | LVPECL | 1100 |  | 1900 | 1440
AFG3252 acts as differential output generator to SI5316 in (J14/J15)
SI5316 out (J16/J17, R209&210 removed) to P7380 diff probe.

## Slide 55: SI5316 out: Input: AFG3252 generator AM modulated with 50 kHz sinus

## Slide 56: SI5316 PLL loopfilter bandwidth at 6,7 kHz
Chart: 
| 1 | 2 | 5 | 10 | 20 | 40 | 50
20logJitterOut/In | -1.65 | -1.95 | -3.35 | -7.4 | -15.5 | -27.35 | -31.75
AFG3252: 160MHz, off=0,6V, amp=1V, MOD=AM sinus, Depth=50%
SI5316: Bandwidth[1:0]=ML=7KHz
kHz | Cleaner disabled |  | Cleaner enabled |  | 20logJitter Out/In
1 | -58,3 | -58,3 | -59,9 | -60 | -1,7
2 | -62,1 | -61,8 | -63,7 | -64,1 | -2,0
5 | -60 | -60 | -63,4 | -63,3 | -3,3
10 | -62,5 | -62 | -69,9 | -69,4 | -7,4
20 | -61,4 | -61,6 | -77,3 | -76,7 | -15,5
40 | -60,8 | -60,5 | -88 | -88 | -27,4
50 | -60,2 | -60,4 | -91,7 | -92,4 | -31,8

## Slide 57: SI5316 with different loopfilters. Source AM noise modulated