## Slide 1: Firmware Overview
J. Schambach

## Slide 2: Readout Unit Connectivity

## Slide 3: Readout Unit Firmware Purpose
Power Unit (PU)
Data @ 3.2 Gb/s
Trigger
GBTx
GBTx
GBTx
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
3.2 Gb/s
SRAM
FPGA
FLASH
FPGA
Programmable Logic
FLASH
Memory
SCA
Optical transceiver
VTRx
Optical transceiver
VTRx
Optical transceiver
VTTx
Data @ 3.2 Gb/s
Data @ 3.2 Gb/s
Control
FLASH
Memory
Readout Unit
Clock (40MHz)
Control (80 Mb/s)
Data: 9 x 960 Mb/s
or 16/28 x 320 Mb/s
Main Tasks of the Readout Unit:
Receive triggers (heartbeat & physics) from CTP & decode
Receive “control” information from CRU
Deliver triggers to stave sensors
Control, configure and monitor stave sensors
Receive data from stave; decode & compress
Deliver monitoring information to CRU (forwarded to DCS)
Deliver CRU framed data packets to CRU
Determine and handle busy information
Monitor and control Power Board
Handle radiation upsets in programmable logic (& sensors)
GBT Links
Copper Links
From/To ITS
From/To CRU
Power Board

## Slide 4: Flash FPGA

## Slide 5: Flash FPGA: Configuration and Scrubbing
Details in
“System scrubbing & re-programming” talk

## Slide 6: ProAsic3 Firmware
Components w/ TMR

## Slide 7: SRAM FPGA

## Slide 8: Readout Firmware Overview

## Slide 9: Firmware modules - Status
Control Interface (Wishbone bus)
  Implemented and tested (lab, test beams)
  Sending and receiving control words over USB and GBT
Power Board Interface
  Implemented and tested for all 4 I2C busses
  Controls sensor power, read status, currents, and voltages
Alpide Control
  Implemented and tested for all 5 FireFly connectors
  Handles configuration and triggers to sensors
Data Readout and Packaging
  2 Flavors: Inner Barrel (MGT transceivers), Outer Barrel (GPIO fabric logic)
  Implemented and tested for MGT (lab, test beams)
  Outer Barrel path under development (only receiving logic different)
  Receives data from sensors, deserialization, idle removal
  Add CRU protocol and Trigger info
  Send data packets over GBT
  Some features still missing (OB sensor data packaging, sparsification)
GBTx Communication
  Implemented and tested (lab, test beams)
  Use only single GBT link for now for trigger, control, and data
  Full access to Wishbone via CRU protocol
Trigger Handler
  Proof of principle implemented and tested
  Needs additional work (pipelining, additional triggers, …)
Radiation Monitor
  Implemented and tested
  SEU observation
System Monitor
  Implemented and tested
  Read voltages, temperatures
USB interface to wishbone
  Implemented and tested
  Used for tabletop tests, lab setups
FIFO interface to PA3
  Implemented and tested
  Used for fast firmware update of flash
  Can be used from GBT (via CRU control protocol)
Datapath Monitor
  Implemented to monitor protocol, gbtx
Error/Busy Handling
  Still missing

## Slide 10: Radiation Protection: Triple Modular Redundancy
TMR completed
To be TMR’ed
No TMR planned
TMR Status

## Slide 11: Alpide Data Path Details

## Slide 12: Data Flow

## Slide 13: Inner Barrel Data Format
Legend:
C<n>W<m>: Cable <n>, Word <m>
Cx_Id: FIFO identifier (1-9, 5bit)
SOP: CRU Start-of-Packet
EOP: CRU End-of-Packet
BC: Bunch Crossing ID (12bit)
Data out of the Alpide Readout firmware module in the inner barrel mode arrives with a rate of 8 bits every 120MHz clock period. Nine 8-bit data words from one cable are combined with an ID for the FIFO they originate from into an 80 bit GBT word as shown here. A round-robin MUX collects data from each of the nine cables. Finally, the data is framed with the appropriate CRU protocol words, and trigger and status information is added to complete a CRU data packet.
Header

## Slide 14: Outer Barrel Data Format
Legend:
C<n>W<m>: Cable <n>, Word <m>
Cx_Id: FIFO identifier (1-28, 5bit)
SOP: CRU Start-of-Packet
EOP: CRU End-of-Packet
BC: Bunch Crossing ID (12bit)
For the outer barrel mode, the same principle on the previous slide applies, but with modified rates and number of fragments combined into a GBT word.
Header

## Slide 15: Continuous Readout
HB = Heart Beat Trigger
HBF = Heart Beat Frame
Strobe<x> = Trigger strobe to sensor with trigger time = BC+Orbit at time<x>
BCID<x> = BC ID (part of SDH) (with BC+Orbit) at time<x> after HB
Data = Sensor Pixel addresses
SOP = “Start Of Packet” (CRU protocol)
EOP = “End Of Packet” (CRU protocol)
“Continuous” readout in ITS is accomplished by using “long” (10’s of µ-seconds) strobe lengths (firmware triggered) with short (10’s of nano-seconds) inter-strobe periods to initiate readout. ITS RU firmware therefore divides a “Heartbeat Frame” into several “Strobe” frames with fixed strobe lengths, synchronized to the received heartbeat triggers.
Heart Beat Triggers come every 89.4 µs, so trigger strobes (“frames”) in this example would be approximately 89.4 / 4 = 22.3 µs long and each Heart Beat Frame (HBF) would thus contain 4 packets from the RU. This parameter is programmable and could be adjusted, e.g. to 89.4/8 to have 8 “sub-frames” in each HBF
Data will appear from the sensor some tens of ns after the end of the strobe signal, and some 40MHz clock cycles later on the GBT links. Data contained in each packet corresponds to all physical signals (“events”) between times tx and tx+1. The packets might also contain the busy status for individual sensors of an RU, which could then be used to determine the need for throttling at the CTP.
Although data packets are shown here contiguous, it is possible that “DATA” GBT words are interspersed with “IDLE” or “SWT” (for DCS data) during data transmission to the CRU. Since there is the possibility of SEUs in the RUs’ FPGAs, there will be a “timeout provision” in the CRU protocol to determine if a packet is corrupted/incomplete/missing.

## Slide 16: CRU Data
FID
3
Time
RU 1
RU 2
RU 8
…
…
8 Readout Units
(up to 3 fibers each)
FID
0
FID
1
FID
2
FID
3
FID
0
FID
0
FID
1
FID
2
FID
0
FID
0
FID
1
FID
2
FID
0
HB1
HB2
FID
3
Need to be combined into 1 Heart Beat Frame (HBF) in FLP
DMA to FLP memory

## Slide 17: Data Hierarchy
Cable 1
Cable 9
RU
…
Cable 1
Cable 16
RU
…
Cable 1
Cable 28
RU
…
RU
....
CRU/FLP
CRU/FLP
.......
EPN
......
....
IB
MB
OB
9
16
28
8
....
8
192
24 (12 FLP?)
8

## Slide 18: Data Format: GBT to CRU to FLP
GBT RDH
CRU memory
FLP memory
79…………………….……………….……….…………0
127……………………………………………………………………...…63………..……………………………………………………………...…0
0x00
0x04
0x08
0x0C
0x10

## Slide 19: Utilization Report
Site Type | Used | Available | Util %
CLB | 6038 | 41460 | 14.56
CLBL | 3062 |  | 
CLBM | 2976 |  | 
LUT as Logic | 23100 | 331680 | 6.96
using O5 output only | 466 |  | 
using O6 output only | 19961 |  | 
using O5 and O6 | 2673 |  | 
LUT as Memory | 0 | 146880 | 0.00
LUT Flip Flop Pairs | 6970 | 331680 | 2.10
fully used LUT-FF pairs | 855 |  | 
LUT-FF pairs with one unused LUT output | 5736 |  | 
LUT-FF pairs with one unissued Flip Flop | 5160 |  | 
Unique Control Sets | 931 |  | 
CLB Registers | 26374 | 663360 | 3.98
CARRY8 | 757 | 41460 | 1.83
F7 Muxes | 702 | 165840 | 0.42
F8 Muxes | 287 | 82920 | 0.35
F9 Muxes | 0 | 41460 | 0.00
Site Type | Used | Available | Util %
Block RAM Tile | 146 | 1080 | 13.52
RAM36/FIFO | 134 | 1080 | 12.41
RAMB36E2 only | 134 |  | 
RAM18 | 24 | 2160 | 1.11
RAMB18E2 only | 24 |  | 
CLB Logic
BLOCKRAM