## Slide 1: MVTX Stave Production Readiness
Ming Liu
LANL
10/12/2018
sPHENIX PMG Meeting

## Slide 2: MVTX Detector
MVTX RUs, PUs & other services
3-layer sensor barrel
- 48 staves, 432 chips
Service cone: signal, power, cooling
and mechanical support
Figure for ALICE ITS/IB design
(slightly modified mechanically for sPHENIX)
MVTX
parameters
End-Wheel
CYSS: Cylindrical Shell Structure

## Slide 3: INTT-MVTX Conflict: a Resolution
INTT 4-layers
The INTT shown only includes ladders; no extension cables, connectors, cooling barbs, etc.
Original design for the ALICE ITS inner tracker; three layers of MAPS type detectors
Interconnect patch-panels
ALICE IB Patch-Panel 3-D Model
- All connectors are located
at the same Z position
- One can move some connectors
out in Z to reduce “R”
- Longer power cables!
- HS FPC untouched!
Layers: 1, 2, 3

## Slide 4
ALICE IB Stave
Flexible Printed Circuit (FPC) for
9 HS Signals, CLK, CTRL
Flexible power extension PCB
DVDD, AVDD and Bias V.
Soldered to FPC
- To be modified for sPHENIX
9 sensors

## Slide 5: IB FPC Layout
506.2 mm
16 mm
41.9 mm
16.15 mm
CHIP 1
CHIP 2
CHIP 3
CHIP 4
CHIP 5
CHIP 6
CHIP 7
CHIP 8
CHIP 9
AVDD
DVDD
75 µm UPILEX
25 µm ALUMINUM
25 µm ALUMINUM
4.1 mm
5.5 mm
20 µm COVERLAY
20 µm COVERLAY
The 9 silicon chips are read out in parallel: each chip sends its data stream to the end of Stave by a dedicated differential pair, 100 mm wide. Two additional differential pairs distribute the clock and configuration signals.
Large planes are used to distribute analogue and digital power and respective ground connections.
DGND
11.15 mm
AGND
4.1 mm
90 µm Glue
50 µm Silicon chip
300 µm
850 µm
p
subs
165 µm
From Antonello Di Mauro

## Slide 6: FPC Extension for Connection to Electrical Services
FPC
DVDD
AGND
DGND
DVDD
DGND
DVDD
AVDD
AVDD
AVDD
AGND
AGND
DGND
The connection to the service cables is achieved by a double FPC extension which is soldered to the HIC
x-section at interconnection between FPC and extensions
signal lines (FPC)
analogue power
digital power
FPC
AVDD
AGND
AVDD
AGND
AGND
AVDD
Flex power extension
FPC
DVDD
DGND
DVDD
DVDD
DGND
DGND
Flex power extension
From Antonello Di Mauro
Modified for sPHENIX:
15cm -> 40cm

## Slide 7
2-layer flex, PI: 50 µm, Cu: 35 µm, solder mask: 20 µm
The two flexes are connected together, AVDD is transferred from top to bottom
The PWR extension is connected to the FPC by iron soldering and wings are cut.
FPC Extension for Connection to Electrical Services
digital
analogue
analogue
digital
digital
AVDD
DVDD
DGND
AGND
From Antonello Di Mauro
Longer copper traces ~30cm
for sPHENIX, no other components
Unchanged

## Slide 8: Two HICs Produced and Tested at CERN w/ Extended Power Cables NO noticeable difference in sensor performance, as expected
MVTX: 40cm flex power PCB
MVTX: 60cm flex power PCB
ALICE IB: 15cm

## Slide 9: Test Stave/HIC with extended power PCB
Built and tested two HICs at CERN in the week of 9/17
  No change in sensor performance (noise, threshold) observed, as expected;
More details presented by Dr. Sho Uemura at last Friday’s sPHENIX general meeting 9/23/2018
60cm PWR FPC
40cm PWR FPC
ALICE: 15cm PWR FPC
Followed identical
ALICE IB QA test procedure,
with a 8m SamTec cable!

## Slide 10: HICs Test Results from CERN
Before: 2 ALICE IB HICs
After: same ALICE HICs, replaced power FPCs
Noise level: ~4 e’s; Threshold: ~180e’s; MIP: ~1000 e’s
Chip-0
Chip-8
HIC1
HIC2
Noise
Noise
Thr.
Thr.

## Slide 11: MVTX middle layer – power extension cable assembly including the reduced ID & OD patch-panel
From Walt Sondheim

## Slide 12
15cm Flex PCB (ALICE): $61/pair
Power PCB cost: Unit price ~ Cable length
40cm Flex PCB (MVTX): $123/pair
Components: ~$40/pair
Assembly: ~$2K

## Slide 13: Latest CAD model patch panels;
From Walt Sondheim
HS signal cable and connector
Extended 40cm
DVDD Flex PCB
Extended 38cm
AVDD Flex PCB

## Slide 14: Summary: Modifications of the Power Extension PCB w.r.t. ALICE IB Design
What to be modified:
  Extend the Flex Power PCB length from 15cm(ALICE) to 40cm(sPHENIX)
  Keep all noise filtering capacitors at current locations, just extend the passive copper traces.
Risks and impacts
  40cm Power extension PCB production
    OK, industry standard
    Extra cost on materials ($61/pair vs $123/pair, 84+ pairs, total cost <$20K)
  Stave assembly (need more inputs from ALICE)
    Wire bonding machine operation clearance?
      Solder power PCB after the wire bonding to make a HIC?
    Jigs modified to hold the longer flex power PCB?
    Extra cost?
  Shipping and storage
    Longer support Al-plate required for shipping and handling
    Extra cost, on-going discussion between ALICE and LBNL on modification and fabrication
  Technical risks: minimal
BNL Director’s Review: July 19-20, 2018

## Slide 15: Sensor Irradiation Test
BNL Director’s Review: July 19-20, 2018
Recently (in 9/2018) ALICE carried out irradiation test up to 2.7MRad:
Sensor can still function well with high efficiency and low noise

## Slide 16: Sensor Radiation Hardness – OK at 2.7MRad
Continuous effort by ALICE (@NPI, Czech)
BNL review recommendation: test sensor up to 1MRad
https://indico.cern.ch/event/758048/
MVTX Operation Window

## Slide 17: sPHENIX MVTX Max. Hit and Noise Rates
From MVTX proposal
sPHENIX MVTX targeted noise level: <10-5
Very conservative estimate

## Slide 18: Expected B-field in the Rack Area (RU, PU Electronics)
Low fringe field, < 50Gauss outside of HCal
ALICE RU and PU designed to operate in 0.5T field
Rack. B < 50G
Thanks John H.
for the plot
Simulation:
Steel 1020

## Slide 19: SamTec Cables Tested and Finalized for ITS: ~8m!
Two cables per IB stave: 2.65m + 5.30m
PP2
HDR-203194 (Type B)
HDR-206142 (Type A)
Staves
RUs
L: 2650 mm
L: 5300 mm

## Slide 20
Type-A
Type-B
Type-A

## Slide 21: Summary:
Technically sPHENIX/MVTX staves are ready for production
Cost being updated

## Slide 22: Backup slides

## Slide 23: sPHENIX/MVTX IB Stave Assembly Procedure (to be confirmed/optimized by ALICE)
Prepare sensors and FPC
Glue 9 sensors to FPC
Wire bonding 9 sensors to FPC
Solder power flex PCB to FPC
  (or do #3 wire bonding after soldering power flex PCB?)
Glue HIC to coldplate/carbon space frame
A stave is ready for QA

## Slide 25
From Antonello Di Mauro

## Slide 26
From Antonello Di Mauro

## Slide 27
Miko
Sho
Alex
Sho
Ming
Felix
Corrado
Actions @CERN
Many thanks to CERN colleagues!
Many are not shown here!
Antoine
Antonello