## Slide 1: MVTX Status
Ming Liu
sPHENIX L2 Meeting
02/06/2020

## Slide 2: Progress and Status
Final Design Review 1/29/2020 at BNL
  Reviewed:
    Carbon structure design, test production and vendor selection
    Installation & insertion
    Power system production
    Cooling plate production
  Received positive report (Draft)
    Follow up discussions among MVTX groups, carbon structure production in March 2020
Stave production at CERN
  Next meeting, ~Feb. 13
  On-going discussion about stave cooling tube replacement
  Stave import paperwork in progress, LBNL/UTK/BNL
MVTX project fund being distributed
  LANL, LBNL, MIT, UT-Austin

## Slide 3: MVTX Stave Cooling Tube Extension Proposal, 02/04/2020
- The pre-built stave cooling tubes are 5~10cm short to fit the current MVTX service support design.
We propose to replace all the cooling tubing with 70cm ones (currently ~55cm)
CERN requests EU$10K to replace ~100 carbon frames
55cm tubes
(from ITS/IB design)
Proposed 70cm tubes
for MVTX
MVTX Stave on a transport plate
Signal connection
power connection
Cooling tubes

## Slide 4: “Full Readout Chain” MVTX 8-stave Telescope Test Beam Run Planned: April – May at Fermilab
A complete readout chain 8-stave telescope of the MVTX detector
  8-stave + 8-RU + 1-FELIX + 1GTM (mGTM?)
  MVTX = 6 x (8-stave telescope)
  RU firmware/software “synced” to a ITS recent version v0.5(11/2019),
  FELIX firmware update next;
A new (derived from GTM) mGTM for MVTX to be developed by BNL
  Provides 2x40.08MHz clock (synced to RHIC) for all FELIX/RU/ALPIDE
    Same hardware, different firmware
  All GTM mode-bit and header information available
  Important for offline event alignment and cross check
  JohnH, JoeM, JohnK, Ming at BNL, with Alex, Gerd, Yasser (remotely)