## Slide 1: SamTec Cable Test & ALPIDE Driver Evaluation
Alex, Ming

## Slide 2
System Setup
w/ MOSAIC
Chip-0
Chip-8
9-chip IB HIC

## Slide 3
Running condition:
-1m SamTec Cable
Default ALPIDE setting
Chip0 signals
Vp-p = 1157 mV
Good signal

## Slide 4
Chip-8 (furthest chip?)
-1m SamTec Cable
Default ALPIDE setting
Vp-p = 934 mV

## Slide 5
5-m cable:
Can’t see chip-0,
only 4 working chips:
Chip-8 used for evaluation
Vp-p = 679 mV
Weaker signal

## Slide 6: 7m and 10m cables
Can’t see signal
No chip found under “test_fifo”.
Under investigation

## Slide 7: 1-m cable test, different Driver Strength
DTUDriver [4-bit]: 0 -15
DTUPreEMP [4-bit]: 0-15
I (mA) | DTUDriver | DUTPreEMP | Chip-0 Vp-p (V)
825 | 15 | 15 | 1.1
815 | 15 | 1 | 0.98
796 | 1 | 15 | 0.69
780 | 1 | 1 | No signal

## Slide 8: Driver = 15 & PreEMP = 15, Chip0
5 enabled chips
Check outputs from
chip0 and chip-8

## Slide 9: Driver = 15 & PreEMP = 1, Chip0

## Slide 10: Driver = 1 & PreEMP = 15, Chip0

## Slide 11: Driver = 1 & PreEMP = 1, Chip0