## Slide 1
sPHENIX LDRD Review
UNCLASSIFIED
Xuan Li
P-25
ALPIDE Introduction and Test Stand
Outline
ALPIDE chip introduction
LDRD test bench setup
Test bench achievements
Plans

## Slide 2
The MVTX Basic Unit: ALPIDE chip
ALPIDE chip Introduction:
The 3 layer MVTX consists of 48 staves and each stave contains 9 ALIPDE chips.
Stave
ALPIDE chip scheme
3cm
1.5cm

## Slide 3
Test bench Components
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5 m
Optical Links
9 Sensor Stave
RCDAQ
Purchased one stave and 5 individual ALPIDE chips.
Test bench
readout module:
MOSAIC
Purchased 1 Power Board

## Slide 4
Power Board Integration Test
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5 m
Optical Links
9 Sensor Stave
RCDAQ
Successful integration of Power Board + ALPIDE chip + MOSAIC!

## Slide 5: ALIPIDE Chip Evaluation Test Configuration
Test in triggered mode with default delay at 2μs:
  Internal trigger with pulse generator (rate:2MHz).
  External trigger with cosmic ray muons (rate: ~0.1HZ).
  External trigger with 90Sr beta decayed electrons (rate: ~1Hz).
Scintillator 1
5mm
Scintillator 2
5mm
5mm
3cm
MAPS chip
e-
Sr90
Scintillator 1
5mm
Scintillator 2
5mm
MAPS chip
μ-
90Sr setup
Cosmic ray setup

## Slide 6: Achievements: Bad Channel
Internal trigger configuration with pulse generator:
  Scanned available chips and stave at LANL through digital scan to verify the dead channel fraction: the bad channel fraction is <1%.
  Similar results with different readout speed.
No. of 0 hits
777
Cold channel
1
Hot channel
0
Bad fraction
0.15%
ALPIDE chip test example

## Slide 7: Achievements: Signal/Noise
Analog charge
Erf function fit: Threshold is at the 50% point.
Threshold and Noise scan per chip
Threshold/Noise ratio scan
1
2
3
4
5
6
7
8
0
Data
Power
control
Active chips on stave
MIP~1000 e-
Internal trigger configuration with pulse generator:
  Scanned available chips and stave at LANL through threshold scan: signal/noise based on charge injection study is around 60. Comparable with CERN test.

## Slide 8: Achievements: Timing in External Trigger
90Sr beta decayed electron with energy <2MeV.
Trigger rate: 1Hz. One cluster per triggered event.
Collimator
ALPIDE chip
Row 0
Row 511
Collimator
90Sr source
ALPIDE
chip
Scintillators
Pixel hit 2D map
Profile along column
Profile along column
Clear collimator structure seen in the ALPIDE chip.

## Slide 9: Achievements: cluster size
Cluster size determined from 90Sr beta decayed electrons.
The average cluster size determined from 90Sr source is comparable with cosmic ray test.
Scintillator 1
Scintillator 2
MAPS chip
μ-
Initial look of tracking with two layers of ALPIDE chips.
Clear cosmic ray muon track found.
Test stands
Event Display

## Slide 10: Under study: Trigger delay latency
Whether the MVTX can adapt the sPHENIX trigger scheme with default trigger delay at 4.5 μs?
Tune the threshold and take cosmic ray data within the same time periods.
The default trigger delay of the ALPIDE chip is 2μs.
Analog IN
Digital IN
Trigger
Trig Delay
Initial look with tuned threshold, no significant differences of performance for trigger delay from 2μs to 6μs.

## Slide 11: Plans
Set up the laser test bench to study the efficiency, noise rate, trigger delay time, optimize the gain, pulse shaping and etc.
Will purchase 10 more ALPIDE dices and build chips at LANL to build the telescope for the cosmic ray, source tests.
Study the ALPIDE performance with the RU+FELIX full readout chain.
X-Y scan table
Laser generator:
Duty cycle: < MHz
Focus area: < 10μm2
μ-
Telescope for cosmic and
source test
scintillator
ALPIDE
chip

## Slide 12: Backup
Cluster evaluation by the CERN team from 450 MeV e- beam test.
Cluster Size
Cluster Profile along X
Cluster Profile along Y
Even particle energies are different, similar results are achieved between the test bench studies with cosmic ray or 90Sr beta decayed electrons.