## Slide 1
sPHENIX LDRD Review
MVTX mechanical conceptual design
UNCLASSIFIED
Walter Sondheim
P-25

## Slide 2
Outline:
Main mechanical components:
  Stave
    Cabling pig-tail
  Half-barrel (3 layer) assembly
  Half-barrel outer shell, including service patch panel in conical region
  Service barrel
  Support cylinder
  sPHENIX CAD model
Integration to sPHENIX tracking system

## Slide 3
ALICE & MVTX tracker stave:
UNCLASSIFIED

## Slide 4
ALICE & MVTX stave structure:
UNCLASSIFIED
MVTX stave support/cold plate geometry:

## Slide 5
ALICE & MVTX stave cooling:
UNCLASSIFIED
Now < 41 mW/cm2
MXTX inner tracker stave cooling and support plate:
Full stave assembly mass 15.1 gms

## Slide 6
Tracker Stave Pigtail:
UNCLASSIFIED
Three layers: signal lines (FPC) 2X twisted pair, digital power, analog power

## Slide 7
Half Barrel Three Layer Assy:
UNCLASSIFIED
Both in the case of ALICE and sPHENIX, the silcon inner tracker is split in two halves since the beryllium beam-pipe will already be installed. The total mass of this assembly 2,200 gms

## Slide 8
Half Barrel Service Interconnect:
UNCLASSIFIED
Layer 0
Layer 1
Layer 2
Layer 0
Layer 1
Layer 2
Stave assy:
Pig-tail
Cooling: negative pressure water, plus dry air (nitrogen) flow
Total power: on detector 119.55 watts
power cables 34.0 watts

## Slide 9
Inner Barrel Assembly Steps:
UNCLASSIFIED

## Slide 10
ALICE Half Barrel Assembly:
UNCLASSIFIED
Stave fixed end
Radiation length of MVTX Assembly 0.3% X0/layer

## Slide 11
ALICE ITS Service Barrel:
UNCLASSIFIED

## Slide 12
MVTX Service Barrel:
UNCLASSIFIED
Overall length 2161.73 mm

## Slide 13
MVTX Service Barrel:
UNCLASSIFIED
Interface rollers to slots in support cylinder

## Slide 14
ALICE ITS Support Cylinder:
UNCLASSIFIED
In sPHENIX we will not use a “service cone, rail system” anywhere near the size of that planned for the ALICE detector (shown here), but we will use their concept.
Eccentric:
Adjustable roller +/- 1.0 mm, by steps of .25 mm
Rail guides for upper half assembly

## Slide 15
sPHENIX Tracking Detectors:
UNCLASSIFIED
sPHENIX TPC inner bore 400.0 mm

## Slide 16
sPHENIX Overall CAD Model:
UNCLASSIFIED

## Slide 17
sPHENIX CAD Model, Detectors:
UNCLASSIFIED
Outer Hcal
BABAR magnet coil
Inner Hcal
EM Cal
TPC
MVTX Service Cone

## Slide 18
sPHENIX INTT TPC CAD model:
UNCLASSIFIED
TPC
INTT
INTT extension cables
INTT readout electronics, FVTX ROC boards
TPC & INTT CAD model, section view
Cross-section view of INTT, four layers of silicon ladders
INTT updated CAD model, 4 layers silicon strip detectors with extension cables

## Slide 19
sPHENIX INTT, TPC, MVTX CAD model:
UNCLASSIFIED
INTT with 1.2 meter extension cables running out both ends of TPC to electronics
MVTX with 18.0 cm extension cables on staves, interconnect conical region and service barrel,
Needed to have adequate clearance from INTT ladders
sPHENIX beryllium beam-pipe
TPC support structure tied to the inner HCal

## Slide 20
sPHENIX Tracking detectors, detail:
UNCLASSIFIED
INTT stave length 480.0 mm
MVTX flex extension cable 180.0 mm
MVTX stave length 280.0 mm

## Slide 21
sPHENIX Tracking detector issues:
UNCLASSIFIED
The current design for the INTT detector does not have a support structure or additional services shown like cooling.
There is interference between the INTT extension cables and the conical region of the MVTX (“Z” locations)
  A possible solution would be locating the conical region of the MVTX at the “Z” location of the INTT readout-electronics disk, this would be an additional 1200.0 mm
Because of the different radial dimensions between the beam-pipe in ALICE and the beam-pipe in sPHENIX, eack of the three MVTX layers need to be moved outward in radius by .75 mm.
  This translation will still allow each layer to be hermetic
A meeting will take place at BNL to discus tracking detector integration issues on Friday January 26th.

## Slide 22
sPHENIX MAPS Detector:
UNCLASSIFIED