## Slide 1
sPHENIX LDRD Review
MVTX mechanical conceptual design
UNCLASSIFIED
Walter Sondheim
P-25

## Slide 2
sPHENIX experiment - MVTX Detector:
UNCLASSIFIED
Personnel involved:
Walter Sondheim, P-25,
  mechanical and integration engineering
Christopher O’Shaughnessy, P-25,
  mechanical engineer, physicist,
    Focusing on MVTX telescope and cooling
Hubert Van Hecke, P-25,
  Physicist,
    Prototype construction
David Lee, P-25,
  Physicist,
    “Project” file management
MVTX mechanical conceptual design:

## Slide 3
Outline:
MVTX mechanical components:
  Stave
    Cabling pig-tail
  Half-barrel (3 layer) assembly
  Service barrel
  Support cylinder

## Slide 4
MVTX tracker stave:
UNCLASSIFIED
Stave assembly consists of:
  One layer with 9 MAPS chips
  One thermally conductive carbon cold plate – space frame
  One carbon filament truss structure
  One flexible printed circuit (FPC) that is wire-bonded to the MAPS chips
  Bonded assembly

## Slide 5
MVTX stave cooling:
UNCLASSIFIED
MXTX inner tracker stave cooling and support plate:
Coolant: negative pressure single phase H2O
Pixel chip operational temperature < 300 C
Pixel chip max temperature non-uniformity < 50 C
Pixel chip (Alpide) power dissipation < 41 mW/cm2
Full length cold plate assembly 290 mm, mass 1.7 gms.
Full stave assembly, chips, FPC, cold plate mass 15.1 gms.
Total power dissipation: 184.5 mW/chip X 9 chips per stave X 48 staves in the MVTX assembly = 79.7 Watts

## Slide 6
MVTX stave radiation length:
UNCLASSIFIED

## Slide 7
Half Barrel Service Interconnect:
UNCLASSIFIED
Layer 0
Layer 1
Layer 2
Layer 0
Layer 1
Layer 2
Stave assy:
Pig-tail
Cooling: negative pressure water, plus dry air (nitrogen) flow
MVTX Services and Cabling and Cooling lines:
Carbon composite outer shell
Interconnect patch-panel:
Signal cables, AC & DC power,
Cooling
Prototype Pig-tail layers:
Signal - Firefly coax
AC
DC and bias

## Slide 8
Composite technology demonstrated:
UNCLASSIFIED
Carbon composite production pieces:
These composite prototype parts made at CERN, similar to ones needed for MVTX detector:

## Slide 9
MVTX layer assembly steps:
UNCLASSIFIED
MVTX layer assembly steps, using fixtures and dummy staves:
Using “dummy staves” to secure positioning
Replace “dummy staves” with production staves
Precision assembly fixture used to hold “end wheels” for placement of staves to required accuracy. Initial use of “dummy staves” maintains the overall required positioning.
Stave “pig-tails” mounted in patch panel

## Slide 10
sPHENIX MVTX Detector:
UNCLASSIFIED
MVTX cabling configuration:

## Slide 11
MVTX composite service barrel:
UNCLASSIFIED
Interface rollers mate to guide slots in support cylinder:
Overall length = 2161.73 mm
Radius = 319.2 mm

## Slide 12
Possible MVTX installation cylinder:
UNCLASSIFIED
In sPHENIX we will not use a “service cone, rail system” anywhere near the size of that planned for the ALICE detector (shown here), but we will integrate their concept.
Eccentric:
Adjustable roller +/- 1.0 mm, by steps of .25 mm
Rail guides for upper half assembly

## Slide 13
sPHENIX experiment CAD model:
7,000 mm
7,000 mm
5,200 mm
sPHENIX experimenter

## Slide 14
MILESTONE: MVTX mechanical system conceptual
design completed:
UNCLASSIFIED
INTT stave length 480.0 mm
MVTX flex extension cable 180.0 mm
MVTX stave length 280.0 mm
TPC
INTT extension cables, 1,200 mm length, to read-out boards

## Slide 15
Milestones & integration issues:
UNCLASSIFIED
Milestones continued:
  Modified model to be compatible with sPHENIX tracking detectors and beam-pipe, installation plan
The current design for the INTT detector does not have a support structure or additional services, power & cooling.
There is interference between the INTT extension cables and the conical region of the MVTX (“Z” locations)
Because of the different radial dimensions between the beam-pipe in ALICE and the beam-pipe in sPHENIX, each of the three MVTX layers needs to be moved outward in radius by .75 mm.
  This translation will still allow each layer to be hermetic
Continuation of integration issues will be taking place with all of the sPHENIX tracking detector systems: TPC, INTT & MVTX by the formation of a sPHENIX tracking integration task force.

## Slide 16
sPHENIX MAPS Detector:
UNCLASSIFIED
Back-up: