## Slide 2
Probing Quark-Gluon Plasma with Bottom Quark Jets
at sPHENIX
UNCLASSIFIED
Ming Liu (PI)
P-25
02/01/2018
Thanks for the strong support from LDRD Office and LANL Program Management

## Slide 3: The LDRD Team
Experimental group
  P-25, AOT
  Detector readout and mechanical support R&D
  Detector modeling and simulations
  Physics simulations
Theoretical group
  T-2, T-5, CCS-7
  Physics modeling & simulations
Budget: 1.6M/Year, FY17-19
  1/3 on experimental T&E
  1/3 on theoretical T&E
  1/3 on Hardware & M&S

## Slide 4: Outline
LDRD scientific goals
Project scope, status and plan
Mission impacts
Transition Plan
Telescope

## Slide 5
Quark-Gluon
Plasma (QGP)
Earliest stage of the universe that can be explored in detail in the laboratory

## Slide 6: QGP Discovery
Unambiguous evidence for phase transition from ordinary nuclear matter to QGP (TQGP~175 MeV, ~1012 degrees)
Fundamental discovery: QGP is not a weakly interacting gas of quarks and gluons, but rather a strongly coupled near-perfect liquid!
Exhibits strong collective behavior, has huge stopping power for color-charged particles (quarks, gluons – the fundamental constituents)
Big Question for Science: From what microscopic structure
do these properties emerge?Requires new observables!
QGP discovery announced in 2004 by RHIC experiments, confirmed later at LHC
PHENIX mission completed in 2016
Upgrade path – sPHENIX @RHIC

## Slide 8: LANL Proposed Monolithic-Active-Pixel-Sensor-based Vertex Detector (MVTX)
sPHENIX Inner Tracking
“Adopt” ALICE/ITS
Mini. risk,
Max. physics
sPHENIX upgrade @RHIC
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics

## Slide 9: sPHENIX Tracking System with MVTX
TPC
INTT
MVTX
Side view of the sPHENIX Tracking system with a conceptual design of MVTX mechanical system
Walt’s talk
TPC:
R = 20-80cm
INTT:
R =6,8,10,12cm
MVTX:
R=2.3, 3.2, 3.9cm
2m

## Slide 10: LDRD Scientific Goals
Develop a next generation QGP physics program with heavy quark jets at RHIC with full detector and physics simulation and modeling
Carry out key detector R&D to demonstrate the open heavy flavor physics capability in the sPHENIX with MVTX
Develop a proposal to DOE to build a state-of-the-art MAPS-based Vertex Detector for the sPHENIX
New theoretical study of QGP
tomography with b-jets
B-jet suppression in QGP
QGP characterization
sPHENIX MVTX Proposal

## Slide 11: New Physics Reach with MVTX
Heavy quarks – unique probe of QGP w/ new scales, mc, mb
  Study mass dependence
    Jet quenching & energy loss
    Flow – interaction with medium
  Access QGP properties
    Temperature, density, coupling, transport coefficients, viscosity etc.
Ivan and Darren’s talks
MeV
1
10
102
103
104
mu md
LQCD
TQGP
mc
mb
Tc
ms
“B meson and b-jet modification”
“B meson and b-jet flow”
“Money plots” from MVTX proposal

## Slide 12: LDRD Project Scope
Minimal scope
  Develop a MVTX prototype telescope with 4 ALPIDE sensors/staves with ALICE readout units, complete sPHENIX DAQ integration
  Complete R&D on mechanical conceptual design, sPHENIX system integration
  Develop b-jet tagging algorithms for p+p and Au+Au
  DOE MIE proposal submitted to fund the full detector construction
  Complete b-jet theory for precision tomography of QGP with sPHENIX
Desired scope
  Develop a full 4-production-staves MAPS telescope, test beam run with integrated sPHENIX DAQ
  DOE MIE proposal approved for the full detector construction
Established at the beginning of this project feasibility review 1/2017

## Slide 13: LDRD Timeline: Experiment
MOU with ALICE
B-tagging in p+p and Au+Au
BNL Director’s Review, recom’ed to proceed w/ full proposal
Talks by Darren, Xuan,
Alex, Sho, Walt, Cesar
On track to succeed!
Full readout chain demonstrated
Mechanical conceptual design
Collaboration formed and full MVTX proposal submitted
Milestones achieved
Today

## Slide 14: LDRD Scope: Theory
Ivan’s talk
Significant progress
  New calculations and new observables
  Met milestones, some ahead of time
Today

## Slide 15: ALICE Pixel Detector (ALPIDE)
ALPIDE highlights:
  Very fine pitch (28x28 μm)
  High hit efficiency (>99%) and low noise (<10-6)
  Fast response, ~5μS
  Ultra-thin/low mass, 50μm (~0.3% X0)
  On-pixel digitization, low power dissipation
  Sensor chip: 1.5cm x 3.0cm, 0.5M pixels (512x1024)
50 μm
28 μm
An ideal detector for QGP b-jet physics!
FPC
9 Chips
Cooling plate
A 9-chip stave
The 2nd generation state of the art MAPS technology

## Slide 16: LDRD Highlights (I) MVTX Sensors, Readout and Control System Developed
Power Board
Filtering
Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
regulators
Power
5~10 m
GBT Optical Links
9-sensor Stave
sPHENIX GL-1 & GTM
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Demonstrated full high-speed readout chain,
  1 Stave + RU + FELIX + RCDAQ/sPHENIX
  Eliminated the highest technical risk - “readout integration”
ALPIDE and Power Unit control and monitor being evaluated
ALPIDE pixel circuit
Alex and Xuan’s talks
RCDAQ
Linux

## Slide 21: Procurements in FY17-18
ALPIDE Sensors
  1 single chip with slow readout DAQ boards
  5 single chip sensors with high-speed readout adaptor
    10 more to be produced locally
  1 9-chip stave module
    5 more ordered for FY18
Readout Units
  1 RU v1.0
    5 RU v1.x ordered FY18
FELIX back end
  1 FELIX v1.5
    2 FELIX v2.0 available soon
Linux DAQ server
  1 Linux in operation
Power system
  1 32-chan power distribution boards
  CEAN rad-hard power modules and server
    CEAN rad-hard bulk power supply available later in FY18
Telescope mechanical support
  1 box made
Cooling system
  Chiller purchased and tested
  Negative-pressure system design in progress
Single chip
FELIX
RU
9-chip
stave
Power
distribution
card
Telescope box
FireFly
cables
Power system

## Slide 22: FY18 Milestones
Achieved:
  Developed full high-speed readout chain with ALPIDE sensors and stave and near final readout electronics RU and FELIX, and integrated the readout chain with sPHENIX RCDAQ
    Removed the highest risk item in the project – the readout system integration
  Completed initial sPHENIX MVTX mechanical system integration and layout
  Completed and benchmarked b-jet tagging for pp and AuAu with full detector GEANT simulations
  Completed and submitted the MVTX full proposal to BNL ALD
In progress:
  To construct a 4-stave/chip MVTX prototype telescope and take cosmic ray data
    Mechanical enclosure completed
    More Staves and RUs ordered
    Cooling system under development
  To complete readout and control integration with the final electronics (RUv.1x and FELIXv2.0) for full system integration

## Slide 23: Major Tasks to Complete the Project
ALPIDE sensor characterization and optimization
  Readout and trigger optimization for sPHENIX
  Laser system in preparation
Full readout and control integration in sPHENIX
  Full readout with RHIC clock and trigger
    RUv1.x, FELIXv2.0 and firmware & controls
    Electronics production/procurements in process
    sPHENIX DAQ system development in progress
MVTX mechanical system integration in sPHENIX
  Barrel section extension R&D
    Signal extension and long SamTec cables
  Mechanical system integration
    MVTX & INTT
MVTX prototype telescope final beam test at Fermilab
  Demonstrate tracking capability, spatial resolution
  High trigger rate (15kHz) at high event multiplicity
2018
2019
2019
2019

## Slide 24: Major Technical Challenges and Risks from Previous Feasibility Review Mitigated/Addressed
Project Risks with timely procurements of R&D items from CERN
  ALPIDE Sensors:
    a “Plan-B” was developed to us ~4 single chip ALPIDE sensors.
  Readout electronics and custom design
    A prototype Readout Unit (RU) with Xilinx evaluation board KC705 was developed before the arrival of RUv1.0
    An alternative path was successfully developed with ATLAS FELIX board to replace ALICE CRU
  Risks mitigated, full readout chain electronics integration designed and tested.
Needs of the test beam for the full proposal
  With the successful R&D of the full readout chain and sensors, we have determined that a test beam is not required for the full proposal submission.
  1st teat beam in preparation, ahead of schedule, to study sensor response and readout characterization.
  Full proposal completed and submitted
Add more milestones to MIE proposal development
  Implicit milestones in the LDRD project:
    To build a collaboration and submit a pre-proposal by the end of the first year FY17;
    To have science and technical reviews in the 2nd year and complete a full proposal by the end of FY18;
    To have the full proposal reviewed and approved by DOE by the end of FY19.
  Achieved:
    The 1st milestone in Feb 2017, ahead of plan; the MVTX detector collaboration is formed and growing, with 22 institutions from the world
    The 2nd milestone in Jan 2018, ahead of plan. Successful MVTX BNL Directors review in July 2017.
    LANL LDRD team is working closely with sPHENIX and BNL management to realize the full program.
  Full proposal completed and submitted
Setup simulation milestones for the MIE proposal
  A full sPHENIX tracking simulation package has been developed, milestones achieved and used for realistic b-jet tagging study for the full MVTX proposal.
  Full proposal completed and submitted

## Slide 25: Mission Impact
This LDRD directly contributes to the LANL NPAC (Nuclear, Particle, Astrophysics and Cosmology) and DOE Nuclear Physics program, expand the leadership of LANL at national & international level:
High impact on big science
  New physics programs at RHIC and EIC
Define the directions for LANL basic and applied programs
  Long-term DOE NP Program
  New hiring - Xuan, Sho(P-25), Darren(XTD/P-25)
  Promotions - Mike(XCP), Cesar
  Applications to LANL applied program
New ideas/proposals developed based on R&D from this LDRD project
  New x-ray imaging with MAPS
  New neutron detector with MAPS
  High-speed MAPS readout R&D for MARIE & EIC programs
Recommendation #1 (RHIC):
Recommendation #3 (EIC):
2020
2015
2025
2030
LDRD
sPHENIX
EIC
NSAC Long Range Plan 2015
The highest priority in this 2015 Plan is to capitalize on the investments made.

## Slide 26: MVTX Full Proposal Development
MVTX detector collaboration formed, 1/2017
  International collaboration of 22 institutions, and counting
  Bi-weekly detector R&D and physics simulation meetings
  Weekly project development meetings, project leaders from LANL, BNL, MIT and LBNL
A pre-proposal completed and submitted through BNL ALD to DOE in Feb. 2017
  Initial feedback from DOE, positive, compelling science
Successful MVTX BNL Directors review, July 2017
  Recommended to proceed with a full proposal
Organized workshops for detector R&D and physics program development
  MVTX physics and detector design, 1/2017, LBNL
  Readout electronics R&D, 4/2017, UT-Austin
  Cost & schedule workfest, 6/2017, BNL
  MVTX and Heavy Flavor physics, 12/2017, Santa Fe
A full MVTX proposal completed and submitted to BNL ALD 1/2018
~1 year ahead of plan
Preproposal
submitted
Full proposal
submitted
MVTX Workfest
@Santa Fe, 12/2017
sPHENIX coll. meeting
@Santa Fe, 12/2017

## Slide 27: Transition Plan
The transition plan details are still being worked out and evolving
  Develop a long term DOE NP program
MVTX funding news (received by MVTX group on 1/19/2018)
  From email by BNL Associate Laboratory Director (ALD) Dr. Berndt Mueller:
    DOE “appreciate the compelling science this instrument could enable …” “but unfortunately in our present outlook, we do not foresee at this time that we would be able to identify new DOE funding for the purpose of implementing the MVTX” and “encourage efforts to secure such [external] contributions…”
LDRD team is working closely with sPHENIX collaboration and BNL management to seek alternative path to fund the full MVTX detector.
  Several options being explored within the sPHENIX collaboration
  Possible direct and indirect foreign contributions
Cesar’s talk
FY-2017
2018
2019
2020
2021
2022
2023
sPHENIX
CD-1
CD-0
CD-2
sPHENIX
installation
physics starts
LDRD:
Readout & mechanics R&D
Secure funding for MVTX
Transition to MVTX/sPHENIX program
Today

## Slide 28: Summary
Achieved all LDRD milestones, some ahead of time, risks mitigated
  Designed and tested full readout system
  Developed mechanical conceptual design
  Completed b-jet tagging and preliminary physics study with full simulations
A MVTX prototype telescope being constructed
  In preparation for the 1st beam test at Fermilab w/ sPHENIX
New theoretical development
  High impact papers published
Developed a new heavy quark physics program for sPHENIX
  Completed and submitted the full MVTX proposal to BNL ALD
  DOE “appreciate the compelling science”, but new funding is challenging at this time
Broad impact on LANL NP and other applied programs
  New hires and promotions, new ideas and proposals
On track to meet LDRD goals for FY18 and FY19