## Slide 1: MVTX mechanical conceptual design
Walter Sondheim, P-25
Los Alamos National Laboratory

## Slide 2: MVTX mechanical conceptual design updated:
Personnel involved:
Walter Sondheim, P-25, engineer
Christopher O’Shaughnessy, P-25, engineer
New team from MIT:*
Dr. Ross Corliss, research scientist
James Kelsey, engineer, Assoc. Director Bates Lab.
Jason Bessuille, engineer, Bates Laboratory
Joseph Dodge, designer, Bates Laboratory
Dr. Mickey Chiu, BNL, sPHENIX integration task force leader
Corrado Gargiulo, CERN, lead engineer ALICE ITS upgrade
LBNL team:*
Dr. Grazyna Odyniec
Eric Anderssen
Joseph Silber
Dr. Yuan Mei
**See summary slide

## Slide 3: Technical Goals (as stated in the proposal)
Develop a conceptual design for a MAPS silicon technology based vertex detector, based on a current design being implemented as a part of the inner tracker system (ITS) upgrade for the ALICE detector at CERN. This new design should be compatible with the proposed upgrade to the PHENIX experiment at BNL, this new detector is called sPHENIX.
The tracking portion of the sPHENIX detector consists of three independent systems:
1, A large TPC (time proportional chamber) detector
2, A two layer silicon strip detector, called the INTT
3, A three layer MAPS based vertex detector, called the MVTX
These three detectors will be located in reverse around the sPHEINX beam-pipe, with the MVTX being the closest.

## Slide 4: MVTX detector as a part of the sPHENIX tracking system:
TPC volume, length 2,160.0mm
INTT detector, 2 layers
MVTX detector with service cylinder
Support brackets for TPC and INTT
TPC inner bore 400.mm

## Slide 5: Mechanical components that make up the MVTX:
MAPS type silicon detector ladders called staves, 3 layers in this assembly
A “conical” region with “pig-tail” ribbon cabling to “patch-panels”
Extension signal and power ribbon cabling
Composite outer shell structure

## Slide 6: Mechanical components that make up the MVTX:
Exploded view of three layer MVTX detector with outer shell. The detector is designed to be in two halves for installation around the installed beam-pipe
Estimated total mass for half assembly 1.2 kgms,
Total power 80. watts

## Slide 7: Detail drawing of stave assembly:
290.0 mm
16.35 mm
5.0 mm
9 silicon MAPS sensors, each 50 microns thick
Mass of stave without the FPC 1.7 grams
FPC

## Slide 8: Reconfiguration of MVTX staves around sPHENIX beam-pipe allowing for 2.0 mm clearance, inner layer:
43.21 mm
Aluminum extension
41.53 mm beryllium
40.01 mm
47.21 mm
61.21 mm
24.31 mm 23.60 mm
The sPHENIX beam-pipe diameter has a bigger diameter then the similar beam-pipe in the ALICE detector at CERN. This means that all of the silicon stave ladders need to be reconfigured to a larger radius (minimum of 2.0 mm) from the diameter of the sPHENIX aluminum extensions to this beam-pipe:

## Slide 9: New configuration of MVTX staves in sPHENIX:
39.92
32.30
24.58
7.76
New stave configuration will be hermetic!

## Slide 10: Modification to stave assembly with 40.cm power cable
Location for patch panel from previous slide -
Location for patch panel for power cables in service cylinder
With the tested extended length of the power cables from the stave we now have a path forward to reduce the diameter of the patch panels in the conical region of the MVTX detector

## Slide 11: Conical sections of MVTX needs to have smaller diameter:
R=107.5mm
R=128.6mm
R=140.0mm
ALICE inner tracker
MVTX tracker
Integration with INTT detector prohibited by original larger diameter of conical region:
Pass-through ports for power cables

## Slide 12: 3D printing – MVTX inner layer patch panel
3D printed MVTX inner layer patch panel that demonstrates the idea of “passing through” the power cables from the stave to a second patch panel in the service cylinder, this allowed for the reduction in radius of the conical sections for each layer.

## Slide 13: 3D printing – MVTX signal cable patch panels;
3D printing of all three signal cable patch panels, used to verify that the power cables will pass through to a second patch panel in the service cylinder -

## Slide 14: MVTX detector with service cylinder added:
Service barrel length 1,200.0 mm, carbon composite with aluminum flanges, this will support signal, power, bias cables along with water and air cooling lines
MVTX detector shown with sPHENIX beam-pipe
Beryllium section

## Slide 15: Detail view of INTT and MVTX detectors inside bore of TPC
Two layer silicon strip INTT detector,,
Extension cables go out each end
Three layer MVTX detector
Extension cables only in service cylinder

## Slide 16: Section view of sPHENIX detector with tracking detectors
Outer hcal
Inner hcal
Superconducting solenoid coil
7,600.mm
sPHENIX tracking system detectors supported off inner hcal end ring

## Slide 17: Summary, work projected for 2019:
Conceptual design for MVTX is complete!!
  Technical design work will begin at MIT*
  Work with LBNL team on composite material pieces*
Prototype cooling system developed at LANL
  Power dissipation MVTX assembly:
    120. watts, power cables an additional 34 watts
    Water cooling 31 liters/hour @ .22 bar (negative pressure)
    Dry air cooling (moisture control) 5 cubic-meters/hour
Develop installation scenario, MIT and LANL engineers*
FEA study of service barrel and support – MIT*
*These activities will be funded by the added sPHENIX operations funds from the DOE

## Slide 18: Backup:

## Slide 19: MIT, LANL engineers study prototype detector at CERN

## Slide 20: MVTX stave assembly:

## Slide 21: Radiation budget for stave assembly:
Water cooling