## Slide 1: Develop telescope with ALICE inner tracker staves for LDRD project. Followed up by the mechanical integration of LANL MAPS inner tracker for the proposed sPHENIX experiment
Walter Sondheim, Hubert Van Hecke, P-25
December 5th, 2016

## Slide 2: ALICE inner tracker stave:
Active length
271.2 mm
High speed data lines
Water cooling lines
Analog power
Digital power
Firefly high speed data cable
Active width 15.0 mm
Power dissipation in one stave assembly;
0.041 watts/cm**2,
1.7 watts for 9 MAPS chips. A safety factor of 2 will be assumed for construction

## Slide 3: ALICE inner tracker stave assembly:
Negative pressure, water cooling
9 MAPS sensor chips
FPC side up
Mounting block
Space frame

## Slide 4: Detail of construction stave assembly:
MAPS chips & FPC

## Slide 5: ALICE inner tracker stave production:
ALICE inner tracker stave filament winding
ALICE inner tracker production stave with cooling tubes and filament support

## Slide 6: ALICE prototype inner barrel assembly:
Prototype inner tracker half barrel layers showing staggered layer overlap to maintain continuous coverage in phi

## Slide 7: ALICE single chip module & single chip modules in a telescope configuration:
Single MAPS chip test module
15 X 30 mm
MAPS chip
6 single MAPS chip modules in test beam.
Scintillator counters
MAPS chip boards in box
Read-out boards
Slow speed readout board

## Slide 8: LANL four stave telescope assembly:
Aluminum box with 4 ALICE inner tracker layer 0 stave assemblies.
Box overall dimension 572.4 X 169.7 X 50.8 mm, inert gas atmosphere @ STP
End patch panel has interconnects for;
Analog power
Digital power
High speed data lines
Water cooling
Cosmic rays
Each stave has a precision hole and slot at either end for precise location to mounting blocks
Add scintillator counters for trigger

## Slide 9: LANL telescope stave design parameters:
Material budget: Material/layer: ~0.3%X0
Geometrical:
  Lengths in Z: 271.2 mm for each layer.
  Number of MAPS chips/layer: 9
Chip power dissipation < 50.0 mW/cm**2
  total power per stave 1.7 watts, 6.8 watts for telescope assembly, add 100% overhead for a total of 13.6 watts
Operational T <30 °C, max. Negative pressure water cooling, 1.02 mm diameter polyimide (Kapton) tubing.
  Tested at flow rates from 3 to 7.5 L/hr, ΔT 2.4 – 1.7°K/chip
  Verified pressure drop <4.35 psi @ 3.0 L/hr flow
  4 loops, 12 liters/hour flow rate each loop

## Slide 10: Current sPHENIX proposed layout:
sPHENIX
Experimenter
RHIC beam
RHIC beam

## Slide 11
SOUTH EMCAL
SOUTH ENDCAP
SOUTH SUPPORT RING
CRYOSTAT/SC COIL
OUTER HCAL
INNER HCAL
NORTH EMCAL
NORTH SUPPORT RING
COIL CHIMNEY
NORTH ENDCAP
(FLUX RETURN)
(FLUX RETURN)
TRACKING DETECTORS
NOT SHOWN; TPC, INTT
& LANL INNER TRACKER
Current sPHENIX detector exploded view:

## Slide 12: CAD model for sPHENIX detector sectioned, with tracking elements:
TPC
INTT
LANL INNER TRACKER
sPHENIX EXPERIMENTER

## Slide 13: CAD model of the three tracking systems, section view:
2300.mm
767.mm
radius
TPC
INTT,
4 layer Si strip detector
LANL MAPS inner tracker
Beam axis

## Slide 14: LANL MAPS inner tracker, exploded view of layers, section view:
Half assembly view
Exploded view showing the three layers
Inner layer 0, 12 ladders
Middle layer 1, 16 ladders
Outer layer 2, 20 ladders
Outer composite shell

## Slide 15: 3 layer LANL MAPS inner tracker:
LANL inner tracker, 3 layers of silicon MAPS detectors with sPHENIX beryllium beampipe, OD of beampipe is 41.5 mm, ID of LANL inner tracker 42.9 mm.

## Slide 16: Summary:
Mechanical construction of the carbon composite stave/space-frame is well underway at CERN
  Much work needed on perfecting stave assembly between MAPS chips and FPC to give highest yield after adhesive bonding and wire bonding, in process at CERN
Integration of entire tracking assembly with sPHENIX needs development – risk level medium but requires full participation of sPHENIX to mitigate
Can a single cooling system be implemented for entire sPHENIX tracking system - this will be a part of the entire integration of the sPHENIX detector system

## Slide 17: Backup:

## Slide 18: Prototype ALICE inner tracker composite stave assembly:
Inner tracker staves mounted to prototype support ends.

## Slide 19
Inner tracker service patch panel prototypes:

## Slide 20
Inner tracker composite shell prototypes: