## Slide 1: sPHENIX LDRD Work
Sho, Ming
01/24/2019
Updated 2/5/2019 after discussions with Jo @CERN;
and Huber, Walt and Abel at LANL 2/6/19

## Slide 2
Discussions with Sho, 1/16/2019

## Slide 3: MVTX Electronics, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
~10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX
(------- ALICE/ITS Hardware --------)
(-- ATLAS Hardware --)

## Slide 4: To do list - Priority
4-stave telescope integration --- Feb – April, test beam in May @FNAL. (all)
---- possibility to joint early test beam w/ sPHENIX/EIC EMCal; April 3-23 (4/15-23 for MVTX), @MT6.2b
  Get 5 staves from ALICE, test/QA at LANL, ~ Feb. 2019
  Cooling system operation and testing –- in Feb-Mar
    Asked Jeff B. to get the chemical to clean up the system , IWD? (Sho)
    Run and checkout the system (Hubert, Chris, AlexW, Ming)
  Stave holding fixtures design and fab (Hubert, Walt et al) – in Feb-March
  Setup and test Readout and controls of {4-stave + 2-RU + 1-Felixv2.0 + 1PU + RCDAC (~ 3days, Sho)}, be ready in ~Mar? (Sho, Cameron, Ming et al)
  Control and readback PU through RU --- get it ready for Test beam?
    USB (~ 1 day, Sho), get it ready for the beam test in May? (followed by AlexW, MIng et al..), through FELIX later (requires completion of #2)
  Data analysis (Yasser, Cameron, Sho et al )
Integrate slow control over FELIX for staves, RU and PU --- by this summer, also working with Jo @UTA
  Upload initial configuration, dead/hot mask; readback V, I, T etc
  FPGA interface work (~5 weeks, Alex/Sho), (Mark/student, Cameron, Ming et al)
Evaluate ~10m SamTec cables, AWG 30/32 vs 36
  Eye diagram with MOSAIC, or RU?, help from Jo
  Direct check on the scope
Stave testbench setup with MOSAIC *
  Run the full ALICE QA, output final results to DB(ALICE)
  Need to check the Status at LBNL, maybe already done there? (Sho/AlexW, Ming )
Setup sPHENIX GTM system at LANL --- check with BNL for the GTM availability [Gerd]
  Timing and Trigger through “Mode-Bit”, to be defined (Gerd, Sho, Ming)
Evaluate chip performance with laser system + MOSAIC., external “injection” [Gerd] – Feb – April, preliminary results before May test beam at FNAL (Gerd, AlexW, Ming, Cameron, Yasser, Sho)
  Study sensor efficiency vs trigger latency
  Operate MOSAIC with external triggered mode with pulsed laser; may need to modify the MOSAIC code for this.
  Obtain laser system safety approval for operation
Full chain test of a complete unit [ 8 staves/sensors + 8RU + 1 FELIX + PU + “sPHENIX GTM”] – later summer, complete by Sep 2019
  Obtain 10 RU, 1 FELIX+GTM by summer (Sho, Cameron, AlexW, Ming et al)

## Slide 5: Telescope work
Hardware
  4 staves available
    One more coming later
  2 RU v1.1
  Samtec cables
    5m, 8m, 10m
  1 FELIX v2.0
    Also one Felix v1.5 (used last time)
  FELIX server and RCDAQ
    2-stave  1 RU
    2 RU  1 FELIX
  Telescope box
    Fixtures for staves
    Cooling (air OK), T-monitoring?
Software
  4-stave readout
    FPGA
    RCDAQ and decoder
  PU control via RU/USB
    4 DVDD, 4 AVDD, 4 BV
    V, I, T monitoring
  Online monitoring
    Event information, hit distribution n
    Sensor V, I, T monitoring
  Offline analysis

## Slide 6
2018 Fermilab Setup

## Slide 7
MVTX Telescope 03/2018
Online Monitoring @FNAL
Test beam at FNAL
March, 2018

## Slide 8: UCLA EMCal TB in 2014, Possible joint TB
MVTX
We could use the table upstream of
UCLA Emcal for MVTX TB;
The same table was used for INTT
last time with MVTX located down stream
https://www.phenix.bnl.gov/WWW/publish/mxliu/sPHENIX/LDRD/FermilabTestBeam-032018/IMG_0673_sPHENIX_Overview.jpg
UCLA EMCal

## Slide 9: Preliminary mechanical support for 4-stave
Abel works with Hubert to fabricate stave
Support frames;

## Slide 10: Early Test Beam with EIC/sPHENIX EMCal? April 3 -23, 2019
Possible MVTX telescope beam test:
- 4/14-23 @ Fermilab
*BNL sPHENIX Director’s review:
4/8-13 @BNL
MVTX and INTT will be reviewed

## Slide 12: Readout Development Work
Sho’s summary page:
https://p25ext.lanl.gov/maps/readout.html
MVTX technical document: https://www.overleaf.com/18152646jkqtztvgnrtp