## Slide 1: MVTX Update 6/4/2018
Project Status – a lot is going now …
  DOE OK to include MVTX in the sPHENIX MIE baseline
    Some Impacts on procurements plan and schedule on MVTX if in MIE
  BNL(w/DOE) to secure funding for MVTX
    Integrated into MIE at CD-2, ~summer 2019
    A separate project
  BNL/MIT working on “CD3a” early procurements/production of staves and RU, starting Oct. 2018, 6~12 months
sPHENIX integration minireview, 7/19
  MVTX/INTT subsystem integration
  Stave & RU procurement readiness
  A final production review ~Sept
Preparation for review, sPHENIX wide effort
  Mechanical integration, MVTX+INTT, a conceptual design, 3-D print model etc
  Electrical integration, readout
  MVTX+INTT+TPC/sPHENIX simulations (INTT optimization …)
LDRD near term R&D and schedules
  FPC PWR extension and mechanical integration. 3-D mock up etc.
  Update RU/FELIX firmware, sync with ALICE
  Add PU control and monitor, sync with ALICE
  Stave production & test at CERN, later summer/Sept-October? New postdoc + LANL folks
  Test negative pressure system, summer 18
  Setup laser system for ALPIDE optimization, ~ Sept-Oct?
  Build a full stave-based telescope ~end of 2018, test beam with INTT @Ferimlab ~Feb. 2019 (dates TBD), offline geometry & analysis code
  Setup and test CAEN power system, in ~Oct-Nov
Long term R&D in FY19+ – expanded LDRD goals
  Open HF trigger for pp and pA
  Develop a test system -> one quadrant (3+4+5) RU -> one FELIX/trigger board
FY18 major procurements update:
5 staves -> early FY19
5(20) final RU->early FY19
2 FELIX v2.0 -> August
CAEN power supply -> mid August
FPC power extension, in progress
Trying to make v2.0 RU in US now…
- CERN chips
- Gerber files
- Make 2~5 test boards?

## Slide 2: B-hadron trigger: pp and pA
- STAR can’t do it, no trigger
sPHENIX, needs HF trigger for full D/B reconstruction
Track-based trigger MVTX+INTT+TPC, B-hadron measurements
Very high event multiplicity ~ <1%
https://www.phenix.bnl.gov/WWW/publish/mxliu/sPHENIX/HF-Trigger/sPHENIX-HF-Trigger-Study-042018.pptx

## Slide 3: HF Trigger Feasibility: DCA & High Multiplicity
3+4+5 RU -> 1 FELIX/Trigger in continuous readout mode,
ALPIDE readout: ~<5uS,
APLIDE->RU timing:
rising time above threshold ~1 uS
Strobe length = 0.1uS
Readout time = hits N_x per region x 80bits @1.2Gbps = 0.1xN_x uS <~ 2uS (slide 7)
Readout frame gap ~ 50nS
Direct passthrough data from RU to FELIX/Trigger board: @1.2Gbps, a few ~0.1uS
Total delay @Trigger board: ~3uS
  Can we get INTT hits?
B-Trigger decision to be made at trigger board: 4~5uS
  Some kind of lookup table for DCA,
  possibly for multiple tracks, N>=2
Very high multiplicity sum for fast trigger (INTT?), most ~1% central event
DCA_XY
B
- Beam center

## Slide 4: Quadrant based trigger logic: 3+4+5 RUs feed 1 FELIX/Trigger baord
sPHENIX Inner Tracking
Offline B-tagging

## Slide 5: expected beam spot size
= 76 μm (ε =10 μm)
= 93 μm (ε =15 μm)
http://www.rhichome.bnl.gov/RHIC/Runs/
obtained parameters from CAD’s web page:
RUN11 AuAu 200GeV
RUN12 pp 200GeV
β* = 0.75 m (PHENIX)
β* = 0.85 m (PHENIX)
= 115 μm (ε =20 μm)
= 129 μm (ε =25 μm)
Average 122um
definition of emittance
ε = (βγ) * (6σ^2)/β*
(βγ) : relativistic factors
σ : RMS beam size
β* : amplitude function
ε :95% normalized emittance
will check vernier scan result
ASANO 2012/07/17

## Slide 6
sPHENIX:
Try to make a B-trigger decision
within (4.5 + 5 ) uS, possible?

## Slide 7: Triggered vs Continuous Readout
Ev. n+1
Ev. n+2
Ev. n+5
Ev. n-1
Ev. n
Ev. n+3
Ev. n+4
Ev. n+6
Time width within signals are recorded on trigger depends on the analog shaping time (≈ 5 µs)
Strobe n
Strobe n+1
Strobe n+2
Strobe n+…
Strobe n-1
Ev. n+1
Ev. n+2
Ev. n+5
Ev. n-1
Ev. n
Ev. n+3
Ev. n+4
Ev. n+6
Triggered Readout
“Continuous” Readout

## Slide 8: ALPIDE readout
DV=Q/C
v
t
PIX_IN
tr> 100 us
tf~= 10 ns
OUT_D
STROBE
~5-6 ms
~5-6 us
v
t
OUT_A
threshold

## Slide 9: PYTHIA simulations
pT > 0.3GeV, muons
DCA_XY > 500 um
  Eff = 52.5%
DCA_XY > 1,000 um
  Eff = 33.9%
sPHENIX DAQ 15kHz
  MB ~ 1kHz
FH sampled by MB:
  1kHz/10MHz = 1x10^-4
Even with 10% HF Trigger Eff, we gain:
  0.1/10^-4 = 1000!
  Enable B-hadron physics at low pT
Ming @4/9/2018

## Slide 10: Trigger Efficiency for B->mu+X, DCA > 1000 um
Ming @4/9/2018