## Slide 1: Full Readout Chain
Trigger Generator
GBT_FPGA
G-RORC
Data Acquisition software
“DATE”
GBTxFMC
RUv0a
Alpide3 Carrier
Trigger Handling
Alpide Control
Alpide Data Readout
CRU packet builder
GBTx
RX
Fiber
Alpide Control Firmware from M. Lupi
Alpide Data Readout Firmware from M. Bonora
G-RORC GBT development from F. Costa, ASUS Server
DATE software from DAQ group
GBTx firmware from GBT tests (JS)
GBTx
TX
USB

## Slide 2: Continuous Readout
Strobe
0
Strobe
1
Strobe
2
Strobe
3
Strobe
0
FID1
SOP
Data
EOP
FID0
SOP
Data
EOP
FID2
SOP
Data
EOP
FID3
SOP
Data
EOP
HB
Time
HB
t1
t2
t3
t4
t5
Trigger Frames
RU Data
HB = Heart Beat Trigger
HBF = Heart Beat Frame
Strobe<x> = Trigger strobe to sensor with trigger time = BC+Orbit at time<x>
evID<x> = event ID (part of CDH?) with BC+Orbit at time<x>
Data = Sensor Pixel addresses
SOP = “Start Of Packet” (CRU protocol)
EOP = “End Of Packet” (CRU protocol)
Comments:
Heart Beat Triggers come every 89.4 µs, so trigger strobes (“frames”) in this example would be approximately 89.4 / 4 = 22.3 µs long and each Heart Beat Frame (HBF) would thus contain 4 packets from the RU. This parameter is programmable and could be adjusted e.g. to 89.4/8 to have 8 “sub-frames” in each HBF
Data will appear from the sensor some tens of ns after the end of the strobe signal, and some 40MHz clock cycles later on the GBT links. Data contained in each packet corresponds to all physical signals (“events”) between times tx and tx+1. The packets might also contain the busy status for individual sensors of an RU, which could then be used to determine the need for throttling at the CTP. It is not yet clear to me how this should be used in the RU, since the RUs are producing their own trigger strobes (i.e. not based on HBa or HBr trigger types). Most likely the RUs would do nothing in response to HBr, but instead the CRU would then discard the 4 (8) packets associated with this HBF?
Although data packets are shown here contiguous, it is possible that “DATA” GBT words are interspersed with “IDLE” or “SWT” (for DCS data) during data transmission to the CRU. Since there is the possibility of SEUs in the RUs’ FPGAs, there has to be a “timeout provision” in the CRU protocol to determine if a packet is corrupted/incomplete.
The CRU will then have to combine packets with evID1 through evID4 (and subsequent packets accordingly) into one Heart beat frame (HBF) with appropriate HB header and HB trailer. I am not sure if the event structure coming from the RU would have to be maintained in the HBFs?
HB Triggers
CTP
Sensor
RU

## Slide 3: Alpide Readout
RUv0a
FireFly Cable
Alpide3
CRU Framing & GBTx TX
GBTx Rx & Trigger handling

## Slide 4
G-RORC
Pattern
Generator
Pattern
Generator
Pattern
Generator
Pattern
Generator
GBT-Link #1
GBT-Link #2
GBT-Link #3
GBT-Link #8
TRG
Data
…
CLK Ref
240 MHz
G-RORC
GBT-Link #1
GBT-Link #2
GBT-Link #3
GBT-Link #8
…
DMA
Controller
PCIe Gen 2 x4

## Slide 6
RUv0a
“CRU”
Alpide
Altera Arria10 Devkit

## Slide 7
1159 x 25ns = 28.975 us
1 column enabled = 512 hits
Pulse duration = 0xff
Frame duration = 1
Pulse Delay = 0x8
236/3 x 25ns = 1875ns
CRU
RUv0a

## Slide 8
1 row enabled
(1024 pixels)
901 x 25ns = 22,525ns
CRU
CRU
RUv0a (zoomed)
RUv0a (zoomed)
RUv0a

## Slide 9
RUv0a
CRU zoomed
RUv0a (zoomed)
Every 8th pixel of 1 row enabled = 128 hits
Pulse duration = 0xff
Frame duration = 1
Pulse Delay = 0x8
Readout with 72bit packets
540/3 x 25ns = 4.5 us
CRU

## Slide 10
FrameDuration = 597 (14,950ns)
FrameGap = 1 (50ns)
ChipMode = 2
EnStrobeGeneration = 1
CRU
CRU
RUv0a
RUv0a
Continuous Mode

## Slide 11
value from alpide_data = 0xff_f0_ff_ff_6b_e0_ff_ff_f1
Why Busy?

## Slide 12
Continuous Data
mode register = 1 (triggered mode), firmware triggered
strobe length = 5us
trigger period = 10us
every 8th pixel of one row enabled (128 hits)

## Slide 13
DATE test