## Slide 1: RUv1 status

## Slide 2: RUv1 baseline
Main FPGA:
  XCKU60FFVA1156 (maintain US+ compatibility)
  Interfacing Alpides & GBTx
Reliable FPGA
  Microsemi PA3 or SF2
  Scrubbing Xilinx
    interfaces Flash device
Height follows VME standard: 6U high

## Slide 3: CAN interface
Employ electrically isolated transceivers?
If so, employ power distribution (4 lines) or isolated DC/DC
Connector via front pannel? What connector? DSUB9?
What Can speed? 1Mbps?
+
All CAN controller need external transceiver
CAN controler | Type | Voltage | TID (krad) | Price
Atmel | AT7908E (CPU interface) | 5 | 300k | 
ESA greece | ETM ASIC (only inputs) | 3,3 | 1M | 
COTS |  |  |  | 
TI | TMS570 Hercules |  | Under NDA | 
Microsemi/ Actel | PA3 + IP in fabric |  |  | IP
 | SF2 + internal ECC CAN periperal |  |  | 
transceiver | type | Voltage | TID(krad) | Price
Intersil | ISL72026/7/8SEH | 3,3 | 75 | $836
Cobham/ aeroflex | UT64CAN333x | 3,3 | 100 | 
TI | SN55HVD233-SP | 3,3 | 50 | Prelim
COTS |  |  |  | 
TI | SN65HVD233M-EP |  | ?? | 5,1

## Slide 4: Other
What about the PU SE control signals
CAN read only or also reset?
PA3=>US(+) read only or also reset?
Any news on PA3 radiation tests?
SelectMap indeed seems to cope with 32bit*100MHz=3.2Gbps

## Slide 5: Old slides

## Slide 6: Scrubbing
    What scrubbing method is used/supported
    Blind
    Readback
    What interface is used/supported for scrubbing
    Select map
    JTAG
    What bandwidth is needed to keep up with scrubbing?
    Is it for select map 100MHz * 32 bit?
    What is the minumum Prom size?

## Slide 7: EEProm/FLASH
    General remarks on Flash memories
Charge pump sensitive part, fail from 10krad.
  Erase/write only in absense beam/radiation.
Smaller Feature sizes & thinner oxide layers improves radiation sensitivity.
  Although optimum around 51n (25 nm worse again)
SLC preferred above MLC above TLC
Cross section COTS NAND flash order couple orders smaller than SRAM
  likely still ECC needed!
Other technologies (not Flash) seem promising: e.g. phase change proms
https://escies.org/download/webDocumentFile?id=63654
https://escies.org/download/webDocumentFile?id=49254
Samsung (σ_norm = 9.15E-13, K9WBG08U1M, datecode: 3708) order better than micron (σ_norm = 8.64E-12, MT29F8G08AAA-WP, datecode: 4208)
https://escies.org/download/webDocumentFile?id=63077
sheet 30: 51 nm Samsung better than 25nm Micron
http://radecs.ies.univ-montp2.fr/fichiers/abstract_13_Irom_2010-07-06_07_32_45_RADECSLATENEWS1.pdf
51 nm performs better than 72, 90 & 120 nm
https://nepp.nasa.gov/workshops/etw2012/talks/Tuesday/T13_Irom_NVM_Radiation.pdf
51 nm performs better than 25, 72, 90 & 120 nm

## Slide 8
Brand | type | Voltage | Feature (nm) | Size Mbit | TID krad | o/ bit | Clock MHz | Width | Bandwidth Mbit/s | Price
Atmel | AT69170F | 3,3 |  | 4 | 20 |  | 15 | 1 | 15 | 
 | AT28C010 | 5 |  | 1 | 10 |  | 8 | 8 | 66 | 
 | AT17LV010 | 3,3 |  | 1 | 20 |  | 10 | 1 | 10 | 
Xilinx | XQR17V16 |  |  | 16 | 50 |  | 33 | 8 | 264 | 
3Dplus | 3DP032 | 3,3 |  | 32 | 50 |  | 33 | 8 | 264 | 
 | 3DP064 |  |  | 64 |  |  |  |  |  | 
 | 3DP128 |  |  | 128 |  |  |  |  |  | 
Northrop | W28C0108 | 3,3 |  | 1 | 300 |  | 4 | 8 | 32 | 
Aeroflex Cobham | UT8MR2M8 | 3,3 |  | 16 | 1000 |  | 22 | 8 | 177 | 
 | UT8MR8M8 |  |  | 64 |  |  | 20 | 8 |  | 
 | UT8QNF8M8 | 3,3 |  | 64 | 10 |  | 16 | 16 | 266 | 
DDC | Rad-package |  |  |  |  |  |  |  |  | 
COTS |  |  |  |  |  |  |  |  |  | 
Atmel | AT45DB161B | 2.5-3.6 |  | 16 | 14 [1] |  | 20 | 1 | 20 | 
MICRON | MT29F4G08AAC | 1,8-3,3 | 72 | 4000 | 250 [2] | E-9,5 | 80 | 8 | 640 | 
MICRON | MT29F8G08AAA |  | 51 | 8000 |  | E-10 |  |  |  | 
Samsung | K9WBG08U1M |  | 51 |  | 70 | E-11 |  |  |  | 

## Slide 9: Alpide/firefly interfacing
Use of transistion board? => Yes
  If so, via front panel or rear transition module? => front
  e.g. VPX VITA 46.10m => No
How many (4, 5 or 6) Firefly connectors and how to route? 5
400MHz via GPIO or SERDES? => TBD
600MHz via GPIO or SERDES? => TBD

## Slide 10: PU interface
Do we interface with PU in the first place? => Yes
If so, is differential I2C and 17*SE oke? => Yes *2
Also CAN interface required? => Yes
Unlike presented before TI C2000 not rad tolerant
CAN controler | type | Voltage | TID (krad) | Price
Atmel | AT7908E | 5 | 300k | 
ESA greece | ETM ASIC | 3,3 | 1M | 
COTS |  |  |  | 
TI | C2000 |  | No data | 
CAN transceiver | type | Voltage V | TID krad | Price
Intersil | 7202xSEH | 3,3 | 75 | 
Cobham/ aeroflex | UT64CAN333x | 3,3 | 100 | 
TI | SN55HVD233-SP | 3,3 | 50 | Prelim
COTS |  |  |  | 
TI | SN65HVD233M-EP |  | ?? | 5,1

## Slide 11: RU crate & coldplate
RU crates
Does RU share coldplate? =>No
If so with PU
    Other RU module
      If so, is rotation symmetry required?
    combination
Do we use a backplane for
      Power distribution => Maybe
      PU status/control => Maybe
      Support for rear transistion modules => No

## Slide 12: Powering and regulators
How are RU powered?
  Which voltage (12V)? => Likely
  Power comes from the back? => Maybe
  What connector? => TBD
  Backplane or induvidial cables? => TBD
  How it is grouped/segmented? => TBD
Do TI DC/DC regulators from RUv0 operate in 0,5T?
=> Initial tests seems promising!!

## Slide 13: USB interface
  Place FX3 on RUv1 board or on a daughterboard? => TBD

## Slide 14: JTAG on front panel
  Do we want a JTAG connector on the front pannel?
  =>if possible, otherwise elso on the board

## Slide 15: US(+) power on current
  US: XCKU85/115 have
  very high power on current
  not in 1156 pin package
  UCKU095 relative expensive =>
  Use XCKU60FFVA1156 (smallest divice with 28 SERDES)

## Slide 16: ProAsic3 options
Estimated minimum number of IOs for FLASH device
price | price
A3P250 | 20
A3P400 | 30
A3P600 | 40
A3P1000 | 50

## Slide 17: New developments
RU must accomodate DCS CAN slave to control PowerBoard:
TI controler
FPGA CAN controler with external transceiver chip
  Commercial CAN (fabric) IP available for e.g. PA3.
  SF2 has integrated CAN pheripheral (SECDED in buffers)
Preliminary: Latest radiation test indicate PA3 as sensitive as SF2
Replacing PA3 with SF2 provides following advantages:
More modern device, better support and availability
Lower power consumption
True native LVDS support (no external resistors needed)
Integrated CAN pheripheral

## Slide 18: US(+) IO sufficient?
bank |  |  | device | Voltage | BLVDS | comment
HP | High Performance | Fast | US/US+ | ...1,8V | No | 
HR | High Range | Voltage range | US | ...3,3V | Yes | 
HD | High Density |  | US+ | ...3,3V | No | No diff out, max 250 MHz

## Slide 19: RUv1 IO
Signal | Speed | Dir |  | # | US IO standard | HP/ HR | VCCO | Speed Mbps | US+ IO Standard | HP/ HD | VCCO | Speed Mbps
e-links | 320 | Inputs | SLVS diff | 28 | SLVS_400_18 SLVS_400_25 | HP HR | 1,8 2,5 |  | SLVS_400_18 SLVS_400_25 | HP HD | 1,8 2,5 | 250
 |  | Outputs | LVDS | 30 | LVDS LVDS_25 | HP HR | 1,8 2,5 | 625 500 | LVDS LVDS_25 | HP HD | 1,8 2,5 | 625 250
alpide DCLK | 40 | Output | LVDS | 5 | LVDS LVDS_25 | HP HR | 1,8 2,5 | 625 500 | LVDS | HP | 1,8 | 625
 |  |  | BLVDS |  | BLVDS_25 | HR | 2,5 |  | No BLVDS | - | - | -
CTRL | 40 | Bidir | BLVDS | 5 |  |  |  |  |  |  |  | 
Data | 400/ 600 | Input | LVDS | 28 4*7 | LVDS LVDS_25 | HP HR | 1,8 2,5 | 625 500 | LVDS LVDS_25 | HP HD | 1,8 2,5 | 625 250
JTAG | 100 | IO | lvcmos | 5 | Bank 0 1,5-3,3V |  |  |  | Bank0 1,5-1,8V |  |  | 
Select Map | 100 | IO | lvcmos | 40 | Bank 0 & 65 1,5-3,3V | HR |  |  | Bank 0 & 65 1,5-1,8V | HP |  | 
Data PA3 | 100 | IO | Lvcmos 1,5-3,3 | 40 | Lvcmos | HP HR | …1,8 …3,3 |  | lvcmos | HP HD | …1,8 …3,3 | 
GPIF II UART | 100 | IO | lvcmos 1,7-3,6 | 48 2 | LVCMOS 1,8-3,3 | HP HR | 1,8 …3,3 |  | lvcmos | HP HD | …1,8 …3,3 | 
JTAG I2C | 100 | IO | Lvcmos 1,2-3,6 | 5 | LVCMOS 1,5/1,8 | HP HR | …1,8 |  | LVCMOS 1,5/1,8 | HP HD | …1,8 | 
GPIO | 100 | IO |  |  |  |  |  |  |  |  |  | 
GBT SCA | 320 | IO | Lvcmos 1,5 | 20 | LVCMOS 1,5 | HP HR | 1,5 |  | LVCMOS 1,5 | HP HD | 1,5 | 

## Slide 20: US(+) IO for RUv1
Speed (Mbps) values are for SDR. Some double when used in DDR
BLVDS_25 requires 3 termination resistors
HP for High speed signals
No diff out on HD (=> HR)
Signal | Speed | Dir | # | #pins | Standard | HP/HR | VCCO
e-link | 320 | In | 28 | 56 | SLVS_400_18 | HP | 1,8
e-link | 320 | Out | 30 | 60 | LVDS |  | 
Alpide data | 400/600 | In | 28 | 56 | LVDS |  | 
Alpide CLK | 40 | Out | 5 | 10 | LVDS |  | 
Total HP |  |  |  | 182 |  |  | 
Alpide CTRL | 40 | Bidir | 5 | 15 | Lvcmos=>BLVDS | * | 1,5-3,3
SelectMap | 100 | IO | 40 | 40 | LVCMOS | Bank65 | 1,5 or 1.8
PA3_data | 100 | IO | 40 | 40 | LVCMOS | * | 1,8-3,3
GPIF/UART | 100 | IO | 50 | 50 | LVCMOS | * | 1,8-3,3
GBT/SCA | 100 | IO | 20 | 20 | LVCMOS15 | HP | 1,5
GPIO | 100 |  |  |  |  |  | 
Total LVCMOS |  |  |  | 165 |  |  | 
Grand Total |  |  |  | 347 |  |  | 

## Slide 21: US(+) IO sufficient? => oke
at least 350 IO with 200 HP IOs => Oke US (>KU035) & US+

## Slide 22: JTAG configuration levels
Master devices | Voltage | Comment
SCA-JTAG | 1,2-3,3 | 
Xilinx cable USB II | 1,5-5 | 
FlashPro cable | 1,2-3,3 | 
Slave devices |  | 
GBTx | 1,5 | 
US | 1,5-3,3 | 
US+ | 1,5-1,8 | 
FX3 | 1,2-3,6 | JTAG bank shared with I2C prom. Min. EEPROM voltage is 1,7V !! On FireFlyFMCv3 JTAG bank is 3,3V
PA3 | 1,4-3,6 | 
With VJTAG=1,5V, problem arises with FX3 I2C
With VJTAG=1,8V, GBTx cannot be included in the JTAG chain
Making VJTAG>1,8V also excludes the US+ connected directly

## Slide 23: RU PS rails
Device | Rail | VMin | VTyp | VMax | ITyp | IMax | PTyp | PMax | comment
GBTx Tx320 | VDD |  | 1,5 |  | 667 | 795 | 1000 | 1193 | 
GBTx Xx320 |  |  |  |  | 1000 | 1125 | 1500 | 1688 | 
GB Tx+2*Xx |  |  |  |  | 2500 | 3046 | 4000 | 4569 | 
SCA | VDD (core) | 1,2 | 1,5 | 1,65 | 36 | 63 | 54 | 95 | 
 | AVDD |  | 1,5 |  | 1 | 1 | 1 | 1 | 
 | DVDD | 1,2 | 2,5 | 3,3 | 7 | 8 | 18 | 21 | Likely on 1,5...1,8V to support US+ selectmap
VTRx | VCC | 2,25 | 2,5 | 2,75 | 200 | 250 | 500 | 625 | 
VTTx |  |  |  |  | 300 | 400 | 750 | 1000 | 
VTTx+2*VTRx |  |  |  |  | 700 | 900 | 1750 | 2250 | 
ProAsic3 IGLOO2 | VCC (core) | 1,425 | 1,5 | 1,575 | 3 | 30 | 5 | 45 | static
 | VCCPLL | 1,4 | 1,5 | 1,6 | 333 | 404 | 500 | 607 | SelectMap 100 MHz, 40in+40out @ 1,8V
 | VJTAG | 1,4 |  | 3,6 |  |  |  |  | 
 | Vpump | 3 | 3,3 | 3,6 |  |  |  |  | Little
 | LVDS diff | 2,375 | 2,5 | 2,625 |  | 14 |  | 35 | 4*out, 2*In
Utrascale | VCCCINT ultrascale+ | 0,922 0,825 | 0,95 0,85 | 0,979 0,875 |  | 10000 20000 |  |  | 
 | VCCO_HR | 1,14 |  | 3,4 | 1 |  |  |  | 
 | VCCO_HP | 0,95 |  | 1,8 | 1 |  |  |  | 
 | VCCAUX | 1,75 | 1,8 | 1,85 |  | 1581 |  |  | 
 | VCCADC | 1,75 | 1,8 | 1,85 |  | 19 |  |  | Optional, needed when ADC in use
 | VREFP | 1,2 | 1,25 | 1,3 |  |  |  |  | Use internal Reference
 | VMGTAVCC Utrascale+ | 0,970 0,873 | 1 0,9 | 1,030 0,927 |  | 2300 |  |  | Estimate for 32 SERDES Rx
 | VMGTAVTT | 1,17 | 1,2 | 1,23 |  | 2400 |  |  | Estimate for 32 SERDES Rx
 | VMGTVCCAUX | 1,75 | 1,8 | 1,85 |  | 0 |  |  | 
 | VMGTAVTTRCA | 1,17 | 1,2 | 1,23 |  |  |  |  | 
 | VCFG (JTAG/SPI) ultrascale+ | 1,5 |  | 3,3 1,8? |  |  |  |  | 
 | VSelectMap Ultrascale+ | 1,5 |  | 3,3 1,8 |  |  |  |  | 
FX3 | (A)VDD (core) | 1,15 | 1,2 | 1,25 |  | 200 |  | 240 | 
 | DIO/UART | 1,7 |  | 3,6 |  |  |  |  | 
 | JTAG/I2C | 1,15 |  | 3,6 |  |  |  |  | 
 | Bus/bat | 3,2 | 3,3 | 6 |  | 60 |  | 200 | 
24LC1025 | V | 2,5 |  | 5,5 |  | 5 |  | 13 | 
24FC1025 |  | 1,8 |  |  |  |  |  | 9 | 

## Slide 24: PS rail and currents
3V3 | PA3_Vpump | FX3_Vbat | SFP | Total
3,3 | 1 | 60 | 150 | 211
2V5 | PA3_LVDS | VTT+2*VTRx |  | Total
2,5 | 14 | 900 |  | 914
1V8 | US_VCCaux | US_VCCADC | US_VMGTVCCAUX | 
1,8 | 1581 | 19 |  | 1600
1V5 | GB Tx+2*Xx | SCA | PA3 | 
1,5 | 3046 | 64 | 336 | 3446
1V2 | US_VMGTx32 | FX3 |  | 
1,2 | 2400 | 200 |  | 2600
VMGT | VMGT |  |  | 
1/0,9 | 2300 |  |  | 2300
VCCINT | VCCINT |  |  | 
0,95/0,85 | 10000 |  |  | 10000

## Slide 25: Optional Regulators
 |  | Test | TID (krad) | Mag. | I (A) | Vi min | Vi max | Vo min | Vo max | Accuracy | $ | Comment
MIC29501 | Linear | Leo | 20 | Oke | 5 |  |  | 1,25 | 25 |  | 6 | 
MIC29710 |  |  | 15 |  | 7,5 |  |  |  |  |  | 10 | Obsolete?
TPS5430 | Switched |  | 20 | ? | 3 | 5,5 | 36 | 1,22 |  |  | 2 | 
LMZ31503 |  |  | 30 | ? | 3 | 4,5 | 14,5 | 0,8 | 5,5 | 1% Ref | 8 | 
LMZ31710 |  |  | ? | ? | 10 | 2,95 | 17 | 0,6 | 5,5 | 1% Ref | 12 | 
FEASTMP | Switched | Cern | 200k | 40.000 Gaus | 4 |  |  | 0,9 | 5 |  | 35 | Height =15mm
FEAST2.1 |  |  |  |  |  |  |  | 0,6 |  |  | 15 | QFN
LHC4913 | Linear |  | 300k | Oke |  | 3 | 12 | 1,22 | 9 |  | 14 | 
MCP1824ST | Linear | Tullio | 100k | Oke | 0,3 |  |  | 0,8 | 5 |  | 1 | 
How large is magnetic field at RU? => 0,5 Tesla
Is/will LMZ31710 tested for radiation? => not yet

## Slide 26: RUv1 PS regulators
3V3 | PA3_Vpump | FX3_Vbat | SFP | Total | 
3,3 | 1 | 60 | 150 | 211 | LMZ31503
2V5 | PA3_LVDS | VTT+2*VTRx |  | Total | 
2,5 | 14 | 900 |  | 914 | LMZ31503
1V8 | US_VCCaux | US_VCCADC | US_VMGTVCCAUX |  | 
1,8 | 1581 | 19 |  | 1600 | LMZ31503
1V5 | GB Tx+2*Xx | SCA | PA3 |  | 
1,5 | 3046 | 64 | 336 | 3446 | FEASTMP or LMZ31710
1V2 | US_VMGTx32 | FX3 |  |  | 
1,2 | 2400 | 200 |  | 2600 | LMZ31503
VMGT | VMGT |  |  |  | 
1/0,9 | 2300 |  |  | 2300 | LMZ31503
VCCINT | VCCINT |  |  |  | 
0,95/0,85 | 10000 |  |  | 10000 | LMZ31710