## Slide 1: Some Thoughts on MVTX Slow Control System
Ming Liu
LANL
03/14/2019

## Slide 2: MVTX System overview
Power Board
Data (9x1.2Gbps), Clock, Control/Trigger
Regulated power
Readout Unit
Front End
FELIX
Back End
Data (3x3.2 Gbps)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
~8m twinax
GBT Optical Links
9-sensor stave
Power supplies
Power
Clock/Trigger
Interaction Region
Experimental Hall
Counting House
DAQ and Slow Control
PCIe
sPHENIX GTM

## Slide 3: Slow Control Functionality
Upload configuration parameters
  MAPS sensor operation
  MAPS dead pixel map
  PU LV pre-settings, V, I (limit) for DVDD, AVDD, Bias
  And more …
Readback and monitoring
  MAPS sensor temperatures, I etc
  PU output V, I, DVDD and AVDD and Bias
  And more …
Python scripts are available for MVTX (ALICE ITS), through USB->RU
  PC->USB on RU to control Staves and PU
  Jo at UT-Austin has developed the python scripts for ALICE
    ALICE: CRU <–> RU; CERN/CRU group has developed the CRU interface to python
    sPHENIX: FELIX<-->RU; need to develop FELIX interface to python
  Implement a few essential ones for Fermilab TB for online monitoring?
    PU output, (I,V) for DVDD, AVDD
    Sensor temperatures?
      We don’t have PT100 sensor installed on the telescope staves

## Slide 5: MVTX (ALICE ITS) DCS
Jo’s python scripts
FELIX

## Slide 6: Each RU reads PU Status Parameters
From WP10 Review, 6/23/2017

## Slide 7: Control Commands for the PU

## Slide 8: Sensors Status Parameters

## Slide 9: Sensor Control Commands

## Slide 10: Sensor Configuration

## Slide 11: What to Monitor at Fermilab?
PU: V, I
  DVDD, AVDD, Bias
Sensor:
  Temperature
  Current?
  Hot/dead channels
Jo’s python scripts
  ITS WP10 RU Python scripts:
  http://wp10ru.web.cern.ch/wp10ru/
  https://gitlab.cern.ch/alice-its-wp10-firmware/RUv1_Test/blob/master/software/py/testbench.py
  https://gitlab.cern.ch/alice-its-wp10-firmware/TestSystem/tree/master/software/py
Also, 2018 MVTX test beam - raw data, decoder, analysis etc.
https://wiki.bnl.gov/sPHENIX/index.php/Test_beam_in_2018_at_FNAL

## Slide 12: Some examples to execute python commands
./testbench.py rdo pwr_unit_1 initialized
./testbench.py rdo pwr_unit_1 power-off-all
./testbench.py rdo pwr_unit_1 log_values-IB 0
./testbench.py rdo dctl set_clk_mod 0
./testbench.py rdo pwr_unit_1 setup-power-IB --bb=0.0
ALICE : works for both USB and CRU
MVTX: USB only