## Slide 1: MVTX Overview
Ming Liu, for the MVTX Group
Los Alamos National Laboratory
MVTX BNL Director’s Review
July 19-20, 2018

## Slide 2: Outline
MVTX technology
MVTX project scope
Detector design and R&D
Status and Plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/
Submitted to BNL ALD 2/2018

## Slide 3: Exciting Science Enabled by MVTX
sPHENIX is the next flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets
  Upsilons
  B-jets and B hadrons
MVTX will complete QGP heavy flavor physics
  Precision study of the “inner workings of QGP”(LRP15)
  Unambiguous determination of key parameters of QGP properties and interactions
complement & extend current and future RHIC and LHC QGP programs
sPHENIX 3 Physics Pillars
Jets
Upsilons
B
D
PRL 108 (2012) 022301
http://arxiv.org/pdf/1501.06197v1.pdf
Dave & Gunther

## Slide 4: Monolithic Active Pixel Sensors (MAPS) The Next-Generation, State-of-the-Art Pixel Tracker
Advantages of ALICE PIxel DEtector (ALPIDE) sensor:
Very fine pitch (27μm x 29μm), for superb spatial resolution
High efficiency (>99%) and low noise (<10-6), for excellent tracking
Time resolution, as low as ~5 μs, for less pileup
Ultra-thin/low mass, 50μm (~0.3% X0), for less multiple scatterings
0.5M channels with on-pixel digitization, for zero-suppression and fast readout
Low power dissipation, 40mW/cm2, for minimal service materials
An ideal detector for QGP physics!
50 μm
~28 μm
ALPIDE design
Flexible Printed Circuit(FPC)
9 Chips
Cold plate
A 9-chip MAPS stave, 1.5cm x 27cm
ALPIDE sensor:
1.5cm x 3.0cm, 0.5M channels

## Slide 5: MVTX: MAPS-based VerTeX Detector
sPHENIX Inner Tracking: MVTX
“Adopt” ALICE ITS/IB:
- Minimum risk
- Maximum physics
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
Leveraging on extensive R&D and design work by ALICE
sPHENIX@RHIC
(2023+)

## Slide 6: sPHENIX vs ALICE
 | ALICE (Run3) | sPHENIX (Max) | Ratio of data rates sPHENX/ALICE
Pb+Pb / Au+Au | 50kHz | 200 kHz | 0.3
p+p | 200kHz | 13 MHz | (1.6)
Trigger/Readout | 50 kHz/(Continues) | 15 kHz | -
MB Event track multiplicity dN/dη
  sPHENIX = 1/3 ALICE (pp)
  sPHENIX = 1/5 ALICE (AA)
sPHENIX triggered data rate fits well within ALICE readout hardware specs;
sPHENIX
ALICE

## Slide 7: MVTX Detector
MVTX RUs, PUs & other services
3-layer sensor barrel
- 48 staves, 432 chips
Service cone: signal, power, cooling
and mechanical support
Figure for ALICE ITS/IB design
(slightly modified mechanically for sPHENIX)
MVTX
parameters
End-Wheel
CYSS: Cylindrical Shell Structure

## Slide 8: Scope of the MVTX Project
MAPS Staves & Electronics
  Readout Integration R&D (LANL LDRD)
    Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Reprogram RU & FELIX for sPHENIX
  Production:
    84 ALICE/ITS-IB staves from CERN
      Acceptance test @LBNL
      48+spares(36)
    58 ALICE/ITS-RU from CERN
      Acceptance test @UT-Austin, 48+spares(10)
    Reproduce 8 ATLAS/FELIX
      Acceptance @LANL
    Final assembly and test in US
      LBNL and BNL
  Ancillary systems, “adopt” ALICE system
Mechanics & Cooling
  Some changes to ALICE/ITS inner tracker mechanical structures,
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration,
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Carbon frames etc., LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Minor modification to fit sPHENIX
    Much smaller heat load than ALICE ITS
Leo Greiner
Jo Schambach
Alex Tkatchev &
Sho Uemura
Walt Sondheim
&
Dan Cacace
Walt Sondheim
- Early R&D by LANL LDRD, $5M, FY17-19, readout, mechanical design and physics
- Established LANL-ALICE MoU in 12/2016 for joint R&D for MVTX

## Slide 9: Schedules and Milestones
2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
MVTX final
design review
End Wheels
CYSS
Half barrel #1
Half barrel #2
Half barrels
arrive @BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrels
@sPHENIX IR
Ready for beam;
sPHENIX day-1 run
FELIX
production
Barrel Assembly & Testing @LBNL
ALICE IB stave done;
Facilities available for
sPHENIX production;
Window of opportunity:
Low technical risk
Cost saving
sPHENIX: CD1 CD2
MVTX
1st collisions
Installation

## Slide 10: sPHENIX DAQ Architecture
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Rack Room
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
Event Builder
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To the
RACF/HPSS
Calorimeters,
INTT, MBD
TPC
MVTX
SEB Sub-Event Buffer
EBDC Event Buffer and Data Compressor
ATP Assembles events and compresses data
Buffer Box Data interim storage before sending data to the computing center

## Slide 11: MVTX Readout, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX/DAM
Alex,Sho, Jo, Leo
#1,2,3
one pixel
ALPIDE pixel:
Shaping
Digitization
Zero-suppression
3x buffer
ATLAS Front-End Link eXchange (FELIX):
sPHENIX Data Aggregation Module(DAM)

## Slide 12: MVTX Sensors and Electronics
Major hardware:
  48 ALICE ALPIDE Staves + Interface Cables
  48 Front End Electronics (ALICE RUv2)
  6 Back End Electronics (ATLAS FELIX v2)
  6 EBDC Linux servers
  24 Power Boards + CEAN Supplies + Cables
  48 Stave to RU cables
  144 data fiber optic cables (3 fibers x 48 FEE)
Stave production spares: 75%
Electronics production spares: 20%
Alex, Sho, Leo, Jo
ALICE ITS/IB stave
ALICE ITS RU

## Slide 13: Projected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX integrated luminosities after 5-year operation
  AuAu: Lum. = 214 nb-1
  pp+pAu: Lum. = 1340 pb-1
Projected sPHENIX MVTX L0 fluence:
Outer layers:
L1 = 0.6 x L0; L2 = 0.4 x L0
Leo
#1
TID = 1060krad
NIEL = 6x1012 Neq/cm2
PHENIX study
arXiv: 0710.2676 [nucl-ex]
Sensors tested to full MVTX NIEL and ~1/2 TID @ALICE

## Slide 14: LANL LDRD Activity Highlights
Sensor source test
MAPS evaluation
Readout integration
4-sensor telescope
Test beam at Fermilab
Mechanical & cooling
Signal integrity
Cooling system
prototype
Service cone R&D
FPC power extension R&D
4-ALPIDE Telescope;
5m-long SamTec cables
Readout R&D
stave
RU

## Slide 15: MVTX Full Readout Chain Demonstrated
Alex & Sho
#1,2,3
4-hit track
4-MAPS telescope
120 GeV proton
beam
Tracking spatial resolution
achieved: <5 um
4-MAPS
telescope
Fermilab Test Beam: Feb-Mar, 2018

## Slide 16: Stave and RU Production QA Plan
Staves
Purchase 84 staves from ALICE/CERN
  48 + 28(spares for 2 inner layers) + 8 spares
  Production following the completion of ALICE ITS/IB
  Starting ~Oct. 2018, will last 6-12 months
  Fully tested at CERN before shipping to US
    All Gold/Silver staves (same as ALICE IB)
    A LANL postdoc (Dr. Yasser Morales) oversees production QA at CERN
Acceptance QA at LBNL
  Full test and QA
    Electrical
    Mechanical
  Detector assembly at LBNL
Readout Units
Purchase 58 RUs from ALICE/CERN
  48 + 10 spares(20%)
  To be part of ALICE production
    Cost saving
    Minimize technical risks
  Initial test at CERN
Acceptance QA at UT-Austin
  Full test
  LANL as the 2nd test site
Leo & Jo
#4,5,6,7,8

## Slide 17: Detector Assembly Plan at LBNL
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Follow ALICE IB assembly procedures to build half-detectors for MVTX
QA records in DB, travelers
Modified jigs for MVTX
Leo’s talk
#4,5,6,7,8
ALICE 1st half inner layer being assembled
6/2018@CERN
staves

## Slide 18: Mechanical Integration
MVTX, INTT and TPC/HCal
  MVTX/INTT detector designs modified
  Global interface being developed
L = 350.0 cm
TPC
TPC
R= 209.6cm
Walt & Dan
#10
INTT
MVTX

## Slide 19: Simulations for Optimization
Task force formed
  Goals and deadline defined
  Evaluate tracking with different INTT layers & geometry
Complementary roles in global tracking:
  MVTX:
    Precision DCA and vertexing
  INTT:
    Matching in-time hits of MVTX and TPC
    Important for p+p and p+A, pileups
Tony & Rachid
#9, 10

## Slide 20: sPHENIX MVTX Group: Institution Roles
Growing number of institutions
  Major institutions lead key tasks

## Slide 21: Summary
Compelling science established
Demonstrated full readout and control chain in sPHENIX framework
  Charge #1,2,3
Demonstrated detector performance with test beam data
  Charge #1,2,3
QA plan developed for RUs and Staves
  Charge #4,5,6,7,8
3D design of mechanical integration
  Charge #10
Simulation to optimize INTT geometry
  Charge #9, 10
Alex & Sho
Alex & Sho
Walt & Dan
Dave & Gunther
Rachid & Tony
Leo & Jo