## Slide 1: MVTX Overview
Ming Liu, for the MVTX Group
Los Alamos National Laboratory
July 19-20, 2018

## Slide 2: Outline
Science by MVTX
MVTX project scope
R&D highlights
Status and Plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 3: Exciting Science Enabled by MVTX
sPHENIX is the next flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets
  Upsilons
  B-jets and B hadrons
MVTX will complete QGP heavy flavor physics
  Precision study of the “inner workings of QGP”(LRP15)
  Unambiguous determination of key parameters of QGP properties and interactions
complement & extend current and future RHIC and LHC QGP programs
sPHENIX 3 Physics Pillars
Jets
Upsilons
B
D
PRL 108 (2012) 022301
http://arxiv.org/pdf/1501.06197v1.pdf

## Slide 4: Monolithic Active Pixel Sensors (MAPS) The Next-Generation, State-of-the-Art Pixel Tracker
Advantages of ALICE PIxel Detector (ALPIDE):
Very fine pitch (27μm x 29μm), for superb spatial resolution
High efficiency (>99%) and low noise (<10-6), for excellent tracking
Time resolution, as low as ~5 μs, for less pileup
Ultra-thin/low mass, 50μm (~0.3% X0), for less multiple scatterings
On-pixel digitization, low power dissipation, 40mW/cm2, for zero-suppression and minimal service materials
An ideal detector for QGP physics!
50 μm
~28 μm
ALPIDE design
Flexible Printed Circuit(FPC)
9 Chips
Cold plate
A 9-chip MAPS stave, 1.5 x 27cm2
ALICE ITS/IB Stave prototype

## Slide 5: MVTX: MAPS-based VerTeX Detector
sPHENIX Inner Tracking: MVTX
“Adopt” ALICE/ITS:
- Minimum risk,
- Maximum physics
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
Leveraging on extensive R&D and design work by ALICE
sPHENIX@RHIC
(2023+)

## Slide 6: MVTX Detector
MVTX RUs, PUs & services
3-layer sensor barrel
Service cone: signal, power, cooling
and mechanical support
Figure for ALICE ITS/IB Design
(slightly modified for sPHENIX)
MVTX
parameters
End-Wheel
CYSS: CYlindrical Shell Structure

## Slide 7: Scope of the MVTX Project
MAPS Staves & Electronics
  Readout Integration R&D (LANL LDRD)
    Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Reprogram RU & FELIX for sPHENIX
  Production:
    84 ALICE/ITS-IB staves from CERN
      Acceptance test @LBNL
      48+spares(36)
    58 ALICE/ITS-RU from CERN
      Acceptance test @UT-Austin, 48+spares(10)
    Reproduce 8 ATLAS/FELIX
      Acceptance @LANL
    Final assembly and test in US
      LBNL and BNL
  Ancillary systems, “adopt” ALICE system
Mechanics & Cooling
  Some changes to ALICE/ITS inner tracker mechanical structures,
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration,
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Carbon frames etc., LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Minor modification to fit sPHENIX
    Smaller heat load than ALICE ITS
Leo
Jo
Alex & Sho
Walt & Dan
Walt
- Early R&D by LANL LDRD, $5M, FY17-19, readout, mechanical design and physics
- Established LANL-ALICE MoU in 12/2016 for joint R&D for MVTX

## Slide 8: Updated Cost & Schedule, July 2018
Tied to sPHENIX and ALICE schedule
  Ready for sPHENIX day-1
  Stave production at CERN, following ALICE
  Readout unit production at CERN, following ALICE
  To minimize technical risk and also for cost saving
Cost based on ALICE/ITS production and recent STAR & PHENIX silicon detector upgrade projects at RHIC
  STAR HFT
  PHENIX FVTX

## Slide 9: Schedules and Milestones
2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
MVTX final
design review
End Wheels
CYSS
Half barrel #1
Half barrel #2
Test half barrels
#1, 2@BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrel
#1, 2@sPHENIX IR;
Ready for beam;
sPHENIX day-1 run
FELIX
production
Barrel Assembly & Testing
ALICE IB stave done;
Facilities available for
sPHENIX production;
Window of opportunity
sPHENIX: CD1 CD2
MVTX
1st collisions
Installation

## Slide 10: sPHENIX MVTX Group: Institution Roles
Growing number of institutions
  Major institutions lead key tasks

## Slide 11: MVTX Readout, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX/DAM
Alex,Sho, Jo, Leo
#1,2,3
one pixel
ALPIDE pixel:
Shaping
Digitization
Zero-suppression
3x buffer
ATLAS Front-End Link eXchange (FELIX):
sPHENIX Data Aggregation Module (DAM)

## Slide 12: Event Multiplicity and Collision Rates: sPHENIX vs ALICE
 | ALICE (Run3) | sPHENIX (Max) | Ratio of data rates sPHENX/ALICE
Pb+Pb / Au+Au | 50kHz | 200 kHz | 0.27
p+p | 200kHz | 13 MHz | 6.5
Trigger/Readout | 50 kHz | 15 kHz | -
MB Event track multiplicity dN/dη: sPHENIX = 1/3 ALICE (pp), 1/4.5 ALICE(AA)
sPHENIX triggered data rate well within readout specs
sPHENIX
ALICE
p+p collisions
sPHENIX/ALICE ~1/3
A+A collisions
sPHENIX/ALICE ~1/4.5
ALICE
sPHENIX

## Slide 13: Projected sPHENIX Data Rates
Readout Units: 3 GBTX @ 0.4 GB/s = 1.2 GB/s >133MB/s
GBTx: 3.2-4.48Gb/s, 0.4 GB/s
FELIX/DAM: 48 input on FELIX, twice the number needed to support 8 RUs (3 links)
2x 8-lane PCIe Gen 3 @ 7880 MB/s = 15,760 MB/s > 848 MB/s
MVTX readout hardware capacity > 10 x Expected data rate
Alex & Sho
#1,2,3
Note: test beam showed noise < 10-5
(FELIX)

## Slide 14: Expected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX integrated luminosities after 5-year operation
  AuAu: Lum. = 214 nb-1
  pp+pAu: Lum. = 1340 pb-1
Projected sPHENIX MVTX fluence, L0 = 0.6 ~ 1.7 x1013 Neq/cm2
Fluences of outer layers:
  L1 = 0.6 x L0
  L2 = 0.4 x L0
- Within the ALPIDE performance specs. (1.7 x1013 Neq/cm2)
- Risk mitigation: 36 spare staves (75%) to replace damaged ones
Leo
#1
Staves per layer:
L0 = 12
L1 = 16
L2 = 20
TID: sPHENIX ~ 4.5 ALICE
PHENIX study
arXiv: 0710.2676 [nucl-ex]

## Slide 15: LANL LDRD Highlights
MAPS evaluation
Readout integration
4-sensor telescope
Test beam at Fermilab
Mechanical & cooling
FireFly cables
A MAPS
chip
MOSAIC
test bench
9-chip
stave
Signal integrity
Sensor source test
cooling test
Service cone R&D
FPC power extension R&D

## Slide 16: MVTX Full Readout Chain Demonstrated
Readout Unit configures Stave using USB interface
FELIX distributes clock to Readout Unit
Readout Unit distributes clock to the Stave
Stave is triggered, sends data at 1.2Gb/s
Configured GBT link to recover clock from FELIX
Readout Unit receives the data and sends the data to FELIX over fiber using GBT link
FELIX packs data, stores it on disk using RCDAQ - the sPHENIX data format and software
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave
Alex & Sho
#1,2,3

## Slide 17: MVTX Telescope Test Beam at Fermilab
Goals:
  Test full readout chain
  Evaluate ALPIDE sensor performance
Experimental setup
  A 4-sensor telescope
  Full readout chain: MAPS+RU+FELIX+RCDAQ
Parasitic with INTT run
Very productive & collaborative
120 GeV
proton
4-sensor
Telescope
Alex & Sho
#1,2,3

## Slide 18: Fermilab Test Beam Results
4-hit track
Cluster size: 2.1 ~ 2.4
Mostly single tracks
4-MAPS telescope
# of tracks per event
Cluster size
120 GeV proton
beam
Hit Efficiency > 99.5%
Pixel size (~28um)
Spatial Resolution: < 5 um
Alex & Sho
#1,2,3
Detector performance consistent
with expectations

## Slide 19: Stave and RU Production QA Plan
Staves
Purchase 84 staves from ALICE Production
  48 + 28(spares for 2 inner layers) + 8 spares
  Production following the completion of ALICE ITS/IB
  Starting ~Oct. 2018, last 6-12 months
  Fully tested at CERN before shipping to US
    All Gold/Silver staves (same ~ALICE IB standard)
    A LANL postdoc (Dr. Yasser Morales) oversees production QA at CERN
Acceptance QA at LBNL
  Full test and QA
    Electrical
    Mechanical
  Detector assembly at LBNL
Readout Unit
Purchase 58 RUs from ALICE
  48 + 10 spares(20%)
  To be part of ALICE production
    Cost saving
    Minimize technical risks
  Initial test at CERN
QA at UT-Austin
  Full test
  LANL as the 2nd test site
Leo & Jo
#4,5,6,7,8

## Slide 20: Detector Assembly Plan at LBNL
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Assembly of layers and carbon fiber structure into half-detector
Stave testing at each step
Metrology survey
Leo’s talk
#4,5,6,7,8
ALICE 1st half inner layer being assembled
6/2018@CERN
ALICE 1st half inner layer,
6/2018@CERN
staves

## Slide 21: Mechanical Integration
MVTX, INTT and TPC
L = 350.0 cm
TPC
TPC
R= 209.6cm
Walt & Dan
#10
INTT
MVTX

## Slide 22: Simulations for Optimization
Task force formed
  Goals and deadline defined
Complementary roles in global tracking:
  MVTX:
    Precision DCA and vertexing
  INTT:
    Matching in-time hits of MVTX and TPC
    Important for p+p and p+A
Tony & Rachid
#9, 10

## Slide 23: Summary
Compelling science established
Demonstrated full readout and control chain in sPHENIX framework
  Charge #1,2,3
Demonstrated detector performance with test beam data
  Charge #1,2,3
QA plan developed for RU and Staves
  Charge #4,5,6,7,8
3D design of mechanical integration
  Charge #10
Simulation to optimize INTT geometry
  Charge #9, 10
Alex & Sho
Leo & Jo
Walt & Dan
Dave & Gunther
Rachid &Tony

## Slide 24: backup

## Slide 25
Electronics &
Controls
LANL
Readout Units
UT-Austin
Back-end
LANL
Power systems
LBNL
Mechanics & Detector Assembly
LBNL
Staves
LANL/LBNL
Carbon Structures
LBNL
Barrel Assembly
LBNL
Integration & Infrastructures
MIT
Cooling
MIT
Safety System
MIT
Global Support
MIT
MVTX
Principal Investigator: M. Liu (LANL)
Lead Coordinator: M. Chamizo-Llatas (BNL)
Co-investigators: G. Odyniec (LBNL),R. Corliss(MIT)
ES&H Liason: W. Sondheim (LANL)
Installation & Commissioning
LBNL/BNL
sPHENIX integration
sPHENIX DAQ
Major institutions lead key tasks

## Slide 27: Schedules and Milestones

## Slide 28: Cable routing
L 3500.0 mm
R 2,096.0mm
R= 209.6cm

## Slide 29
Main parameters: Loop shape
All connections (signal excluded)
Signal connections

## Slide 30: Bonding wire/Wedge
Wire 25 uM
Wedge