## Slide 1: MVTX Overview
Ming Liu, for the MVTX Group
Los Alamos National Laboratory
July 19-20, 2018

## Slide 2: Outline
Science by MVTX
MVTX project scope
R&D highlights
Status and Plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 3: Exciting Science Enabled by MVTX
sPHENIX is the next flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets
  Upsilons
  B-jets and B hadrons
MVTX will complete QGP heavy flavor physics
  Precision study of the “inner workings of QGP”(LRP15)
  Unambiguous determination of key parameters of QGP properties and interactions
complement & extend current and future RHIC and LHC QGP programs
sPHENIX 3 Physics Pillars
Jets
Upsilons
B
D
PRL 108 (2012) 022301
http://arxiv.org/pdf/1501.06197v1.pdf
Dave & Gunther

## Slide 4: Monolithic Active Pixel Sensors (MAPS) The Next-Generation, State-of-the-Art Pixel Tracker
Advantages of ALICE PIxel DEtector (ALPIDE) sensor:
Very fine pitch (27μm x 29μm), for superb spatial resolution
High efficiency (>99%) and low noise (<10-6), for excellent tracking
Time resolution, as low as ~5 μs, for less pileup
Ultra-thin/low mass, 50μm (~0.3% X0), for less multiple scatterings
0.5M channels with on-pixel digitization, for zero-suppression and fast readout
Low power dissipation, 40mW/cm2, for minimal service materials
An ideal detector for QGP physics!
50 μm
~28 μm
ALPIDE design
Flexible Printed Circuit(FPC)
9 Chips
Cold plate
A 9-chip MAPS stave, 1.5cm x 27cm
ALICE ITS ALPIDE sensor:
1.5cm x 3.0cm, 0.5M channels

## Slide 5: MVTX: MAPS-based VerTeX Detector
sPHENIX Inner Tracking: MVTX
“Adopt” ALICE/ITS:
- Minimum risk,
- Maximum physics
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
Leveraging on extensive R&D and design work by ALICE
sPHENIX@RHIC
(2023+)

## Slide 6: MVTX Detector
MVTX RUs, PUs & services
3-layer sensor barrel
Service cone: signal, power, cooling
and mechanical support
Figure for ALICE ITS/IB Design
(slightly modified for sPHENIX)
MVTX
parameters
End-Wheel
CYSS: Cylindrical Shell Structure

## Slide 7: Scope of the MVTX Project
MAPS Staves & Electronics
  Readout Integration R&D (LANL LDRD)
    Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Reprogram RU & FELIX for sPHENIX
  Production:
    84 ALICE/ITS-IB staves from CERN
      Acceptance test @LBNL
      48+spares(36)
    58 ALICE/ITS-RU from CERN
      Acceptance test @UT-Austin, 48+spares(10)
    Reproduce 8 ATLAS/FELIX
      Acceptance @LANL
    Final assembly and test in US
      LBNL and BNL
  Ancillary systems, “adopt” ALICE system
Mechanics & Cooling
  Some changes to ALICE/ITS inner tracker mechanical structures,
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration,
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Carbon frames etc., LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Minor modification to fit sPHENIX
    Smaller heat load than ALICE ITS
Leo
Jo
Alex & Sho
Walt & Dan
Walt
- Early R&D by LANL LDRD, $5M, FY17-19, readout, mechanical design and physics
- Established LANL-ALICE MoU in 12/2016 for joint R&D for MVTX

## Slide 8: Updated Cost & Schedule, July 2018
Tied to sPHENIX and ALICE schedule
  Ready for sPHENIX day-1
  Stave production at CERN, following ALICE
  Readout unit production at CERN, following ALICE
  To minimize technical risk, and also for cost saving
Cost based on ALICE/ITS production and recent STAR & PHENIX silicon detector upgrade projects at RHIC
  STAR HFT
  PHENIX FVTX

## Slide 9: Schedules and Milestones
2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
MVTX final
design review
End Wheels
CYSS
Half barrel #1
Half barrel #2
Test half barrels
#1, 2@BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrel
#1, 2@sPHENIX IR;
Ready for beam;
sPHENIX day-1 run
FELIX
production
Barrel Assembly & Testing
ALICE IB stave done;
Facilities available for
sPHENIX production;
Window of opportunity
sPHENIX: CD1 CD2
MVTX
1st collisions
Installation

## Slide 10: sPHENIX MVTX Group: Institution Roles
Growing number of institutions
  Major institutions lead key tasks

## Slide 11: MVTX Readout, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX/DAM
Alex,Sho, Jo, Leo
#1,2,3
one pixel
ALPIDE pixel:
Shaping
Digitization
Zero-suppression
3x buffer
ATLAS Front-End Link eXchange (FELIX):
sPHENIX Data Aggregation Module (DAM)

## Slide 12: Event Multiplicity and Collision Rates: sPHENIX vs ALICE
 | ALICE (Run3) | sPHENIX (Max) | Ratio of data rates sPHENX/ALICE
Pb+Pb / Au+Au | 50kHz | 200 kHz | 0.3
p+p | 200kHz | 13 MHz | 6.5
Trigger/Readout | 50 kHz | 15 kHz | -
MB Event track multiplicity dN/dη: sPHENIX = 1/3 ALICE (pp), 1/4.5 ALICE(AA)
sPHENIX triggered data rate well within readout specs
sPHENIX
ALICE
p+p collisions
sPHENIX/ALICE ~1/3
A+A collisions
sPHENIX/ALICE ~1/4.5
ALICE
sPHENIX

## Slide 13: Projected sPHENIX Data Rates
Readout Units: 3 GBTX @ 0.4 GB/s = 1.2 GB/s >133MB/s *
GBTx: 3.2-4.48Gb/s, 0.4 GB/s
FELIX/DAM: 48 input on FELIX, twice the number needed to support 8 RUs (3 links)
2x 8-lane PCIe Gen 3 @ 7880 MB/s = 15,760 MB/s > 848 MB/s
MVTX readout hardware capacity > 10 x Expected data rate
Alex & Sho
#1,2,3
Note: test beam showed noise < 10-5
(FELIX)
* Note: one central collision + 2 pileup MB events, cluster size 3.0

## Slide 14: Expected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX integrated luminosities after 5-year operation
  AuAu: Lum. = 214 nb-1
  pp+pAu: Lum. = 1340 pb-1
Projected sPHENIX MVTX L0 fluence:
Outer layers:
L1 = 0.6 x L0; L2 = 0.4 x L0
Leo
#1
TID = 1060krad
NIEL = 6x1012 Neq/cm2
PHENIX study
arXiv: 0710.2676 [nucl-ex]
Sensors tested to full MVTX NIEL and ~1/2 TID @ALICE

## Slide 15: LANL LDRD Activity Highlights
MAPS evaluation
Readout integration
4-sensor telescope
Test beam at Fermilab
Mechanical & cooling
FireFly cables
A MAPS
chip
MOSAIC
test bench
9-chip
stave
Signal integrity
Sensor source test
cooling test
Service cone R&D
FPC power extension R&D

## Slide 16: MVTX Full Readout Chain Demonstrated
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave
Alex & Sho
#1,2,3
4-hit track
4-MAPS telescope
120 GeV proton
beam
Fermilab Test Beam: Feb-Mar, 2018
Tracking spatial resolution
achieved: <5 um

## Slide 17: Stave and RU Production QA Plan
Staves
Purchase 84 staves from ALICE production
  48 + 28(spares for 2 inner layers) + 8 spares
  Production following the completion of ALICE ITS/IB
  Starting ~Oct. 2018, last 6-12 months
  Fully tested at CERN before shipping to US
    All Gold/Silver staves (same ~ALICE IB standard)
    A LANL postdoc (Dr. Yasser Morales) oversees production QA at CERN
Acceptance QA at LBNL
  Full test and QA
    Electrical
    Mechanical
  Detector assembly at LBNL
Readout Units
Purchase 58 RUs from ALICE
  48 + 10 spares(20%)
  To be part of ALICE production
    Cost saving
    Minimize technical risks
  Initial test at CERN
QA at UT-Austin
  Full test
  LANL as the 2nd test site
Leo & Jo
#4,5,6,7,8

## Slide 18: Detector Assembly Plan at LBNL
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Modified jigs for MVTX
Follow ALICE assembly procedures to build half-detectors
QA records in DB
Leo’s talk
#4,5,6,7,8
ALICE 1st half inner layer being assembled
6/2018@CERN
ALICE 1st half inner layer,
6/2018@CERN
staves

## Slide 19: Mechanical Integration
MVTX, INTT and TPC
  MVTX detector design modified
  Global interface being developed
L = 350.0 cm
TPC
TPC
R= 209.6cm
Walt & Dan
#10
INTT
MVTX

## Slide 20: Simulations for Optimization
Task force formed
  Goals and deadline defined
  Evaluate tracking with different INTT layers & geometry
Complementary roles in global tracking:
  MVTX:
    Precision DCA and vertexing
  INTT:
    Matching in-time hits of MVTX and TPC
    Important for p+p and p+A, pileups
Tony & Rachid
#9, 10

## Slide 21: Summary
Compelling science established
Demonstrated full readout and control chain in sPHENIX framework
  Charge #1,2,3
Demonstrated detector performance with test beam data
  Charge #1,2,3
QA plan developed for RU and Staves
  Charge #4,5,6,7,8
3D design of mechanical integration
  Charge #10
Simulation to optimize INTT geometry
  Charge #9, 10
Alex & Sho
Leo & Jo
Walt & Dan
Dave & Gunther
Rachid & Tony
Leo & Jo

## Slide 22: backup

## Slide 23: Cable routing
L 3500.0 mm
R 2,096.0mm
R= 209.6cm

## Slide 24: Radiation Level Outside of HCal: for Electronics
Simulation from Jin Huang, 7/2018
R = 274 cm
Z =0
AuAu 200kHz
Flux = 0.002/cm^2 x 200kHz x190/650
= 120 Hz/cm^2 << 1kHz/cm^2(ALICE)
RU tested OK to 1kHz/cm^2 at ALICE

## Slide 25
Main parameters: Loop shape
All connections (signal excluded)
Signal connections

## Slide 26: Bonding wire/Wedge
Wire 25 uM
Wedge

## Slide 27: MVTX Telescope Test Beam at Fermilab
Goals:
  Test full readout chain
  Evaluate ALPIDE sensor performance
Experimental setup
  A 4-sensor telescope
  Full readout chain: MAPS+RU+FELIX+RCDAQ
Parasitic with INTT run
Very productive & collaborative
120 GeV
proton
4-sensor
Telescope
Alex & Sho
#1,2,3

## Slide 28: Fermilab Test Beam Results
4-hit track
Cluster size: 2.1 ~ 2.4
Mostly single tracks
4-MAPS telescope
# of tracks per event
Cluster size
120 GeV proton
beam
Hit Efficiency > 99.5%
Pixel size (~28um)
Spatial Resolution: < 5 um
Alex & Sho
#1,2,3
Detector performance consistent
with expectations