## Slide 1: MVTX Overview
Ming Liu
Los Alamos National Laboratory

## Slide 2
Presentations:
sPHENIX overview
MVTX project overview
Readout integration & test beam
Stave production & QA
RU production & QA
INTT overview
Mechanical integration
Tracking simulations
Summary

## Slide 3: Outline
Science of MVTX
Scope of MVTX project
R&D highlights
Project Status & Plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/

## Slide 4: Exciting Science
sPHENIX is the next flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets
  Upsilons
  B-jets and B hadrons
MVTX will complete QGP heavy flavor physics
  Precision study of the “inner workings of QGP”(LRP15)
  Unambiguous determination of key parameters of QGP properties and interactions
complement & extend current and future RHIC and LHC QGP programs
sPHENIX 3 Physics Pillars
Jets
Upsilons
B
D
PRL 108 (2012) 022301
http://arxiv.org/pdf/1501.06197v1.pdf

## Slide 5: MVTX: Monolithic-Active-Pixel-Sensor-based VerTeX Detector
sPHENIX Inner Tracking
“Adopt” ALICE/ITS
Mini. risk,
Max. physics
sPHENIX@RHIC (2023+)
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
MVTX could also be a day-1 EIC detector

## Slide 6: B-Hadron & b-Jet Tagging
Physics Reminder
Detected using the long lifetime of bottom quark hadrons:
  Displaced tracks
  Large 2nd vertex invariant mass
Need high precision tracking and vertex determination – MVTX!
Need excellent jet detection capabilities – sPHENIX!

## Slide 7: Simulation for b-jet and B-meson tagging
Design to Simulation
sPHENIX Geant4 display of pT=30 GeV/c B+-hadron
MVTX and INTT _
_ MVTX Ladders modeled in details
MVTX sensors

## Slide 8: Expected Performance
Tony’s talk

## Slide 9: MVTX Physics Highlights
Heavy quarks – unique probe of QGP w/ new scales, mc, mb
  Study mass dependence
    Jet quenching & energy loss
    Flow – interaction with medium
  Access QGP properties
    Temperature, density, coupling, transport coefficients, viscosity etc.
MeV
1
10
102
103
104
mu md
LQCD
TQGP
mc
mb
Tc
ms
“B meson and b-jet modification”
“B meson and b-jet flow”

## Slide 10: Monolithic-Active-Pixel-Sensors (MAPS) The next Generation State of the Art Pixel Tracker
Advantages of ALICE MAPS/ALPIDE:
  Very fine pitch (28x28 μm)
  High efficiency (>99%) and low noise (<10-6)
  Time resolution, as high as ~5 μs
  Ultra-thin/low mass, 50μm (~0.3% X0)
  On-pixel digitization, low power dissipation
An ideal detector for QGP physics!
50 μm
28 μm
ALPIDE design
FPC
9 Chips
Cooling plate
A 9-chip MAPS stave, 1.5 x 27cm2

## Slide 11: ALPIDE/MAPS Operation
Well fit sPHENIX/RHIC environment, 10MHz Clock (LHC 40MHz)
DV=Q/C
v
t
PIX_IN
tr> 100 μs
tf~= 10 ns
OUT_D
STROBE
~5-6 ms
~5-6 μs
v
t
OUT_A
threshold
sPHENIX trigger latency: ~4 μs
shaping time: 2, 5, 10 … μs

## Slide 12: MVTX Readout and Control System
Power Board
Filtering
Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Regulated Power
FELIX
Data (9.6 Gb/s max)
Control
Trigger
9 ALPIDE Sensors
FPC
Cold Plate
regulators
Power
5~10 m
GBT Optical Links
9-sensor Stave
sPHENIX GL-1 & GTM
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Jo, Sho, Alex’s talks
LANL, UT-Austin, LBNL, BNL, ALICE/ITS …
ALPIDE Sensor

## Slide 13: sPHENIX MVTX vs ALICE ITS/IB Hit Rates
 | ALICE (Run3) | sPHENIX (Max)
Pb+Pb / Au+Au | 100 kHz (50kHz) | 200 kHz
p+p | 400 kHz (200kHz) | 13 MHz
Trigger/Readout | >50 kHz | 15 kHz
MB Event track multiplicity dN/dη: sPHENIX = 1/3 ALICE (pp), 1/4.5 ALICE(AA)
sPHENIX
ALICE
p+p collisions
A+A collisions

## Slide 14: Projected sPHENIX Data Rates @15kHz Trigger
Readout Units: 3 GBTX @ 0.4 GB/s = 1.2 GB/s >133MB/s
GBTx: 3.2-4.48Gb/s, 0.4 GB/s
FELIX: 48 input on FELIX, twice the number needed to support 8 RUs (3 links)
2x 8-lane PCIe Gen 3 @ 7880 MB/s = 15760 MB/s > 848 MB/s
Sho & Alex
Note: test beam showed noise < 10-5

## Slide 15: Expected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX radiation level after 5-year operation
  AuAu: L = 214 nb-1
    @R=10cm, D_AA = 214/50 x 0.2x1012 = 0.86x1012 nEq/cm2
  pp/pA: L = 1340 pb-1
    @R=10cm, D_pp = 1340/700 x 0.3x1012 = 0.57x1012 nEq/cm2
Projected sPHENIX MVTX L0 received fluence = 0.6 ~ 1.7 x1013 nEq/cm2
Within the ALIPDE performance specs.

## Slide 16: ITS Radiation Load
Position respect to beam |  |  | Radiation levels (total) |  |  | 
r | z | Name | TID | 1 MeV neq fluence | High energy hadron flux* | Charged particle flux
[cm] | [cm] |  | [krad] | [cm-2] | [kHz cm-2] | [kHz cm-2]
2.2 | [-13.5 ÷ 13.5] | ITS L0 | 2734 | 1.7 × 1013 | 765 (770) | 890 (910)
43 | [-73.7 ÷ 73.7] | ITS L6 | 20 | 8.1 × 1011 | 3.4 (4.9) | 4.5 (6.7)
79 | [-260 ÷ 260] | TPC In | 5.6 | 7.0 × 1011 | 1.35 (1.8) | 1.7 (3.45)
100 | 330 | RE | ≈ 5 | ≈ 1.6 × 1011 | 0.86 | 1.7
258 | [-260 ÷ 260] | TPC Out | 0.86 | 1.4 × 1011 | 0.27 (0.37) | 0.2 (0.3)
290 | [-290 ÷ 290] | TRD | 0.6 | 1.2 × 1011 | 0.23 (0.31) | 0.15 (0.23)
Hadrons and charged particles as for 50 kHz Pb-Pb collisions

## Slide 17: Radiation Level in sPHENIX (I): - by cross section scaling: LHC vs RHIC
LHC: Pb-Pb 5.5TeV,
  sigma_NN = 72mb
  Sigma_PbPb = 7750mb
  L = 13nb-1
N_evts = 7750mb x 13nb^-1
= 100 x109
RHIC: AuAu 200GeV
  Sigma_NN = 42mb
  Sigma_AuAu = 7000mb
  L = 214nb-1
N_evts = 7000mb x 214nb^-1
= 1,500 x 109
RHIC (AuAu) dN/deta = 1/4.5 LHC(PbPb):
Fluence (RHIC, AuAu) = 1/4.5 x 1500/100 = 3.3 x LHC(PbPb)
Fluence (RHIC, pp) = 6/9 x Fluence (RHIC, AuAu)
Total (RHIC: AuAu+pp+pA) = 3.3 x (1+6/9) x LHC(PbPb)
= 5.5 ALICE(PbPb) L0
= 5.5 x 1012 nEq/cm2
MVTX: at slightly larger R,
dR = +1.3mm

## Slide 18: Radiation Level in sPHENIX (II) - by PHENIX measurements
Projected sPHENIX radiation level after 5-year operation
  AuAu: L = 214 nb-1
    @R=10cm, D_AA = 214/50 x 0.2x1012 = 0.86x1012 nEq/cm2
  pp/pA: L = 1340 pb-1
    @R=10cm, D_pp = 1340/700 x 0.3x1012 = 0.57x1012 nEq/cm2
MVTX R_0 = 2.6cm
R-factor:
(10/2.6)1.83 = 11.8
Fluence from AuAu runs:
- 10 x 1012 nEq/cm2
Fluence from pp runs:
- 6.7 x 1012 nEq/cm2
Total: 1.7 x 1013 nEq/cm2
RHIC-II projected dosage based
on PHENIX measurements:
arXiv: 0710.2676 [nucl-ex]

## Slide 19: MVTX Full Proposal
Pre-proposal submitted to DOE, 2/2017
  Follow-up discussions with DOE and BNL managers
  Weekly proj. leaders’ meeting, BNL/LANL/LBNL/MIT
Full proposal submitted to BNL ALD, Feb 2018
  Expanded science + Cost & Schedule
  Assumed funding starts in FY18
A growing collaboration
  15+ institutions from US and abroad
Adapt ALICE ITS Upgrade Inner Barrel 3-layer MAPS detector
  Mini. risk, Max. Physics
Precision vertexing for b-jet/B-hadron tagging in HI with high efficiency and high purity
B-jet modification in QGP at low-medium pT to determine QGP properties, study mass-dependence on collisional vs radiative energy loss, flow etc.
Early R&D by LANL LDRD, $5M, FY17-19, readout, mechanical design and physics; established LANL-ALICE MoU in 12/2016 for joint R&D and training

## Slide 20: Updated Funding & Schedule, July 2018
Tied to sPHENIX and ALICE schedule
  Stave production
  Readout electronics
  To minimize technical risk and also for cost saving
Cost based on ALICE/ITS and recent STAR & PHENIX upgrade projects at RHIC
  STAR HFT
  PHENIX FVTX

## Slide 21: Scope of the MVTX Project
MAPS Staves & Electronics
  Produce 84 ITS inner Barrel Staves
    No modification on high-speed
    Extended power cables
  Readout Electronics R&D (LANL LDRD)
    Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Reprogram RU & FELIX for sPHENIX
  Production:
    Extend ALICE/ITS MAPS stave production
      WBS 1.5.3.1, LANL, LBNL
      sPHENIX personnel help at CERN
    Reproduce additional ALICE/RU & ATLAS/FELIX
      WBS 1.5.2.2, UT-Austin, RU
      WBS 1.5.2.3 , LANL, FELIX
    Final assembly and test in US
      WBS 1.5.3, LBNL
  Ancillary systems, “adopt” ALICE system
    Power distribution, cables, crates, racks etc.,
      WBS 1.5.2.3, LBNL
    Slow control, safety and monitoring
Mechanics & Cooling
  Some changes to ALICE/ITS inner tracker mechanical structures,
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration,
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Carbon frames etc., LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Minor modification to fit sPHENIX
    Smaller heat load than ALICE ITS
  Metrology and Survey

## Slide 22: Schedules and Milestones
2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
MVTX final
design review
End Wheels
CYSS
Half barrel #1
Half barrel #2
Test half barrels
#1, 2@BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrel
#1, 2@IR
Ready for beam
FELIX
production
Barrel Assembly & Testing

## Slide 23: Readout Integration into sPHENIX

## Slide 24: MVTX Electronics, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 25: MVTX Full Readout Chain Demonstrated
Readout Unit configures Stave using USB interface
FELIX distributes clock to Readout Unit
Readout Unit distributes clock to the Stave
Stave is triggered, sends data at 1.2Gb/s
Configured GBT link to recover clock from FELIX
Readout Unit receives the data and sends the data to FELIX over fiber using GBT link
FELIX packs data, stores it on disk using RCDAQ - the sPHENIX data format and software
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave

## Slide 26: MVTX Test Beam at Fermilab 02/20-03/10, 2018
Goals:
  Test full readout chain
  Evaluate ALPIDE sensor performance
Experimental setup
  A 4-sensor telescope
  Full readout chain: MAPS+RU+FELIX+RCDAQ
Parasitic with INTT run
Very productive & collaborative
120 GeV
proton
4-sensor
Telescope

## Slide 27: Fermilab Test Beam Results (I)
4-hit track
Cluster size: 2.1 ~ 2.4
Mostly single tracks
4-sensor telescope
# of tracks per event
Cluster size
120 GeV proton beam
Beautiful analysis done by Sanghoon and Darren + others

## Slide 28: Fermilab Test Beam Results (II)
Hit Efficiency > 99.5%
Pixel size (~28um)
Hit Spatial Resolution: < 5 um

## Slide 29: Staves Production and QA Plan
Purchase 84 staves from ALICE Production
  48 + full 2 inner layers(28) + 8 spares
  Production following the completion of ALICE ITS/IB
  Starting ~Oct. 2018, last 6-12 months (TBD)
  Fully tested at CERN before shipping to US
    All Gold/Silver staves or allow some Silvers? (same ~ALICE IB standard)
    A LANL postdoc (Dr. Yasser Morales) oversees QA at CERN
Acceptance QA at LBNL
  Full test and QA at LBNL
    Electrical
    Mechanical
  Detector assembly at LBNL
ALICE status
  IB stave in full production
Leo’s talk

## Slide 30: Detector Assembly
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Assembly of layers and carbon fiber structure into half-detector
Stave testing at each step
Metrology survey
Leo’s talk

## Slide 31: Readout Unit Production and QA Plan
Purchase 58 RUs from ALICE at CERN
  48 + 10 spares(20%)
  To be part of ALICE production
    Cost saving
    Minimize technical risks
  Initial test at CERN
QA at UT-Austin
  Full test
  LANL as the 2nd test site
Jo’s talk

## Slide 32: Mechanical Integration
MVTX and INTT
Walt, Dan & Mickey’s talk

## Slide 33: Simulations for Optimization
Task force formed
  Goals and deadline defined
  Details TBD soon?
Complementary roles in global tracking:
  MVTX:
    Precision DCA and vertexing
  INTT:
    Matching in-time hits of MVTX and TPC
    Important for p+p and p+A
Tony’s talk

## Slide 34: Summary
Compelling science
Demonstrated full readout and control chain in sPHENIX framework
  ALPIDE + RU + FELIX + RCDAQ
  Trigger rate > 15kHz
  sPHENIX raw data format defined
Demonstrated detector performance with test beam data
  Spatial resolution better than 5um
  Hit efficiency > 99%
QA plan developed for RU and Staves
  QAP documents ready for review
  Follow ALICE ITS QA procedures
Preliminary design of mechanical integration
  MVTX + INTT + (TPC/sPHENIX)
Ready for stave and RU production

## Slide 35: Backup slides

## Slide 41: A Multi-Year Plan for sPHENIX 2023+
Projected maximum collision rates:
  Au+Au: 240 kHz ( ~70 kHz, |Z|<10cm)
  p+p: 13 MHz ( ~2.4 MHz, |Z|<10cm)
  p+A: 2.8 MHz ( ~0.7 MHz,|Z|<10cm)
  sPHENIX DAQ: 15kHz
Precision vertexing for B-tagging:
  Tracking resolution better than 60um @pT=1GeV
  High multiplicity HI collisions
  Low multiplicity but high rate p+p collisions
  High efficiency and high purity
B hadrons/pT<15GeV: O(1M)
b-jets/pT>15GeV: O(100K)
sPH-TRG-2018-001

## Slide 42: MVTX Status: Where do we stand?
Full proposal submitted to BNL Associate Laboratory Director Dr. Berndt Mueller in Feb. 2018
March 27, a meeting of ALD, MVTX principals, co-SP and sPHENIX project office. Given improved DOE funding fiscal outlook, ALD recommended to bring MVTX into MIE baseline:
  This would be post-OPC/CD-1 Review(5/23-25, 2018), MIE baseline will be defined in the CD-2 (~summer 2019); MS Project -> P6 in progress
  Exploring advance-funding options to procure Readout Units ($250K, now) and staves from ALICE at CERN ($1.2M, fall 2018)
    Cost saving and reduce technical and schedule risks
  ALD seeks DOE agreement to proceed
MVTX workfest at MIT 4/30-5/1, 2018
  Refine MVTX roadmap – cost & schedule etc
  Prepare for sPHENIX integration mini review (~summer 18)
    MVTX+INTT+TPC…
    Both electrical and mechanical systems
https://indico.bnl.gov/event/4380/

## Slide 43: MVTX Eta Coverage
Eta = - ln(tan(theta/2))
Layer | Eta @Z=0 | Eta @Z=10cm | Eta @Z=9.0cm | Eta @Z=0/10cm (ALICE <R>) | <R> (mm) | dLz (mm)
1 | 2.36 | 1.12 | 1.33 | 2.41/1.16 | 25.85 | 135.5
2 | 2.10 | 0.92 | 1.11 | 2.14/0.95 | 33.65 | Lz–100 = 35.5
3 | 1.90 | 0.78 | 0.95 | 1.94/0.80 | 41.25 | Lz – 90 = 45.5
Note: MVTX radius increased by 1.3mm to fit sPHENIX beam pine, from the full proposal, 2/4/2018
R1 = 23.7 – 28.0 mm <R1> = 25.85 mm
R2 = 31.4 – 35.9 mm <R2> = 33.65 mm
R3 = 39.1 – 43.4 mm <R3> = 41.25 mm, dZ’ = 4.85cm, Lz’ = 135.5 – 48.5 = 87mm; R3 -> eta = 1.0

## Slide 44: MVTX – Bring sPHENIX to a New Horizon
Unambiguously determine quark energy loss mechanisms, particularly over the interesting transition region, pT ~ M
  Radiative dE/dX
  Collisional dE/dX
  Other effects
Expectations @sPHENIX
Learned @CERN
B-hadron
sPH-HF-2017-002
sPHENIX
B-jet
sPH-HF-2017-001
QM’17
pT >> M
pT << M
sPHENIX

## Slide 45: Expected Luminosities and Collision Rates

## Slide 46: dN/dη in p+p collisions
With |η|<2.0 region, dN(ALICE) ~2.9*dN(sPHENIX).
sPHENIX
ALICE

## Slide 47: dN/dη in MB Au+Au/Pb+Pb collisions
With |η|<2.0 region, dN(ALICE) ~4.6*dN(sPHENIX).
Ncoll(Au+Au)=258, Ncoll(Pb+Pb)=401.
sPHENIX
ALICE

## Slide 48: dN/dη in 0-10% Au+Au/Pb+Pb collisions
With |η|<2.0 region, dN(ALICE) ~5.1*dN(sPHENIX).
Ncoll(Au+Au)=962, Ncoll(Pb+Pb)=1670.
sPHENIX
ALICE

## Slide 49: Hit Density on STAR PXL at RHIC Environment
 | PXL inner | PXL outer
Radius (cm) | 2.8 | 8
MB pileup hits (cm-2) | 13 | ~3
UPC electrons (cm-2) | 33 | ~3
Total bkgd hits (cm-2) | 46 | ~6
MB signal Au+Au (cm-2) | ~8 | ~1
Simulation@50kHz
Signal hits fraction in MB (Central) events:
~15% (~30%) at PXL inner
Increasing fake matches in low pT
Technology chosen considering both physics and technology readiness
Au+Au MB real data (cm-2) | ~50 | ~5
Simulation
- Ming’s note:
With 5uS integration time, BG rate can be reduced by,
5/200 = 1/40
S/B ~ 8/1 for sPHENIX

## Slide 50: Hits and Event Data Rate
Event size: sPHENIX = 1/3 ALICE
Identical geometry for MVTX and ITS/IB(layer 0-2)
sPHENIX integration time ~5uS, less noise compared with ALICE with 10~20uS.

## Slide 51
48 inner staves;
48 RU boards;
6 FELIX boards;
- 8RU ->1 FELIX
Readout Units Required for ITS & sPHENIX

## Slide 52: sPHENIX DAQ Architecture
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Rack Room
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
Event Builder
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To the
RACF/HPSS
Calorimeters,
INTT, MBD
TPC, MVTX
SEB Sub-Event Buffer
EBDC Event Buffer and Data Compressor
ATP Assembles events and compresses data
Buffer Box data interim storage before sending data to the computing center

## Slide 53
ALPIDE Modes of Operation
The ITS is planned to be operated in two modes:
  Triggered mode: Pixels are latched with a short strobe window and read out based on an external trigger.
  Continuous mode: Pixels are latched using a long, periodic strobe window and read out.

## Slide 54: ALICE Data Rate and Dead Time

## Slide 55: sPHENIX Radiation Level

## Slide 56: Radiation Measurements in PHENIX
Used RadMons from CERN
  RadFET sensitive primarily to ionizing radiation
  Pin Diode sensitive to neutrons
  Both are integrating devices
Placed in the IR for RUNs 13-16
  Run 13: 510 GeV p-p
  Run 14: Mixed Heavy Ion Running
  Run 15: 100 GeV p-p
  Run 16: 200 GeV Au-Au
Locations:
  3 positioned on North Nose Cone @ ~ 3cm, ~8 cm and ~16 cm (shown)
  Others positioned inside the pistons, used for SiPM damage, … (Not shown)
From Eric Mannel
sPHENIX Directors Review, 3/2018

## Slide 57: RadFET Results
510 GeV p-p
Mixed Heavy Ion
100 GeV p-p
200 GeV Au-Au

## Slide 58: Pin Diode Fluence Measurements @PHENIX
For Au-Au running we expect @ sPHENIX EMCal:
  Integrated ionizing radiation dosages of order 10’s of kRad/run
  Integrated neutron fluences of order 2x1011 n/cm2
MVTX: <R>_0/1/2 = 2.6/3.4/4.1cm
MVTX R_0 fluence = 6~17 x1012 nEq/cm2
The dose due to collisions @PHENIX:
D_collisions / D_total = 61% @Run6
arXiv:0710.2676 [nucl-ex]

## Slide 59: ALICE ITS Upgrade – PRR 4/13/2018
RU/PU location

## Slide 60: ALICE ITS Upgrade
RU/PU location

## Slide 61: ALICE ITS Upgrade
RU/PU location

## Slide 62: ITS Readout - Radiation Load
Position respect to beam |  |  | Radiation levels (total) |  |  | 
r | z | Name | TID | 1 MeV neq fluence | High energy hadron flux* | Charged particle flux
[cm] | [cm] |  | [krad] | [cm-2] | [kHz cm-2] | [kHz cm-2]
2.2 | [-13.5 ÷ 13.5] | ITS L0 | 2734 | 1.7 × 1013 | 765 (770) | 890 (910)
43 | [-73.7 ÷ 73.7] | ITS L6 | 20 | 8.1 × 1011 | 3.4 (4.9) | 4.5 (6.7)
79 | [-260 ÷ 260] | TPC In | 5.6 | 7.0 × 1011 | 1.35 (1.8) | 1.7 (3.45)
100 | 330 | RE | ≈ 5 | ≈ 1.6 × 1011 | 0.86 | 1.7
258 | [-260 ÷ 260] | TPC Out | 0.86 | 1.4 × 1011 | 0.27 (0.37) | 0.2 (0.3)
290 | [-290 ÷ 290] | TRD | 0.6 | 1.2 × 1011 | 0.23 (0.31) | 0.15 (0.23)
TID & fluence = (table 1 × 1.3data taking efficiency + Table 2 / 10better vacuum) × 10safety factor
Safety factor of 10 on top of TID and fluence calculated as in the above line.
Hadrons and charged particles as for 50 kHz Pb-Pb collisions (table 1, worst case scenario).
The average value within the z span is reported first, in brackets the peak value within the z interval.
* Momentum > 20 MeV.

## Slide 63: ALICE ITS Upgrade

## Slide 64: ALICE ITS Upgrade

## Slide 65: ALICE ITS Upgrade

## Slide 66: Fermilab Test Beam Results

## Slide 67
LANL Fermilab Test Beam Setup 03/2018
4-ALPIDE Telescope + 4-SamTec cables + 1 RU + 1 FELIX(“CRU”)
LHC 40MHz
mockup
CLK recovered from
FELIX through GBT link;
Trigger from FELIX
4-ALPIDE Telescope
4 5-m SamTec Cables, 1.2Gbps
FELIX (“CRU”)
Online Display

## Slide 68
FELIX(“CRU”) in Server
KC705
LHC 40MHz
Mockup
4-ALPIDE Telescope;
5m long SamTec cables
4-ALPIDE Telescope Setup at Fermilab Test Beam
RU
Summary:
Successfully operated the full readout chain
Confirmed all communications links and data path
Confirmed telescope performance
  Primarily 120GeV proton beam; also with low energy pion beams
  Beam trigger rate ~7kHz
  Tested High ALPIDE occupancy runs, with 10cm lead bricks in front of the sensors
Nice work by Sho, Alex, Hubert, Chris + others