## Slide 1: sPHENIX MVTX Radiation Dosage after 5 years
Layer | <R> cm | TID, krad | NIEL (1), 1012Neq/cm2 | NIEL(2), 1012Neq/cm2
0 (scaling =1) | 2.6 | 1060 | 6.6 | 17
1 (scaling = 0.61) | 3.4 | 650 | 4.0 | 10
2 (scaling=0.43) | 4.1 | 460 | 2.8 | 7.3
ALICE L0 | 2.2(Min.) | 273 (tested OK up to 500) | 1.7 (tested OK up to 17) | -
Note:
- TID scales with Dosage, high energy particles
- NIEL(1): cross section scaling, from ALICE
- NIEL(2): phenix measurements, scaled to sPHENIX
Npart(sPHENIX, 200GeV) = 109.1, (0-92.2%)
N_coll = 4.1
Npart(ALICE, 5.5TeV) = 113.9 (0-100%)
N_coll(ALICE) = 5.58

## Slide 2: Radiation Level in sPHENIX (I): TID/NIEL (high energy particles) - by flux cross section scaling: LHC vs RHIC
LHC: Pb-Pb 5.5TeV,
  sigma_NN = 72mb
  Sigma_PbPb = 7750mb
  L = 13nb-1
N_evts = 7750mb x 13nb^-1
= 100 x109
RHIC: AuAu 200GeV
  Sigma_NN = 42mb
  Sigma_AuAu = 7000mb
  L = 214nb-1
N_evts = 7000mb x 214nb^-1
= 1,500 x 109
RHIC (AuAu) dN/deta = 1/4.5 LHC(PbPb):
Flux (RHIC, AuAu) = 1/4.5 x 1500/100 = 3.3 x LHC(PbPb)
Flux (RHIC, pp) = 0.32 x Flux (RHIC, AuAu), R_Npart = 0.5
Total flux(RHIC: AuAu+pp+pA) = 3.3 x (1+0.32) x LHC(PbPb)
= 4.4 ALICE(PbPb) Flux
sPHENIX/MVTX L0:
- NIEL = 0.88 x 4.4 x (1.7 x10^12) =6.6 x1012 Neq/cm2
- TID = 0.88 x 4.4 x (273 krad) = 1060 krad = 1.1 Mrad
ALICE Note: PUB-2443
ALICE L0: 13n-1PbPb + 50nb-1 + 6pb-1
(PbPb: 97% Lum_total, dominant)
@L0 R=2.2cm, sPHENIX: dR=+1.25mm
R_factor = (2.2/2.35)^2 =0.88
TID = 273 krad
NIEL = 1.7 x 1012 Neq/cm2
http://dde.web.cern.ch/dde/glauber_lhc.htm

## Slide 3: Radiation Level in sPHENIX (II): NIEL - by PHENIX measurements
Projected sPHENIX radiation level after 5-year operation
  AuAu: L = 214 nb-1 = 8,300 pb-1
    @R=10cm, D_AA = 214/50 x 0.2x1012 = 0.86x1012 Neq/cm2
  pp/pA: L = 1340 pb-1
    @R=10cm, D_pp = 1340/700 x 0.3x1012 = 0.57x1012 Neq/cm2
MVTX:
R0/R1/R2 = 2.6/3.4/4.1cm
R-factor:
(10/2.6)1.83 = 11.8
(10/3.4)1.83 = 7.2
(10/4.1)1.83 = 5.1
Fluence from AuAu runs:
- L0 = 10 x 1012 Neq/cm2
Fluence from pp runs:
- L0 = 6.7 x 1012 Neq/cm2
Totals:
L0 = 1.7 x 1013 Neq/cm2
L1 = 1.0 x 1013 Neq/cm2
L2 = 0.7 x 1013 Neq/cm2
RHIC-II projected dosage based
on PHENIX measurements:
arXiv: 0710.2676 [nucl-ex]
Neq = 1MeV Neutron Equivalent

## Slide 4: Radiation Level in sPHENIX: TID/Flux - by PHENIX measurements
Projected sPHENIX radiation level after 5-year operation
  AuAu: L_AuAu = 214 nb-1 = 8,300 pb-1
  pp+pA: L_pp = 1,340 pb-1
  R_Npart = 0.5, low pT @RHIC,
  Effective AuAu-equivalent luminosity (for TID/flux) = L_AuAu + L_pp/R_Npart = 214nb-1 (1 + 1340/8300/R_Npart) = 214 (1+0.32) nb-1 = 282nb-1
  AuAu equivalent collisions = 1,500 x 109 x (1 + 0.32)
ALICE PbPb: 100 x 10^9 collisions:
Flux ratio: sPHENIX/ALICE = 1/4.5 x (1500 x 1.32)/100 = 4.4
sPHENIX TID L0 = (R: 2.2/2.35)^2 x 4.4 x 273 krad = 1050 krad
MVTX:
R0/R1/R2 = 2.6/3.4/4.1cm
R-factor:
(10/2.6)1.83 = 11.8
(10/3.4)1.83 = 7.2
(10/4.1)1.83 = 5.1
Fluence from AuAu runs:
- L0 = 10 x 1012
Fluence from pp runs:
- L0 = 6.7 x 1012 Neq/cm2
Totals:
L0 = 1.7 x 1013 Neq/cm2
L1 = 1.0 x 1013 Neq/cm2
L2 = 0.7 x 1013 Neq/cm2
RHIC-II projected dosage based
on PHENIX measurements:
arXiv: 0710.2676 [nucl-ex]
ALICE Note: PUB-2443
ALICE L0: 13n-1PbPb + 50nb-1 + 6pb-1
(PbPb: 97% Lum_total, dominent)
TID = 273 krad
NIEL = 1.7 x 1012 Neq/cm2
http://dde.web.cern.ch/dde/glauber_lhc.htm

## Slide 5: Event Multiplicity and Collision Rates: sPHENIX vs ALICE
 | ALICE (Run3) | sPHENIX (Max) | Ratio of data rates sPHENX/ALICE
Pb+Pb / Au+Au | 50kHz | 200 kHz | 0.27
p+p | 200kHz | 13 MHz | 6.5
Trigger/Readout | 50 kHz | 15 kHz | -
MB Event track multiplicity dN/dη: sPHENIX = 1/3 ALICE (pp), 1/4.5 ALICE(AA)
sPHENIX triggered data rate well within readout specs
sPHENIX
ALICE
p+p collisions
sPHENIX/ALICE ~1/3
A+A collisions
sPHENIX/ALICE ~1/4.5
ALICE
sPHENIX

## Slide 6: Projected sPHENIX Data Rates
Readout Units: 3 GBTX @ 0.4 GB/s = 1.2 GB/s >133MB/s
GBTx: 3.2-4.48Gb/s, 0.4 GB/s
FELIX/DAM: 48 input on FELIX, twice the number needed to support 8 RUs (3 links)
2x 8-lane PCIe Gen 3 @ 7880 MB/s = 15,760 MB/s > 848 MB/s
MVTX readout hardware capacity > 10 x Expected data rate
Alex & Sho
#1,2,3
Note: test beam showed noise < 10-5
(FELIX)

## Slide 7: Expected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX integrated luminosities after 5-year operation
  AuAu: Lum. = 214 nb-1
  pp+pAu: Lum. = 1340 pb-1
Projected sPHENIX MVTX fluence, L0 = 0.6 ~ 1.7 x1013 Neq/cm2
Fluences of outer layers:
  L1 = 0.6 x L0
  L2 = 0.4 x L0
- Within the ALPIDE performance specs. (1.7 x1013 Neq/cm2)
- Risk mitigation: 36 spare staves (75%) to replace damaged ones
Leo
#1
Staves per layer:
L0 = 12
L1 = 16
L2 = 20
TID: sPHENIX ~ 4.5 ALICE

## Slide 8: Staves – Specification/radiation tolerance
sPhenix TID radiation levels (5 years) are expected to be 4.5 times this.
NIEL levels are expected to be 1.7 x 1013 1 MeV Neq

## Slide 9
From L. Musa – 7/26/2017 DOE review
Staves – Specification/radiation tolerance
Sensors have been tested to full MVTX NIEL levels and 1/5.4 of the TID.
Spare staves are available for replacement of staves that show degradation.

## Slide 10: Staves – Specification/radiation tolerance
Pixel Sensor Chip – Resolution and Cluster Size
From L. Musa – 7/26/2017 DOE review

## Slide 11: Expected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX radiation level after 5-year operation
  AuAu: Lum = 214 nb-1
    @R=10cm, D_AA = 214/50 x 0.2x1012 = 0.86x1012 Neq/cm2
  pp/pA: Lum = 1340 pb-1
    @R=10cm, D_pp = 1340/700 x 0.3x1012 = 0.57x1012 Neq/cm2
Projected sPHENIX MVTX fluence, L0 = 0.6 ~ 1.7 x1013 Neq/cm2
Fluences:
  L1 = 0.6 x L0
  L2 = 0.4 x L0
Within the ALIPDE performance specs.

## Slide 12: ITS Radiation Load
Position respect to beam |  |  | Radiation levels (total) |  |  | 
r | z | Name | TID | 1 MeV neq fluence | High energy hadron flux* | Charged particle flux
[cm] | [cm] |  | [krad] | [cm-2] | [kHz cm-2] | [kHz cm-2]
2.2 | [-13.5 ÷ 13.5] | ITS L0 | 2734 | 1.7 × 1013 | 765 (770) | 890 (910)
43 | [-73.7 ÷ 73.7] | ITS L6 | 20 | 8.1 × 1011 | 3.4 (4.9) | 4.5 (6.7)
79 | [-260 ÷ 260] | TPC In | 5.6 | 7.0 × 1011 | 1.35 (1.8) | 1.7 (3.45)
100 | 330 | RE | ≈ 5 | ≈ 1.6 × 1011 | 0.86 | 1.7
258 | [-260 ÷ 260] | TPC Out | 0.86 | 1.4 × 1011 | 0.27 (0.37) | 0.2 (0.3)
290 | [-290 ÷ 290] | TRD | 0.6 | 1.2 × 1011 | 0.23 (0.31) | 0.15 (0.23)
Hadrons and charged particles as for 50 kHz Pb-Pb collisions

## Slide 13: Expected Luminosities and Collision Rates

## Slide 14: dN/dη in p+p collisions
With |η|<2.0 region, dN(ALICE) ~2.9*dN(sPHENIX).
sPHENIX
ALICE

## Slide 15: dN/dη in MB Au+Au/Pb+Pb collisions
With |η|<2.0 region, dN(ALICE) ~4.6*dN(sPHENIX).
Ncoll(Au+Au)=258, Ncoll(Pb+Pb)=401.
sPHENIX
ALICE

## Slide 16: dN/dη in 0-10% Au+Au/Pb+Pb collisions
With |η|<2.0 region, dN(ALICE) ~5.1*dN(sPHENIX).
Ncoll(Au+Au)=962, Ncoll(Pb+Pb)=1670.
sPHENIX
ALICE

## Slide 17: Hit Density on STAR PXL at RHIC Environment
 | PXL inner | PXL outer
Radius (cm) | 2.8 | 8
MB pileup hits (cm-2) | 13 | ~3
UPC electrons (cm-2) | 33 | ~3
Total bkgd hits (cm-2) | 46 | ~6
MB signal Au+Au (cm-2) | ~8 | ~1
Simulation@50kHz
Signal hits fraction in MB (Central) events:
~15% (~30%) at PXL inner
Increasing fake matches in low pT
Technology chosen considering both physics and technology readiness
Au+Au MB real data (cm-2) | ~50 | ~5
Simulation
- Ming’s note:
With 5uS integration time, BG rate can be reduced by,
5/200 = 1/40
S/B ~ 8/1 for sPHENIX

## Slide 18: Hits and Event Data Rate
Event size: sPHENIX = 1/3 ALICE
Identical geometry for MVTX and ITS/IB(layer 0-2)
sPHENIX integration time ~5uS, less noise compared with ALICE with 10~20uS.

## Slide 19
48 inner staves;
48 RU boards;
6 FELIX boards;
- 8RU ->1 FELIX
Readout Units Required for ITS & sPHENIX

## Slide 20: Radiation Measurements in PHENIX
Used RadMons from CERN
  RadFET sensitive primarily to ionizing radiation
  Pin Diode sensitive to neutrons
  Both are integrating devices
Placed in the IR for RUNs 13-16
  Run 13: 510 GeV p-p
  Run 14: Mixed Heavy Ion Running
  Run 15: 100 GeV p-p
  Run 16: 200 GeV Au-Au
Locations:
  3 positioned on North Nose Cone @ ~ 3cm, ~8 cm and ~16 cm (shown)
  Others positioned inside the pistons, used for SiPM damage, … (Not shown)
From Eric Mannel
sPHENIX Directors Review, 3/2018

## Slide 21: RadFET Results
510 GeV p-p
Mixed Heavy Ion
100 GeV p-p
200 GeV Au-Au
1 Gy = 100 rad

## Slide 22: Pin Diode Fluence Measurements @PHENIX
For Au-Au running we expect @ sPHENIX EMCal:
  Integrated ionizing radiation dosages of order 10’s of kRad/run
  Integrated neutron fluences of order 2x1011 n/cm2
MVTX: <R>_0/1/2 = 2.6/3.4/4.1cm
MVTX R_0 fluence = 6~17 x1012 nEq/cm2
The dose due to collisions @PHENIX:
D_collisions / D_total = 61% @Run6
arXiv:0710.2676 [nucl-ex]

## Slide 23: ALICE ITS Upgrade – PRR 4/13/2018
RU/PU location

## Slide 24: ALICE ITS Upgrade
RU/PU location

## Slide 25: ALICE ITS Upgrade
RU/PU location

## Slide 26: ITS Readout - Radiation Load
Position respect to beam |  |  | Radiation levels (total) |  |  | 
r | z | Name | TID | 1 MeV neq fluence | High energy hadron flux* | Charged particle flux
[cm] | [cm] |  | [krad] | [cm-2] | [kHz cm-2] | [kHz cm-2]
2.2 | [-13.5 ÷ 13.5] | ITS L0 | 2734 | 1.7 × 1013 | 765 (770) | 890 (910)
43 | [-73.7 ÷ 73.7] | ITS L6 | 20 | 8.1 × 1011 | 3.4 (4.9) | 4.5 (6.7)
79 | [-260 ÷ 260] | TPC In | 5.6 | 7.0 × 1011 | 1.35 (1.8) | 1.7 (3.45)
100 | 330 | RE | ≈ 5 | ≈ 1.6 × 1011 | 0.86 | 1.7
258 | [-260 ÷ 260] | TPC Out | 0.86 | 1.4 × 1011 | 0.27 (0.37) | 0.2 (0.3)
290 | [-290 ÷ 290] | TRD | 0.6 | 1.2 × 1011 | 0.23 (0.31) | 0.15 (0.23)
TID & fluence = (table 1 × 1.3data taking efficiency + Table 2 / 10better vacuum) × 10safety factor
Safety factor of 10 on top of TID and fluence calculated as in the above line.
Hadrons and charged particles as for 50 kHz Pb-Pb collisions (table 1, worst case scenario).
The average value within the z span is reported first, in brackets the peak value within the z interval.
* Momentum > 20 MeV.

## Slide 27: ALICE ITS Upgrade

## Slide 28: ALICE ITS Upgrade

## Slide 29: ALICE ITS Upgrade