## Slide 1: Integration of staves + RU + FELIX into sPHENIX
Alex Tkatchev, Sho Uemura
Los Alamos National Laboratory
July 19-20, 2018

## Slide 2: Charge
Does the current design demonstrate that the MVTX Staves and Readout Units will be compliant with its specifications?
Can the data from MVTX staves be extracted, readout and integrated into sPHENIX Data Acquisition System?
Are the electrical interfaces of the Staves and Readout Units to the other sPHENIX components at a proper level of understanding?

## Slide 3: Acronyms
ALICE – A Large Ion Collider Experiment
ITS – Inner Tracking System
ALPIDE – ALICE Pixel Detector
RU – Readout Unit, designed for ALICE
GBTx – Radiation Tolerant Gigabit Transceivers, designed by CERN
GBT-SCA – Radiation Tolerant Slow Control Adapter
FELIX – Front End Link Exchange, designed for ATLAS
RCDAQ – Really Cool Data Acquisition
BER – Bit Error Rate, used for testing
PRBS – Pseudo-Random Binary Sequence, used for testing
TMR – Triple Modular Redundancy
SEU – Single Event Upset
SEL – Single Event Latch-up
TID – Total Ionizing Dose
LET – Linear Energy Transfer
DMA – Direct Memory Access
PCIe - Peripheral Component Interconnect Express

## Slide 4: MVTX Electronics Overview
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
ALPIDE
Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 5: 9-sensor Stave Highlights
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 6: 9-sensor Stave Highlights
Control+Trigger
Stave– 9 chips, common clock and control, independent data lines
Chip1
Chip2
Chip3
Chip4
Chip5
Chip6
Chip7
Chip8
Chip9
Bias, Readout, Control
Readout (zero suppression)
Readout (zero suppression)
Readout (zero suppression)
Readout (zero suppression)
512 pixel rows
1024 pixel columns
In pixel: Amplification
Discrimination
3 hit storage registers (MEB)
Clock
ALPIDE Architecture Highlights:
Multi-event buffering
Data output rate:1.2 Gb/s, 0.6Gb/s, or 0.4Gb/s
Zero suppression on ALPIDE
Readout modes: triggered or continuous
Calibration: Internal charge injection (pulsing logic)
Static Pattern Generation and PRBS
Pixel masking functionality
MVTX will use triggered mode at 1.2Gb/s
Serial Outputs (1.200 Gbps)
THR
COMP
AMP

## Slide 7: Timing
Threshold
Amp. out
Sensing node
Amplifier
Comparator
And
Threshold
Strobe window
Pixel memory
Pixel cell
Only pixel with signal higher than threshold DURING the strobe window will get latched in memory
Cmp. out
Strobe window
Signal
Analog “slow” shaping time acts as a memory (µs order) to buffer the signal until the trigger arrives.
Called “pulse length”
Latch set
Time
Confirmed at LANL: pulse length can be extended to meet sPHENIX trigger latency requirement
(Charge 1)

## Slide 8: ALPIDE in triggered mode, RU trigger filtering
From GTM to RU
From RU to sensor
From sensor to RU
Triggers from the
Timing System (GTM)
≈ trg latency
Triggers to the sensor
Labeled with trgID, through the Ctrl line.
Time [µs]
0
-1
1
2
3
4
5
6
7
0001
0010
0011
0100
Time [µs]
0
-1
1
2
3
4
5
6
7
Busy flag
The RU can retrieve which trigger has failed even if the trailer is corrupted/missing
0001
0100
0011
0010
Time [µs]
0
-1
1
2
3
4
5
6
7
Data from the sensor
Trailers labeled with trgID, through the Data line.
Multiple GTM triggers can be grouped into a single trigger, sent to the sensor from the RU.
The RU labels the data frame with all the triggers associated to its trgID
Triggers close in time re-record the same information, and the sensor can handle a minimum trigger spacing of about 1 µs. The RU will therefore “filter” close-in-time (< 1 µs) triggers.

## Slide 9: ALPIDE Data format and BUSY
DS0
DS1
DL0
DL1
DL2
TRAILER
IDLE
DS0
DS1
IDLE
TIME
REGION
HEADER
IDLE
IDLE
IDLE
IDLE
IDLE
Data Long
Data Short
Hit Data
Chip Trailer
Time
Data Bytes
HEADER 0
HEADER 1
Chip Header
DS0
DS1
DL0
DL1
DL2
TRAILER
DS0
DS1
TIME
HEADER 0
REGION
HEADER
IDLE
HEADER 1
IDLE
DATA LONG
DATA SHORT
CHIP HEADER
CHIP TRAILER
BUSY ON
BUSY OFF
BUSY
BUSY- chip near saturation of its data processing capabilities (multi-event buffers full).
ALPIDE simulations by ALICE show <10-6 deadtime (busy asserted, events flagged) at 100 kHz trigger rate.
Busy is the way the ALPIDE informs the RU of close-in-time triggers.

## Slide 10: TMR protection on ALPIDE
16 double columns
32 readout regions
Region Readout (1)
128x24b DPRAM
RR (2)
RR (3)
RR (32)
Top Readout Unit
Data Management Unit
Readout Sequencing
Control Bus Logic
Configuration Registers
Pixels Config
8b DACs
11b ADC
Differential Control Port
(40 Mbps)
Bandgap +
Temp Sens
Data Transmission Unit
Driver
PLL
Serializer
Serial Out Port
(1200 Mbps / 600 Mbps/ 400 Mbps)
24b×40MHz
24b×40MHz
8b/10b
30b×40MHz
32:1 DATA MUX
Triggers
ALPIDE elements potentially SEU sensitive
1. Pixel Logic: mask and pulse registers (not protected)
Mitigation : Refresh pixel mask bits in background
2. Periphery logic: state machine, FIFO pointers, counters and configuration registers with TMR
3. Top readout unit and data management unit FIFO with Hamming protection
4. Region Readout DPRAM partially protected
format protected
hit data not protected
5. Data Transmission Unit: PLL and Serializer with TMR
1
2
3
4
5
RESET_VALUE
FF0
OUT
FF1
FF2
VOTING LOGIC
SEU_ERROR
IN
AUTO CORRECTION
Basic Triple Modular Redundancy register cell

## Slide 11: ALPIDE Radiation Upsets
SEU impact estimates for elements in chip matrix and periphery (based on cross section values measured using CERN beam tests):
  Operation-critical registers protected using TMR
  Probability of corrupted single hit clusters below 1×10-10 s-1
  <0.1% of pixel mask bits toggled each hour
Pixel mask bits will be refreshed periodically in the background (10 ms deadtime to refresh all pixels in MVTX)
SEL cross section measured per ALPIDE
  About 1 SEL per day in MVTX, automatically recovered
The measured SEU and SEL cross sections are not a risk for the operational stability of MVTX
TID effects will be discussed in the stave presentation by Leo Greiner

## Slide 12: Readout Unit Highlights
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Front End-Readout Unit
Data readout from Stave
Stave control and monitoring
Trigger & busy management
Power control and monitoring
Data building and transmission through the rad-hard Gigabit Transceivers

## Slide 13: Samtec cables
From CERN Team:
2.3 m + 6 m long (meets MVTX requirements)
Tests show no PRBS errors over 48 h-equivalent of a single chip
BER < 2.22 * 10−14
Transmission is reliable (eye diagram is open) down to minimum ALPIDE driver strength
Stave
Patch Panel
Readout Unit
Eye diagram
2.3 m
6 m

## Slide 14: Readout Unit
1 trigger downlink directly
VTTx
VTRx
VTRx sm
1 uplinks (data/CTRL) to FELIX
2 uplink (data) to FELIX
1 downlink (CTRL) from FELIX
Power Boards link
Diagnostic / busy IO
Transition Board
Samtec Firefly cable
CAN bus
Architecture Highlights:
Xilinx Kintex Ultrascale FPGA
ProAsic FPGA (Detect and Mitigate Radiation Upsets; Scrubbing)
GBTx ASIC (Radiation hard Giga Bit Transceiver) to FELIX
  VTRx: Transceiver up & down link
  VTTx: Double Transmitter 2 * up link
GBT-SCA: Rad. hard Slow Controls Adapter for monitor and control
Samtec “FireFly” copper twinax cable to the stave
Covered in more detail in
Readout Unit Overview
by Jo Schambach
Notes: Bla foo this is a test

## Slide 15: System Power Overview
Power Board
Readout Unit
RU configures and monitors
stave current and voltage
through I2C interface of power board
V, I monitor
PT100 Interface
Overcurrent
detection
Overcurrent
reset
Overcurrent
threshold
Bias section
PT100 Interface
PT100 Interface
Negative LDO
FET Switch
V adjust (DP)
V control /
V, I monitor
Power in (3.3V)
I2C isolator
x16
Power in (-5V)
RDO
Interface
(I2C)
Positive voltage domains
FET Switch
FET Switch
FET Switch
x3
Detector
Readout Unit
Bulk Power
x4
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
LDO
Power Board designed by
LBNL
MVTX staves

## Slide 16: Power Board Radiation
Power Boards located alongside RUs, same environment
Power channels tested to 17 krad, bias channels to 20 krad
  Good stability (no self oscillations)
  No degradation of noise
  Negligible shifts of voltages and currents
Full production Power Board tested at CERN to 14.8 krad TID, no significant effect
Single Event Upsets observed on current DAC and negative voltage regulator;
  expect weeks of operation between power system interrupts
Radiation studies by
LBNL

## Slide 17
FELIX Highlights
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
ALPIDE Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Back End-FELIX:
Data readout from 8 Readout Units
Slow Control and Monitoring of Stave and RU
Trigger and Timing systems interface
Data aggregation and sub-event packaging
Data transmission through the PCIe to Server CPU

## Slide 18: FELIX (also used by sPHENIX TPC)
Architecture Highlights:
Xilinx Kintex Ultrascale KU115 FPGA
48 bi-directional GBT links
16 lane Gen3 PCIe
Mezzanine site for sPHENIX timing system card
Performance:
PCIe Tx > 100Gb/s
FELIX v1.5
FELIX v2.0
sPHENIX Timing Mezzanine
FELIX Block Diagram
FELIX designed by BNL

## Slide 19: FELIX Clock Distribution
Test point
Si5345 Block Diagram
FELIX Clock Block Diagram
Current lab setup: External clock taken as input on test points, and sent to an on-board si5345 (configurable PLL) to generate the 40Mhz clock required by FELIX.
sPHENIX: FELIX will take the RHIC 9.362 MHz clock from the sPHENIX Timing System. Mezzanine Card will convert the 40Mhz clock required by FELIX.

## Slide 20: MVTX Full Chain
Successfully configured, triggered and readout Stave:
  Readout Unit configures Stave
  FELIX distributes clock to Readout Unit
  Readout Unit distributes clock to the Stave
  Stave is triggered, sends data at 1.2Gb/s
  Configured GBT link to recover clock from FELIX
  RU receives data and sends it to FELIX over GBT optical link
  FELIX packs data, stores it on disk using RCDAQ
  ALPIDE triggered and read out at 15kHz, 448 hits
  Emulated 8 RU’s using 1 fiber link per RU on FELIX, 15kHz
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave
Demonstrated Full MVTX Chain Readout
(charge 1 & charge 2 & charge 3)

## Slide 21: sPHENIX DAQ Architecture
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Rack Room
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
Event Builder
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To the
RACF/HPSS
Calorimeters, INTT, MBD
TPC
Acronyms:
FEE Front End Electronics
FELIX FrontEnd LInk eXchange
EBDC Event Buffer and Data Compressor
ATP Assembly and Trigger Processors
Buffer Box Interim storage
FEM Front End Module
DCM2 Data Collection Module
SEB Sub-Event Buffer
MVTX
MVTX Hardware:
  48 Staves
  48 FEE (Readout Units v2.0)
  6 FELIX v2.0
  6 EBDC servers

## Slide 22: RCDAQ
RCDAQ = sPHENIX Data Acquisition framework
  rcdaq plugin developed which will serve as a conduit between the FPGA DMA PCIe endpoint and software used to transfer data to sPHENIX Data Acquisition framework
  Plots generated by RCDAQ in the initial stage of integration using pulsed mode of the ALPIDE Pixels readout by Readout Unit and FELIX in the lab.
Full MVTX integrated with sPHENIX DAQ
(charge 2)
RCDAQ developed by Martin Purschke, BNL

## Slide 23
FELIX in Server
KC705
Process Scintillator Trigger
40 Mhz
Clock
4-ALPIDE Telescope;
5m long SamTec cables
RUv1.0
Fermilab Beam:
Primarily 120GeV proton beam
  also with low energy pion beams
Approximate beam trigger rate 7kHz
4-ALPIDE Telescope at Test Beam

## Slide 24: Test Beam Block Diagram
CLK recovered from
FELIX through GBT link;
Trigger from FELIX
4-ALPIDE Telescope
4 5m SamTec Cables, 1.2Gbps
On Carrier
Board
Slow Controls
Online Monitoring

## Slide 25: Test Beam Results
Successfully operated the full readout chain
  RU configured and readout 4 ALPIDEs
  FELIX successfully integrated into RCDAQ
Online monitoring
  Hit distribution, relative alignment
Sensor performance
  Cluster size
  Threshold parameters
  Trigger delay
High multiplicity events
  ALPIDE occupancy runs with 10cm of lead
Analysis confirmed telescope performance
  Hit resolution < 5 um
Online monitoring and offline data analysis
using RCDAQ and Fun4All (sPHENIX framework)
(charge 2)

## Slide 26: Estimated Data Rate
Readout Units 3 GBTX @ 400 MB/s = 1200 MB/s >133MB/s
FELIX (48 input on FELIX, twice the number needed to support 8 RUs (3 links each))
2x 8-lane PCIe Gen3 @ 7880 MB/s = 15760 MB/s > 848 MB/s
Meets specification (charge 1)
RU
FELIX
MVTX
Worst Case Conservative Estimates

## Slide 27: Summary
Does the current design demonstrate that the MVTX Staves and Readout Units will be compliant with its specifications? Yes.
  Triggered system at 15kHz using pulser at expected MVTX data rate, and approximately 7Khz at random during beam test.
Can the data from MVTX staves be extracted, readout and integrated into sPHENIX Data Acquisition System? Yes.
  Test beam data from ALPIDE sensors was taken using full MVTX readout chain:
    ALPIDE Sensor->Readout Unit->FELIX->rcdaq (sPHENIX daq).
  Data was recorded in PRDF (sPHENIX data format) and is being analyzed in Fun4All (sPHENIX analysis framework).
Are the electrical interfaces of the Staves and Readout Units to the other sPHENIX components at a proper level of understanding? Yes.
  The optical interface from the Readout Unit to the other sPHENIX components has been validated with FELIX.
    Demonstrated clock and trigger and gigabit data transmission.
  Power System is well understood.