## Slide 1: Integration of staves + RU + FELIX into sPHENIX

## Slide 2: Charge
Does the current design demonstrate that the MVTX Staves and Readout Units will be compliant with its specifications?
Can the data from MVTX staves be extracted, readout and integrated into sPHENIX Data Acquisition System?
Are the electrical interfaces of the Staves and Readout Units to the other sPHENIX components at a proper level of understanding

## Slide 3: Outline
Specifications/system description
Integration
Beam test Results

## Slide 4: Specifications
Trigger rate: 15KHz
Data rate:
  133 MB/s per stave
  5089 MB/s for MVTX worst-case
Resolutions: ask Darren

## Slide 5: MVTX Electronics Overview
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 6: Sensor
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX

## Slide 7: Stave
Control+Trigger
Stave– 9 chips, common clock and control, independent data lines
Serial Outputs (1.200 Gbps)
Chip1
Chip2
Chip3
Chip4
Chip5
Chip6
Chip7
Chip8
Chip9
THR
COMP
AMP
Bias, Readout, Control
Readout (zero suppression)
Readout (zero suppression)
Readout (zero suppression)
Readout (zero suppression)
512 pixel rows
1024 pixel columns
In pixel:
Amplification
Discrimination
3 hit storage registers (MEB)
Clock
ALPIDE Architecture Highlights
Multi-event buffering capability
-reduces Readout data throughput requirements
Digital data output
Data output rate at 1.2 Gb/s, 0.6Gb/s, or 0.4Gb/s
Pixel pitch 28x28μm2
Material budget:~0.3%/layer
Readout rate: continuous or triggered
State Of the Art:

## Slide 8: MVTX Overview Readout Unit
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Experimental Hall
Front End-Readout Unit
Data readout from Stave
Stave status and power control
Control and monitoring to/from the sensors
Trigger & busy management
Data building and transmission through the rad-hard Giga Bit Transceivers
8

## Slide 9: Readout Unit
1 trigger downlink directly
to ensure low latency
VTTx
VTRx
VTRx sm
1 uplinks (data/CTRL) to FELIX
2 uplink (data) to FELIX
1 downlink (CTRL) from FELIX
Power Boards link
Diagnostic / busy IO
Transition Board
Samtec Firefly cable
CAN bus
State Of the Art:
Xilinx Kintex Ultrascale FPGA
ProAsic FPGA (Manage Radiation Upsets)
GBT ASIC (Rad. Tolerant Giga Bit Transceiver)
  VTRx: Transciver up & down link
  VTTx: Double Transmitter 2 * up link:
Special order (Halogen Free) Samtec firefly copper twinax cable interface
  9 independent 1.2Gb/s data streams
  1 40MHz Clock
  1 Control Line
Notes: Bla foo this is a test

## Slide 10: System Power Overview
reg
reg
reg
reg
V, I mon/buffer
Power in
32 reg
PT100 interface
Overcurrent
detection
Overcurrent
reset
Power Board
RDO
interface
Overcurrent
threshold
reg
reg
V adjust
Isolated bias section
reg
V, I mon/buffer
switch
x8
10
Breakout Boards
Bias daisy chain
to next PB
CAEN
power
CAEN
bias
Infrastructure GND
to VME backplane
Readout
Unit
CANbus
I2C control

## Slide 11: cables

## Slide 12
FELIX(“CRU”) in Server
KC705
LHC 40MHz
Mockup
4-ALPIDE Telescope;
5m long SamTec cables
4-ALPIDE Telescope Setup at Fermilab Test Beam
RU
Summary:
Successfully operated the full readout chain
Confirmed all communications links and data path
Confirmed telescope performance
  Primarily 120GeV proton beam; also with low energy pion beams
  Beam trigger rate ~7kHz
  Tested High ALPIDE occupancy runs, with 10cm lead bricks in front of the sensors

## Slide 13: Fermilab Beam Test Block Diagram
CLK recovered from
FELIX through GBT link;
Trigger from FELIX
4-ALPIDE Telescope
4 5m SamTec Cables, 1.2Gbps

## Slide 14: Summary
Successfully operated the full readout chain
  RU Configured and readout 4 ALPIDEs
  FELIX successfully integrated into RCDAQ
Sensor Performance
  Cluster Size
  Threshold parameters
  trigger delay
High multiplicity events
  ALPIDE occupancy runs with 10cm lead bricks
Online Monitoring
  Hit distribution, relative alignment
Analysis confirmed telescope performance
  Hit resolution < 5 um

## Slide 15
MVTX Overview FELIX
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Counting House
Back End-FELIX:
Data readout from 8 Readout Units
Slow Control and Monitoring to/from sensors
Trigger and Timing systems interface
Data aggregation and sub-event packaging
Data transmission through the PCIe to Server CPU

## Slide 16: FELIX
State Of the Art:
Xilinx Kintex Ultrascale FPGA
48 bi-directional GBT links
16 lane Gen3 PCIe
Performance Summary:
PCIe Tx > 101.7 Gb/s
FEE Rx < 80 Gb/s

## Slide 17
Put picture here of the Rus conneted to felix and emphasize connection to the outside world of MVTX are all optical!

## Slide 18: Data Rate Requirements
Readout Units 3 GBTX @ 0.4 GB/s = 1.2 GB/s >133MB/s
GBTx: 3.2-4.48Gb/s, 0.4 GB/s
FELIX (48 input on FELIX, twice the number needed to support 8 RUs (3 links))
2x 8-lane PCIe Gen 3 @ 7880 MB/s = 15760 MB/s > 848 MB/s
DAREN BOX

## Slide 19: MVTX Full Chain
Once the Readout Unit arrived, successfully configured, triggered and readout Stave:
  Readout Unit configures Stave using USB interface
  FELIX distributes clock to Readout Unit
  Readout Unit distributes clock to the Stave
  Stave is triggered, sends data at 1.2Gb/s
  Configured GBT link to recover clock from FELIX
  Readout Unit receives the data and sends the data to FELIX over fiber using GBT link
  FELIX packs data, stores it on disk using RCDAQ
  ALPIDE triggered and read out at 15kHz, 448 hits
  Developed prototype RCDAQ plugin
  FELIX packs and places ALPIDE data on disk
  Emulated 8 RU’s using 1 fiber link per RU on FELIX, 15kHz
Demonstrated Full MVTX Chain Readout
Readout
Unit
Stave
FELIX
Server + FELIX
Readout Unit + Stave

## Slide 20: RCDAQ
RCDAQ = sPHENIX DAQ
  Our accomplishments of integrating FELIX with RCDAQ prove that MVTX should tie into sPHENIX day one.
  Plots generated by RCDAQ show pulsed Pixels readout by Readout Unit and FELIX
Full MVTX Readout Chain integrated with sPHENIX DAQ

## Slide 21: sPHENIX DAQ Architecture
DCM
DCM
DCM
DCM2
SEB
SEB
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Buffer Box
Rack Room
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
DCM2
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
DCM
DCM
DCM
FEM
Event Builder
SEB
EBDC
FELIX
EBDC
FELIX
EBDC
FELIX
Network
Switch
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
ATP
Buffer Box
Buffer Box
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
DCM
DCM
DCM
FEE
To the
RACF/HPSS
Calorimeters,
INTT, MBD
TPC, MVTX
SEB Sub-Event Buffer
EBDC Event Buffer and Data Compressor
ATP Assembles events and compresses data
Buffer Box data interim storage before sending data to the computing center

## Slide 22: Summary
Successfully operated the full readout chain
  RU Configured and readout 4 ALPIDEs
  FELIX successfully integrated into RCDAQ
Sensor Performance
  Cluster Size
  Threshold parameters
  trigger delay
High multiplicity events
  ALPIDE occupancy runs with 10cm lead bricks
Online Monitoring
  Hit distribution, relative alignment
Analysis confirmed telescope performance
  Hit resolution < 5 um

## Slide 23: Risk Mitigation
Risks:
Previous LDRD Review
Custom Electronics concerns
CRU FELIX finalization
BNL Directors Review
MVTX readout scheme integration into sPHENIX DAQ
Achievements
Successfully demonstrated full readout chain:
  STAVE->Readout Unit->FELIX
  Successfully integrated readout chain with RCDAQ (sPHENIX DAQ)
  Validated FELIX and Readout Unit performance for MVTX
    System triggered at 15Khz
    emulating 8 RU’s on FELIX
  Power System at LANL
Reduced cost of LDRD Contingencies

## Slide 24
azv