## Slide 1: sPHENIX MVTX Cost and Schedule Review MVTX Mechanical Design
Walter Sondheim LANL, Joe Dodge, Jason Bessuille, Jim Kelsey, Ross Corliss, Camelia Mironov MIT
July 29-30, 2019 - BNL

## Slide 2: Focus scope from WBS structure:
  WBS number: WBS Title:
  3.02.03.02.01 Mechanical detector design
  3.02.03.01.02 End Wheels
  3.02.03.01.03 Mechanical Fabrication
  3.02.03.02.03.01 Cylindrical Support Structure CYSS

## Slide 3: MVTX Detector nomenclature:
Layer 0
Layer 1
Layer 2
Layer 3, outer shell
staves
Patch panels, (PP1)
Analog and digital power pig-tails, FPC

## Slide 4: MVTX detector parameters:
Estimated total weight for four layer half assembly – 1.1 kg
Estimated total power for four layer half assembly – 90 watts
  24 staves, 9 MAPS chips, 180 mW/chip
CYSS – cylindrical support structure (layer 3)
  Radius cylindrical end to service barrel – 107.50 mm
  Overall length – 606.42 mm
  radius cylindrical end wheel – 52.7 mm
Survey markers: CYSS aluminum end flange and CYSS large aluminum half ring – location for pins
Cooling – room temp, water, negative pressure
  Flow: 3 liters/hour/stave

## Slide 5: MVTX half assembly:
MVTX half detector with cables, cooling lines interconnection patch panel at the end of the service barrel
MVTX half detector without services
Detector

## Slide 6: MVTX Detector – stave mounts:
Ruby sphere mounted in carbon-PEEK block, matching socket at end of stave,
Secured with a screw.
Ruby sphere mounted in PEEK block, matching slot at end of stave assembly, secured with a screw.
Carbon composite end flange
Carbon composite conical shell
Prior to mounting staves, both end flange and conical shell are mounted in a precision assembly fixture where the spacing is set using a master stave - locate mounting blocks.

## Slide 7: Integrated stave grounding:
Stave cold plate is Parylene coated to isolate the glued MAPS chips.
A nickel foil embedded in the cold plate has a wire attached using conductive epoxy. This wire runs comes out along the digital FPC, where it is soldered. This ground appears on a separate pin on the digital power SAMTEC connector.
Ground wire coming out from cold plate
Ground wire running along digital FPC from stave
Ground wire soldered into digital FPC brought out through SAMTEC connector

## Slide 8: MVTX, end wheel assembly:
Each detector layer’s end flange is registered in the precision aluminum end flange of the outer shell.
Each of these detector layers is registered in this flange by two pins and secured with screws. Additional holes are to allow for dry air to pass through, air flow ~ 200. l/hour.
Aluminum end flange, air vent holes can be used for survey
Carbon composite shell
End wheels

## Slide 9: Start producing detailed drawings:
Detailed production drawings for layer 0 end flange composite pieces for prototype fabrication -

## Slide 10: MVTX Detector beryllium beam-pipe:
R=20.765 mm sPHENIX
Beryllium beam-pipe.
ALICE beam-pipe R=19.0 mm
R=22.75 mm, layer 0
end flange, the delta is 1.985 mm
Note; the Inner Radius for the outer shell end flange is also 22.75 mm

## Slide 11: MVTX Detector stave positioning:
In order to accommodate for the larger beam-pipe in sPHEINX vs the ALICE detector and maintain hermeticity in all three layers, the staves were translated in radius and slightly rotated.
Gap 370 microns,
Detail A
Detail A

## Slide 12: MVTX Detector beryllium & aluminum:
R=21.605 mm, aluminum beam-pipe extensions to sPHENIX beryllium beam-pipe
R=22.75 mm, layer 0 end flange, this delta = 1.145 mm

## Slide 13: 3D mock-ups used to aid design phase:
Verification of pass-through concept for power cables from stave
Patch panels #1

## Slide 14: MIT 3D prints of MVTX shell assembly:
Verification of smaller diameter to fit with in INTT detector envelope as well as verifying that the shells nestle together

## Slide 15: MVTX conical ends assembly & CYSS:
Aluminum pass-through patch panels in PP1, maintain structure between detector layers
As the MVTX detector is assembled from the outer shell to the inner layer; the next layer’s shell is captured by the previous layer’s inner cylindrical ring – attached to the aluminum pass-through panels
PP1 patch panel
CYSS

## Slide 16: Composite fabrication, CYSS:
CYSS – cylindrical support structure
  Detailed drawing
  Vendor qualification
    Molds and fixtures
    Material selection
    Tolerance requirements
  Two possible vendors in Europe;
    Loson, in Milan, Italy
    Work-Shape, in Les Serres, France
  US fabrication
    LBNL Composite Shop, Berkeley, California

## Slide 17: FEA study of current MVTX design:
Detailed FEA analysis has already been carried out on all elements of the ALICE ITS design, which in scope is very similar to the MVTX detector. Similar analysis will be studied at MIT on the latest CAD model/assembly.
The goal of the structural analysis will be to minimize the maximum sag of the detector and maximize the first natural frequency
  ALICE conical shell design max sag of 115 microns, 1st natural frequency 46 hertz, note; ALICE half detectors are mounted horizontally, MVTX detector halves are vertical

## Slide 18: Patch panel design:
Using layer 0 the signal cables transition from the stave FPC to a SAMTEC firefly cable, which runs the length of the service barrel to PP2
The power extension of the stave FPC terminates 400. mm further away in Z in a patch panel that is a part of the service barrel
Steve water cooling lines
PP2

## Slide 19: PP3 patch panel at end of service barrel:
Data cable interconnection,
Samtec Fire-Fly high density
connection
Fisher S105 + DPB 105
Analog and Digital power + stave cooling plate carbon ground
Pass through hole for water line

## Slide 20: MIT and LANL engineers at CERN:
It was to our great benefit to be able to work with Corrado Gargiulo, the chief engineer for the ALICE ITS upgrade project, his sharing of information has been invaluable.

## Slide 21: Schedules & Milestones
WBS 3.02.03.02.01
WBS 3.02.03.02.02
WBS 3.02.03.02.03.01
WBS 3.02.03.02.03

## Slide 22: L3 Technical Overview
Current CAD model for the MVTX detector and service barrel are near completion
Work on producing detailed drawings for both composite and aluminum pieces are in production
Demonstration of current design for patch panels has been shown to work with stave cabling, using 3D printed models
On-going integration issues with other tracking detector systems have been addressed through the sPHEINX Office of System Integration (OSI)

## Slide 23: Schedule Drivers
Integration management – ongoing
FEA studies – next six months
Detail drawings for shell components – next four months
CYSS production – next three months prototype
Stave testing and qualifying – production beginning at CERN
Jigs and fixtures for assembly – design and fabrication next eight months

## Slide 24: Status and Highlights
Update completed for MVTX CAD model, compatible with other sPHEINX tracking detectors (INTT and TPC)
Negotiate with BNL CAD department on extending the current PHENIX beam-pipe
Looking at commercial vendors to produce carbon composite pieces for assembly, produce prototype for evaluation

## Slide 25: Back Up

## Slide 26: Precision layer assembly fixture:

## Slide 27
Layer 0 with master stave, fixture used for gluing ruby pads
Layer 1 with dummy staves

## Slide 28: ALICE layer 0 assembly

## Slide 29: MVTX stave cooling circuit:
Detector stave
Service barrel
PP2a
PP2b,
Transition from, 4 to
6 mm
Dia.

## Slide 30: Metrology and survey, stave alignment in layer

## Slide 31: ALICE FEA optimized carbon lay-up, CYSS:
Sag ~ 115μm

## Slide 32: FEA stave static and modal: