## Slide 1: MVTX Scope & Overview
Ming Liu, for the MVTX Group
Los Alamos National Laboratory
MVTX Interim Design Review
November 19, 2018

## Slide 2: Today’s Agenda
13:00 → 13:20 Scope and Overview, 20’
  Speaker: Ming Liu (Los Alamos)
13:20 → 13:40 Electronic Components, 20’
  Speaker: Sho Uemura (Los Alamos National Laboratory)
13:40 → 14:20 Mechanical Components and Installation, 40’
  Speaker: Walter Sondheim (Los Alamos National Laboratory)

## Slide 3: Outline
MVTX technology
MVTX project scope
Design and R&D progress
Near term plan
Document: sPH-HF-2018-001
https://indico.bnl.gov/event/4072/
Submitted to BNL ALD 2/2018

## Slide 4: MVTX Detector
MVTX RUs, PUs & other services
3-layer sensor barrel
- 48 staves, 432 chips
Service cone: signal, power, cooling
and mechanical support
MVTX
parameters
End-Wheel
CYSS: Cylindrical Shell Structure
Extended power FPC

## Slide 5: Scope of the MVTX Project
MAPS Staves & Electronics
  Readout Integration R&D by LANL LDRD
  Frontend: ALICE/ITS, RU
    Backend: ATLAS FELIX
    Reprogram RU & FELIX for sPHENIX
  Production:
    84 ALICE/ITS-IB staves from CERN
      Acceptance test @LBNL
      48+spares(36)
    60 ALICE/ITS-RU from CERN
      Acceptance test @UT-Austin, 48+spares(12)
    sPHENIX production, 8 ATLAS/FELIX
      Acceptance test @LANL
    Final detector assembly in US
      LBNL and BNL
  Ancillary systems, “adopt” ALICE system
Mechanics & Cooling
  Changes to ALICE/ITS inner tracker mechanical structures,
    End Wheels
    Cylindrical structure shells
    Detector half barrels
    Detector and Service half barrels
  Mechanical Integration,
    Conceptual design by LANL LDRD
    Prototype by sPHENIX R&D, MIT/LANL
    Design integration frames
    Composite structures, LBNL
    Installation tooling etc.
  Adopt ALICE cooling plant design
    Modifications to fit sPHENIX
    Much smaller heat load than ALICE ITS
Sho Uemura
Walt Sondheim
Walt Sondheim

## Slide 6: MVTX Readout, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit | Back End-FELIX/DAM
one pixel
ALPIDE pixel:
Shaping
Digitization
Zero-suppression
3x buffer
ATLAS Front-End Link eXchange (FELIX):
sPHENIX Data Aggregation Module(DAM)

## Slide 7: MVTX Full Readout Chain Demonstrated
4-hit track
4-MAPS telescope
120 GeV proton
beam
Tracking spatial resolution
achieved: <5 um
4-MAPS
telescope
Fermilab Test Beam: Feb-Mar, 2018

## Slide 8: Updated MVTX Model with Extended Power FPC
This model shown with 38 and 40cm flat power extension cables
Walt’s talk
PP-1a: signal cables
PP-1b: power cables

## Slide 9: Confirmed HIC with Extended Power FPC
Built and tested two HICs at CERN in the week of 9/17/2018
  No change in sensor performance (noise, threshold) observed, as expected;
More details presented by Dr. Sho Uemura at last Friday’s sPHENIX general meeting 9/23/2018
60cm PWR FPC
40cm PWR FPC
ALICE: 15cm PWR FPC
Followed identical
ALICE IB QA test procedure,
with a 8m SamTec cable!
Sho’s talk

## Slide 10: MVTX + 4-layer INTT 3-D Mockup: OK
MVTX and INTT
Space conflict resolved!

## Slide 11: ALICE HS SamTec Signal Cables: ~8m!
Two cables per IB stave: 2.65m + 5.30m
PP-2
HDR-203194 (Type B)
HDR-206142 (Type A)
Two
Staves
Two
RUs
L: 2650 mm
L: 5300 mm
Sho’s talk
PP-1
(for sPHENIX, this one could be shorter, ~1m,
optimization in progress)
(for sPHENIX, this one could be longer,
optimization in progress)
The total length of readout cable < 8m, from stave to RU

## Slide 12: Global Mechanical Integration
MVTX, INTT and TPC/HCal
  MVTX/INTT detector designs modified
  Global interface being developed
  Office of System Integration
L = 350.0 cm
TPC
TPC
R= 209.6cm
Walt & Sho
INTT
MVTX
PP-1a:
short signal cables
PP-2:
Signal and power cables
PP-1b:
power cables
Service Barrel

## Slide 13: Detector Assembly Plan at LBNL
Precision positioning and installation of staves on end-wheels
IB CYSS
Layer 0
Layer 1
Layer 2
Follow ALICE IB assembly procedures to build half-detectors for MVTX
QA records in DB, travelers
Modified jigs for MVTX
Build two full half-barrel detector with the service structures
ALICE 1st half inner layer being assembled
6/2018@CERN
staves
Install SamTec & power cables during half-barrel assembly with the service barrel at LBNL(?,TBD)

## Slide 14: MVTX Services
MVTX Service rack located close to MVTX detector
  RU
  PU
  “Minimal cable length”, < 800cm
48 RU and 24 PU
RU and power units located inside the same crate
  1PU ->2RU
CAEN bulk power supply located on the top platform or on the ground
MVTX
RU/PU
& PS

## Slide 15: Near Term Task & Schedule
RU production through ALICE: 60 RUs
  Being started at CERN, first batch of ALICE production ~ Dec., 2018
  sPHENIX RUs available: ~Summer 2019
  Acceptance test and QA at UT-Austin: starting ~summer 2019
    Good opportunity for training and contribution
Stave production through ALICE: 84 staves (ALICE Gold/Silver QA)
  sPHENIX sensor production ~Dec. 2018
    3 months (wafer production) + 1 month (dicing & testing)
    Stave assembly starts @CERN, ~ April 2016, will take 6~12 months to finish
    Training & contribution at CERN, Stave test and QA
  Acceptance test and QA at LBNL, ~Summer 2019
    Hand-carrying staves to LBNL, ~4 trips, ~20 staves each trip
Mechanical system integration design
  In good progress, under OSI
Carbon and non-composite structure design and fabrication
  Design – LANL/MIT/LBNL
  Carbon structures fabrication @LBNL
  Non-composite structure fabrication @MIT

## Slide 16: Schedules and Milestones
CY-2018 | 2019 | 2020 | 2021 | 2022 | 2023
Stave & RU
production
Power system
production
Detector mechanics design & production, global interface to sPHENIX
Service barrel
design & production
End Wheels
CYSS
Half barrel #1
Half barrel #2
Half barrels
arrive @BNL
MVTX installation & commissioning @BNL
RU, FELIX, PS, cables etc.
Install half barrels
@sPHENIX IR
Ready for beam;
sPHENIX day-1 run
FELIX
production
Barrel Assembly & Testing @LBNL
ALICE IB stave done;
Facilities available for
sPHENIX production;
A window of opportunity:
Low technical risk
Cost saving
sPHENIX: CD1/3a CD2
MVTX
1st collisions
Installation
Global integration
/interface design?
design & procure
interface to
sPHENIX rails
Design & procure
sPHENIX rails
To be finalized @FSU 12/2018
Work in progress:
LANL/MIT/LBNL
Design and fabrication

## Slide 17: Recent Progress - I
Completed sensor/HIC/stave evaluations at CERN
  Built and tested two HICs with 40cm and 60cm long power FPC
    Confirmed sensor performance same as the ALICE default configuration
  Sensors irradiated up to 2.7MRad, no problem (updated 9/18/2018).
  Addressed all recommendations on stave/sensor R&D from recent BNL review
Technical specs document completed for production
  Cost are set for staves/RU, UTK has started purchase paperwork
  RUs, production starts soon as part of ALICE production
  Staves, sPHENIX production starts ~ January 2019, expect to last 6-12 months
MVTX/INTT integration
  Mechanical design being updated and mockup done
  Inner tracking task force completed evaluation, preferred INTT-layer < 4
  SamTec readout cables
    ALICE confirmed signal performance with 8m long readout cables
Cables
  BNL approved the use of SamTec blue cables
    Electrically better & mechanically compact
  Signal and power cable samples ordered for mechanical global system integration mockup

## Slide 18: Progress & Plan - II
Preliminary design from CERN for stave transportation plates
  To get quote soon for production at CERN
MVTX/Tracking workfest @FSU, 12/5, 8,9
  Project update, task, schedule & plan
  Tracking and simulations
  Update physics plots
Extended design from CERN
for MVTX
ALICE ITS IB

## Slide 19: sPHENIX MVTX Group: Institution Roles
Major institutions lead key tasks

## Slide 20: Summary: MVTX - WBS 3.2
MS Project being updated, now moved into P6
  Stave and RU production through ALICE, moved out of the scope
  The rest of tasks, being optimize for cash flow and schedule
Early procurements of staves and readout units (RU) through US-Alice
  DOE and BNL agreed, DOE directly pays UTK/US-ALICE
  Received signed letter from CERN on the cost of 60 RUs and 84 Stave, ~$1.36M
  Purchase paperwork in progress at UTK, aiming to complete by ~ December 2018
About $5M to be added to the sPHENIX Management Portfolio
  Open MVTX accounts in progress
  As a separated project from the MIE, for the rest of MVTX tasks
    Mechanical system design and fabrication
    Monthly report to sPHENIX and BNL upper management
    Update baseline cost and schedule by January 2019
  Will NOT be part of CD-2/3 DOE review
    Prepared for a separate DOE review in FY19

## Slide 21: Backup slides

## Slide 22: MVTX: MAPS-based VerTeX Detector
sPHENIX Inner Tracking: MVTX
“Adopt” ALICE ITS/IB:
- Minimum risk
- Maximum physics
ALICE ITS Upgrade @CERN;
Inner Tracker System (2021+)
Key integration tasks:
Readout
Mechanics
Leveraging on extensive R&D and design work by ALICE
sPHENIX@RHIC
(2023+)

## Slide 23: Monolithic Active Pixel Sensors (MAPS) The Next-Generation, State-of-the-Art Pixel Tracker
Advantages of ALICE PIxel DEtector (ALPIDE) sensor:
Very fine pitch (27μm x 29μm), for superb spatial resolution
High efficiency (>99%) and low noise (<10-6), for excellent tracking
Time resolution, as low as ~5 μs, for less pileup
Ultra-thin/low mass, 50μm (~0.3% X0), for less multiple scatterings
0.5M channels with on-pixel digitization, for zero-suppression and fast readout
Low power dissipation, 40mW/cm2, for minimal service materials
An ideal detector for QGP physics!
50 μm
~28 μm
ALPIDE design
Flexible Printed Circuit(FPC)
9 Chips
Cold plate
A 9-chip MAPS stave, 1.5cm x 27cm
ALPIDE sensor:
1.5cm x 3.0cm, 0.5M channels

## Slide 24: MVTX Sensors and Electronics Production
Major hardware:
  48 ALICE ALPIDE Staves + Interface Cables
  48 Front End Electronics (ALICE RUv2)
  6 Back End Electronics (ATLAS FELIX v2)
  6 EBDC Linux servers
  24 Power Boards + CAEN Supplies + Cables
  48 Stave to RU cables
  144 data fiber optic cables (3 fibers x 48 FEE)
Stave production: total 84, 75% spares
  Two inner layers: 12+16=28
  10% spares: 8 staves
RU production: 60 in total, 25% spares
ALICE ITS/IB stave
ALICE ITS RU

## Slide 25: sPHENIX vs ALICE
 | ALICE (Run3) | sPHENIX (Max) | Ratio of data rates sPHENX/ALICE
Pb+Pb / Au+Au | 50kHz | 200 kHz | 0.3
p+p | 200kHz | 13 MHz | (1.6)
Trigger/Readout | 50 kHz/(C.R.) | 15 kHz | -
MB Event track multiplicity dN/dη
  sPHENIX = 1/3 ALICE (pp)
  sPHENIX = 1/5 ALICE (AA)
sPHENIX triggered data rate fits well within ALICE readout hardware specs

## Slide 26: Sensor Irradiation Test – OK at 2.7MRad
Continuous effort by ALICE (@NPI, Czech)
BNL review recommendation: test sensor up to 1MRad
https://indico.cern.ch/event/758048/

## Slide 27: Projected Radiation Level after 5-year Runs
sPH-TRG-2018-001
Projected sPHENIX integrated luminosities after 5-year operation
  AuAu: Lum. = 214 nb-1
  pp+pAu: Lum. = 1340 pb-1
Projected sPHENIX MVTX L0 fluence:
Outer layers:
L1 = 0.6 x L0; L2 = 0.4 x L0
TID = 1060krad
NIEL = 6x1012 Neq/cm2
PHENIX study
arXiv: 0710.2676 [nucl-ex]
Sensors tested to full MVTX NIEL and ~3x TID @ALICE

## Slide 28
Type-A
Type-B
Type-A

## Slide 29: Stave and RU Production QA Plan
Staves
Purchase 84 staves from ALICE/CERN
  48 + 28(spares for 2 inner layers) + 8 spares
  Production following the completion of ALICE ITS/IB
  Starting ~Oct. 2018, will last 6-12 months
  Fully tested at CERN before shipping to US
    All Gold/Silver staves (same as ALICE IB)
    A LANL postdoc (Dr. Yasser Morales) oversees production QA at CERN
Acceptance QA at LBNL
  Full test and QA
    Electrical
    Mechanical
  Detector assembly at LBNL
Readout Units
Purchase 60 RUs from ALICE/CERN
  48 + 12 spares(20%)
  To be part of ALICE production
    Cost saving
    Minimize technical risks
  Initial test at CERN
Acceptance QA at UT-Austin
  Full test
  LANL as the 2nd test site

## Slide 30: sPHENIX/MVTX IB Stave Assembly Procedure at CERN by ALICE ITS Group
Prepare sensors and FPC
Glue 9 sensors to FPC
Wire bonding 9 sensors to FPC
Solder power flex PCB to FPC
Glue HIC to coldplate/carbon space frame
A stave is ready for QA
CMM

## Slide 31: Two HICs Produced and Tested at CERN w/ Extended Power Cables NO noticeable difference in sensor performance, as expected
MVTX: 40cm flex power PCB
MVTX: 60cm flex power PCB
ALICE IB: 15cm

## Slide 32: HICs Test Results from CERN
Before: 2 ALICE IB HICs
After: same ALICE HICs, replaced power FPCs
Noise level: ~4 e’s; Threshold: ~180e’s; MIP: ~1000 e’s
Chip-0
Chip-8
HIC1
HIC2
Noise
Noise
Thr.
Thr.

## Slide 33: FPC Extension for Connection to Electrical Services
FPC
DVDD
AGND
DGND
DVDD
DGND
DVDD
AVDD
AVDD
AVDD
AGND
AGND
DGND
The connection to the service cables is achieved by a double FPC extension which is soldered to the HIC
x-section at interconnection between FPC and extensions
signal lines (FPC)
analogue power
digital power
FPC
AVDD
AGND
AVDD
AGND
AGND
AVDD
Flex power extension
FPC
DVDD
DGND
DVDD
DVDD
DGND
DGND
Flex power extension
From Antonello Di Mauro
Modified for sPHENIX:
15cm -> 40cm

## Slide 34
2-layer flex, PI: 50 µm, Cu: 35 µm, solder mask: 20 µm
The two flexes are connected together, AVDD is transferred from top to bottom
The PWR extension is connected to the FPC by iron soldering and wings are cut.
FPC Extension for Connection to Electrical Services
digital
analogue
analogue
digital
digital
AVDD
DVDD
DGND
AGND
From Antonello Di Mauro
Longer copper traces ~30cm
for sPHENIX, no other components
Unchanged

## Slide 35: LANL LDRD Activity Highlights
Sensor source test
MAPS evaluation
Readout integration
4-sensor telescope
Test beam at Fermilab
Mechanical & cooling
Signal integrity & cables
Cooling system
prototype
Service cone R&D
FPC power extension R&D
4-ALPIDE Telescope;
5m-long SamTec cables
Readout R&D
stave
RU