## Slide 1: Dark Photon/Higgs Search in the SeaQuest/E1067 Experiment at Fermilab
Ming Liu
Los Alamos National Lab
Light Dark World International Forum 2017
Pittsburgh, PA

## Slide 2: Outline
Dark sector physics @SeaQuest/E1067
  Experimental setup
Detector upgrade @SeaQuest/E1067
  Commissioning run in 2017
Future plan and opportunity
  Phase I: 2017 - 2020
    Parasitic run with E1039(polarized Drell-Yan)
    Electron/hadron ID w/ EMCal upgrade
  Phase II: 2020 -2025+
    Dedicated dark photon program @Fermilab
You inputs to further develop the program

## Slide 3: Dark Sector Physics at Low Mass
Current and near future high-intensity colliders and fixed target experiments offer an ideal environment to probe dark sector physics,
in O(MeV) ~ O(GeV), SeaQuest@Fermilab
WIMP Search
P. Schuster et al.

## Slide 4: SeaQuest Dimuon Experiment at the Intensity Frontier at Fermilab
25 m
Beam
120 GeV proton from Main Injector
19ns RF, 4s spill, 0.5×1013 protons per spill
Focusing magnet
and solid iron dump
Δpt = 2.9 GeV
Spectrometer magnet
Δpt = 0.4 GeV
Absorber wall and proportional
tube based Muon ID
Target system
Liquid H and D
Solid C, Fe, W
High intensity proton beam: “beam dump mode” @SeaQuest/E1067
35K fb-1 (in a 2-year parasitic run, 1.4x1018 POT @7% beam)
LHC-II: 300 fb-1 (~2025), achieved 25fb-1 in Run-I
- Beam dump mode: p+Fe collisions! Target ~ 10%λI
- Parasitic run mode possible with other experiments, E906/E1039
SeaQuest

## Slide 5
SeaQuest: Nuclear Physics with Drell-Yan
DOE/Nuclear Physics Programs: 2008-2017(E906), 2017-2020(E1039)
Quark Energy Loss dE/dx in p+A collisions
High mass Drell-Yan:
4<M<8 GeV

## Slide 6
A target Drell-Yan event
A beam-dump dark photon event --- parasitic run possible!
E906
A new idea
developed
in ~2014

## Slide 7: A Great Opportunity Dark Photons and Dark Higgs Search at SeaQuest
Photon portal: “vector”
Higgs portal: “scalar”
θ = μ v/mh2
A great advantage
for proton beam!

## Slide 8: Dark Photon Detection in the Dilepton Channel
Drell-Yan like
p0, h, … decay
Bremsstrahlung
p
p
l+
l-
(DM)
(DM)

## Slide 9: Upgrades Required for Dark Sector Search Events collected in SeaQuest/E906
Invariant mass spectrum from 2015 data
Data agrees well with Monte Carlo (spectrometer works as expected)
Data with Mass > 4.2 GeV are mostly dimuons coming from the Drell-Yan process
For Dark Photon Search:
1)DAQ upgrade required to collect low mass dimuons
2)Trigger upgrade for displaced/long-lived particles
J/y Monte Carlo
y’ Monte Carlo
Drell-Yan Monte Carlo
Random Background
Combined MC and bg
E906 preliminary

## Slide 10
A heart-full endorsement
from Fermilab Director and PAC
July 15, 2015!
A New experiment! SeaQuest/E-1067
Generous LANL LDRD support:
- 2016-2018
- $1M to implement
the trigger/DAQ upgrade and theory development
Goals:
Trigger installed, 2017
Physics run, 2017-20
Preliminary results 2018!

## Slide 11: Detector Upgrades and Expected Signals
Dark photon trigger upgrade
  A fine-granularity trigger/tracking to tag dimuons from the same decay Z-vertex
  A new trigger for events with displaced down-stream dimuons
Unique signals
  Displaced dimuon decay vertex for long-lived particles
  Invariant mass peak in dimuon mass spectrum
Planned beam time
  Run parasitically with E906/E1039 (2017-2020)
  Possible dedicated runs later with further upgrade (e+/-, h+/-)
Z (meter)
-- 2.5%
-- 6.0%
Dimuon mass resolution

## Slide 12: A New High-Granularity Displayed Dark Photon/Higgs Dimuon Vertex Trigger
Y-Plane (non-bending) Trigger:
A quadrant panel: 80cm x 80cm (100cmx100cm @ST-2)
  ST1: 1cm x 1cm x 80 cm scintillating strips, SiPM readout
  ST2: 2cm x 2 cm x 100 cm strips
- Straight line projection, σZ ~30cm
Displaced z-vertex, mostly low mass < 3GeV
St1
St2
Coincident Z-vtx
Matched @Lvl-2
Dimuon Z-vertex (cm)
Z
High rejection power, low rate, < 1 kHz (previous E906 DAQ limit)
X
Y
ST1
ST2
Z1=9m
Z1=12m

## Slide 13: Completed modules, 8 of them in total
Station-1: 1cm scintillators, 80 x 80 cm2,
Station-2: 2cm scintillators, 100 x 100 cm2

## Slide 14: Trigger detectors shipped to Fermilab for installation 4/3/2017

## Slide 15: Dark Photon/Higgs Trigger Upgrade Completed in Summer 2017
LVL-1 + LVL-2
Trigger &
Calibration
Systems
Station-2 Trigger Plane
Successfully took 1-week of production data with E906!

## Slide 16: DAQ Upgrade Completed in Early 2017
Take advantage of beam structure: 4 sec/ 60 sec.
Locally store data during collisions
  10x DAQ improvement
4sec, 56sec to others
Time
New DAQ boards

## Slide 17: Trigger Detector Performance from 2017 Run
Hit rate vs Channel
Hit occupancy
Station-1
Station-2
Performed as expected

## Slide 18: Expectations from 2017 data … Preliminary results ~2018
Expectation from 2018 run:
The dashed black curve stands for 4 months of data, blue dashed curve stands for 1 month of data,
and red curve shows 5 days of existing data.
2017
2018
2019
2020
Displaced Dark Photon
Prompt Drell-Yan Like
Eta decays
1-week
1-month
4-month
Polarized target
installation/E1039

## Slide 19: Full Projections - Dark Photons (parasitic run w/ E1039: 2018-2020)
Signals considered:
Drell-Yan like
Eta decays
Bremsstralung
Covers a wide range of unexplored parameter phase space
Displaced dimuons
- Minimal SM background
Prompt dimuons
- Good coverage
- Possible dedicated runs later to fully
restore mass < 3GeV (Phase-II)
Possible EMcal upgrade (a new proposal)
Access below 200MeV with di-electrons
Work in progress!

## Slide 20: SeaQuest/E-1067 Upgrade Opportunity
Add tracking detectors close to “target” to improve mass resolution
Add EMCal, PID
e+/-, h+/- , π+/-
EMCal

## Slide 21: Displaced Low Mass Dark Photons with EMCal upgrades
Detector upgrades
  EMCal: e+/-
  HCal: π+/-
  Recycle from other experiments, PHENIX/RHIC etc.
Timeline of dedicated runs
  2020+
Detector configuration
  Access low mass region with optimized FMag settting
Projection: POT 1.4 x 1018

## Slide 22: EMCal Upgrade: More Physics
EMCal opens up:
  dark 𝝆 decays to 𝛑𝛑
  enhanced dark higgs sensitivity
  SIMP, “dark QCD-like” etc.
Potential bonus of better background rejection on trigger level (studies underway).

## Slide 23: EMCal Identified & DOE Approved!
Two EMCal sectors are available from PHENIX experiment at RHIC, ~April of 2018
- dE/E = 8.1%/sqrt(E) + 2.1%
- dT < 200 ps
- Excellent e/pi separation
PHENIX @RHIC

## Slide 24: Dark Higgs!
Phase-I:
High-mass: μ+μ- and hadrons
Advantage of using hadron beams
with muon probes over electrons
Phase-II:
Low-mass: e+e-, <200MeV possible
High-mass: hadrons, (5x)
Y. Zhang et al, arXiv:1502.06983
arXiv:1312.4992
θ = μ v/mh2
e+e-
μ+μ-
Electron ID
upgrade!

## Slide 25: Projected Dark Higgs Sensitivity POT:1.4x1018 (Phase-I)
Dimuons with downstream displaced decay vertices
Limited sensitivity to “prompt” large mixing case due to small cross-section
Dark Higgs or dark photons?
  Dimuon kinematic and angular distributions
Y. Zhang (2015)
POT:4x1020

## Slide 26: SeaQuest/E1067 Summary and Outlook
2017
  Successfully completed Trigger and DAQ Upgrade
  Successfully took production data parasitically with E906
  Data analysis in progress
  Ready for full data taking with E1039
2018
  Take more data parasitically with Polarized Drell-Yan experiment E1039
  First preliminary search results
Fermilab dark sector physics program @Seaquest/E1067:
Phase-I (2017-2020)
  Great discovery potential!
  Parasitic data taking with E906/E1039, 2017-2020
  POT 1.4 x1018 or more
  Possible detector upgrade, add electron and hadron capability
Phase-II (2020-2025+)
  A dedicated dark sector physics program at Intensity Frontier!
Dark Higgs
search
2015
2016
2017
2018
2019
2020+
Preparation Phase-I (parasitic runs)
Phase-II

## Slide 27: Comparison with SHiP Proposal
120 GeV@FNAL: 2018 -2020
1.4x1018 POT or more, future dedicated runs
Phase-II: 2020-2025+, POT: 4x1020
400 GeV@SPS: 2025 -2030
4x1020 POT
POT:4x1020

## Slide 28: Come to Join Us!

## Slide 29: backup

## Slide 30: Beyond Exclusive Channels possible missing pT measurements being explored
Chien-Yi Chen, 2017

## Slide 31: Side View of the Upgraded SeaQuest Experiment
F Mag
K Mag
St-1 trigger plane, 160 x 160 cm
Made of 4 1cm x 1cm x 80cm
scintillator planes
St-2 trigger plane, 200 cm x 200 cm
Made of 4 2cm x 2cm x 100cm
scintillator planes
ST-1
ST-2
ST-3
ST-4

## Slide 32: Very Successful Team Work!

## Slide 33: Trigger, DAQ R&D and Final Cosmic Test @LANL in 2017
TDC_1
TDC_2
Trigger & DAQ hardware and firmware designed and tested at LANL, in collaboration with Fermilab Engineers
Readout from a full module for cosmic test
  Full SiPM readout and Trigger
  E906 upgraded DAQ and firmware
Timing resolution, < 1.5nS (19nS RF)
Detector eff. > 96%

## Slide 34: All Trigger Detectors Designed and Built at LANL, Truck loaded to Fermilab on 4/3/2017
Eight trigger detector modules
Electronics and Power supplies

## Slide 35: New trigger rate: ~5%DAQ
Parasitic run OK!
Down stream view

## Slide 36: Trigger Scintillator Size Optimization Single Muon Z-Vertex Resolution
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Sigma_Z ~ 30cm
Current
E906
Forward: 1cm
Backward: 1cm
Forward: 1cm
Backward: 2cm
Forward: 2cm
Backward: 2cm
E906
σZ (cm)
σZ (cm)
σZ (cm)
Open. Angl.

## Slide 37: Search Mode (2): “Prompt” Dark Photons vs Drell-Yan Bump hunt at Z-vertx < 3m
Expected Drell-Yan like signal and backgrounds:
Drell-Yan Background
Dark photon
signal
Excluded phi
resonance region
Work in progress:
- optimization …,
- understand BG ...

## Slide 38: Low Mass Prompt Dimuon Trigger Rate Study
Current E906 setup
Proposed 2-layer trigger upgrade (10x improvement)
Additional Y-trigger after ST-3 absorber, and also using existing E906 X-Plane trigger
(additional ~2x improvement)
DAQ upgrade completed
  Previous E906 DAQ 1kHz
  Now 10+ kHz
  Can take all dark photon events of interest
Expected (Prompt) Low mass dimuon trigger performance
4s spill, 60s cycle
time

## Slide 39: Displaced Dark Photon Trigger Logic
Q1 (LVL1)
Q2 (LVL1)
Q3 (LVL1)
Q4 (LVL1)
LVL2
(vtxZ matching)
4 x 16-bit from 4 V1495 boards
(2 x 32LVDS cables)
Per quadrant Q(1-4): 80(ST1) + 50 (ST2) + 2x8(ST4-Y1/2) = 146, FANOUT ST4 Hodo
DAQ/Data stream
TS
(12 inputs total)
(1-free bit available)
DP Trigger
1-bit
DAQ Trigger
V1495
Trigger fired: Q1 & Q3 & VTX
VTX