## Slide 1: Open Heavy Flavor Physics with the sPHENIX MVTX Detector at RHIC
Ming X. Liu
Los Alamos National Laboratory
for the sPHENIX Collaboration
WWND 2019, CO

## Slide 2: Outline
Science
MAPS-based VeTex detector (MVTX)
Physics prospects

## Slide 3: The Scientific Mission at RHIC

## Slide 4: Three Physics Pillars
Jet cor. & substructure
Justin Frantz, Monday sPHENIX jet physics
Upsilon spectroscopy
Size of the probe
ϒ(2s) – 0.56fm
ϒ(3s)-0.78fm
ϒ(1s) – 0.28fm
Parton energy loss & cor.
mass dependent
This talk : HF program

## Slide 5: Heavy Quarks - Unique Probe of QGP
Study mass dependence in
  Jet quenching and dE/dx
  Flow – interaction with medium
Access QGP properties
MeV
1
10
102
103
104
mu md
LQCD
TQGP
mc
mb
Tc
ms

## Slide 6: Charm RAA
RAA (D-meson) ~ RAA (h) at high pT ~> 4 GeV/c
significant suppression of charmed hadron RAA in central A+A collisions
strong charm-medium interactions
mass effect expected important at low pT, dead-cone effects etc.
STAR: arXiv:1812.10224

## Slide 7: Charm V2
v2 of D0 follows the same trend as light hadrons
Charm quarks flow the same as light quarks
Strong coupling to medium at low pT

## Slide 8: Direct Flow of Charm at RHIC
Singha, WWND19

## Slide 9: Beauty?
RAA (B->e) > RAA (D->e, h) @low pT
B+ & b-jet ~ light hadrons & charm @high pT
STAR, QM17
Highly desired:
precision measurements of
B @low pT ~< 50GeV

## Slide 10: The sPHENIX Detectors
Φ ~ 5m
Outer HCal
SC Magnet
EMCal
TPC
INTT
15 kHz trigger
>10 GB/s data
MVTX
Inner HCal
Parallel Activities “upgrade”
MAPS-based Vertex Detector (MVTX)
Intermediate Silicon Strip Tracker (INTT)
Baseline detectors: HCal/EMCal/TPC
Notes: 15kHz matched to collision rate.

## Slide 11: sPHENIX MVTX Detector Design
ALICE ITS Upgrade:
Inner Barrel Tracker
Adapt ITS/IB design
- Min. Risks
- Max. Phys.
Adapts ALICE ITS/IB design, modifications to fit sPHENIX environment:
-Sensors:
Use ALICE ALPIDE sensors and the identical ITS/IB design of the active part
-Readout:
A hybrid design using ALICE frontend Readout Unit(RU) and ATLAS upgrade backend PCIe based FELIX boards for sPHENIX
-Mechanics:
Modified mechanical frame design for sPHENIX
R = 2.5/3.5/4 cm
Z = 27 cm
Modified MVTX detector
layout for sPEHINX

## Slide 12: MVTX Electronics, Power and Controls
Power Board
Filtering Capacitors
Samtec Twinax “FireFly”
9 Data (1.2Gbps)
1 Clock, 1 Control/Trigger
Readout Unit
Front End
Regulated Power
FELIX
Back End
Data (9.6 Gb/s max)
Control
Trigger
Alpide Sensors
FPC
Cold Plate
regulators
Power
5-10 m
GBT Optical Links
9-sensor Stave
DCS
CAN bus
Power supplies
Power
Trigger & Clock
Interaction Region
Experimental Hall
Counting House
MVTX Detector Electronics consists of three parts
Sensor-Stave (9 ALPIDE chips) | Front End-Readout Unit |Back End-FELIX
(------- ALICE/ITS Hardware --------)
(- ATLAS Hardware -)

## Slide 13: MVTX R&D Highlights 2018 test beam @Fermilab
MVTX Hit Spatial Resolution: < 5 um
Feb-July 2018 FermiLab Test beam facility, test of each sPHENIX detector subsystem
4x MVTX sensor in beam sPHENIX DAQ
INTT
MVTX EMCal HCal

## Slide 14: MVTX Production Status
Active length ~ 30 cm
Diameter ~ 8 cm
Sensor tested with sPHENIX extension
Readout Unit v2
Data Assembly Module (FELIX v2)
Stave & RU: starts soon following ALICE ITS production at CERN
  84 Staves: 3-layer + spares (full inner 2-layer + 20%); 60 RUs: 48 + 25% spares
Back-end DAQ: sPHENIX production of ATLAS FELIX cards at BNL
In close coordination with R&D and production for ALICE/ATLAS Phase-I upgrade
Notes: 48 staves + 100% spares
30-um-pitch, 200 M pixel, 0.3% X0/layer, 4-10 us integration time

## Slide 15
New MVTX Stave Configuration

## Slide 16: sPHENIX Tracking Detectors
Outer tracker: |eta|<1
TPC: gateless and continuous readout
  Provide momentum measurement
δp/p < 2% for pT<10 GeV/c
Inner tracker: |eta|<1
MVTX: MAPS pixel sensors (3-layer)
  Modified ALICE ITS IB staves integrated into sPHENIX
  Precision vertexing
INTT: strip silicon sensors (2-layer)
  Pattern recognition, timing
Diameter ~ 1.6 m
MVTX
INTT
TPC
See also calorimeters – Justin Frantz

## Slide 17: Simulation for b-jet and B-meson
Design to Simulation
sPHENIX Geant4 display of pT=30 GeV/c B+-hadron
MVTX and INTT _
_ MVTX Ladders modeled in details
MVTX sensors
New design: 2-layer INTT (was 4)

## Slide 18: Tracking Performance
MVTX geometry modeled and digitized according to ALICE ITS/IB
Cluster resolution: ~5 µm
DCA2D , DCAz<30 µm down to 1 GeV/c
Robust tracking at top projected RHIC collision rate
DCA_rf

## Slide 19: Open Charm & Beauty Production
Hadron | Abundance | ct (mm)
D0 | 61% | 123
D+ | 24% | 312
Ds | 8% | 150
Lc | 6% | 60
B+ | 40% | 491
B0 | 40% | 455
Bs | 10% | 453
Lb | 10% | 435
b-tagged jet and cor.
60%
0.5%
pT<15 GeV
pT>15 GeV
Exploring and more

## Slide 20: B-hadron Tagging
Impact parameter (DCA) method to tag non-prompt D0 from B-meson decays
Inclusive and exclusive channels possible

## Slide 21: B-meson Projections
A+A: non-prompt D-meson and predictions for sPHENIX
High precision non-prompt-D suppression and flow at RHIC
Determine the bottom quark collectivity → clean access to DHQ at RHIC energy
sPH-HF-2018-001 - MVTX Proposal
Notes: Exploring B->J/psi (and maybe B->e high pT) channels

## Slide 22: B-jet Tagging
Multi-tracks w/ large DCA
2nd vertex mass reco’d

## Slide 23: b-jet Projections
High precision inclusive b-jet suppression and v2 at RHIC
Strong constraints on energy loss models in QGP
Inclusive b-jet v2
A+A: Inclusive b-jet RAA
sPH-HF-2018-001 - MVTX Proposal

## Slide 24: A Broad HF Physics Program
Exclusive B± in most central Au+Au
HF di-jet/hadron correlations, HF jet substructures
HF baryons, chemistry and hadronization
Total b-cross section for Upsilon baseline reference
A great opportunity for new ideas and new measurements
Di-b-jet pT balance
90%
67%
sPH-HF-2018-001 - MVTX Proposal

## Slide 25: sPHENIX Status and Plan
MVTX funded

## Slide 26: A Rapidly Growing Collaboration

## Slide 27: Summary and Outlook
sPHENIX is the next generation flagship heavy ion physics experiment in the US (NSAC LRP2015)
  Jets & Upsilons
  B hadron and b-jet physics enabled by MVTX
MVTX will complete QGP heavy flavor physics at RHIC
  Unambiguous determination of key parameters of QGP through precision study of open HF productions
MVTX on track for day-1 physics in 2023
  Production begins now
  Strong community support, ALICE, ATLAS, BNL, LANL et al
Complement & extend current and future RHIC and LHC QGP programs
sPHENIX Three Physics Pillars
Jets
Upsilons
B
D

## Slide 28: backup

## Slide 30: RHIC Multi-Year Plan: sPHENIX 2022-2026+
Precision vertexing for B-tagging:
  Tracking resolution better than 50um @pT=1GeV
  High multiplicity HI collisions
  Low multiplicity but high rate p+p collisions
  High efficiency and high purity
B hadrons/pT<15GeV: O(1M)
b-jets/pT>15GeV: O(100K)
Evolving

## Slide 31: Recent Achievements on Bottom
LHC 2.76 TeV
RAA(J/yB) > RAA(D)
RAA(eB) > RAA(eD+B)
RAA(eB) > RAA(eD)
RHIC 200 GeV

## Slide 32
Latest Design: 3-layer MVTX + 2-layer INTT

## Slide 33: sPHENIX vs LHC Projections
sPHENIX
projections

## Slide 34: sPHENIX vs ALICE Specifications
 | ALICE (Run3) | sPHENIX
Pb+Pb / Au+Au | 100 kHz (50kHz) | 200 kHz
p+p | 400 kHz (200kHz) | 13 MHz
“Trigger” | C.R. (>50 kHz) | 15 kHz
Event size, dN/dη: sPHENIX = 1/3 ALICE (pp), 1/5 ALICE(AA)
sPHENIX
ALICE

## Slide 35: Monolithic-Active-Pixel-Sensors (MAPS) The next Generation State of the Art Pixel Tracker
Advantages of ALICE MAPS/ALPIDE:
  Very fine pitch (27x29 μm)
  High efficiency (>99%) and low noise (<10-6)
  Fast readout, ~5 μS
  Ultra-thin/low mass, 50μm (~0.3% X0)
  On-pixel digitization, low power dissipation
An ideal detector for QGP b-jet physics!
50 μm
28 μm
ALPIDE design
FPC
9 Chips
Cooling plate
A 9-chip MAPS stave, 1.5 x 27cm2