## Slide 1: RHIC Status and Plans
RSC Meeting
3/23/12
V. Schoefer

## Slide 2: RHIC Status
Good news: We came very quickly to near last year’s peak performace
Bad news: Appears to be exactly last year’s performance
Golden store 16602:
  Peak lumi 130 1030 cm-1s-1, 1.5e11/bunch
  ZDC emittance: 23 pi mm mrad
  Lumi Lifetime comparable to Run 12
Assuming a small increase in intensity at store to 1.65e11 and this is slightly better than peak performance last year (lumi would be ~160 compared with Run11 145 s.u)
Polarization (B, Y) ~ (48%, 44%), averaging all available longitudinal Jet numbers, though not really the same conditions

## Slide 3: Polarization
Energy ramp transmission
  Snake rotation magnitude scan
    Run11 rotation angle scans showed little effect
    Have not tried to adjust the magnitude of the rotation (could be off from 180 degrees)
    Could also affect store lifetime
  Orbit harmonic compensation (APEX)

## Slide 4: Polarization
Rotator ramp transmission
  (see Elke’s presentation for pC data)
  May account for systematic difference between blue and yellow at 255 GeV
  Spin manipulation may not be local to the IP
    Change both rotators of one color at one IP by a large amount, local pol at the other experiment and pC should see no change in direction (change in magnitude might result from depolarization during current change)
    This could also contribute to polarization lifetime

## Slide 5: Polarization
Store lifetime
  Suggestive indication on one store that when snake angle in yellow drifts, polarization lifetime suffers, can scan store-to-store. Adjusts the spin tune, which may be shifted by another source
  Spin tune measurement at store with AC dipole